## Slide 1
How do you verify a complex signal processing algorithm?
Modern testbenches use constrained random (CR) stimulus
  Self-checking CR testbenches require a predictor
  Predictors for complex algorithms can be difficult to come by
Co-simulation may use Python and/or MATLAB and can be an excellent implementation of a predictor
Many people avoid co-simulation because existing frameworks have serious drawbacks
Common concerns with using co-simulation:
  Degradation of simulation performance
  Major architecture changes (existing techniques and infrastructure will not work)
  More complexity in the build process
All these concerns can be avoided by using the right framework and testbench architecture
Some well-known co-simulation frameworks:
  COroutine-based COsimulation TestBench (CocoTB)
  HDL Verifier from MathWorks
B
An alternative framework:
  High-level Abstraction Language API (HALA) developed at Verus Research
All test code must be written in Python
Use asyncio “co-routines” to simulate parallel execution
All HDL infrastructure (constraint solvers, BFMs, etc.) must be replaced with Python equivalent
If MATLAB code already exists, it makes sense to reuse it as a predictor in a testbench
MATLAB functions are run according to a set schedule
Supports both MATLAB and Python; support for other languages possible (any language with C-API)
Utilizes the strengths of both SystemVerilog and the high-level language of choice
Makes NO attempt to replace existing infrastructure
Because the engineer can limit the number of external language calls, simulation performance is not reduced
sean.little@verusresearch.net
Sean Little
Verus Research
A Survey of Predictor Implementation using High-Level Language Co-simulation
Considerations When Using CocoTB:
Co-simulation is the way to go!
Investigating the Options for Co-simulation
Considerations When Using the HDL Verifier:
High-level Abstraction Language API (HALA)
Conclusion
Drawbacks:
Non-standard python code
Simulation performance is reduced
Python attempts to replace all simulation infrastructure
Awkward compilation framework
Drawbacks:
A predictor must be modeled as an entity/module and implemented as a MATLAB function
No built-in BFMs
Careful, nonintuitive tuning required to avoid reducing performance
Awkward MATLAB code
Drawbacks:
Would benefit from more development
HALA outclasses other frameworks by overcoming barriers to adopting co-simulation for predictor design!
Co-simulation can be seamlessly integrated into your existing verification architecture, without attempting replace functionality that already works well.
Use languages for what they were built for!
  MATLAB/Python for algorithm prototyping
  SystemVerilog for testing and modeling hardware
  Co-simulation for predictor implementation
Effective co-simulation can dramatically simplify modern testbench design for verification of complex algorithms.