## Slide 1: What’s New in IEEE 1801 and Why?
Progyna Khondkar
progyna@cadence.com

## Slide 2: Agenda
Overview of different versions UPF LRMs and its Focus
What are the changes and Why?
  The Concept of UPF and Simple Power Intent: UPF 1.0
  The IEEE Standard and Concept of Supply Set: UPF 2.0
  The Evolution of IEEE 1801 Standards: UPF 2.1
  The Information Model of IEEE 1801 Standards: UPF 3.0
  More Evolution of IEEE 1801 Standards: UPF 3.1
  Furthermore Evolution of IEEE 1801 Standards: Coming in UPF 4.0
How changes improves UPF verification
Concluding Remarks

## Slide 3: Differences Between LRM
Release | Year | Standard | Major Focus on Releases
UPF 1.0 | Early 2007 | Accellera | - Focused on adding power intent to HDL (VDD, VSS i.e. supply net and supply port) - Relatively simple concepts and commands (add_port_state, add_pst_state, create pst for PST)
UPF 2.0 | March 2009 | IEEE-1801 | - Backward compatible with UPF 1.0 (create_supply_set, supper set of supply port, net) - Supports IP development, refinement (add_power_state, create_logic_port, and –update)
UPF 2.1 | March 2013 | IEEE-1801 | - Clarifies and enhances UPF 2.0 features (set_repeater, master/slave 0 pin RET, set_equivalent) - Adds a few new capabilities (define_always_on_cell, define_diode_clamp_cell & others ISO)
UPF 3.0 | Dec 2015 | IEEE-1801 | - Clarifies and enhances UPF 2.1 features (new semantic of power model) - Adds UPFIM & new capabilities (SPA is_analog, -parameter for bind_checker)
UPF 3.1 | Sept. 2018 | IEEE-1801 | - Clarifies and enhances UPF 3.0 features (Path base strategy association, precedence rules) - Adds a few new capabilities (UPF Info Model, Power Model, Hard & Soft Macro)
UPF 4.0 | Dec 2024 | IEEE-1801 | - Clarifies and enhances UPF 3.1 features (Retention, power models, Supply set/net, Precedence rules) - Adds a few new capabilities (New Commands, Refinable macro, Virtual supply, AMS, UPF library,)

## Slide 4: UPF 1.0
Navigation:
- set_scope
- set_design_top
Supply Nets:
- create_supply_port
- create_supply_net
- connect_supply_net
- create_power_switch
Power States:
- add_port_state
- create_pst
- add_pst_state
Power Domains:
- create_power_domain
- set_domain_supply_net
Code Management:
- upf_version
- load_upf
- save_upf
HDL Interface:
- bind_checker
- create_hdl2upf_vct
- create_upf2hdl_vct
Strategies:
- set_retention
- set_retention_control
- set_isolation
- set_isolation_control
- set_level_shifter
Implementation:
- map_retention_cell
- map_isolation_cell
- map_level_shifter_cell
- map_power_switch_cell

## Slide 5: Concept of UPF Overlaying on HDL Blocks and Simple Power Intent UPF 1.0

## Slide 6: UPF 2.0
Navigation:
- set_scope
- set_design_top
Supply Nets:
- create_supply_port
- create_supply_net
- connect_supply_net
- create_power_switch
Power States:
- add_port_state
- create_pst
- add_pst_state
- add_power_state
- describe_state_transition
Simstates:
- add_power_state
- set_simstate_behavior
Power Domains:
- create_power_domain
- set_domain_supply_net
- create_composite_domain
Code Management:
- upf_version
- load_upf
- save_upf
- load_upf_protected
- load_simstate_behavior
- find_objects
HDL Interface:
- bind_checker
- create_hdl2upf_vct
- create_upf2hdl_vct
Strategies:
- set_retention_elements
- set_retention
- set_retention_control
- set_isolation
- set_isolation_control
- set_level_shifter
Attributes:
- set_port_attributes
- set_design_attributes
- HDL and Liberty attributes
Supply Sets:
- create_supply_set
- supply set handles
- associate_supply_set
- connect_supply_set
Implementation:
- map_retention_cell
- map_isolation_cell
- map_level_shifter_cell
- map_power_switch_cell
- use_interface_cell
Control Logic:
- create_logic_port
- create_logic_net
- connect_logic_net
Newly added in this release

## Slide 7: Basic Construct of Supply Set

## Slide 8: UPF 2.1
Navigation:
- set_scope
- set_design_top
Supply Nets:
- create_supply_port
- create_supply_net
- connect_supply_net
- create_power_switch
Power States:
- add_port_state
- create_pst
- add_pst_state
- add_power_state
- describe_state_transition
Simstates:
- add_power_state
- set_simstate_behavior
Power Domains:
- create_power_domain
- set_domain_supply_net
- create_composite_domain
Code Management:
- upf_version
- load_upf
- save_upf
- load_upf_protected
- load_simstate_behavior
- find_objects
- begin_power_model
- end_power_model
- apply_power_model
HDL Interface:
- bind_checker
- create_hdl2upf_vct
- create_upf2hdl_vct
Strategies:
- set_repeater
- set_retention_elements
- set_retention
- set_retention_control
- set_isolation
- set_isolation_control
- set_level_shifter
Attributes:
- set_port_attributes
- set_design_attributes
- HDL and Liberty attributes
Supply Sets:
- create_supply_set
- supply set handles
- associate_supply_set
- connect_supply_set
- set_equivalent
Power Management Cells:
- define_always_on_cell
- define_diode_clamp
- define_isolation_cell
- define_level_shifter_cell
- define_power_switch_cell
- define_retention_cell
Implementation:
- map_retention_cell
- map_isolation_cell
- map_level_shifter_cell
- map_power_switch_cell
- use_interface_cell
Control Logic:
- create_logic_port
- create_logic_net
- connect_logic_net
Newly added in this release
Legacy / Deprecated in this release

## Slide 9: Special from 2.1: set_equivalent

## Slide 10: UPF 3.0
Navigation:
- set_scope
- set_design_top
Supply Nets:
- create_supply_port
- create_supply_net
- connect_supply_net
- create_power_switch
Power States:
- add_port_state
- create_pst
- add_pst_state
- describe_state_transition - add_power_state
- add_supply_state - add_state_transition - create_power_state_group
Simstates:
- add_power_state
- set_simstate_behavior
Power Domains:
- create_power_domain
- set_domain_supply_net
- create_composite_domain
Code Management:
- upf_version
- load_upf
- save_upf
- load_upf_protected
- load_simstate_behavior
- find_objects
- begin_power_model
- end_power_model
- apply_power_model
- add_parameter
HDL Interface:
- bind_checker
- create_hdl2upf_vct
- create_upf2hdl_vct
Strategies:
- set_repeater
- set_retention_elements
- set_retention
- set_retention_control
- set_isolation
- set_isolation_control
- set_level_shifter
Attributes:
- set_port_attributes
- set_design_attributes
- HDL and Liberty attributes
Supply Sets:
- create_supply_set
- supply set handles
- associate_supply_set
- connect_supply_set
- set_equivalent
Power Management Cells:
- define_always_on_cell
- define_diode_clamp
- define_isolation_cell
- define_level_shifter_cell
- define_power_switch_cell
- define_retention_cell
Implementation:
- map_retention_cell
- map_isolation_cell
- map_level_shifter_cell
- map_power_switch_cell
- use_interface_cell
Control Logic:
- create_logic_port
- create_logic_net
- connect_logic_net
variation and correlation:
- set_correlated
- set_variation
Newly added in this release
Legacy / Deprecated in this release

## Slide 11: Special from 3.0: UPF Information Model
IEEE 1801-2015/UPF 3.0 introduces a concept model that captures
  “Power-management Information” from “UPF Semantics” on a “Design”
The model contains information from
  UPF Objects and
  User Design (i.e. HDL Objects)
The model allows to access (read/write) the Information through API
UPF power domain, supply sets, design groups, design models, design instances etc. are collectively known as UPF Objects
So IM is an abstraction of power management framework/database

## Slide 12: UPF 3.1
Navigation:
- set_scope
- set_design_top
Supply Nets:
- create_supply_port
- create_supply_net
- connect_supply_net
- create_power_switch
Power States: - add_power_state
- add_supply_state - add_state_transition - create_power_state_group
Simstates:
- add_power_state
- set_simstate_behavior
Power Domains:
- create_power_domain
- available_supply
- boundary_supplies
Code Management:
- upf_version
- load_upf
- save_upf
- load_upf_protected
- load_simstate_behavior
- find_objects
- begin_power_model
- end_power_model
- apply_power_model
- add_parameter
HDL Interface:
- bind_checker
- create_hdl2upf_vct
- create_upf2hdl_vct
Strategies:
- set_repeater
- set_retention_elements
- set_retention
- set_isolation
- set_level_shifter
Attributes:
- set_port_attributes
-literal_supply
-exclude_model/_elements
- set_design_attributes
- HDL and Liberty attributes
Supply Sets:
- create_supply_set
- supply set handles
- associate_supply_set
- connect_supply_set
- set_equivalent
Power Management Cells:
- define_always_on_cell
- define_diode_clamp
- define_isolation_cell
- define_level_shifter_cell
- define_power_switch_cell
- define_retention_cell
Implementation:
- map_retention_cell
- map_power_switch_cell
- use_interface_cell
Control Logic:
- create_logic_port
- create_logic_net
- connect_logic_net
variation and correlation:
- set_correlated
- set_variation
Verification Control:
- sim_assertion_control
- sim_corruption_control
- sim_replay_control
Newly added in this release
Legacy / Deprecated in this release

## Slide 13: Special from 3.0/3.1: create_power_state_group
create_power_state_group - Defines a group name
  Used in conjunction with the add_power_state command
A power state group is used to collect
  Related power states defined by add_power_state.
  The -group (<group_name>) is defined in the current scope.
The power state group defines
  Legal combinations of power states in current scope and/or from the descendant subtree
  Represents combinations of power states that can be active at the same time
# Grouping of legal Power States
create_power_state_group PG_SOC
add_power_state -group PG_SOC \
-state {RUN -logic_expr {primary==ON && PD_L2==RUN && PD_COREA==RUN}} \
-state {DMT -logic_expr {primary==OFF && PD_L2==RUN && PD_COREA==SHD}} \
-state {SHD -logic_expr {primary==OFF && PD_L2==SHD && PD_COREA==SHD}}
-state {RET -logic_expr {primary==OFF && LP_RET1N == 1'b1 PD_COREA == OFF}} \
-state {OFF -logic_expr {primary==OFF && LP_RET1N == 1'b0 PD_COREA == OFF}}
add_power_state -group PG_SOC -update \
-state "RET.PD_CPUA0_ACT -logic_expr {PD_COREA.PD_CPUA0.ACT} -illegal" \
-state "OFF.PD_CPUA0_ACT -logic_expr {PD_COREA.PD_CPUA0.ACT} -illegal"

## Slide 14: UPF 4.0
Newly Added Options:
[-applies_to <flop | latch | any>]
[-save_event_condition ]
[-restore_event_condition ]
[-powerdown_period_condition]
[-restore_period_condition]
[-async_set_reset_effect <ignored | retained_value | output_value>]
Legacy/Deprecated:
[-retention_power_net net_name]
[-retention_ground_net net_name]
[-save_condition ]
[-restore_condition ]
[-retention_condition ]
Newly Added Commands:
- create_abstract_power_source
- create_vcm
- create_upf_library
- load_upf_library
- use_upf_library
- map_retention_clamp_cell
Newly added in this release
Legacy / Deprecated in this release

## Slide 15: What’s New in 4.0
AMS:
  New features for the verification of Digital-on-top designs with analog blocks.
  connecting and modeling supply nets across the analog/digital boundary.
UPF library concept:
  A container for UPF constructs that makes it easier to share common code/macros
  limited to VCM's, but our expectation is that it will grow to include macros.
Retention:
  semantics to provide a more consistent and clear semantics and to model more complex retention cells.
  Semantic changes
    The *_condition options can only contain UPF_GENERIC_CLOCK
    These options can now be an expression. Example”
    {UPF_GENERIC_CLOCK == 0 || UPF_GENERIC_CLOCK == Z}

## Slide 16: What’s New in 4.0
UPF Power Aware Model:
  define_power_model: New options: -update, -complete
    Addition of -implementation flag to allow update with implementation details for Refinable macro support
    Clarification on what happens during apply power model
  apply_power_model: clarification on how it is applied
    clarification of namespace
    addition of -update to allow update with supply_net

## Slide 17: What’s New in 4.0
Virtual Supply: Not a real physical net
  a mechanism to connect supplies (often internal supplies of macros) to aide in verification, checking, and even power state definition
  These can be used in most the same manners of real nets/ports/supplies
Virtual supply comes in combination of followings
    create_supply_net-virtual
    create_supply_port -virtual
    create_supply_set -virtual
In a design virtual supplies simplifies
  The specification of power states definition
  When multiple functionally equivalent internally switched supplies are present

## Slide 18: What’s New in 4.0
Refinable Macro: Concept of Handling “Pre-verified Macro”
A new concept for handling hierarchical IP,
  The Refinable macro allows implementation to optimize a block
  As long as it does not change the functional intent of the block.
The concept originated as a "pre-verified IP", implying
  The functional verification was done,
  But some in context optimizations would be allowed.
This provides a new mechanism for IP deliverables.
  A design block may have two input supplies, but at the top-level these supplies are shorted together.
  Isolation/LS between these lower domains would no longer be needed based on this upper-level context.

## Slide 19: Concluding Remarks
Why so many versions of standards (LRMs)?
Obvious answer - this is mainly because of
  correction,
  amendment,
  extensions of semantics and
  addition of new syntax-semantics
Which were previously either
  incomplete,
  misleading,
  error prone,
  easily mis-interpretable or
  found impossibilities while adopting/implementing in verification tools and so on.

## Slide 20: Questions
Finalize slide set with questions slide