## Slide 1
Samsung Electronics Co., LTD., Yongin-si, Korea
Contact Info : ky12.shim@samsung.com
Kiyoon Shim, Seungsik Eom, Beomseok Kang, Jaechul Park, Kyubeum Lee, Youngjin Chung, Hyogyuem Rhew
Samsung Electronics
An Effective Digital Logic Verification Methodology of High Speed Interface IP Using a Configurable AFE Behavioral and Channel Model
MOTIVATION & PROBLEM STATEMENT
PROPOSED MODEL
CONCLUSIONS
REFERENCES
RESULTS
OBJECTIVES
 | Verification Period (Hour) |  | 
 | Conventional | Proposed | Reduction Rate
Average Sim Time | 6.53 | 2.01 | 69.2%
Time to achieve CC 100% | 54.26 | 16.13 | 70.3%
Time to achieve FC 100% | 106.75 | 33.87 | 68.3%
PROPOSED METHODOLOGY
<UVM TB ARCHITECTURE>
<VERIFICATION FLOW>
Digital Logic in Mixed Signal Design is Getting More Significant
Logic that estimates and compensates for Inter-Symbol Interference (ISI) caused by an increased data transmission rate and channel loss
Logic that calibrates the offset caused by mismatch of Analog Front End (AFE) device characteristics due to increased PVT variation
Challenges in Digital Logic Verification of Mixed Signal Design
Need repeated extraction of behavioral models for each analog characteristic
AFE offset and ISI through the channel cannot be determined immediately
Long simulation time due to extensive computation required to reflect the analog nature
Verification of Digital Logic
In various AFE and channel environments with fast configuration
With knowledge of the AFE offset and ISI magnitude
With fast simulation and achieve early bug detection
AFE Behavioral and Channel Model (ABC Model)
Configurable Analog Behavioral model that focuses on modeling built-in offset of the AFE components and ISI from the channel
Provides controllability over all AFE offset and channel coefficients which can be randomized in UVM-based testbench
Channel is implemented as a FIR filter which has 10 tap coefficients
AFE offset is applied to the received data when it pass through each AFE component
Magnitude of the AFE offset and ISI can be mathematically calculated
Proposed UVM Testbench Architecture
Integrate the ABC model with a Simplified Behavioral model that doesn’t have AFE offset and channel characteristics
Test cases that need Rx data reflecting AFE offset and ISI will only select the ABC model branch of the multiplexer
Application of Proposed Methodology
Applied to 16GT/s PCIe IP
Rx digital logic including EOM, Offset Calibration, DFE Adaptation, Rx Margin was verified with ABC model
Checkers are implemented based on the parameters of the ABC model
Found bugs that cannot be detected with a conventional analog behavioral model that reflects the actual circuit
Experimental Result
Comparison performed on the verification period of Rx digital logic
Conventional methodology used Xmodel for the analog behavioral model
Code coverage closure : 70.3% reduced
Function coverage closure : 68.3% reduced
Verification methodology for digital logic in mixed signal design is proposed
ABC model ensures fast debugging and high accuracy in digital logic verification
Average simulation time of digital logic reduced by 69.2% and achieved fast DV closure
Additional enhancements in verification period are expected, considering the time saved in configuring various AFE and channel environments and reduced debugging time
Can be effective except in cases where verification with the real analog circuit is necessary
[1] Mariam Maurice, “Functional Verification of Analog Devices modeled using SV-RNM” DVCON US, 2023
[2] Xmodel - "xmodel: Empower SystemVerilog with Event-Driven Analog Models," 2023. Available: https://www.scianalog.com/xmodel/