## Slide 1: Breaking the Formal Verification Bottleneck
Menachem Rappaport, Ariel Ansbacher, Elchanan Rappaport - Veriest Solutions

## Slide 2
Standard design – with parameters
Any parameter value change requires a new run.
All legal input signal values are tested in a single run.
Design
Input signals
Parameters
output signals

## Slide 3
Signal design
All legal input signal values are tested in a single run.
Design
Only
Input signals
output signals

## Slide 4
General Idea – P2S (Parameters to Signals)
Design
Input signals
Parameters
output signals
Design
Only
Input signals
output signals
convert parameters to signals
This will be used for syntheses
This will be used for verification
Verify the blocks are functionally equivalent

## Slide 5: Interface Changes
We modified the DUT interface so that stable input signals replace the parameters.

## Slide 6
Compiler flow
Parameter
code
Parameter
AST
Signal
AST
Signal
code
AST generator
P2S script
code generator
We used an open-source AST and code generator.
We have written our own script to modify the AST.

## Slide 7
LEC test
LEC proves that both blocks are functionally equivalent.
The runtime is short and insignificant.

## Slide 8
Runtime results
Design example | Number of Permutations | Tool 1 Speedup | Tool 2 Speedup | Tool 3 Speedup
Advanced FIFO | 96 | 258% | 400% | 644%
ALU | 24 | 675% | 511% | 346%
APB XBAR | 16 | 357% | 334% | -
AXI bridge | 27 | 304% | 147% | 184%
We did our research on 3 different tools and 4 different blocks

## Slide 9: Conclusions
We tested 4 different designs with 3 different tools.
For almost all designs, the runtime improved.
For most designs, performance improvements exceeded 300%.

## Slide 10: Questions?
Thank you
You can view an example at: https://github.com/MenachemRapp/p2s_fifo_example