## Slide 1: Performance verification for AI Heterogenous Multicore Systems using Portable Stimuli Standard
Pietro Locci, Hillel Miller

## Slide 2: Agenda
Introduction challenge and motivation
AI application data flow
PSS Solution
Performance optimization and results

## Slide 3
100 GOPS
1 TOPS
10 TOPS
100 TOPS
1000 TOPS

## Slide 4: Heterogenous AI Multicore System

## Slide 5: AI performance verification challenge
Variety and fast evolution of AI Application
AI heterogenous system programming complexity
Configuration space of the system
High simulation time of benchmarks

## Slide 6: Verification environment reusability requirements
Technique Reuse
Single module
Hierarchical Reuse
Sub system
Full system
Convolution Accelerator
# cores
Memory size
accelerators
Configurability Reuse

## Slide 7: Neural Network concept
Neural networks (NNs) are computational models of interconnected layers that transform input data through successive operations to extract meaningful patterns
A NN Layer is a computational block that transforms input data, producing an output called a feature map
Feature Map is the output of a layer after applying specific operations to the input data

## Slide 8: Neural network data flow
1
2
N-1
N
…
DMA read
DMA write
tile_processing
1
1
2
3
N-2
N
N-1
N
tile height + 2
tile height
input channels
output channels
Input featuremap
output featuremap
input blockbuffer
output blockbuffer
L1 Memory
L2/L3 memory

## Slide 9: PSS performance network layer test
Network layer tests are defined based the most common NN
The compute part is represented by a single or few layers of the NN (Conv + Relu)
The results of the layer (feature maps) are compared for functional correctness with golden model results
The performance are measured in terms of cycles and compared with KPI that depends on layer time budget and configuration

## Slide 10: PSS model implementation – base actions
In_descr
Src_b
Dst_b
Start
wait
Start.out_descr wait.in_descr
Start.out_b
wait.dst_b
out_descr
out_b
The base actions are used for all the main atomic and compound actions in the PSS model with for both move and compute actions

## Slide 11: PSS model implementation – scenario
PSS model describe the scenario in terms of
  actions
  dependency of the flow objects (buffers) of the actions
The actions sequences is not directly described in the model

## Slide 12: PSS Generated Solutions
PSS solver generates all possible valid solutions
Performance test should measure optimal scheduling only
Optimal scheduling rules
  Start has priority over Wait
  High exec times Start has priority over low exec time
  Low exec time Wait has priority over high exec time

## Slide 13: Cost function
Cost functions are analytical representation of the execution time of each action
They are determined by analyzing the performance of the single kernels under different conditions
Cost functions are used in the PSS model to enforce scheduling priority
Chart: trx size KB
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128
throughput | 0.21591 | 0.36868 | 0.56418 | 0.72305 | 0.83914 | 0.91518 | 0.94718 | 0.96405
Ideal Throughput | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Chart: exec time
| 0.74 | 0.76 | 0.78 | 0.8 | 0.82 | 0.84 | 0.86 | 0.88 | 0.9 | 0.92 | 0.94 | 0.96 | 0.98 | 1 | 1.02 | 1.04 | 1.06 | 1.08 | 1.1000000000000001 | 1.1200000000000001 | 1.1399999999999999 | 1.1599999999999999 | 1.18 | 1.2 | 1.22 | 1.24
idma | 140 | 430 | 120 | 180 | 64 | 63 | 8 | 2
compute | 65 | 260 | 560 | 140
odma | 83 | 95 | 210 | 260 | 180 | 64 | 110 | 26

## Slide 14: Results
Modular PSS model tests enable efficient scaling:
  Single-core optimization extended to multi-core
  Parallel processing of sub-feature maps
Over 95% of NN layers met exceeded KPIs
Kernel name | Fmap input | number of cores | (exec_time-KPI)/KPI%
Conv W<128×512×1×1> + Relu | (512, 135,240) | 1 | 2.43%
Conv W<1024×256×1×1> + Add + Relu | (256, 66, 117) | 1 | -1.01%
Conv W<64×3×7×7> + BatchNormalization + Relu + Maxpool | (3, 1920, 1080) | 1 | 1.49%
Matmul B<2048×1001> + Add + Identity + 2 * (Softmax + Identity) | (2048, 1, 1) | 1 | -0.19%
SpaceToDepth + Conv W<32×128×3×3> + Relu +DepthToSpace | (32, 128, 512) | 1 | -1.88%
Conv W<64×64×3×3> + Relu | (64, 180, 320) | 2 | -3.18%
Conv W<128×128×1×1> + Relu | (128, 535, 127) | 8 | 2.12%
Conv W<64×64×3×3> + Relu | (64, 180, 320) | 16 | 0.39%

## Slide 15: Conclusion
Portable Stimuli Standard (PSS) is a robust framework for AI performance verification
  HW/SW co-verification and co-optimization
  Configuration scalability
  Modular approach
The methodology can be easily applied to other domains

## Slide 16: Questions