## Slide 1: Automatic Test Pattern Generation Using Formal Verification and Fault Injection Methods
Jad Al Halabi, Endri Kaja, Wolfgang Ecker

## Slide 2: Introduction and motivation (1)
SoCs in safety critical applications
  Functional safety and in-field testing
Cost of DFT infrastructure
  Area and performance
Software Based Self-Test (SBST)
  SBST fault coverage depends on generated software test pattern quality

## Slide 3: Introduction and motivation (2)
In this work, an automated SBST generation technique is developed:
  Designed for stuck-at faults in RISC-V processors
  Combines formal methods with fault simulation
  Automation through model-driven approach
  Fault detection using Program Flow Checking (PFC) technique

## Slide 4: Background: Model Driven Code Generation
Metagen is Infineon’s metamodel based code generation framework [https://ieeexplore.ieee.org/document/6800525]
Metagen is composed of many reusable user libraries:
  MetaRTL
  MetaRTL RISCV
  MetaFI
Model
Formalized specifications
Code
Template

## Slide 5: Background: MetaRTL
Hardware specification
Microarchitecture blueprint
Platform and technology indipendent hardware description
Maps MoD to MoV elements
Tree based, target language specific
Formalized specification
Template of design (ToD)
Target Code
Model of Design
(MoD)
Template of view (ToV)
Model of view (MoV)

## Slide 6: Background: MetaRTL RISCV
Extension for MetaRTL to generate RISCV CPU
Feature extensability
Custom instructions
Instantiation of hardware
RTL HDL generation

## Slide 7: Background: Program Flow Checking (PFC)
Hardware to detect anomalies in program flow execution
  Compile time and execution time signatures are computed
  A signature mismatch indicates a fault
Decoded instructions are hashed using the same hash function during run time and compile time
PFC can be enabled or disabled in MetaRTL RISCV

## Slide 8: Background: MetaFI
A metalib for fault injection and mixed granularity design generation
DUT
Synthesis
Original design RTL
Fault injected DUT
Gate level DUT
Mixed granularity FI design RTL
Fault list
Equivalence check
Transform

## Slide 9: Background: Fault Simulation Framework
Functionality of MetaFI
Generates SystemVerilog testbenches to conduct different fault simulation campaigns:
  Statistical fault injection
  Direct fault injection
  Exhaustive fault injection

## Slide 10: Pattern Generation Technique (1)
A fault affects a circuit if the fault is activated and propagated to an output
Example:
A = 1, B = 1, C = 0, D = 1 can be used to test for sa-0 at e
A
B
C
D
e
f
g
sa-0
1
1
1
0
1
0
1
1
0

## Slide 11: Pattern generation (2)
Miter circuit:
Formal property:
  Assume 1 fault in FI-DUT, prove
Checker disproves property -> counter example -> input test pattern
DUT
FI-DUT
g
g’
Inputs
Fault activation signals

## Slide 12: Pattern Generation Technique (3)
Note: A = 1, B = 1, C = 0, D = 1 can also detect other faults
Example:
Idea: Perform exhaustive fault simulation to test for other faults in the design to reduce generation time
A
B
C
D
e
f
g
sa-0
1
1
1
0
1
1
1
0

## Slide 13: Fault Detection Mechanism
PFC is extended
  Hash CSR, activation/deactivation instruction and logic are automatically generated
Any signal can be monitored
Hashed values are compared in software
Run-time fault detection is possible

## Slide 14: SBST Flow: Overview
DUT
FI-DUT
Transformation
Miter Circuit
Transformation
Injection of Faults via Properties
Counterexample
Extraction of individual
Test Patterns
All faults covered?
Fault Simulation + Fault Dropping
Complete Test Patterns
Insertion of PFC Instructions in the Test Pattern
Comparison of HW PFC value with expected PFC value
Fault Injection
Fault Detection Rate
Yes
No

## Slide 15: SBST flow: RISCV Considerations
Custom CSR to reset Register File
Pattern chaining to guarantee the expected fault coverage
Constraints for TPG:
  Consider legal instructions
  External interrupts are disabled
  Control flow instructions are disabled
  The PC is constrained to increase linearly
  Only a single fault is allowed to be injected per property
  All CSR instructions are disabled

## Slide 16: Application and Results (1)
A RISC-V RV32IMC was utilized for experiments
Tested components include both combinational and sequential components
PFC modules attached to
  Decoded instruction
  RegisterFile outputs
  ALU outputs

## Slide 17: Application and Results (2)
Component | # Faults | # Patterns | Fault Coverage | Fault Detection rate of PFC | Time
HDU | 111 | 19 | 91.89% | 100% | 0.61 h
ALU | 4732 | 313 | 97.63% | 100% | 13.6 h
RegisterFile | 11747 | 492 | 96.86% | 100% | 40.5 h
Decoder | 3224 | 104 | 76.3% | 92.19% | 38.87 h
MEM-WB | 410 | 10 | 54.8% | 100% | 8.5 h

## Slide 18: Conclusion and Future Work
An efficient and automated technique for generating customized SBST for RISC-V processors
Combination of formal verification and fault simulation
High fault coverage of over 91% for most of the tested components
High fault detection rate using PFC modules
Future work:
  Extend the application beyond RISCV
  Achieve a deterministic generation
  Augment SBST with manual code

## Slide 19: Questions?
Thank you