## Slide 1: Automated Formal Verification of Area-Optimized Safety Registers in Automotive SoCs
Shuhang Zhang, Bryan Olmos
Infineon Technologies AG, Neubiberg, Germany

## Slide 2: Outline
Motivation
Area-Optimized Safety Registers
Verification Challenges
Framework
Results
Conclusion

## Slide 3: Motivation
Increasing number of car safety features
Smart Airbags
Powertrain
Advanced Driver Assistant Systems
Electric Power Steering
Antilock brakes
Electronic Stability Control
...

## Slide 4: ISO 26262 Standard
ASIL Classification
Automotive microcontroller, e.g. AURIX™ (ASIL D)
Safety verification on top of functional verification
Diagnostic coverage analysis
Documentation, requirement traceability
Higher product complexity, area and power consumption, higher development and production costs
ASIL D
QM
ASIL A
ASIL B
ASIL C
Low Risk
High Risk

## Slide 5: Safety Register
Error Detection Code (EDC)
  Parity (PAR)
  Double Error Detection (DED)
  Self-test feature
Redundancy
  Double Module Redundancy (DMR)
  Triple Module Redundancy (TMR)
  Self-test feature
Encoder
FFs
Decoder
SFF Wrapper
d_i
encoded
data
corrupted
data
d_o
d_o
alarm
SFF Wrapper
d_i
d_i
d_i
FFs
FFs
FFs

## Slide 6: Safety Register
SFF Controller
  Trigger self-test
  Collect self-test and alarm signals
  Communicate with SMU
Async clock domain supported
  Synchronization in SFF Controller
Safety Management Unit (SMU)
SFF Controller
test_en
test_done
alarm
SFF PAR
SFF DED
SFF Domain 0
Sync clock
SFF DED
SFF TMR
SFF Domain 1
Async clock
test_seq
alarm
test_seq
alarm

## Slide 7: Safety Register
#Redundant bits does not increase linearly with the data width
Code rate higher with a bigger data width

## Slide 8: Area-Optimized Safety Register
Solution: Merge multiple safety registers into a bigger one
Area optimization via Best-Fit or ILP technique (w/o or w/ register fragmenting)

## Slide 9: Verification Challenges
Parameterized Components and Configurable Safety Structure
Area-Optimized Implementations
Solution: Automated property generation for all safety registers

## Slide 10: Framework
S. Zhang, B. Olmos, and B. Naik, “Automated Formal Verification of a Highly-Configurable Register Generator,” in Design & Verification Conference U.S., 2024.

## Slide 11: Specification Extraction
MetaModel creation
  Define which spec. are extracted
  Both register and bitfield level
Model of Things (MoT)
  Internal spec.

## Slide 12: Generated Properties

## Slide 13: Results
 | Initial Design | Verification Time Overhead | 
 | #Safety Registers | BFD (32-bit) | ILP (32-bit)
SoC1 | 1827 | 6.53% | 14.87%
SoC2 | 2392 | 71.05% | 84.32%
SoC3 | 49 | 144.27% | 131.02%
 | Area-Opt. | CEX Trace | Functional | Integration
This Work | yes | yes | yes | yes
DVCon Europe 24 | no | no | no | yes

## Slide 14: Conclusion
Safety registers are critical components to ensure automotive chips
Significant area-overhead caused by safety registers
Area-optimized safety registers bring verification challenges
Proposed formal verification framework addresses this issue efficiently but longer verification time due to larger registers

## Slide 15: Questions
Thank you!