## Slide 1: Addressing Advanced Mixed-Signal Verification Scenarios by Developing a UVM Framework for Analog Models
Simul Barua - Ulkasemi, Inc.
Shahriar Kabir - Ulkasemi, Inc.
Henry Chang - Designer’s Guide Consulting, Inc.

## Slide 2: Agenda
Motivation and purpose of the AMSV utility framework
Structure of the framework
Case study: application of the framework
Framework implementation in models and testbench
Simulation results
Summary & future scopes

## Slide 3: Increased Complexity in IC Verification
Modern applications outpaces design complexity
Declining verification success rates
Key factors include analog design issues and mixed-signal interface bugs.
Insights from our previous research
  Integrating validated functional analog models enhances chip-level verification.
  Improved bug detection at the system level
Remaining gap
  Traditional methodologies still lack the robustness needed to address more complex system requirements

## Slide 4: Evolving Verification Needs for the Digital Twin
Must include analog elements
System performance
  Simulating temperature effects, parametric variations, and analog non-idealities
  Ensuring real-world performance criteria are met
Safety Requirements
  Modeling how analog blocks, subsystems, and systems can fail
  Verifying fault tolerance and mitigation strategies
Conventional verification methodologies lack the support needed for these critical features

## Slide 5: Limitations of Traditional Methodologies
Transistor-level simulations for real-world complex scenarios
  Accurate, yet impractical for system-level verification
  Environmental effects (e.g. temperature) demand prolonged runs
Verifying critical features using system-level testbenches
  No direct control over environmental factors (e.g. temperature)
  Difficult to observe system responses (e.g. thermal shutdowns)
  Predictable failures require design modifications accommodating fault conditions
Need for a flexible and efficient approach
  Designs must accommodate the verification of both environmental and safety features
  System-level verification must efficiently handle complex, mixed-signal scenarios efficiently
  Faster simulation time

## Slide 6: Overcoming the Limitations
Leveraging analog models
  Feasible simulation speeds compared to transistor-level
  Straightforward incorporation of complex effects (e.g. environmental stress, parametric shifts)
  Enables real-world scenario modeling (e.g. AI performance under analog degradation)
Enhancing the UVM Testbench
  Enhanced monitoring and control for analog models
Bridging the gap
  A dedicated mechanism is required to enhance both the analog model and the UVM testbench

## Slide 7: The AMSV Utility Framework
Overview
  Leverages SystemVerilog OOP constructs
  Enhances analog models and system-level UVM testbench
  Efficient communication between the models and the testbench
  Simulates real-world conditions: temperature effects, parametric variations, and failures
Addressing limitations of traditional methodologies
  Enables modeling of real-world scenarios
  Faster, practical alternative to slow transistor-level simulations
  Enables direct control and monitoring of environmental impacts
Key features
  Introduces bidirectional data flow for advanced observation and control without compromising pin accuracy
  Dynamic parameter adjustment from UVM testbench
  Continuous fault detection and debugging via model-to-testbench reporting

## Slide 8: Structure of the AMSV Framework
Stores configuration details and parameters for each analog model
Centralized resource for system-wide variables
SystemVerilog package with OOP classes, LUTs, pre-defined macros, and utilities
Provide essential functions for framework setup, model management, and dynamic parameter control.

## Slide 9: Code Snippet of the AMSV Utility Package

## Slide 10: Pre-defined Utility Macros
Simplify integration and reduce repetitive code
Ensure consistent usage across models and verification environments
Minimize complexity, making the framework more accessible and efficient
Key Macros
  Model registration macros
  Global parameter macros
  Signal monitoring macros
  Fault reporting macros

## Slide 11: Case Study: Application of the AMSV Framework
Design Overview
  System-on-chip (SoC) design with digital and analog components.
  Includes a Power Management Unit (PMU) and Phase-Locked Loop (PLL)
Key Objectives
  Integrate AMSV framework with analog models and UVM testbench
  Verify complex scenarios like environmental impacts and safety mechanisms
Critical analog components
  PLL: sensitive to system temperature, leading to frequency drift; monitored by a digital control unit for compensation
  Thermal shutdown (TSD): monitors system temperature; designed to shut down upon reaching unsafe limits

## Slide 12: Case Study: AMSV Integration and Verification Scenarios
Verification scenarios
  Verify temperature effects on PLL frequency drift
  Assess system response when the TSD block fails to trigger
AMSV framework integration
  Configure parameters and inject faults via UVM testbench
  Real-time control and monitoring through the AMSV framework

## Slide 13: Modeling Analog Blocks & AMSV Integration
Used SystemVerilog discrete electrical (user-defined nettype) approach
Generated validated models and self-checking MVS testbenches with the Model-in-Minutes (MiM) tool
  Automatically generates models from a specification
  Allows user-defined custom code integration
  Enabled seamless AMSV framework integration across multiple models

## Slide 14: Integrating the AMSV Framework into Models
`timescale 1s/1ps
// Importing AMSV Utility Framework Package
import amsv_utils_pkg::*;
// Include the AMSV Utility Macros
`include "amsv_utils_macros.sv"
// MODULE HEADER {{{1
module VCO (
output out, // VCO Output
input in, // Input control voltage of the VCO
input[7:0] vcoCF, // Settings for VCO center frequency
input enable, // Enable Pin
input bias, // Bias Input
input vdda, // Supply
input gnda // Ground
);
// Registering model to AMSV Utilities
`amsv_utils_register_model("VCO", "vco")
// Discrete-Electrical (DE) Transceivers {{{2
real in$Vobs, in$Iobs, in$Idrv, in$Gdrv;
DE_norton Xtcvr_in (in, in$Vobs, in$Iobs, in$Idrv, in$Gdrv);
...........................
// Local variable to sync with AMSV Global Temperature Parameter [C]
real temp = 27;
...........................
// Sync temp variable with Global Parameter 'temperature'
`amsv_utils_sync_globals(temp, "temperature")
...........................
// Discrete Variables {{{2
assign Kvco = 25e6;
assign delta_T = (temp + 273) - TEMP_NOMINAL;
assign temp_freq_drift = TEMP_COEFF*delta_T;
...........................
always @(posedge osc) Ctrl <= min(max(in$Vobs - 1.25+0, -500e-3+0), 500e-3+0);
assign F0 = 2.374e9 + 500e3*vcoCF_val;
assign f = F0 + (Kvco*Ctrl) - temp_freq_drift;
always wait (On) osc = #(`fromSeconds(max(500e-3/f, `TIME_PREC))) ~osc;
assign out = osc;
...........................
// ASSERTIONS {{{1
// Check for V(vdda) out of range (1.7V to 1.9V) {{{2
assign #(`fromSeconds(25e-9), 0) _faults.V_vdda = !((
(1.7 <= vdda$Vobs) && (vdda$Vobs <= 1.9))
|| !_locals.enableAsserts);
always @(_faults.V_vdda)_reportFault(_faults.V_vdda, "V(vdda) out of range");
...........................
endmodule
`amsv_utils_register_model macro registers the model in Model LUT
`amsv_utils_sync_global macro synchronizes model variable temp with Global LUT parameter temperature
Models frequency drift due to global temperature changes
AMSV framework reports block-level assertions directly to the system-level testbench
Importing the AMSV package and macros
Registering the model to the Model LUT
Synchronizing local variable temp with global temperature
Modeling temperature-induced frequency drift
Block-level self reporting assertions

## Slide 15
Testbench-controlled fault injection mechanism in the Thermal Shutdown (TSD) model
  Synchronized with global tsd_force_fail parameter via amsv_utils_sync_globals macro
  Bypasses shut down even as the temperature rises
  Allows system behavior analysis under failure conditions
Implementing Safety-Critical Scenarios

## Slide 16: Integration into the UVM Testbench
Import amsv_utils_pkg at the testbench top-level
Create a singleton instance using the create_amsv_utils method
Global testbench access through UVM configuration database

## Slide 17: Accessing AMSV Utilities in UVM
Retrieve the AMSV instance from the UVM configuration database
Initialize global parameters using AMSV utility methods

## Slide 18
Objective: AMSV utility global parameter variation and system behavior verification
Test Scenarios & Expected Outcomes
  Nominal condition (27°C): PLL achieves stable lock
  Gradual increase (60°C): PLL maintains lock as the feedback loop compensates
  Rapid increase (65°C): PLL controller adjusts VCO frequency; lock achieved within 250µs
  Exceeding operational range (85°C): TSD block triggers shutdown, verifying protection
  Recovery check (65°C): PLL resumes operation, confirming proper TSD recovery
  TSD failure simulation (90°C, tsd_force_fail = 1): Verifies system response without TSD protection
Test Cases

## Slide 19: Simulation Results
1
2
3
4
5
6
27°C: PLL establishes a stable lock
60°C: PLL maintains lock (loop compensation)
65°C: system adjusts vcoCF to regain lock
85°C: TSD activates, shutting down PLL
65°C: TSD resets, PLL reactivated, confirms safe system recovery
(90°C, tsd_force_fail=1): TSD inactive, system adjusted vcoCF maxed ('d255), but PLL remains unstable

## Slide 20: AMSV Framework – Key Contributions
Introduced as an innovative approach to mixed-signal verification
Seamlessly integrates analog models with UVM testbenches, enabling efficient system-level verification
Simulates real-world conditions such as temperature variations, environmental changes, and fault conditions
Overcomes traditional verification limitations by providing speed, flexibility, and real-time parameter control beyond transistor-level simulations
Enhances connectivity verification, system-level assertions, and coverage of analog-digital interactions
Establishes a new standard in efficiency and accuracy, ensuring robust validation of complex mixed-signal designs

## Slide 21: Future Directions
Expanding capabilities
  Future updates will include expanded model libraries for broader AMS applications
  Support for automatic mixed-signal connectivity check
The Road Ahead
  A transformative shift in mixed-signal verification, driving efficiency and innovation
  Encouraging industry-wide adoption to refine and advance verification methodologies

## Slide 22: Questions
Any questions