## Slide 1: Lessons Learned Using Formal for Functional Safety
Doug Smith
Notes: Hi, my name is Doug Smith, and I'm a engineer and instructor at Doulos. I've been involved with automotive functional safety for a number of years, performing random fault campaigns on designs using formal, developing a formal functional safety app and fmeda creation tool, and combining formal results with other tool flows. While I don't claim to be an expert, I thought I could share a few lessons I've learned using formal with functional safety in hopes it might help you in your automotive functional safety project.

## Slide 2: The role of formal within functional safety
5. Product development at the hardware level
5-5 Initiation of product development at the hardware level
5-6 Specification of hardware safety requirements
5-7 Hardware design
5-8 Evaluation of the hardware architectural metrics
5-9 Evaluation of the safety goal violations due to random hardware failures
5-10 Hardware integration and testing
(ISO26262-5)
Model checking
Equivalence checking
Super lint
Connectivity
X-propagation
Register checking
…
Functional verification
Systematic failures
Fault pruning
Fault injection
Fault propagation
Random fault testing
Random failures
Notes: Hardware design for systematic failures (bugs)
  Verifying the design
  Verifying safety mechanisms
  Use model checking
  Use formal apps …
Random fault testing
  Generating a reduced fault list
  Injecting the fault in the design or safety mechanism
  Propagating the fault to a safety output or alarm to see if it's detected

## Slide 3: Functional verification of safety mechanisms
// ECC implementation
wire logic p1 = 1 ^ data[0] ^ data[1] ^ data[3] ^ data[4] ^ data[6];
wire logic p2 = 1 ^ data[0] ^ data[2] ^ data[3] ^ data[5] ^ data[6];
wire logic p4 = 1 ^ data[1] ^ data[2] ^ data[3] ^ data[7];
wire logic p8 = 1 ^ data[4] ^ data[5] ^ data[6] ^ data[7];
logic [12:0] expected_ecc;
assign expected_ecc[11:0] == { data[7], data[6], data[5], data[4],
p8, data[3], data[2], data[1], p4,
data[0], p2, p1 };
assign expected_ecc[12] = ^expected_ecc[11:0]; // Overall parity
assert property ( ecc_from_dut == expected_ecc );
cut data
Pseudo-code
Model checking
memory
DUT
Safety mechanism insertion
DUT
DUT
Safety
alarm
=
error
Sequential Equivalency

## Slide 4: Sequential depth challenges
Combinational CRC – probably
Sequential CRC – formal friendly?
crc[30] = D[63] ^ D[61] ^ D[59] ^ D[58] ^ D[56] ^ D[53] ^
D[52] ^ D[51] ^ D[48] ^ D[46] ^ D[45] ^ D[43] ^
D[42] ^ D[35] ^ D[32] ^ D[30] ^ D[29] ^ D[28] ^
D[27] ^ D[26] ^ D[24] ^ D[23] ^ D[22] ^ D[14] ^
D[10] ^ D[8] ^ D[7] ^ D[4] ^ C[0] ^ C[3] ^
C[10] ^ C[11] ^ C[13] ^ C[14] ^ C[16] ^ C[19] ^
C[20] ^ C[21] ^ C[24] ^ C[26] ^ C[27] ^ C[29] ^
C[31];
crc[31] = D[62] ^ D[60] ^ D[59] ^ D[57] ^ D[54] ^ D[53] ^
D[52] ^ D[49] ^ D[47] ^ D[46] ^ D[44] ^ D[43] ^
D[36] ^ D[33] ^ D[31] ^ D[30] ^ D[29] ^ D[28] ^
D[27] ^ D[25] ^ D[24] ^ D[23] ^ D[15] ^ D[11] ^
D[9] ^ D[8] ^ D[5] ^ C[1] ^ C[4] ^ C[11] ^
C[12] ^ C[14] ^ C[15] ^ C[17] ^ C[20] ^ C[21] ^
C[22] ^ C[25] ^ C[27] ^ C[28] ^ C[30];
Lesson: C to RTL equivalency may work better for sequential CRC.
assign crc_next = data ^ crc[14];
assign crc_tmp = {crc[13:0], 1'b0};
always @ (posedge clk)
begin
if(initialize)
crc <= #Tp 15'h0;
else if (enable)
begin
if (crc_next)
crc <= #Tp crc_tmp ^ 15'h4599;
else
crc <= #Tp crc_tmp;
end
end

## Slide 5: Fault list generation

## Slide 6: Formal + random fault testing
Emulation
Formal Synthesis
RTL Synthesis
Simulation
Formal Analysis
Formal Fault List Pruning
Fault List Creation
Fault List Pruning
Random Fault Testing

## Slide 7: How to identify safe faults
cover property ( @(posedge clock) safety_output );
Lesson: Identify safe faults using the formal cone-of-influence.
Formal FuSa app not required!
Fault list
(Cone-of-influence)
Safe faults (cannot affect output)
Safety Element
report coi <property>
Pseudo-code

## Slide 8: Do all faults need tested?
 | ASIL B | ASIL C | ASIL D
Single-Point Fault Metric (SPFM) (ISO 26262-5, Table 4) | >= 90% | >= 97% | >= 99%
Latent Fault Metric (LFM) (ISO 26262-5, Table 5) | >= 60% | >= 80% | >= 90%
100% ± 10%
99% ± 9%
98% ± 8%
97% ± 7%
96% ± 6%
95% ± 5%
94% ± 4%
93% ± 3%
92% ± 2%
91% ± 1%
100% ± 3%
99% ± 2%
98% ± 1%
100% ± 1%
Acceptable SPFMs with margin of error:
Margin of error

## Slide 9: Calculating the margin of error
where
= margin of error
= 2.58 (critical value for 99% confidence interval)
= 0.5 (50% chance of selecting a fault - the most pessimistic value)
= sample size
= total number of faults
R. Leveugle, A. Calvez, P. Maistri and P. Vanhauwaert. "Statistical fault injection: Quantified error and confidence." Design, Automation & Test in Europe Conference & Exhibition. Nice, France, 2009 . 502-506.
Population sampling from statistics

## Slide 10: A practical sample size
Margin of error

## Slide 11: Margin of error
Chart: Random Sampling Margin of Error
| 500 | 1000 | 2000 | 3000 | 4000 | 5000 | 6000 | 7000 | 8000 | 9000 | 10000
10,000 | 0.056233 | 0.038702 | 0.025801 | 0.019706 | 0.0158 | 0.012901 | 0.010533 | 0.0084455 | 0.0064503 | 0.0043002 | 0
20,000 | 0.056966 | 0.039761 | 0.027366 | 0.021714 | 0.018244 | 0.0158 | 0.013934 | 0.012431 | 0.011172 | 0.010085 | 0.0091219
30,000 | 0.057209 | 0.040108 | 0.027868 | 0.022344 | 0.018989 | 0.016654 | 0.014896 | 0.013501 | 0.012351 | 0.011377 | 0.010533
40,000 | 0.05733 | 0.040281 | 0.028115 | 0.022652 | 0.01935 | 0.017065 | 0.015354 | 0.014005 | 0.0129 | 0.011971 | 0.011172
50,000 | 0.057402 | 0.040384 | 0.028263 | 0.022835 | 0.019564 | 0.017307 | 0.015623 | 0.014299 | 0.013219 | 0.012313 | 0.011538
100,000 | 0.057546 | 0.040589 | 0.028556 | 0.023196 | 0.019985 | 0.017782 | 0.016147 | 0.014869 | 0.013834 | 0.012972 | 0.012238
500,000 | 0.057662 | 0.040753 | 0.028788 | 0.023481 | 0.020315 | 0.018152 | 0.016554 | 0.01531 | 0.014307 | 0.013475 | 0.01277
1,000,000 | 0.057676 | 0.040773 | 0.028816 | 0.023517 | 0.020356 | 0.018198 | 0.016604 | 0.015364 | 0.014365 | 0.013536 | 0.012835

## Slide 12: So are all faults necessary?
Probably not …
  ASIL B, ASIL C – 4000-5000 faults +/- margin of error may be sufficient
  ASIL D – ASIL decomposition or other techniques (e.g., lockstep, etc.)
Lesson: Testing around 4k random faults is usually sufficient.

## Slide 13: Why not collapse faults?
stuck-at 0
stuck-at 0
stuck-at 1
stuck-at 1
?
Equivalent faults
?
Output fault equivalent to input fault
Only one fault needs tested
?
?
stuck-at 0
stuck-at 1
stuck-at 0
stuck-at 1
Dominant faults
Output fault dominates input fault
Ignore input when testing for output

## Slide 14: Collapse or not collapse?
RTL not as easy to find equivalent and dominant faults
ISO26262 requires uniform random distribution and selection
  Does collapsing faults change the fault distribution?
Dominant faults collapsing requires the dominant fault to be tested
Why collapse if only 4000-5000 faults are needed?
if ( a > b )
q <= c;
else
q <= d;
Lesson: Fault collapsing probably violates the intent of random testing.
>
a
b
a_gt_b
q
c
d
cd
internal signals?
gates?

## Slide 15: Formal proves independence
Design independence show by Fault Tree Analysis (FTA)
Formal COI proves data independence
Lesson: COI can prove independence when partitioning a safety element.
cover property ( safety_output );
OpenCores Ethernet MAC

## Slide 16: Fault campaign on RTL or gates?
More faults → greater DC %
OpenCores SPI Example
Lesson: RTL is more pessimistic than gates so just use RTL.
 | Fault Count | 
 | RTL | Gates
 | 2533 | 26789
Example: NRF= 100 | DC = 1 - 100 faults = 96% 2533 | DC = 1 - 100 faults = 99.9% 26789
RTL more pessimistic

## Slide 17: Is RTL okay?
Depending on the purpose, fault injection can be implemented at different abstraction levels (e.g., semiconductor component top-level, part or sub-part level, RTL, etc.) A rationale for the abstraction level is provided.
Selection of the abstraction level can also depend on the nature of the fault that is intended to be modelled by fault injection: the stuck-at fault can be injected at gate level netlist, whereas for bit-flips an RTL level abstraction is sufficient.
(ISO26262:2018-11, p.64)

## Slide 18: Running a fault campaign with formal

## Slide 19: Fault campaigns with formal
DUT
Safety
alarm
=
Sequential Equivalency
DUT
Safety
alarm
Faulted
Original
module fault_injector(...);
default clocking cb @($global_clock); endclocking
bit [$clog2(N)-1:0] fault = '0;
...
always @($global_clock)
if ( inject ) injected = 1;
asm_stable_sf_fault : assume property ( injected |-> $stable(fault) );
asm_delay_injection : assume property ( $fell(reset) |-> !inject[*START] );
always @($global_clock) begin
violated = injected && ( original.output != faulted.output );
detected = injected && ( !original.error && faulted.error );
end
// Find residual fault(s)
cov_res1: cover property (( fault == 1 ) && violated && !detected );
cov_res2: cover property (( fault == 2 ) && violated && !detected );
...
endmodule
// Pseudo-code - Tool directive for conditional cut point (sa0 fault injection)
cut { impl.signal1 } –cond { injected && fault == 1 } –value 0
FuSa app better!

## Slide 20: Keep it simple
ISO26262 requires testing "normal operating modes" and "conditions"
  Constraint formal to reduce state space complexity
  More likely to converge on results
Lesson: Constraint formal to normal modes and conditions.

## Slide 21: Sampling formal friendly faults
Status | Node
 | dut.p_wbspi.wb_dat_o[0]
 | dut.p_wbspi.wb_dat_o[1]
 | dut.p_wbspi.wb_dat_o[1]
 | dut.p_wbspi.shift.data[0]
 | dut.p_wbspi.shift.data[1]
 | dut.p_wbspi.shift.data[2]
 | …
Ignore
inconclusives
Sample formal friendly faults
Lesson: Never "cherry pick" formal friendly faults.
Introduces bias
Violates uniform random distribution principle

## Slide 22: Latent fault analysis
Safety
element
Safety
alarm
detected?
Latent fault analysis
Fault detected with a fault in alarm?
May have a secondary alarm
Safety
alarm
detected?
Typical latent fault analysis
Too many permutations for 2 faults
LFM is negligible in PMHF

## Slide 23: Latent analysis with multiple faults
Some faults won't propagate to the alarm → less undetected faults
LFM becomes more optimistic (and realistic)
// Allow formal to pick any safety element fault (free variable)
assume property { design_fault inside [1:max] }
// Latent fault analysis with 2 injected faults
cover property { alarm_fault == 1 && injected && violation && !detected }
Lesson: Formal has good capability for latent fault analysis.

## Slide 24: Formal fault campaign results

## Slide 25: Limitations of formal
Formal only fault analysis possible, but …
  State space limits formal analysis
  Non-formal friendly blocks yield poor results
Emulation
Formal Synthesis
RTL Synthesis
Simulation
Formal Analysis
Formal Fault List Pruning
Lesson: Formal FuSa best combined with other verification tools.

## Slide 26: Typical diagnostic coverage levels
Ranking | DC
Low | 60%
Medium | 90%
High | 99%
ISO26262 Part 5, Appendix D
Lesson: Consider DC guideline instead of an unnecessary fault campaign.

## Slide 27: ISO Terminology
Term
SPF
Residual
MPF, latent
MPF, d/p
Safe
ISO26262, Part 5, Figure B.2

## Slide 28: EDA tools
EDA Tools
Detected
Undetected
Activated
Non-propagated
Non-detected
Safe
ISO26262
SPF
Residual
MPF, latent
MPF, d/p
Safe
Lesson: Learn what vendor terminology means.

## Slide 29: Conclusion

## Slide 30: Lessons learned
Use formal for functional verification of safety elements and mechanism
Use formal's COI to prune out safe faults and provide a minimal set
Combine formal with simulation and emulation
Use formal for fault propagation testing via a FuSa or SEC app
Use a small fault sampling with a low margin of error and high level of confidence
Save effort using ISO DC guidelines instead of a fault campaign

## Slide 31: Questions