## Slide 1
Gaurav Kumar Yadav
Debasis Mishra Pattan Farooq Khan
Aniruddha N Anavatti
PrashantKumar Sonavane
Garima Srivastava
A Comprehensive Safety Verification Solution for SEooC Automotive SoC

## Slide 2
Agenda
Safety Element out of Context
Unique Design Requirements of SEooC SoCs
  Fault Manager(Fault in SoC)
  Safety Controller (For maintaining the FFI)
  Design Implementation
    FM Design
    SC Design
Verification Challenges
  FM Verification
  SC Verification
Comprehensive Solution
  Verification framework
  Solution implemented for the problems
    FM VC
    SC VC
Results - Data
Impact/Takeaway

## Slide 3
Safety Element out of Context (SEooC)
SEooC: ISO 26262-10:2018, Clause 9
“Safety related elements which are not developed for a specific item (Not developed in the context of particular vehicle)”
SoC
Infotainment system
Drowsiness detection
Infotainment and Drowsiness detection
Notes: The Windscreen Company
Drowisness Detection Systems | ADAS ...

## Slide 4
Safety Element out of Context (SEooC)
SEooC: ISO 26262-10:2018, Clause 9
“Safety related elements which are not developed for a specific item (Not developed in the context of particular vehicle)”
Infotainment system
Drowsiness detection
Infotainment and Drowsiness detection
SoC
Display Processing Unit
Image Signal Processing
Neural Processing Unit
Audio Processing Unit
IP_1
DRAM 2
DRAM1
IP_2
.
IP_n
SoC
Notes: The Windscreen Company
Drowisness Detection Systems | ADAS ...

## Slide 5
Safety Element out of Context (SEooC)
SEooC: ISO 26262-10:2018, Clause 9
“Safety related elements which are not developed for a specific item (Not developed in the context of particular vehicle)”
SoC
Display Processing Unit
Image Signal Processing
Neural Processing Unit
Audio Processing Unit
IP_1
DRAM 2
DRAM1
IP_2
.
IP_n
SoC
Infotainment system
Drowsiness detection
Infotainment and Drowsiness detection
Notes: The Windscreen Company
Drowisness Detection Systems | ADAS ...

## Slide 6
Safety Element out of Context (SEooC)
SEooC: ISO 26262-10:2018, Clause 9
“Safety related elements which are not developed for a specific item (Not developed in the context of particular vehicle)”
SoC
Display Processing Unit
Image Signal Processing
Neural Processing Unit
Audio Processing Unit
IP_1
DRAM 2
DRAM1
IP_2
.
IP_n
SoC
Infotainment system
Drowsiness detection
Infotainment and Drowsiness detection
Notes: The Windscreen Company
Drowisness Detection Systems | ADAS ...

## Slide 7
Safety Element out of Context
SEooC: ISO 26262-10:2018, Clause 9
“Safety related elements which are not developed for a specific item(Not developed in the context of particular vehicle)”
  Freedom From Interference (FFI): ISO 26262-1:2018, Clause 3.65
  “Absence of cascading failures between two or more elements that could lead to the violation of safety requirement”

## Slide 8
Unique Design requirements for an SEooC design
Talk about the need of configurable design elements. 2 such CE’s are:
Fault Manager
Safety Controller

## Slide 9
Unique Design requirements for an SEooC design
Need of Fault Manager
A typical Automotive SoC can generate ~5k faults from various safety mechanisms.
The main task of Fault manager is to log the faults and take correct action for each fault.
Fault manager routes the faults considering the actual use case of the fault
Reset Request
Power Down
Interrupt
External Alarm
Every fault is unique and need unique approach to handle it
Talk about the need of configurable design elements. 2 such CE’s are:
Fault Manager
Safety Controller
ADD FM diagram here

## Slide 10
Unique Design requirements for an SEooC design
Requirement of Safety Controller
Multi master Architectures: Safety Master, Security Master, DMA etc.
Safety and Security are 2 independent aspects to take care of in the SoC
Co-existence of ASILs and possibility of interference
Maintaining FFI
Safety Attribute controller (Configurable due to SEooC) Configuration at master side
Safety Controller at the block level for
Transaction monitoring
Reporting failures
Safety Controller Capabilities and configurations
Configuration of window access
Traffic monitoring once SC is enabled
Raising a flag if there are any un intended access
ADD SC DIAGRAM HERE
Talk about the need of configurable design elements. 2 such CE’s are:
Fault Manager
Safety Controller

## Slide 11
Unique Design requirements for an SEooC design
A typical SoC can generate ~5k faults from various safety mechanisms.
The main task of Fault manager is to log the faults and take correct action for each fault.
Fault manager routes the faults considering the actual use case of the fault
  Reset Request
  Power Down
  Interrupt
  External Alarm
Every fault is unique and need unique approach to handle it
SM 1
SM 2
SM n
FM
PMU
External MCU
CPU
Reset
Power-down
Alarm
Interrupt
SoC
.
.
.
.
.
.
Register 1
Register n
Register 2
..
M1
Fault_in[0]
Fault_in[n]
Fault_in[1]
M2
Mn
..
..

## Slide 12
Safety Controller
Multi master Architectures: Safety Master, Security Master, DMA etc
Safety and Security are 2 independent aspects to take care of in the SoC
Co-existence of ASILs and possibility of interference
Maintaining FFI
Safety Attribute controller (Configurable due to SEooC) Configuration at master side
Safety Controller at the block level for
  Transaction monitoring
  Reporting failures
Safety Controller Capabilities and configurations
Configuration of window access
Traffic monitoring once SC is enabled
Raising a flag if there are any un intended access
SC
Interconnect
Safe
Masters
Masters
Non-safe
Safe
Safe
Non-safe
Non-safe
Non-safe
Safe/non-safe attribute SC
FM
SoC
External block
SC
SC

## Slide 13
Trivial Solution and Challenges
Fault Manager verification
Typical SoC has 5000+ faults
Each DV engineer needs to understand and configure 30+ FM registers
Unintended Fault behaviour
Fault table change during design maturity
Scalability & Portability
Unverified fault might result in silicon bug/s
FM verification in Multi Die will pose a significant challenge for DV Engineers
Safety Controller verification
40+ blocks , 60+ instances
Verification of scenarios for all master slave pair
End to end verification SC-> FMU-> GIC
DV engineer needs a thorough understanding of SFRs of SC and FM
Human error might lead to silicon bug/s
Ensuring 100% functional coverage may not be possible
Functional coverage of 100% may not be guaranteed
Need to add about trivial verification methods here

## Slide 14
Safety controller verification
40+ blocks , 60+ instances
Verification of scenarios for all master slave pair
End to end verification SC-> FMU-> GIC
DV engineer needs a thorough understanding of SFRs of SC and FM
Human Error-> Silicon bug
Ensuring 100% functional coverage
Verification Challenges

## Slide 15
Proposed Solution

## Slide 16
Examples of distributed SEooC IP’s

## Slide 17
Inline checks
SCVC Execution
Auto Test Generation
Functional Coverage
Start
User Input
Pre-configuration checks
Post Check
Common Verification Framework
Slide looks dull. Need to enhance

## Slide 18
Application of Framework in Exynos SEooC IP’s
FM Common Task
SC Common Task

## Slide 19
Application of Framework in Exynos SEooC IP’s
FM Common Task
SC Common Task

## Slide 20
Application of Framework in Exynos SEooC IP’s
FM Common Task
SC Common Task
Insert SC flow diagram here

## Slide 21
Start
User Input
FM Register Configuration
Initial Status Check
Expected fault check
Fault alias check
FMVC POST Check
Output type. Interrupt request?
CPU ack received?
FM output check
Test Pass
Test Fail
FM Configuration
FM Check
Pass
Pre-set fault?
Fail
No
Yes
Pass
Pass
Pass
Fail
Fail
Fail
Fail
Yes
No
Inline checks
SCVC Execution
Auto Test Generation
Functional Coverage

## Slide 22
Proposed Solution Fault Manager
Auto generated test
Excel based checks.
Functional Checks
FM auto-configuration with minimalistic user inputs
Checkers for intended fault type, polarity, effect, etc. including spurious fault(s) detection
Fault reporting and SoC reaction check
Fault aliasing and connection check
Functional coverage for all the faults
Sanity checks for FM connections
Scalability to multichip solutions
Proposed Solution Safety Controller
Configurable safety attribute of the master as safe or non-safe
Allow or block transaction based on safety attribute
Check Safety Controller fault output to Fault Manager (FM) and GIC
Configuration of Safety Controller with minimalistic user inputs
Error logging of the blocked transaction
Functional Coverage for all the Safety Controllers in SoC
Automated test case generation
Different verification mode supported for user configuration
Scalable to other verification solutions to catch FFI issues in bus component
Proposed Solution (Delete if not required)

## Slide 23
Proposed Solution Fault Manager
Auto generated test
Excel based checks.
Functional Checks
FM auto-configuration with minimalistic user inputs
Checkers for intended fault type, polarity, effect, etc. including spurious fault(s) detection
Fault reporting and SoC reaction check
Fault aliasing and connection check
Functional coverage for all the faults
Sanity checks for FM connections
Scalability to multichip solutions
Proposed Solution Safety Controller
Configurable safety attribute of the master as safe or non-safe
Allow or block transaction based on safety attribute
Check Safety Controller fault output to Fault Manager (FM) and GIC
Configuration of Safety Controller with minimalistic user inputs
Error logging of the blocked transaction
Functional Coverage for all the Safety Controllers in SoC
Automated test case generation
Different verification mode supported for user configuration
Scalable to other verification solutions to catch FFI issues in bus component

## Slide 24
Configurable safety attribute of the master as safe or non-safe
Allow or block transaction based on safety attribute
Check Safety Controller fault output to Fault Manager (FM) and GIC
Configuration of Safety Controller with minimalistic user inputs
Error logging of the blocked transaction
Functional Coverage for all the Safety Controllers in SoC
Automated test case generation
Different verification mode supported for user configuration
Scalable to other verification solutions to catch FFI issues in bus component
Proposed Solution Safety Controller
Methodology

## Slide 25
Results
Safety Controller Common Task
240+ tests added with a TAT of half day instead of 3weeks.
Overall 95+% DV effort reduction for Safety Access Control verification Component
100% Functional Coverage
Architectural Impact:-
Safe read transactions being overridden as non-safe transactions has resulted in IP change. RTL change in > 40 instances
Bugs found:-
Bug found for fault from SAC instance to Fault Manager > 20 instances
Fault Manager Common Task
Configurable by the user
Scalable and Portable
Functional coverage is ensured
Fault aliasing
Typical verification
Critical timelines
Verification will be quick and robust
Human efforts reduced to single person. Executables taken and can be run.
Automated test creation flow will add multiple tests in short time.

## Slide 26
Conclusion
Plug and play Solution
Automated script based solution
Supports multiple modes
Functional Checkers and Error Logging feature
Systematic Coverage , Cross Functional Scenario
Scalability
Can be easily scalable to any safety SoC/Multi Chip, Multi Die, Cyber security SoC’s
Slide looks dull. Need to enhance

## Slide 27
Thank you

## Slide 28
Backup