## Slide 1: End-to-End Framework for Novel Datatype Arithmetic Verification
Qiuwen Lou, Ji Bing, Stevo Bailey, Nilabja Chattopadhyay, Deepak Shivarudrappa and Sankalp Dayal

## Slide 2: Presentation Outlines
Motivation
Background Work
Our Framework
Our Deployment
Results

## Slide 3: Introduction
New datatypes like FP16 and microscaling are widely adopted
Unique verification challenges arises from these new datatypes
Proposed: an end-to-end flow for novel datatype verification

## Slide 4: Motivation
Challenges
  Complex arithmetic operations and stringent correctness requirements.
  Time-consuming traditional simulation-based verification
Goals
  Faster time-to-market
  High reliability in novel datatype hardware module

## Slide 5: Framework
FP16 IP-Level Verification
  Modularization for both RTL and C
  Customized Interface
Application-Level Verification
  Accuracy for running model end-to-end
Performance Estimation

## Slide 6: Datapath Validation
A formal verification method proving functional equivalence between C++ models and hardware RTL
Benefits
  Exhaustive coverage
  Early error detection
  Faster convergence

## Slide 7: Challenges in FP16 Verification
Complexity factors
  Large input space (4+ billion combinations)
  Precision and rounding challenges
  Special cases like NaNs, infinities, subnormal numbers

## Slide 8: Verification Methodologies
Methodology | Pros | Cons
Formal (DPV) | Exhaustive coverage, early flaw detection | Scalability issues, specialized expertise
Simulation | Relistic scenarios, easier setup | Incomplete coverage, resource-intensive

## Slide 9: Application-level Verification
Integration with PyTorch
  C reference model wrapped with Python bindings
  Enable early accuracy verification within ML models
Results
  Accuracy within 0.1% of original PyTorch models

## Slide 10: Performance Estimation with DPV
Innovative Use
  Verified function-specific performance
  Eliminate need for separate simulations
Method
  Ready-valid protocol for output handshaking

## Slide 11: Our Deployment
Setup
  Versatile RTL interface
  Unified C model
  Dynamic TCL file mapping
Benefits
  Single RTL build for multiple functions
  Reduced compilation time

## Slide 12: Covergence Strategies
Case Splitting
  Divide complex properties into manageable sub-cases
  Parallel processing for faster convergence
Assume Guarantee
  Break down tasks into smaller subproblems
  Verify submodules before full system

## Slide 13: Results
Bugs Identified
  11 bugs across RTL and C model, including corner cases
Development Time Reduced
  From 6 months to 2 months
Performance
  Our model level error is within 0.1% between RTL and PyTorch

## Slide 14: Conclusions
Framework benefits
  Faster time-to-market
  High confidence in novel datatype hardware
  Scalable to other datatypes like FP4, FP6, FP8
Future work
  Extend framework for new datatypes and formats

## Slide 15: Questions
Finalize slide set with questions slide

## Slide 16: Questions??