## Slide 1: Test bench Framework for Fully Automated Register Tests of Numerous IPs in SoC
Wonyeong So, Minje Kim, Jihye Lim, Sunil Roe, Youngsik Kim, Sunil Brian Choi
Samsung Electronics

## Slide 2: Contents
Background
IP access test
Proposed Methodology
Result
Conclusion
Question

## Slide 3: Background 1 - Role of verification engineer
Understanding the specifications
Testbench implementation and maintenance
Achieving all test passes
  Power, Clock, Core function, Register access and etc..

## Slide 4: Background 2 - Challenges already at hand
Increasingly complex design
  Complex bus architecture
  More IPs
Increasing verification time
  Increased simulation time from scenario complexity
  Massive testbench maintenance
Limited verification schedule
This trend will intensify
  Advancement of process miniaturization

## Slide 5: Background 3 - Prioritize and focus
Increased likelihood of bug occurrence
Focus on complex verification scenarios
  Scenarios similar to SW operations
Automate what can be automated
  IP register access test, connection test and etc..

## Slide 6: IP access test - Background
Test whether the master can access each IP
Most fundamental task in SoC verification
In principle, tests must be rerun with every RTL update
Rerunning tests every time is impractical

## Slide 7: IP access test - Crucial but Troublesome
Tests must be performed on all IPs
Sometimes feels unnecessary
But it must be done
Chart: Average ratio of IP access tests to total tests across 5 SoC projects
| Other test | IP access test
Ratio of IP access tests to total tests | 9600 | 5200

## Slide 8: What if tasks were automated?
Improves verification quality
Creates more value in the same time
More precise coverage
More scenario
Time save

## Slide 9: How to automate it?
Everything is already prepared
All verification is based on specifications
Several scripting languages

## Slide 10: Proposed Methodology
Five key components
  Specification Collector
  Test bench generator
  Test executor
  Debugger
  Reporter
Automated platform enables RTL update adaptation

## Slide 11: Proposed Methodology - Specification Collector
IP-XACT
SoC address map
UVM register model
Security spec
Parsing required spec files
  IP-XACT, SoC address map, UVM register model, Security spec
YAML data
<spirit:vendor>VENDOR</spirit:vendor>
…
…
<spirit:version>1.0</spirit:version>
<spirit:componentInstances>
<spirit:componentInstance>
<spirit:instanceName>IP_A</spirit:instanceName>
IP-XACT XML
BLK_A | … | …
 | … | …
 | … | …
 | … | …
 | IP_D | 0x1003_0000
 | IP_C | 0x1002_0000
 | IP_B | 0x1001_0000
 | IP_A | 0x1000_0000
SoC address map excel file
class reg_blk_c extends base_reg_blk_c;
…
rand ip_a_reg_blk_c ip_a_reg_blk;
rand ip_b_reg_blk_c ip_b_reg_blk;
…
endclass
…
`define IP_A_BASE_ADDRESS ‘h1000_0000
…
UVM register model class
Register name | Field | Range | Access | Reset Value | … | TZPC usage | Description
TZPC_PROT0 |  |  |  |  |  |  | 
 | … | … | … | … |  | … | …
 | TZPC8 | [8] | RO | 0x1 |  | S/NS | …
 | TZPC7 | [7] | RO | 0x1 |  | S/NS | …
 | TZPC6 | [6] | RO | 0x1 |  | S/NS | …
 | TZPC5 | [5] | RO | 0x1 |  | S/NS | …
 | TZPC4 | [4] | RO | 0x1 |  | S/NS | …
 | TZPC3 | [3] | RO | 0x1 |  | S/NS | IP_A TZPC control
 | TZPC2 | [2] | RO | 0x1 |  | NS | …
 | TZPC1 | [1] | RO | 0x1 |  | S/NS | …
Security specification table
- REG_BLK :
ip_a_reg_blk_c : ip_a_reg_blk
SECURITY :
REG_NAME_FOR_SECURITY : reg_0
SECURITY_FIELD : 3
SECURITY_IP : tzpc_blk_a_reg_blk
…

## Slide 12: Proposed Methodology – Test bench generator
Rendering using the Jinja2 Python library
- REG_BLK :
ip_a_reg_blk_c : ip_a_reg_blk
SECURITY :
REG_NAME_FOR_SECURITY : reg_0
SECURITY_FIELD : 3
SECURITY_IP : tzpc_blk_a_reg_blk
…
…
Generated test bench
Generated input data
Python Jinja2 library
Rendering

## Slide 13: Proposed Methodology – Test executor
RTL compilation and regression execution
Perform full test once after testbench creation
Batch run via vManager

## Slide 14: Proposed Methodology – Debugger
Spec bugs and bus traffic bugs
Debugging solution for error tags
Automated bus traffic debugging via BTS(Bus Trace System)

## Slide 15: Proposed Methodology – Debugger
…
[5701957] UVM_INFO (bts_c) BTS::Error response debugger is called
bts_intf_inst:: flush function is called
[5701957] UVM_INFO (bts_c) BTS::Error response occurrence instance : top.dut.BLK_A.AXI2APB
[5701957] UVM_INFO (bts_c) BTS::Please refer bts directory to get more detail about debug result
[5701957] UVM_ERROR (AXI::cdn_ps_amba_if::prd) [SLVERR] Error response occured. UVM_READ, addr = 0x1000_0100, data = 0x0000_0000, id = 0x22 (ip_a_reg_blk.reg_a)
…
[23971539] UVM_WARNING (CDN_AXI_NONFATAL_WARNING_VR_AXI1001_WRITE_BURST_RESPONSE_TIMEOUT_AND_DISCARDED)
Write burst response timeout
…
Timeout burst: kind:INCR address: address:0x0012000040 id:37 len:1 size:WORD access:NORMAL
Title: Write burst response timeout
…
[23971539] UVM_WARNING (DENALI_CDN_AXI_CB_Error) Agent master dropped transaction with transaction id: -1
[23971539] UVM_INFO (bts_c) BTS::Timeout debugger is called
[23971539] UVM_INFO (bts_c) BTS::Bus hang occurrence instance : top.dut.BLK_B.IP_B
[23971539] UVM_INFO (bts_c) BTS::Please refer bts directory to get more detail about debug result
Debugged by BTS
Debugged by BTS
B. Error response log and debug result by BTS
C. Bus hang log and debug result by BTS
[0] UVM_ERROR (reg_access_with_security_seq_c) [SFRSEC][NOSECUREG] security_reg_num_for_rd is not given.
[0] UVM_INFO (reg_access_with_security_seq_c) Debugging guide
[0] UVM_INFO (reg_access_with_security_seq_c) 1. Open sim.log file in log path
[0] UVM_INFO (reg_access_with_security_seq_c) 2. Check the "[SFRSEC][NOSECUREG]" issue in log file
[0] UVM_INFO (reg_access_with_security_seq_c) 3. Assign the correct value to the security_reg_num_for_wr/rd variable. Below is an example code.
[0] UVM_INFO (reg_access_with_security_seq_c) sfr_access_with_tzpc_seq.security_block = “security_ip_a_reg_blk";
[0] UVM_INFO (reg_access_with_security_seq_c) sfr_access_with_tzpc_seq.security_reg_num_for_rd = 0;
[0] UVM_INFO (reg_access_with_security_seq_c) sfr_access_with_tzpc_seq.security_reg_num_for_wr = 2;
A. Predefined error log and error solution
Error tag
Error solution

## Slide 16: Proposed Methodology – Reporter
Easily view large-scale IP access test results
High responsiveness with GO based implementation
Test type
IP list in block F
Test result
Error type

## Slide 17: Automated framework trigger
RTL release becomes the event
Triggering via API
RTL integration engineer
Shared DB
Verification engineer
Test bench framework
Register release event
API
Query
API
Response
Test result

## Slide 18: Result
Approximately 35% of tests can be automated
SoC project | IP(#) | IP access test(#) | Total test(#) | Ratio
A | 1,845 | 5,418 | 13,894 | 0.39
B | 1,632 | 4,804 | 13,687 | 0.351
C | 1,279 | 3,798 | 10,501 | 0.3617
D | 1,184 | 2,839 | 8,570 | 0.3313
E | 1,756 | 6,595 | 18,127 | 0.3638

## Slide 19: Conclusion
About 35% test automation possible
Efficient reduction of verification TAT

## Slide 20: Questions