## Slide 1: AI - accelerating coverage closure using intelligent stimulus generation
Jainender Kumar, Ronak Bhatt, Garima Srivastava, Ashutosh Sinha, Prashant Teotia

## Slide 2
Agenda
System on Chip (SoC)
Proposed AI/ML Solution with SimAI
How SimAI Helps in Coverage Closure
Result and Key Metrics
Conclusion
Coverage and its Challenges in SoC NOC Interconnect

## Slide 3
SOC
With a growing consumer market in AI, IOT & mobile applications, the design of SOC is becoming more complex than ever
Source: www.grandviewresearch.com

## Slide 4
Complex SOC System
The customers have come to experience sophisticated applications, which is possible with the advent of complex SOC
Source: slideshare

## Slide 5
NOC
The Interconnects allows for the connection and communication between all the IPs in the SOC
METRICS
Reliability
Performance
Power
Cost
Simplified NOC
There can be 100s of masters and ~1000 slaves in the real system.
SOCs have evolved from single processors connected to a few IP blocks to multimode networks that connect to hundreds of IP blocks
Nested NOC

## Slide 6
Verification Challenges
Complex interconnects
Explosion in Coverage Parameters
Massive number of bins
Impact on Time to Market
Ineffective coverage closure
Extensive functional coverage
Extended timeliness and increased consumption
Complicate verification efforts
Demand advanced solutions.
NOC Verification
Coverage is crucial for verification as it ensures all scenarios, edge cases, and requirements are exercised for comprehensive validation.

## Slide 7
Random stimulus reaches a plateau, leading to diminishing returns in verification progress.
Coverage Complexity
Resource
Bottlenecks
Coverage
Saturation
Simulation demands exceed available computational and memory resources.
Massive numbers of parameters and cross-products create over a million bins in SOC verification.
NOC Coverage Challenges
AXI
(Master)
Len 1
Len 2
Len N
Size 1
Size 2
Size N
Kind 1
Kind 2
Kind-N
READ
WRITE
ID 1
ID 2
Cover group -1
Cover group -2
Cover group -N
Slave-1
Slave-2
Slave-N

## Slide 8
NOC Coverage Traditional Approach
Test/vPlan
Execute regression suite
Bug Fixes
Test bench Fixes
Constraint Fixes
Measure the metrics
Huge time
Large resources
Coverage closure
Done
Identify closure strategies
Directed
Stimulus
Yes
No
Chart: Original Regression – Traditional Approach
| 5.5 | 11 | 16.5 | 22 | 27.5 | 33 | 38.5 | 44 | 49.5 | 55.5 | 61 | 66.5
Series 1 | 46.56 | 69.53 | 82.8 | 89.46 | 93.8 | 96.46 | 97.2 | 97.9 | 98.4 | 98.8 | 99.1 | 99.3
Manual intervention
Randomized
Stimulus
More iteration/cycle
Less improvement
Need Directed test case

## Slide 9
Proposed Solution
Constraints
Reachability
Address Space
Automation
Coverage Model
SimAI input Bias config
Devise
Test Plan
Randomized
Stimulus
Execute regression suite
Measure the metrics
Coverage closure
Done
SimAI
AI generated test suite
2-6x seed
reduction
Maximized
coverage
Yes
No

## Slide 10
SimAI Introduction
Jasper Formal
Jasper Formal
Xcelium
Verisium
SimAI
AI Optimized Randomization
Stimulus
Coverage
Jasper Formal
Jasper Formal
Xcelium
Regression Efficiency
Coverage Hit Ratio
Hole
Related hits to target

## Slide 11
simAI - Input Bias
Input Bias maximizes coverage by stressing user-specified random variables.
  It fills efficiency gap of the autonomous coverage maximization of SimAI.
  It targets “hard-to-hit” coverage bins that have strong correlations to random variables
Coverage
SimAI
Input Bias
Randomization
Trace
Test
Random
points
Constraints
Variable File
Variable File
Users specify random variables and value ranges to stress
Users may specify groups of variables and values that should be assigned together.
Input Bias Flow
Reads the Variable File as additional input in SimAI
Evaluates how the variables in Variable File are assigned in user’s tests in the user’s regression
Generates a SimAI regression:
  Constrains so that the variables and values in Variable File are assigned effectively in user’s tests.

## Slide 12
Proposed Solution
Constraints
Reachability
Address Space
Automation
Coverage Model
SimAI input Bias config
Devise
Test Plan
Randomized
Stimulus
Execute regression suite
Measure the metrics
Coverage closure
Done
SimAI
AI generated test suite
2-6x seed
reduction
Maximized
coverage
Yes
No

## Slide 13
Impact of AI on coverage efficiency
Result and Key Metrics
Significant time reduction
Higher coverage achieved
Improved resource utilization
Figure 6. simAI tool generated coverage vs normal regression coverage after applying ML at 88%.
Without input-bias
With input bias

## Slide 14
Result and Key Metrics
Figure 6. simAI tool generated coverage vs normal regression coverage after applying ML at 46%.
Figure 7. AI-generated coverage vs normal regression coverage applied on the same regression with different base regression
Without input-bias
Without input-bias
With input-bias

## Slide 15
Dynamic Stimulus Adjustment
Easy Integration
Scalability and Efficiency
Why AI/ML in NOC Coverage Closure Stands Out ?
Advantages and Features

## Slide 16
Leveraging AI/ML for Enhanced Functional Coverage
Efficient Coverage Closure without coverage saturation
Resource Optimization
Highly Scalable
Reduced coverage complexity with use of automation
Conclusion

## Slide 17: Thank you