## Slide 1: Applications of Supply Tunneling in Unified Power Format 4.0 for Mixed Signal Design
Daniel Cross
Cadence Design Systems, P1801 Working Group

## Slide 2: What is Tunneling?
Jacek Halicki, CC BY-SA 4.0

## Slide 3: Motivation
UPF 4.0 permits HDL UPF supply nets
UPF defines the supply network
Conversion HDL UPF HDL = loss of information or resolution
Standardization needed

## Slide 4: Situations – Starting Simple
create_supply_net VDDA -tunneling force -resolve unresolved
connect_supply_net VDDA -ports {UA1/VDD UA2/VDD} -vcm UDN2UPF
HDL Model
(supply source)
UDN
HDL Model
(load)
UDN
UA1
VDDA
UA2
VDD
VDD

## Slide 5: Situations – Starting Simple
create_supply_net VDDA -tunneling force -resolve unresolved
connect_supply_net VDDA -ports {UA1/VDD UA2/VDD} -vcm UDN2UPF
HDL Model
(supply source)
UDN
HDL Model
(load)
UDN
UA1
VDDA
UA2
VDD
VDD
VDDA created by UPF, but will be simulated as the UDN
Legal values: force, inhibit, automatic

## Slide 6: Situations – Starting Simple
create_supply_net VDDA -tunneling force -resolve unresolved
connect_supply_net VDDA -ports {UA1/VDD UA2/VDD} -vcm UDN2UPF
HDL Model
(supply source)
UDN
HDL Model
(load)
UDN
UA1
VDDA
UA2
VDD
VDD
Can a UPF resolution be applied without converting to UPF type?
more issues ahead …

## Slide 7: More Complexity
create_supply_net VDDA -tunneling force -resolve unresolved
set_scope UD1
create_supply_port VDD
set_scope ..
set_scope UD2
create_supply_port VDD
set_scope ..
connect_supply_net VDDA -ports {UA1/VDD UA2/VDD UD1/VDD U2/VDD} -vcm UDNA2UPF
HDL Model
(supply source)
UDN
HDL Model
(load)
UDN
UA1
VDDA
UA2
digital HDL
digital HDL
UPF
UPF
UDNA2UPF VCM
UD1
UD2
VDD
VDD
VDD
VDD

## Slide 8: More Complexity
create_supply_net VDDA -tunneling force -resolve unresolved
set_scope UD1
create_supply_port VDD
set_scope ..
set_scope UD2
create_supply_port VDD
set_scope ..
connect_supply_net VDDA -ports {UA1/VDD UA2/VDD UD1/VDD U2/VDD} -vcm UDNA2UPF
HDL Model
(supply source)
UDN
HDL Model
(load)
UDN
UA1
VDDA
UA2
digital HDL
digital HDL
UPF
UPF
UDNA2UPF VCM
UD1
UD2
VDD
VDD
VDD
VDD
Value Conversion Method (VCM) inserted by UPF

## Slide 9: More Complexity
create_supply_net VDDA -tunneling force -resolve unresolved
set_scope UD1
create_supply_port VDD
set_scope ..
set_scope UD2
create_supply_port VDD
set_scope ..
connect_supply_net VDDA -ports {UA1/VDD UA2/VDD UD1/VDD U2/VDD} -vcm UDNA2UPF
HDL Model
(supply source)
UDN
HDL Model
(load)
UDN
UA1
VDDA
UA2
digital HDL
digital HDL
UPF
UPF
UDNA2UPF VCM
UD1
UD2
VDD
VDD
VDD
VDD
What if UD2 is a driver?

## Slide 10: UPF Driver
create_supply_net VDDA -tunneling force -resolve unresolved
set_scope UD1
create_supply_port VDD
set_scope ..
connect_supply_net VDDA -ports {UA1/VDD UA2/VDD UD1/VDD} -vcm UPF2UDNA
HDL Model
(supply source)
UDN
HDL Model
(load)
UDN
UA1
VDDA
UA2
digital HDL
UPF
UPF2UDNA VCM
UD1
VDD
VDD
VDD

## Slide 11: UPF Driver
create_supply_net VDDA -tunneling force -resolve unresolved
set_scope UD1
create_supply_port VDD
set_scope ..
connect_supply_net VDDA -ports {UA1/VDD UA2/VDD UD1/VDD} -vcm UPF2UDNA
HDL Model
(supply source)
UDN
HDL Model
(load)
UDN
UA1
VDDA
UA2
digital HDL
UPF
UPF2UDNA VCM
UD1
VDD
VDD
VDD
HDL net VDDA has multiple drivers (including the VCM)

## Slide 12: Multiple HDL Drivers
create_supply_net VDDA -tunneling force -resolve unresolved
set_scope UD1
create_supply_port VDD
set_scope ..
connect_supply_net VDDA -ports {UA1/VDD UA2/VDD UA3/VDD UD1/VDD} -vcm UDNB2UPF
UDNA
UDNB
VDDA
UPF
UDNB2UPF VCM
HDL Model
(supply source)
UA1
VDD
HDL Model
(load)
UA3
VDD
digital HDL
UD1
VDD
HDL Model
(supply source)
UA2
VDD
UDNB

## Slide 13: Multiple HDL Drivers
create_supply_net VDDA -tunneling force -resolve unresolved
set_scope UD1
create_supply_port VDD
set_scope ..
connect_supply_net VDDA -ports {UA1/VDD UA2/VDD UA3/VDD UD1/VDD} -vcm UDNB2UPF
UDNA
UDNB
VDDA
UPF
UDNB2UPF VCM
HDL Model
(supply source)
UA1
VDD
HDL Model
(load)
UA3
VDD
digital HDL
UD1
VDD
HDL Model
(supply source)
UA2
VDD
UDNB
HDL resolution of multiple drivers and nettypes occurs first

## Slide 14: Multiple HDL Drivers
create_supply_net VDDA -tunneling force -resolve unresolved
set_scope UD1
create_supply_port VDD
set_scope ..
connect_supply_net VDDA -ports {UA1/VDD UA2/VDD UA3/VDD UD1/VDD} -vcm UDNB2UPF
UDNA
UDNB
VDDA
UPF
UDNB2UPF VCM
HDL Model
(supply source)
UA1
VDD
HDL Model
(load)
UA3
VDD
digital HDL
UD1
VDD
HDL Model
(supply source)
UA2
VDD
UDNB
Type tunneled to HDL receiver depends on port type

## Slide 15: Switch Dilemma
create_supply_net VDDA
create_suppy_net VDDA_SW
create_power_switch S0 -input_supply_port VDDA \
-output_supply_port VDDA_SW -control_port {EN vddaEn} \
-on_state {on VDDA {EN}} -off_state {off VDDA {!EN}}
set_scope UD1
create_supply_port VDD
set_scope ..
connect_supply_net VDDA -ports {UA1/VDD S0/VDDA} -vcm UDNA2UPF
connect_supply_net VDDA_SW -ports {UA2/VDD UD1/VDD S0/VDDA_SW} -vcm UPF2UDNA
UDNA
UDNA
VDDA
UPF
UDNA2UPF VCM
HDL Model
UA1
VDD
HDL Model
(load)
UA2
VDD
digital HDL
UD1
VDD
S0
UPF2UDNA VCM
VDDA_SW
Power switch S0 created by UPF:
Do we want UDNA tunneled to UA2?

## Slide 16: One Solution – HDL Switch Model
create_supply_net VDDA -tunneling force
create_suppy_net VDDA_SW -tunneling force
set_scope UD1
create_supply_port VDD
set_scope ..
connect_supply_net VDDA -ports {UA1/VDD S0/VDDA}
connect_supply_net VDDA_SW -ports {UD1/VDD S0/VDDA_SW UA2/VDD} -vcm UDNA2UPF
UDNA
UDNA
VDDA
UPF
UDNA2UPF VCM
HDL Model
UA1
VDD
HDL Model
(load)
UA2
VDD
digital HDL
UD1
VDD
S0
VDDA_SW
Manually place S0 and connect its control ports

## Slide 17: Tunneling Options
FORCE: Tunneling is requested for the created UPF supply net
INHIBIT: Tunneling is prevented on the created UPF supply net
AUTOMATIC: A tool-specific algorithm is used to determine whether tunneling is applied to the created UPF supply net
If -tunneling is not included in the create_supply_net command, a default value of UNSPECIFIED will be applied to the created UPF supply net.
Priority: FORCE/ INHIBIT > AUTOMATIC > UNSPECIFIED

## Slide 18: Summary
HDL supply tunneling is introduced in UPF 4.0
Use UPF HDL supply tunneling to construct the power network with UPF without losing expressiveness or resolution of HDL User Defined Nettypes
Do not try to mix UPF supply net resolution and HDL supply tunneling
Be mindful of design and verification priorities when deciding on a power switch modeling strategy
Review the new standard (IEEE 1801-2024) for more details
https://ieeexplore.ieee.org/browse/standards/get-program/page

## Slide 19: References
"IEEE Standard for Design and Verification of Low-Power, Energy-Aware Electronic Systems," in IEEE Std 1801-2024 , (Publication pending).

## Slide 20: Thank You
Questions?