## Slide 1
Varun Kumar C, Jyoti Verma, Sekhar Dangudubiyyam
Samsung Semiconductor India Research (SSIR)
Efficacious Verification of Irreproachable and Steady Data Transfer Protocol for high-speed die-to-die communication on a 3DIC Chip

## Slide 2
Introduction
D2D Interface
Stack Level Verification
SOC Level Verification
Issues and Bugs
Result
Future work
Conclusion
AGENDA

## Slide 3
Limitations on the Moore’s Law
2.5D technology (Interposer technology) integrates several electronic devices inside a single package by assembling them side-by-side on a shared interposer
3DIC technology consists of multiple tiers of active devices stacked above each other
Introduction – 3DIC Technology

## Slide 4: Guidelines (3)
Introduction – Advantages of 3DIC
1
4
2
3
5
3
5
1
4
5
3
2
3
5
Reduction in wire-length
Efficient power consumption
Improved packing density
Noise immunity
Superior performance

## Slide 5
Introduction – Motivation for D2D protocol
TSVs enable 3DIC technology and are still experimental
Higher operating temperature
High temperature differences between the layers
Conventional data transfer through AXI interface across the dies poses challenges
Lack of reliability
Data loss
Higher pin count (450 pins)
High latency
Complex die to die NOC timeout

## Slide 6
D2D Interface
TSV based interface
Supports transfers up to 100 GBps
20 unique interrupts
Reduced number of inputs and outputs
AXI transactions monitoring
CRC Error checks and data retry
SDR and DDR modes
Center aligned and Delay alligned
ECC Error detection and correction (QEDTEC)
Bus maintenance and cleany operation
D2D Interface

## Slide 7
Levels of Verification
Stack Level Verification
Master VIPs for traffic generation and configuration
Back to back IP wrap with TSV IO modules
Functional verification
Code coverage and functional coverage
SOC Level Verification
Real time masters for traffic
Low power verification
Performance verification
System level tests for ATE
Cross die interrupt handling

## Slide 8
Stack Level Verification
D2D_FIFO SI
D2D_FIFO SI
D2D_FIFO MI
D2D_FIFO MI
SI_IOCTRL
MI_IOCTRL
AXI_CH_ARBITER
AXI_CH_ARBITER
AXI_CH_DEMUX
AXI_CH_DEMUX
SPECIAL
FUNCTIONREGISTERS
SPECIAL
FUNCTIONREGISTERS
AXI4 MASTER VIP
APB MASTER VIP
APB MASTER VIP
AXI4 SLAVE VIP
ERROR INJECTION
ERROR INJECTION
AXI4 I/F
AXI4 I/F
APB I/F
APB I/F
AR, AW, W
AR, AW, W
B, R
B, R
RESPONSE
PAYLOAD
SDRCLK, DDRCLK1, DDRCLK1, INITN
SDRCLK, DDRCLK1, DDRCLK1, INITN
PAYLOAD
PAYLOAD
PAYLOAD
RESPONSE
RESPONSE
RESPONSE
49
49
49
49
9
9
9
9
SCOREBOARD
COVERAGE MODULE
COVERAGE MODULE
VERIFICATION COMPONENTS
ACLK DOMAIN(1 GHz)
PCLK DOMAIN(250MHz)
CORECLK DOMAIN(4GHz)
D2D_Slave_interface
D2D_Master_interface
INTERFACE MONITOR
INTERFACE MONITOR

## Slide 9
SOC Level Verification
NOC
NOC
Master
Master
Master
. . .
CPU Cores
CPU Cores
LPDDR5
PCie4
Master
Master
EP
AXI Performance Monitor
AXI Performance Monitor
Error Injection Module
Master
Testbench Components
TOP DIE
BOTTOM DIE
D2D Slave Interface
D2D Master Interface
D2D Slave Interface
D2D Master Interface
TSV IOs
Clock Skewer/Jitter Inducing

## Slide 10
SOC Level Verification
Real Time Application Scenarios
Multiple masters in top and bottom die
Concurrent traffic generation from all the CPU cores, traffic generator and PCIE master
Clock jitter and skew introduction
Different crystal oscillators in top and bottom die
Tuning of coarse grain and fine grain delays
Variable clock ratios with traffic stress
Independent operational clocks of D2D_master_interface and D2D_slave_interface
Confirmation on robustness of flow control
Clock skewer and jitter inducing testbench component

## Slide 11
SOC Level Verification
System level tests for ATE
Verification in a single IP environment
Internal loopback, external loopback and remote loopback
Cross die interrupt handling
Support for 20 unique interrupts
Two GIC600s present in top and bottom die
Low power verification
Dies operate at different voltages
Various power aware verification checks
Testing on various pattern generation modes
Communication between GIC 600s happen through AXI stream interface
Different voltage rails for PLLs, D2D core, TSV_TX_IO and TSV_RX_IO

## Slide 12
SOC Level Verification – Link reliability and bus maintenance
D2D_Slave_Interface
D2D_Master_Interface
CRC Error Injection
ECC Error Injection
Payload
Response
49
9
49
9
Injection enable, number of CRC error, CRC error bit position, ECC error, ECC error type(single, double, uncorrectable), Payload type(AW, AR, W, B, R),…
Error scenario monitoring in the sequences
Multiple instances of D2D interface, hence error injection through force is not feasible
Development of error injection module which can be scaled up to any payload based protocol
Error condition behavior was monitored in the sequences through registers, counters and interface signals

## Slide 13
Issues and bugs
Protocol violations for various configurable AXI parameters
Transactions hang during multi-master D2D interface access
Improper payload formation due to clock skew and jitter
Issues in P and Q channel handshakes for Low power verification
Issues in reliability features like ECC and CRC errors

## Slide 14
Results – Code coverage

## Slide 15
Results – Performance verification
BLK_D2D_TOP
WRITE ONLY PERFORMANCE Source :: BLK_D2D TOP ---------> Destination :: BLK_D2D BOT RAM Traffic = 8k MO = 04 awlen = f WR Bandwidth from 1st WVALID posedge to last WLAST negedge = 8192/614.88 = 13.32 GBs => 106.968 Gbits per sec
BLK_D2D BOT
READ ONLY PERFORMANCE Traffic = 8k MO = 04 arlen = f RD Bandwidth from 1st RVALID posedge to last RLAST negedge = 8192/547.344 = 14.96 GBs => 119.968 Gbits per sec
WRITE ONLY PERFORMANCE Source :: BLK_D2D BOT ---------> Destination :: BLK_D2D TOP RAM Traffic = 32k MO = 04 awlen = f WR Bandwidth from 1st WVALID posedge to last WLAST negedge = 32768/2501.856 = 13.09 GBs => 104.77 Gbits per sec
READ ONLY PERFORMANCE Traffic = 32k MO = 04 arlen = f RD Bandwidth from 1st RVALID posedge to last RLAST negedge = 32768/2192.4 = 14.94 GBs => 119.56 Gbits per sec

## Slide 16
Future work
Dynamic CDC verification using metastability injection (CDC jitter) mechanism during simulation
Utilization of emulation for accelerating the functional verification closure

## Slide 17
Conclusion
Die-to-die interfaces provide major use cases for targeting applications
Presented D2D protocol offers plenty of features and hence better die to die communication
Functionality, timing, power, energy consumption and reliability impacted the complexity of verification
Master like VIPs used for stack level verification
Reuse of sequences at SOC level verification
New methods in clock scenarios verification, loopback verification, performance verification, CRC and ECC error verification and functional verification

## Slide 18: Questions