## Slide 1: A Faster and Efficient Timing Constraint Verification Methodology for GFX SOCs
Vineeth B, SOC Design Engineer
Deepmala Sachan, SOC Design Manager
Intel Technology India Pvt. Ltd.

## Slide 2: Introduction
Complex High-Performance Designs
Accuracy of timing constraints is critical for proper synthesis results and timing closure
Gate-Level Simulation (GLS) is the conventional methodology used to verify the timing constraints
  Occurs too late in the design cycle
  Long turnaround time (TAT)
  Less coverage
  Huge effort to debug failures

## Slide 3: Timing Constraint Verification Methodology
Primary Inputs
  RTL Filelist
  HIP Collateral (Liberty File)
  Timing Constraints (TCL File)
  Block Configuration File (TCL file)
Ensure Zero Clock Warnings
Ensure 100% Constraint Mapping
Timing Exception Formal Verification
  Generate Assertions for Failures
  Separate Functional & DFX Assertions
Assertion Verification in Simulation

## Slide 4: Formal Verification Improvements
Specifying Synchronizer Cells in Design
  Formal verification passes for all timing paths with synchronizer cell as endpoint
Constrain Input/Asynchronous Reset Ports affecting formal verification of timing exceptions
  Input ports must be constrained to its legal values
  Asynchronous reset ports must be constrained to its non-reset value
  Formal verification passes for all timing paths having static startpoint
Excluding Timing Don’t Cares
Importing Clock Domain Crossing (CDC) Constraints

## Slide 5: Noise Elimination from Formal Verification
Eliminate Timing Exceptions that do not require Formal Verification
# | Scenario | Description
1 | NO PATH | No valid startpoints/endpoints were found or no sensitizable combinational path found between them
2 | SKIPPED (I/O Ports) | Exceptions that can only be verified at higher block level where the logic that drives input ports can be inferred
3 | SKIPPED (Async Clocks) | Exceptions having asynchronous launch/capture clocks
4 | SKIPPED (MCP Hold<Setup) | MCPs having hold shift value less than setup shift value of the corresponding MCPs
5 | SKIPPED (Duplicate) | Duplicate Exceptions
6 | WAIVED | Exceptions corresponding to timing don’t cares

## Slide 6: Timing Exception Assertion Verification

## Slide 7: Plugging-in Assertions in RTL Simulations
Handling Differences between Synthesis/Simulation Standard Cell Models
  Standard cells have different implementation in synthesis and simulation
  Results in cross-module reference resolution errors (XMREs)
  Restrict tapping internal standard cell signals and refer signals only at the boundary of standard cell wrappers
Signals inside standard cell wrappers are still tapped if sequential elements are present between the signal and its input ports
  Verification warnings issued on tapped internal standard cell signals
  Requires mapping file to post-process generated assertions
  Mapping File Syntax: <module name> <simulation name> <synthesis name>

## Slide 8: Uncovered Assertions Sign-off Methodology

## Slide 9: Unmapped Constraints/Clock Warnings Results
Zero Clock Warnings
100% Constraint Mapping
# | Issues Found
1 | Unmapped timing constraints due to syntax errors
2 | Net has clock-like behavior, but no clock propagates to it
3 | Clock propagation was stopped by a clock
4 | Generated clock has an invalid edge specification
5 | There is a clock-to-clock false path, but the clocks have the same master clock and are not exclusive
6 | The clock crossing from clock to clock has been specified as logically exclusive, but there is a nonexclusive crossing between these clocks
7 | Clocks have been specified as physically exclusive, but they can co-exist in the design at the same time
8 | Clocks are logically exclusive, but they have not been specified as such

## Slide 10: MCP Exception Verification Results
SOC MCP Exception Formal Verification Results
SOC MCP Exception Assertion Verification Results
% of PASSING MCPs | % of FAILING MCPs | % of NO PATH MCPs | % of SKIPPED MCPs | % of WAIVED MCPs
58.76% | 27% | 10.11% | 3.46% | 0.67%
% of Functional (non-DFX) MCP Assertions | % of PASSED Assertions | % of FAILED Assertions | % of UNCOVERED Assertions | % of MCPs corresponding to Assertion Failures
2% | 22% | 0.02% | 77.98% | 0.1%

## Slide 11: Conclusion
Faster, Scalable and more Efficient than conventional methods (such as GLS)
Achieved Significant Shift-Left in the Timing Closure of the design
  Enabled all the unmapped constraints and clock warnings to be uncovered and resolved at an early stage of the design cycle
Achieved Significant Noise Reduction in Timing Exception Verification
  All the timing exceptions that do not require verification were identified upfront and excluded from the formal verification
Identified and Fixed all Incorrect MCP Exceptions before Timing Closure
  Prevented any potential silicon escape and costly re-spins
Improved the Overall Accuracy and Reliability of Timing Constraints leading to a Higher Quality Design

## Slide 12: Questions