## Slide 1: Revolutionizing Proof Convergence for Algorithmic Designs: Combining Multiple Formal Verification Tools
Suraj Kamble, Rajib Lochan Jana, Disha Puri

## Slide 2: Agenda
Floating point Arithmetic and Design Overview
Traditional Formal Verification and its Challenges
Introduction to Tool Agnostic Flow
Overall Proof Strategy
Interesting Corner case scenarios
Optimizing the next generation FV
Conclusion
Future Work

## Slide 3: Real life & FV
Image Courtesy:- https://kathakids.com/folktales/unity-is-strength
FV Eng
FV Tool 1
FV Tool 2
FV Tool n
FV Tool 3
FV problem
Let’s explore SPFMA/DPFMA design
Let's Start with the childhood story (nostalgic?)
Moral of the story
  Unity is strength
  Is it true for FV?

## Slide 4: Why FMA Design?
Integral part of any execution unit
Hard problem for Formal Verification
Can optimized uses of multiple tools help here to ease this problem?
Let’s explore 😊

## Slide 5: Floating point SP/DP Multiply Add: Case Study
MUL
(A.s ^ B.s) (A.e + B.e) (A.m * B.m)
ADD
(P.e != C.e |->
shift P.m)
A
B
C
A * B
OUT =A * B + C
A, B, C, OUT can be single precision (SP MAD) or Double precision (DP MAD)
Sign = A.s, B.s
Exponent = A.e,B.e,C.e,P.e
Mantissa (Fraction) =A.m,B.m,P.m
Image Courtesy:- https://en.wikipedia.org/wiki/IEEE_754-1985#Single_precision

## Slide 6: Design Overview
Preprocessing
(source modification function)
Data computation
(A’ * B’ + C’)
Postprocessing (saturation output )
A’
B’
C'
A
B
C
A”
B”
C”
Output
Align
Invert
Mul Block
Adder
Complement
LZA
Normalize
Rounding
sign, exp result
mant C’
mant A’
mant B’

## Slide 7: Datapath Formal Verification (SPFMA/DPFMA Design)
Untimed C/C++ Model
Pipelined RTL
Equivalent?
Input space is huge
Focus is on proving single transaction
Run E2E setup for ~48 hours

## Slide 8: Complexity Reduction: Standard case split on inputs
A | B | C
N | N | N
N | N | D
N | D | N
N | D | D
D | N | N
D | N | D
D | D | N
D | D | D
Inf/Nan | Inf/Nan | Inf/Nan
Single Precision |  | Double Precision |  | Number Represented
Exp [30:23] | Mantissa [22:0] | Exp [62:52] | Mantissa [51:0] | 
!= 0xFF | Any value | != 0x7FF | Any value | Normal Number
= 0 | != 0 | = 0 | !=0 | Denormal Number
= 0xFF | =0 | = 0x7FF | =0 | Infinity
= 0xFF | !=0 | = 0x7FF | !=0 | Not a Number(Nan)
N : Normal Number
D : Denormal Number
-∞ max- -1.0 min- ±0 min+ +1.0 max+ +∞
Denorms
Nan
Normal numbers
Zero
Infinity
Infinity
Normal numbers
Nan

## Slide 9: So far……
Created C2RTL setup
Standard case split on Inputs
Still facing convergence issue
Multiple tools available, can I use them
Aimed Single transaction
Proof ran for 48 hours
Pure Datapath Check
No more FV setup issues
Complexity reduction technique
Step-by-step Approach:
Impact of Deep Drive:
More Time & Resource investment
Need Design expertise
Chance to missing deadline
Un-convergence may lead to the escape of bug
Problem
SP-1
SP-2
SP-2.1
SP-2.n
SP-n
Level 0
Level 2
Level 1
Tool Agnostic
Flow

## Slide 10: Tool Agnostic Flow: Challenges & Approaches
Creating Multiple Verification Setups
  Design compilation, mapping and Checkers are in tool specific format
  Assume SVA of Design Constraints
Handling Design Constraints
  Coded Design Constraints as SVA (portable/reusable)
  Reduce setup time
  DV integration gives confidence on FV Setup
Creating Multiple Verification Setups
Handling Design Constraints
Approaches:
Compilation
Design Constraints
Checkers
Design Constraints
Compilation
Checkers
Assume SVA
Setup
SVA
Setup
FV SETUP
Compilation & Checkers -> 20%
Design Constraints -> 80%

## Slide 11: SPFMA/DPFMA: Level-1 Subproblems

## Slide 12: Overall Proof Strategy: SPFMA
A,B,C
Proved and Assumed Multiplier Block
NNN
NND
NDN
NDD
DNN
DND
DDN
DDD
Primary inputs
Standard Casesplit
Multiplier Assume Guarantee
out_cs0 out_cs1 out_cs2 out_cs3 out_cs4 out_cs5 out_cs6 out_cs7
OUT
Each Casesplit result
Final output
Standard case split
Assume guarantee
Tool Agnostic flow
 | Gen 1(C vs RTL) | 
 | SPFMA | DPFMA
E2E setup | Unconverged | Unconverged
Standard case split | Unconverged | Unconverged
Tool Agnostic flow | Proved (~15h) | Proved (~25h)

## Slide 13: Overall Proof Strategy: DPFMA
A,B,C
Proved and Assumed Multiplier Block
NNN
Primary inputs
Input constraint: spec limitation(POC)
Multiplier Assume Guarantee
Casesplit (level1)
0 1 ………...7…………12………….…….24………....31
Casesplit (level2)
Level 2 casesplit for unconverged cases
0 1 2……………………………….126 127
OUT
Final output
Standard case split
Assume guarantee
Tool Agnostic flow
 | Gen 1(C vs RTL) | 
 | SPFMA | DPFMA
E2E setup | Unconverged | Unconverged
Standard case split | Unconverged | Unconverged
Tool Agnostic flow | Proved (~15h) | Proved (~25h)

## Slide 14: Bug Revealed: SPFMA
Bug Scenario:
Denorm mode is off and intermediate value before round up is Max Denorm, then the RTL output is zero.
RTL flushes intermediate value (Max Denorm) to zero before round up.
A | 0x0B381E20
B | 0x2DF2067E
C | 0x808002B8
Expected output | 0x80800000
Impl output | 0x0
Scenario
Criticality:
Corner case bug; One in billion cases( possible values for Internal signal)
Some few input combinations from possible values
-∞ max- -1.0 min- ±0 min+ +1.0 max+ +∞
Denorms
Max- Denorm
0x807FFFFF
Min- Normal
0x80800000
Zero

## Slide 15: Bug Revealed: DPFMA
Bug Scenario:
Denorm mode is off and intermediate value before round up is Max Denorm, then the RTL output is mismatched with expected value.
RTL flushes intermediate value (Max Denorm) to zero before round up.
Not revealed even after running the setup for 50hrs.
A | 0xA3E59B1BB76CF3A6
B | 0x1F39C4CE02FEB9A5
C | 0x0331660EC998B4B7
Expected output | 0x8010000000000000
Impl output | 0x8000000000000000
Scenario
-∞ max- -1.0 min- ±0 min+ +1.0 max+ +∞
Denorms
Max- Denorm
0x800FFFFFFFFFFFFF
Min- Normal
0x8010000000000000
Zero
Criticality:
Corner case bug; One in billion cases( possible values)
Some few input combinations from possible values

## Slide 16: Optimizing the next generation FV
 | Next Gen (RTL vs RTL) | 
 | SPFMA | DPFMA
E2E setup | Unconverged | Proved (~5h)
Standard case split | Unconverged | NA
Tool Agnostic flow | Proved (~3h) | NA
Now 1st Gen RTL became Golden
Easy Setup bringing up
Easy debug
Less abstraction difference
Low effort high ROI

## Slide 17: Conclusion
FV is primary vehicle for Execution Unit instructions.
  Reported 10+ bugs including more than 2 corner cases
  Automated weekly regressions to catch early bugs without manual efforts
Tool agnostic approach is used to get complete convergence.
  100% convergence on unit much before deadlines
  Huge shift left achieved
Integration of Design constraints (SVA) with DV gives confidence on FV Setup.
  Simulation + SVA to prevent over-constraint env
Vendor collaboration to improve engines for complex blocks

## Slide 18: Future work
Compilation
Input Mapping
Output checkers
Spec
Design Constraints
(SVA creation Env)
E2E Setup
Tool Info
Setup Database
Updating setup with Convergence Techniques
Convergence Techniques
Setup with Convergence Technique
E2E Setup
Generation Env
Convergence Env
FV Tool Execution Env
Converge ?
Impl
End
Proof
In-House Tool for TAF
No
Yes
TAF Architecture

## Slide 19: Questions