## Slide 1: Quiescent Formal Checks (QFC) for Detecting Deep Design Bugs – Sooner and Faster
Somesh Mishra, Mayank Kumar, Ketan Mishra, Anshul Jain, Bharath Varma Gottumukkala

## Slide 2: Agenda
Introduction
Concept of Quiesce State in Software domain
Concept of Quiesce State in Formal domain
Problem statement
Proposed Solution
Use Cases
Our Implementation Experience
Conclusion

## Slide 3: Introduction
Quiesce State - A silent system state
Quiesce Command
  Force block all Incoming transactions
QUIESCE COMMAND

## Slide 4: Agenda
Introduction
Concept of Quiesce State in Software domain
Concept of Quiesce State in Formal domain
Problem statement
Proposed Solution
Use Cases
Our Implementation Experience
Conclusion

## Slide 5: Quiesce – Software Edition
Quiesce State in DBMS
  A state in which the database is set into a read-only mode
  All modifications to the data are halted
Applications of Quiesce State in DBMS
  Schema changes
  Database Replication
  Backup and Recovery
Notes: In Quiesce state, normal transactional activities and modifications are halted

## Slide 6: Quiesce – Software Edition
Quiesce State in Networking
  A state in which certain network functions are temporarily suspended
Applications of Quiesce State in Networking
  Network Redundancy
  Load Balancer Maintenance
  Virtualization and Migration
Notes: In Quiesce state, normal transactional activities and modifications are halted

## Slide 7: Agenda
Introduction
Concept of Quiesce State in Software domain
Concept of Quiesce State in Formal domain
Problem statement
Proposed Solution
Use Cases
Our Implementation Experience
Conclusion

## Slide 8: Quiesce – Formal Edition
What is Formal?
  A technique to ensure correctness of complex designs using mathematical proofs
How is Quiesce Command achieved in this context?
  A floating pulse is used to block incoming transactions
Quiesce command

## Slide 9: Quiesce – Formal Edition
What is our view of Quiesce State in Formal?
  There are no input transactions
  Outside dependencies are resolved
  The state formed will be Quiescent State.

## Slide 10: Agenda
Introduction
Concept of Quiesce State in Software domain
Concept of Quiesce State in Formal domain
Problem statement
Proposed Solution
Use Cases
Our Implementation Experience
Conclusion

## Slide 11: Problem Statement
Formal Complexity
  Formal tries to explore all possible states and transitions
  However, the same attribute introduces challenges – State Space Explosion
  As a result, Formal tools reach a point where they cannot continue to explore further states

## Slide 12: Problem Statement
Bug Activation-Detection Gap
  Sophisticated bugs often exhibit a “warm-up” period before causing issues
  Bugs with such “warm-up” period can be challenging to identify and are often missed due to high complexity

## Slide 13: Problem Statement
Undetected Bugs
  The combination of formal complexity and bug activation-detection gap can result in undetected bugs
  We often require additional techniques to tackle these challenges

## Slide 14: Agenda
Introduction
Concept of Quiesce State in Software domain
Concept of Quiesce State in Formal domain
Problem statement
Proposed Solution
Use Cases
Our Implementation Experience
Conclusion

## Slide 15: Proposed Solution – Quiesce Formal Checks
QFC Methodology

## Slide 16: Proposed Solution – Quiesce Formal Checks
Identifying Hotspots
  When applied to specific parts of a design can yield highly beneficial results
  Common Hotspots are
    FSM
    Counter
    Validator Signals
  Furthermore, Quiesce Formal Checks can be applied to signals that are expected to stabilize when design has entered a Quiesce state

## Slide 17: Agenda
Introduction
Concept of Quiesce State in Software domain
Concept of Quiesce State in Formal domain
Problem statement
Proposed Solution
Use Cases
Our Implementation Experience
Conclusion

## Slide 18: Use Cases
Resource Leakage
  Often occurs when there is an implementation error while capturing or releasing a resource
  In corner-case scenarios, these error can become more apparent
Adverse Effects of Resource Leakage
  Performance degradation
  Starvation
  Deadlocks

## Slide 19: Agenda
Introduction
Concept of Quiesce State in Software domain
Concept of Quiesce State in Formal domain
Problem statement
Proposed Solution
Use Cases
Our Implementation Experience
Conclusion

## Slide 20: Our Implementation Experience
Our module simple_qfc provides checkers for testing the behavior of a DUT at Quiesce state
The module supports several parameters
  MAX_PENDING_TXNS
  MAX_WAIT_TIME
  SIG_WIDTH
The module has three main inputs
  incoming_txn_valid
  outcoming_txn_valid
  sig_under_check

## Slide 21: Our Implementation Experience

## Slide 22: Our Implementation Experience
The two main assertions at Quiesce state would be
  check_quiesce_consistency
  check_quiesce_stability
Additionally, there is an assumption that ensures that no new incoming transactions are allowed after the quiesce command has been seen
  input_stop_at_quiesce_indication

## Slide 23: Conclusion
QFC is an innovative approach aiming to improve efficiency and effectiveness of Formal verification for complex designs.
QFC offers a promising bug-hunting strategy that can overcome some of the limitations faced by conventional FV techniques.
We encourage adoption of Quiesce check technique to unlock its full potential in optimizing design verification in various scenarios.
Further research and development in this area could lead to even more powerful and practical verification methods for large-scale industrial designs.

## Slide 24: Questions