## Slide 1: Pseudo-LRU Not Efficient in Real World? Use Formal Verification to Bridge the Gap
Paras Gupta, Sachin Kumawat,
and Kevin Bhensdadiya
Intel Corporation

## Slide 2: Agenda
Introduction
PLRU vs LRU
PLRU Overview
Tree-based PLRU Transition – Hit Read Case
Why FV for PLRU?
PLRU FV – Initial Approach
Challenges with Initial Approach
PLRU FV – Final Approach
Critical Bug Summary
Overall Results
Conclusion
Future Scope

## Slide 3: Introduction
In hardware systems, a set associative cache is a critical component utilized to store data that has been recently accessed, in N number of ways
In case of cache full and miss, we employ an eviction mechanism to make space for the recently accessed data. Below listed are two of those eviction mechanisms
  Least Recently Used (LRU) Mechanism
  Pseudo Least Recently Used (PLRU) Mechanism

## Slide 4: LRU vs PLRU
LRU
LRU mechanism which keeps track of the least recently used entry.
It is the most accurate cache replacement policy
Due to its precise nature, LRU requires additional hardware overhead to maintain the ordering of cache lines.
For N way cache, number of LRU bits required = ceiling(log2(N!))
E.g., for 8 ways, number of bits required = ceiling(log2(8!)) = 16
PLRU
As the name “pseudo” suggests PLRU does not keep track of exact age of cache lines, but an approximation measure of age
Due to its approximation nature, PLRU requires much less hardware overhead
For N way cache, number of PLRU bits required = N - 1
E.g., for 8 ways, number of bits required = 8 – 1 = 7
PLRU vs LRU is a trade off between resource efficiency and accuracy
In large complex modern hardware system, resource efficiency is becoming the bottleneck of design

## Slide 5: PLRU Overview
PLRU
Binary PLRU
Ternary PLRU
Tree-based PLRU
K-bit PLRU
d8
d7
d6
d5
d4
d3
d2
d1
0
0
0
0
0
0
0
L0
L1
L2
n0
n1
n2
n3
n4
n5
n6
XOR-based PLRU
Node = 0 –> Lower Half
Node = 1 –> Upper Half
MRU Way
PLRU Way

## Slide 6: Tree-based PLRU Transition – Hit Read Case
d8
d7
d6
d5
d4
d3
d2
d1
0
0
0
0
0
0
0
L0
L1
L2
n0
n1
n2
n3
n4
n5
n6
d8
d7
d6
d5
d4
d3
d2
d1
0
L0
L1
L2
n0
Cache read to d5
1
0
n1
n2
0
1
0
0
n3
n4
n5
n6

## Slide 7: Tree-based PLRU Transition – Hit Read Case
d8
d7
d6
d5
d4
d3
d2
d1
0
0
0
0
0
0
0
L0
L1
L2
n0
n1
n2
n3
n4
n5
n6
d8
d7
d6
d5
d4
d3
d2
d1
0
1
0
0
1
0
0
L0
L1
L2
n0
n1
n2
n3
n4
n5
n6
Cache hit to d5

## Slide 8: Why FV for PLRU?
Therefore, FV helps us to find all critical corner cases bugs and other low hanging bugs easily
PLRU is prone to corner cases bugs like not accessing some ways of cache set after a set of events as it is just an approximation not absolute like LRU.
FV is a technique to verify complex digital design using mathematical models. Its breadth first analysis is exhaustive enough to provide complete coverage of design functionality

## Slide 9: PLRU FV – Initial Approach
PLRU generic properties derived from LRU
When the cache is not full and a cache miss occurs, a write happens on an invalid way.
When the cache is full and a cache miss occurs, no write happens on the most recently used(MRU) way.
Generic properties for LRU
When a cache is not full and a cache miss occurs, then write should happen at one of the invalid entries
When a cache is full and a cache miss occurs, then write should happen on the oldest valid entry present
The PLRU mechanism is derived from the LRU mechanism, resulting in its test plan to be slightly a modified version of LRU test plan

## Slide 10: Challenges with Initial Approach
Initial test plan faced challenges due to counterexamples(CEX) generated by FV tool
Most of the CEXs became an exception for PLRU mechanism
For example,
  In case of a multi-hit scenario, Property #2 failed as the MRU way became the PLRU way in the subsequent cycle, leading to the victimization of the MRU way

## Slide 11
Challenges with Initial Approach(Cntd...)
Cache read for d4, d5, d6, d7 & d8
d8
d7
d6
d5
d4
d3
d2
d9
1
1
1
1
0
0
1
L0
L1
L2
n0
n1
n2
n3
n4
n5
n6
d8
d7
d6
d5
d4
d3
d2
d9
1
L0
L1
L2
n0
0
0
n1
n2
1
1
0
1
n3
n4
n5
n6

## Slide 12
Challenges with Initial Approach(Cntd...)
Cache read for d4, d5, d6, d7 & d8
d8
d7
d6
d5
d4
d3
d2
d9
1
1
1
1
0
0
1
L0
L1
L2
n0
n1
n2
n3
n4
n5
n6
d8
d7
d6
d5
d4
d3
d2
d9
1
L0
L1
L2
n0
0
0
n1
n2
1
1
0
1
n3
n4
n5
n6

## Slide 13: PLRU FV – Final Approach
Most of the CEX ended up being exceptions of PLRU, which prompted us to come up with a further relaxation of 2 generic PLRU properties.
For example,
  Property #2 of initial test plan is converted to 4 directed properties as shown below
When the cache is full and a cache miss occurs, no write happens on the most recently used(MRU) way
If cache miss follows another cache miss, then if first victim way is in first half of PLRU tree then next victim way should be from another half of PLRU tree provided there is no invalid ways
If cache hit followed by cache miss, then if hit way is in first half of PLRU tree then next victim cache line should be from another half of PLRU tree provided there is no cache hit or invalid ways
If all the cache hits are in first half of PLRU tree, then in the next cycle victim way should be from another half of PLRU tree
If both the half of a PLRU tree get hit, then in the next cycle victim way should be from same half of PLRU tree

## Slide 14: Critical Bug Summary
//Tracker parameters
parameter TRACK_ADDR = 23;
parameter TRACK_PAGE = 4K;
parameter TOTAL_WAY = 4;
//Glue logic to store MRU way
logic [1:0] fv_mru_way;
logic fv_mru_stored;
always@ (posedge clk) begin
if (rst | hit_en) begin
fv_mru_way <= '0;
fv_mru_stored <= '0;
end
else if (wen &
(wraddr==TRACK_ADDR)&
(page_type==TRACK_PAGE))
begin
fv_mru_way <= victim_way;
fv_mru_stored <= 1'b1;
end
end
//Property Implementation
PLRU_way_in_diff_half_whn_b2b_miss: assert property (​
@(posedge clk) disable iff(rst)​
(wen & (wraddr==TRACK_ADDR) & (page_type==TRACK_PAGE)&
full & fv_mru_stored & (fv_mru_way >= TOTAL_WAY/2)​)
|-> ​
(victim_way < TOTAL_WAY/2)​
);
Property: If cache miss follows another cache miss, then if first victim way is in first half of PLRU tree then next victim way should be from another half of PLRU tree provided there is no invalid ways

## Slide 15: Overall Results
Reported 15+ bugs in PLRU design
Achieved 100% functional coverage
Bugs found by FV were analyzed across the IP and some of them were found in multiple other flavors of PLRU
FV tool identified almost all bugs within 10 cycles using minimal CEX
Chart: 
| Exception | Critical Bug | Major Bug | Minor Bug
 | 3 | 3 | 7 | 4

## Slide 16: Conclusion
Employed both initial and final test-plan to verify PLRU through FV
Some of the identified bugs were particularly challenging, as they represented rare corner cases that could have had severe consequences on the resource utilization and overall performance of the System-on-Chip (SOC)
Significantly, the bugs discovered through formal verification were thoroughly analyzed across the entire IP, revealing that some of them were present in multiple variants of the PLRU design.

## Slide 17: Future Scope
Going forward, we plan to formally verify all the PLRU designs in the IPs using generic initial test plan or directed final test plan to avoid any corner case issues from creeping into Silicon. While we have only focused on PLRU algorithms, similar methodology can be employed to verify such algorithms and avoid any showstopper performance issues

## Slide 18: Questions
Finalize slide set with questions slide

## Slide 19: Backup Slide

## Slide 20: Final Test plan
Write cache in not full condition
When cache is not full then victim cache line should happen on one of the invalid cache lines
Write cache in full condition
Spurious check
If there is neither cache hit nor cache miss, then victim cache line should remain same
If cache hit followed by cache miss, then if hit way is in first half of PLRU tree then next victim cache line should be from another half of PLRU tree provided there is no cache hit or invalid ways
If all the cache hits are in first half of PLRU tree, then in the next cycle victim way should be from another half of PLRU tree
If both the half of a PLRU tree get hit, then in the next cycle victim way should be from same half of PLRU tree
If cache miss follows another cache miss, then if first victim way is in first half of PLRU tree then next victim way should be from another half of PLRU tree provided there is no invalid ways