## Slide 1: Efficient Verification of Arbitration Design with a Generic Model
Kevin Kotadiya, Ishita Agrawal
eInfochips An Arrow Company

## Slide 2: Agenda
Introduction
Arbitration Model Architecture
Approach to Integrate Arbitration Model
Coverage Model and Results
Summary

## Slide 3: Agenda
Introduction
Arbitration Model Architecture
Approach to Integrate Arbitration Model
Coverage Model and Results
Summary

## Slide 4: Introduction
Generic SystemVerilog-based Weighted Round Robin arbitration model
Challenges - Why this model?
  Multiple Arbitration – High redundancy
  High maintenance
  Complex functional coverage
  Above leads to human errors

## Slide 5: Agenda
Introduction
Arbitration Model Architecture
Approach to Integrate Arbitration Model
Coverage Model and Results
Summary

## Slide 6: Arbitration Model Architecture
Channel 0
Expected Packet
Arbitration Model
Channel 1
Channel *
Channel N
 |  |  |  | q0
 |  |  |  | q1
 |  |  |  | q*
 |  |  |  | qN
push_packet
> { ID, CI }
set_weight
> { ID, n }
Actual Packet
Checker
Coverage
Config
check_actual_packet
> { ID, CI }
Core Logic
get_expected_packet
{ ID } >
Two approaches for arbitration :
  Get immediate result
  Built-in result checking

## Slide 7: Features
N Number of Input Channels
Integrated APIs
set_weight : Setting weightage for each arbitration input channel
push_input : Feeding input to arbitration channel where input is encoded channel ID
check_actual_packet : Fetch actual arbitration result and compare it with expected
get_expected_packet : Get expected arbitration result, where output is encoded channel ID

## Slide 8: Features (Cont.)
A1
A2
B1
a1-ci0
a1-ci1
a2-ci1
b1-ci0
b1-ci1
a1-ci0
Input
Output
In-built Coverage Model
Channel Information
  Custom information passed with channel ID (string, enum, class, etc.)
a2-ci0
a2-ci1
b1-ci1

## Slide 9: Agenda
Introduction
Arbitration Model Architecture
Approach to Integrate Arbitration Model
Coverage Model and Results
Summary

## Slide 10: Approach to Integrate Arbitration Model
Design
Processing Output Signal and Comparison
Processing Input Signal
Active Agent
Passive Agent
Reference Model
Environment
Top
Arbitration
Model

## Slide 11: Approach to Integrate Arbitration Model (Cont.)
Block Reference Model
Ch 0
Ch 1
Expected Packet
Ch 2
Actual Packet
Arbitration Model
Logic 0
Logic 1
Logic 2
Channel 0
Channel 1
Channel 2
Logic 3
Actual Packet
Design
Single Level

## Slide 12: Approach to Integrate Arbitration Model (Cont.)
Block Reference Model
Ch 0
Ch 1
Output 0
Ch 2
Actual Pkt
Arbitration Model 1
Channel 0
Channel 1
Channel 2
Logic 8
Actual Packet
Design
Ch 0
Ch 1
Output 1
Ch 2
Actual Pkt
Arbitration Model 2
Channel 3
Channel 4
Channel 5
Ch 0
Ch 1
Output 2
Actual Pkt
Arbitration Model 3
Logic 6
Logic 7
Checking
Ch 2
Logic 9
Logic 0
Logic 1
Logic 2
Logic 3
Logic 4
Logic 5
Multi Level

## Slide 13: Integration Steps
Instantiate and construct
Feed input packets
Feed actual packet to compare with expected packet
  Configure weightage
13

## Slide 14: Agenda
Introduction
Arbitration Model Architecture
Approach to Integrate Arbitration Model
Coverage Model and Results
Summary

## Slide 15: Coverage Model
Sr. No. | Name | Bin | Description
1 | <name>_arb_cg | - | Arbitration Cover group.
1.01 | arb_input_cp | auto[1] | Cover point for sampling all possible input combinations. N = number of input channels Ignore Bin = auto[0]
 |  | auto[2] | 
 |  | ... | 
 |  | auto[2^N -1] | 
1.02 | arb_cycle_start_cp | auto[CH 0] | Cover point for sampling channel from where one arbitration cycle started.
 |  | auto[CH 1] | 
 |  | … | 
 |  | auto[CH (N -1)] | 
1.03 | arb_output_transition_cp | CH 0 => CH 1 | Cover point for sampling all possible output transitions.
 |  | CH 0 => CH 2 | 
 |  | … | 
 |  | CH (N -2) => CH (N -1) | 
1.04 | arb_output_transition_reason_cp | NO_INPUT | Cover point for sampling all output transitions reason.
 |  | NO_WEIGHT | 
 |  | NO_INPUT_NO_WEIGHT | 
1.05 | arb_output_transition_cp_X_arb_output_transition_reason_cp | - | Cross of output transition with its transition reason.

## Slide 16: Results

## Slide 17: Agenda
Introduction
Arbitration Model Architecture
Approach to Integrate Arbitration Model
Coverage Model and Results
Summary

## Slide 18: Summary
Used in a complex SoC project
  Multi-Level arbitration
Reduce coding effort (~91%)
  1 arbiter - ~400 code lines
  12 arbiters - ~4800 code lines
Reduce code errors and simplifies maintenance
Reusable, organized and adaptable
Includes built-in coverage
Quicker and efficient reference model development

## Slide 19: Questions