## Slide 1: Advanced RISC-V Verification Technique Learnings for SoC Validation
Using Breker SystemVIP for RISC-V System Ready
David Kelf, CEO, Breker Verification Systems
Nambi Ju, Principle Engineer, Breker Verification Systems

## Slide 2: Agenda
Test Suite Synthesis and SystemVIP
RISC-V Core Verification SystemVIP
RISC-V SoC Verification SystemVIP

## Slide 3: Agenda
Test Suite Synthesis and SystemVIP
RISC-V Core Verification SystemVIP
RISC-V SoC Verification SystemVIP

## Slide 4: The High Cost of Developing Test Content
Testbench
Block UVM
Lack of abstraction & reuse
SOC Integration
Ad hoc verification methods
System Validation
Low coverage real workloads
Chart: 
| Design | Verification: Other | Verification: Debug | Verification: Test Dev.
Sales | 30 | 13 | 25 | 32
Design:
32%
Verification:
Other 13%
Verification:
Content Development
30%
Project Resource Deployment
Verification:
Debug
25%
DUT
Can we re-use the same knowledge ?
Complex tests hard to get right
Why? Resource Intensive Test Content
Test development drives debug
Source: Wilson Research 2020
Can we abstract verification intent ?
Largest Functional Verification Challenge

## Slide 5: Test Suite Synthesis… Analogous to Logic Synthesis
Describe intent
Generate implementation
Map to platform
Specify goals
Constrain
Synthesize
Optimize
Timing/Area
Constraints
Design Synthesis
3D Coverage
Closure
AI Planning
Algorithms
Synthesizable VerificationOS
Breker Core Technology
AI Planning Algorithms
Constrain
Synthesize
Optimize
Coverage
Constraints
Test Suite Synthesis
Scenario Model
Specification
Model
SD
Sys
DC
PP
Cam
UVM
SoC
Silicon
DUT
Stimulus
Checks
Coverage/Debug

## Slide 6: Breker SystemVIP Library
SoC SystemVIP Library
The RISC-V Core TrekApp provides fast, pre-packaged tests for RISC-V Core and SoC integrity issues
The Coherency TrekApp verifies cache and system-level coherency in a multiprocessor SoC
The End-to-end IP TrekApp IP test sets ported from UVM to SoC
The Power Management TrekApp automates power domain switching verification
The Security TrekApp automates testing of hardware access rules for HRoT fabrics
The Networking & Interface TrekApp automates packet generation, CXL, UCIe interface tests

## Slide 7: Constrained Random vs AI Planning Algorithm Synthesis
Constrained Random Generation
UVM SV & other PSS tools
AI Planning Algorithm
Breker Test Suite Synthesis
time / cycles
states
time / cycles
states
White Paper Discussing AI Planning Algorithm Test Generation on Breker Website
Design black box, shotgun tests to search for key state
Low probability of finding complex bug
Black
Box
White
Box
Starts with key state and intelligently works backward through space
Deep sequential, optimized test discovers complex corner-cases
legal state
illegal state
target state

## Slide 8: A Look At RISC-V
Open Instruction Set Architecture (ISA) creating a discontinuity in the market
Appears to be gaining significant traction in multiple applications
Significant verification challenges
  Arm spends $150M per year on 1015 verification cycles per core
  Hard for RISC-V development group to achieve this same quality
  Lots of applications expands verification requirements
  Requires automation, reuse and other new thinking

## Slide 9: RISC-V Verification & Validation Tasks
CPU Cores
Testbench
VIP
VIP
IP DUT
Testbench
VIP
VIP
IP DUT
Uncore IPs
Firmware
First Instruction Completion
ISA compliance
Micro-architecture functionality
Interrupts/Paging/Memory Order
Core Integrity
Complexity
IP Configuration
Concurrency Testing
End-to-End Use Cases
IP Integrity
Complexity
Interrupts/Paging/Memory Order
Cache Coherency
Security
Power Management
Power/Performance Profiling
SoC Integrity
Complexity
HW/Firmware Compatibility
Concurrency Testing
End-to-End Use Cases
Firmware Integrity
Complexity

## Slide 10: Breker RISC-V SystemVIP Portfolio
CPU Cores
Testbench
VIP
VIP
IP DUT
Testbench
VIP
VIP
IP DUT
Uncore IPs
Firmware
SVIPs for Core Integrity
Register Hazards
Load/Store
Core Cache Coherency
Core Interrupts
…
SVIPs for IP Integrity
Mem2Mem (dma)
IO Offload (PCIE/Eth)
WQ Servicing
…
SVIPs for SoC Integrity
SoC Cache Coherency
Memory Ordering
Power Management
System Interrupts
…
SVIPs for Firmware Integrity
Mem2Mem (dma)
IO Offload (PCIE/Eth)
WQ Servicing
…

## Slide 11: Single Source of Truth for all stages of Verification & Validation
SoC
Memory
DMAC
AES
Fabric
Fabric
UART1
VIP
System
and
Power
Control
UART0
VIP
CPU
CPU
UVM Testbench
Hybrid Emulation Environment
SoC
Memory
DMAC
AES
Fabric
Fabric
UART1
VIP
System
and
Power
Control
UART0
VIP
CPU
CPU
UVM Testbench
Virtual Platform Environment
UVM Block Environment
UART1
VIP
AES
Silicon / Prototyping Environment
Test Suite Synthesis
UVM Testbench
SoC
RTL
Memory
DMAC
AES
Fabric
Fabric
UART1
VIP
System
and
Power
Control
UART0
VIP
VIP
VIP
Simulation Acceleration
Performance Profiling
Coverage Analysis
High Level Debug
SVIPs for Core Integrity
Register Hazards
Load/Store
Core Cache Coherency
Core Interrupts
…
SVIPs for IP Integrity
Mem2Mem (dma)
IO Offload (PCIE/Eth)
WQ Servicing
…
SVIPs for SoC Integrity
SoC Cache Coherency
Memory Ordering
Power Management
System Interrupts
…
SVIPs for FW Integrity
Mem2Mem (dma)
IO Offload (PCIE/Eth)
WQ Servicing
…

## Slide 12: Different Challenges for Core vs SoC Verification
Random Instructions | Do instructions yield correct results
Register/Register Hazards | Pipeline perturbations dues to register conflicts
Load/Store Integrity | Memory conflict patterns
Conditionals and Branches | Pipeline perturbations from synchronous PC change
Exceptions | Jumping to and returning from ISR
Asynchronous Interrupts | Pipeline perturbations from asynchronous PC change
Privilege Level Switching | Context switching
Core Security | Register and Memory protection by privilege level
Core Paging/MMU | Memory virtualization and TLB operation
Sleep/Wakeup | State retention across WFI
Voltage/Freq Scaling | Operation at different clock ratios
Core Coherency | Caches, evictions and snoops
System Coherency | Cover all cache transitions, evictions, snoops
System Paging/IOMMU | System memory virtualization
System Security | Register and Memory protection across system
Power Management | System wide sleep/wakeup and voltage/freq scaling
Packet Generation | Generating networking packets for I/O testing
Interface Testing | Analyzing coherent interfaces including CXL & UCIe
Random Memory Tests | Test Cores/Fabrics/Memory controllers across DDR, OCRAM, FLASH etc
Random Register Tests | Read/write test to all uncore registers
System Interrupts | Randomized interrupts through CLINT
Multi-core Execution | Concurrent operations on fabric and memory
Memory Ordering | For weakly order memory protocols
Atomic Operation | Across all memory types
RISC-V Core Verification Challenges
RISC-V SoC Verification Challenges

## Slide 13: Agenda
Test Suite Synthesis and SystemVIP
RISC-V Core Verification SystemVIP
RISC-V SoC Verification SystemVIP

## Slide 14: RISC-V Core Testbench Integration
L1
CPU
Memory Model
Compiler
test.c
test.c
test.c
TrekBox
test.c
test.c
test.tbx
Snoop
VIP
Interrupt
VIP
Scenario Model
Virtualized OS Services

## Slide 15: RV64 Core Instruction Generation
Random register instructions

## Slide 16: Instruction Coverage Analysis
27/103 reachable opcode have been exercised
Atomics, loads and stores not reachable in register only test

## Slide 17: RV64 Core Load/Store
Locality of write addrs

## Slide 18: Example Address Allocation Patterns
Random Clusters with locality of reference
Stride Patterns across fixed address distances
Sequential Addresses matching a specific Hash

## Slide 19: Application to Unit Bench and Sub-System Bench
NOC/Cache Unit Testbench
NOC/L2
VIP
VIP
VIP
VIP
VIP
NOC/Coherency Sub-Subsystem
Testbench

## Slide 20: RV64 Core Exception Testing
Generates for example,
asm("UNIMP");
Check exception counts

## Slide 21: Page Based Virtual Memory Tests

## Slide 22: RV64 Core Page Based MMU Tests
Swap MMU PTE’s and
Check memory access

## Slide 23: Agenda
Test Suite Synthesis and SystemVIP
RISC-V Core Verification SystemVIP
RISC-V SoC Verification SystemVIP

## Slide 24: RISC-V SoC Testbench Integration
Cache-Coherent Switching Fabric
CPU
CPU
CPU
CPU
L1
L1
L1
L1
L2
CPU
CPU
CPU
CPU
L1
L1
L1
L1
L2
…
L3 Cache / Snoop Filter
Memory Controller
Memory Controller
Offload
Compiler
test.c
test.c
test.c
TrekBox
test.c
test.c
test.tbx
PCIE
Ethernet
PCIE
VIP
Ethernet
VIP
Scenario Model
Virtualized OS Services

## Slide 25: Multi-Agent Scheduling Plans: Overview
N Transition Scenarios
Concurrent Scenario Test Case
N Transition Sequences
Schedule Memory
Interleave & Pack
Resolve Dependencies
True Sharing within scenario
False Sharing across scenarios

## Slide 26: RV64 MultiCore MoesiStates
Planned Cache State
Transitions

## Slide 27: Efficacy of System-Integrity Testing using the RISC-V TrekApp
Typical directed coherency test …
… vs. RISC-V TrekApp
automated Sys-Integrity tests

## Slide 28: Atomics Testing
Check result is aggregate of synchronized atomic operations

## Slide 29: RISC-V SoC Memory Ordering: Dekker Algorithm
Assume initial state A=0 , B=0
The Dekker Algorithm States
  core 0: ST A, 1; MEM_BARRIER; LD B
  core 1: ST B, 1; MEM_BARRIER; LD A
  error iff ( A == 0 && B == 0 )
This is a test for a weakly ordered memory system
  Such a system must preserve the property that a LD may not reorder ahead of a previous ST from the same agent

## Slide 30: Dekker Memory Ordering
Check ordering across synchronized Dekker scenarios

## Slide 31: MultiCore MMU Tests
All cores Swap MMU PTE’s and check memory access

## Slide 32: False-Share Memory Stress Tests
Byte 0
Byte 1
Byte 2
Byte 3
Byte 4
Byte 5
Allocate set of memory blocks
Random cores with synchronized start
Each core operates on a “slice” of memory
Each core has free running loop

## Slide 33: Thanks for Listening! Any Questions?