## Slide 1: Tackling the verification complexities of a processor subsystem using Portable Stimulus
Vivek Gopalkrishna
Ponnambalam Lakshmanan
Nitish Swamy

## Slide 2: Agenda
Introduction and need for PSS
PSS based verification process
Prerequisites for deploying PSS framework
PSS implementation in ADI project
PSS for SPI in all target platforms
  Defining scenario space
  Verify compatibility with the existing verification setup
  Modeling plan
  PSS integrated verification setup: Simulation, emulation, VP and FPGA
Results

## Slide 3: DV Challenges
Verification Productivity
Creating all possible scenarios to test design
DV
Challenges
Achieving 100% Coverage
Duplication of test content across platforms
Under pressure to do more, faster
Reuse across Projects and platforms

## Slide 4: PSS: The Latest Verification Trend
Portable Stimulus Standard (PSS) is a new standard from Accellera
Allows stimulus reuse across multiple platforms
  Vertical reuse
  Horizontal reuse
Works at higher layer of abstraction, reusing the verification environments
Enhanced test quality with simplified test authoring
Allows better coordination, resource sharing and increased productivity
DSL (Domain specific Language) is used for Modelling

## Slide 5: PSS Based Test Development Process
Architect
System
Design/DV
Apps
Eval
Test
Software
TLM Model, VP
SystemC
Simulation
SV, UVM
C/C++
Evaluation,
Customer
Boards
C/C++
Tester
Different patterns
Emulation,
FPGA/VP
Silicon
C/C++
IP
Design/DV
PSS Framework
Defines Use Cases, PSS Models
Device
Drivers
DUT,
PSS Models
Scenarios
Scenarios
IP DUT,
PSS Models

## Slide 6: Horizontal and Vertical Reuse
IP
Sub system
SOC
(HW+SW)
VP
Simulation
Emulation
FPGA
Silicon
Integration
levels
Execution
platform
UVM
Embedded/ Host C test
PSS
Verification intent captured at higher abstraction
Portability wall
Notes: Shift left portability

## Slide 7: PSS Terminologies
Represent the design elements that make up the hierarchy
Eg: spi, i2c, uart
Elements which capture test behaviors in a PSS model
Eg:spi_config, uart_tx
A set of action instances, flow objects and scheduling constraints which makes up testcases
Represents incoming or outgoing data/control flow for actions
Eg: buffer, state, stream
Hardware design resources that are needed to perform the test functionalities
Eg: dma channels, processor cores
Component
Action
Flow Objects
Resources
Activity (Scenario)

## Slide 8: PSS usage flow
Spec driven PSS models
(resources, components, actions, data structures, covergroups)
Tool libraries
(memory and processor tables)
config.csv
Abstract Use-case creation
(scenarios, native operators)
test_table.csv
Solving and Test generation
(C, SV, C+SV)
Solved scenario diagram
Run on multiple platforms
Coverage analysis & debug
target
platform
integration
SV test
C test
C test
C test
Simulation
Virtual Platform
Emulation
FPGA/Si
native operators
Coverage viewer
Test generation coverage
Runtime simulation coverage
Merged coverage
memory and processor info table
design topology config table
Spec doc
Model writer
Test writer
Notes: SML: System methodology library
UML: Unified modeling language

## Slide 9: Prerequisites for deploying PSS framework
Understand the need for PSS
Define scenario space
Verify compatibility with existing verification setup
Detailed Modeling Architecture and development plan
PSS-integrated verification setup plan
Get the buy-in from all stake holders
Qualify the subsystems/IPs in the design for PSS
Capture all the modes of operation with config variables and their legal range of values
Identify the C/SV APIs
PSS modeling details with components, data flow objects and actions planned
Functional coverage plan
Design/DV/Eval/SW/Emulation/Post-Si to develop unified flow

## Slide 10: PSS Adoption and Results

## Slide 11: Processor subsystem
SPI
UART
DMA
QSPI
I2C
PINMUX
GPIO
GPT
WDT
RTC
Security module
MAILBOX
Core

## Slide 12: Need for PSS in this Project
Test content reuse across Platforms
  Virtual Prototyping Platform, DV simulation, emulation, FPGA
Generate complex test scenarios, for different configurations of the subsystem
Unified randomization
  Offload the randomization to PSS engine to be able to generate a flattened directed testcase.

## Slide 13: SPI with PSS: Defining Scenario space
SPI can be configured for the following scenarios of operation
State: initiator or target
Mode of operation: half duplex, full duplex
Tx/Rx DMA: enabled or disabled
Continuous chip select: enabled or disabled
Various interrupt controlling fields
Tx/Rx transaction count

## Slide 14: SPI with PSS: Existing verification setup
A reference test was chosen for initial bringup:
main.c
UVM Test
init
seq
test_cfg. randomize()
dut config
Tx
Test end
wait4tb
sync2tb
SPI DUT
(Initiator)
SPI VIP
(Target)
hdtx
SPI VIP
Score board

## Slide 15: Modeling plan
How PSS can capture the verification requirements
Identify the modeling elements
  data structures, components, resources, actions, scenarios
Identify the data flow objects
  buffers, streams, states
Plan for integration with target platforms
  exec block implementations, constraints
  VIP modeling
  executor threads, mailbox synchronization
Capturing the design architecture in csv file
  Cores, IP instances, Memory mapping
Architectural diagram

## Slide 16: Modeling plan - SPI
pss_top
Modeling elements and data flow objects
spi_c
spi_config_a
config
state
sml_write_data
sml_buf
spi_tx_a
spi_vip_c
spi_vip_config_a
spi_rx_a
data stream
actions
state
buffer
stream
component
Flow objects

## Slide 17: Modeling plan - SPI
pss_top
Model + Integration with target platforms
spi_c
Actions + data flow elements
spi_vip_c
Actions + data flow elements
Mailbox
(SRAM1: 0x2004000)
Config.csv
cores = 1, vip executor = 1,
spi_inst = 1, dma_inst =1,
memory map
Stub codes for target platforms
Executables, schemes
Challenge faced
Generating tests with both C and SV target languages for core and agent threads.
Solution
Dual executable setup with automated mailbox syncs

## Slide 18: Separation of test intent with implementation
Test intent captured in SpiTx_a action
Test implementation specified in exec body

## Slide 19: PSS Test generation flow
Generated tests
PSS SPI Model
generated_test.c
(Generated core test)
pss_spi_modeling.pss
pss_spi_al.c
(Wrapper file)
pss_spi_sv_bindings.pss
generated_test_sv.c
(Generated vip test)
pss_bindings.sv
pss_spi_modeling.pss
Solver

## Slide 20: PSS integrated SPI test
PSS generated SV thread
cortex sync
init seq
mailbox sync
vip config
cortex sync
test end
mailbox sync
Template SV UVM test
SV tasks
vip config()
testcfg
C functions
wait4tb
dut config
mailbox sync
sml write
spi tx
sync2tb
F2.0 reg write()
F2.0 Tx()
wrapper write()
wrapper Tx()
PSS Generated C thread
PSS Generated
Exec implementation
syncs
Functions
mailbox sync
vip config
mailbox sync
vip config()
test_cfg
mailbox sync

## Slide 21: PSS on Emulation
Simulator
Emulator
dut config
mailbox sync
sml write
spi tx
dut config
sml write
Interface
mailbox write
mailbox read
vip config
mailbox sync
vip config()
mailbox sync
interface task calls
Virtual UART
Supports sending/receiving data from terminal for FW validation.
Supports all the standard and non-standard baudrates.
Challenges faced
Memory accesses for mailbox communication
Tb-syncs for polling operations
Solution
Interface tasks for mailbox write and read with tb_import and tb_export.
Polling logic ported to emulator with an added export_event to the TB.

## Slide 22: PSS on Virtual Prototyping platform
Spec driven PSS models
(resources, components, actions, data structures, covergroups)
Abstract Use-case creation
(scenarios, native operators)
Solving and Test generation
(C)
Linux
Windows
RUN
design.exe: System C model
Compile
(IAR Workbench)
generated tests
Virtual UART
Supports sending/receiving data from terminal for FW validation.
Supports all the standard and non-standard baudrates.
Tool challenge faced
License checkout failure due to VP being run on C compilers on Windows.
Solution
Hooks provided to resolve the licensing issue.
Seamlessly ported to VP

## Slide 23: PSS on Custom FPGA
Spec driven PSS models
(resources, components, actions, data structures, covergroups)
Abstract Use-case creation
(scenarios, native operators)
Solving and Test generation
(C)
DUT FPGA
generated tests
Test agent FPGA
generated tests
JTAG
JTAG
Virtual UART
Supports sending/receiving data from terminal for FW validation.
Supports all the standard and non-standard baudrates.
Challenges faced
System configuration based on C# project. Reg read write APIs in C#
Solution
Ported the setup to C. PSS generates individual tests for DUT to be run by core and for test agent FPGA

## Slide 24: Results
Portability of test-intent across all execution platforms achieved.
  PSS has helped us shorten the design verification cycle, with an estimated reduction of 50% of time spent in test generation for Emulation, VP, FPGA and Firmware
Randomization of attributes is offloaded to the PSS engine, thereby reducing the effort and time on the run time simulator.
Recreation of bugs caught across platforms made easy.
Next Steps
Enabling test generation coverage extensively to generate meaningful tests.

## Slide 25: Acknowledgements
Nitish Jindal, Rajiv Nadig, Paul Drum, Jatin Nagpal, Sonal Patil, Akshata Kulkarni, Shriyanshi Kapoor, Kyle Jansen and Kajal Majalatti from ADI for the continuous effort in modeling and bring-up.
Gnaneshwara Tatuskar, Sandeep Katti and Ranjith S for their consistent guidance and tool support.

## Slide 26: Questions
© Accellera Systems Initiative