## Slide 1: HISIG- An Efficient Gate Level Simulation Flow for a Hard IP Inside a Soft IP
Ishwar Ganiger, Vishal Dalal
Infineon Technologies, Bangalore
Johannes Grinschgl
Infineon Technologies, Munich

## Slide 2: Contents
Introduction
Hybrid IP Gate Level Simulation (GLS) Problem
Hard IP inside Soft IP GLS (HISIG) Flow
HISIG Automation and Testbench (TB) Setup
Results
Advantages and Limitations
Conclusion

## Slide 3: Introduction
GLS - important component of SoC design cycle
Can identify issues missed by RTL simulations, STA, and LEC
Natural choice at SoC level
Synthesis, timing closure done at SoC level
What is Hard IP?
Synthesis and timing closure done at IP level
GLS needs to be done at IP level
What is Hybrid IP?
Specific IP sub-block timing closed at IP level
How to do Hard IP sub-block GLS inside Hybrid IP?
Hardened IP used as it is in SoC netlist
Rest of the IP remain as RTL only

## Slide 4: Hybrid IP GLS Problem
Hard IP
Hybrid IP
Complete IP is timing closed
RTL TB can be reused for GLS
Only specific sub-block hardened
Timing issues at crossover
RTL TB can NOT be reused

*VIP - Verification IP, SB - Scoreboard

## Slide 5: Hybrid IP GLS Problem….
*MM – Man Months
Timing issues in flops of hardened sub-block
Behavioural model of hard IP sub-block with timing information was not available
Can not reuse existing RTL IP verification TB
How to create stimulus for hardened sub-block GLS?
High efforts to create standalone TB for hard IP sub-block  5 MM
Different approach needed to solve these problems
Only hardened part is timing annotated  Rest is still RTL

## Slide 6: HISIG Flow
Generate standalone TB
Replay stimulus from RTL tests
Perform timing & functional checks
HISIG - Hard IP inside Soft IP GLS
Run additional tests for timing critical paths & desired coverage - Single Data Rate (SDR) & Double Data Rate (DDR)

## Slide 7: HISIG Automation & TB setup
Standalone TB for Hard IP sub-block
Reads VCD from RTL simulation of full IP
Drive inactive values to Power control & test mode pins

## Slide 8: Converting VCD Toggles to SV TB
Functional input pins captured as SV nets along with all toggle information
SV – System Verilog

## Slide 9: GLS & RTL Output Comparison
Assertions to compare all outputs b/w GLS and RTL toggles
rtl_out_x – RTL output
gls_out_x – GLS output

## Slide 10: HISIG Pseudo-Code

## Slide 11: Results
HISIG flow applied to an IP that uses SPI for IO communications
  Hardened sub-block had 162 input, 68 output and 21 inout ports
IP gate count | ~50K
# Testcases | 7
Timing corners checked | MIN, MAX
Average Test run time | ~15 minutes
GLS setup time | 0.5 MM
Efforts saving | ~90%
Reusability across designs | YES

## Slide 12: Advantages
HISIG
Less effort to create GLS setup
Simple and easy to use
Improved Verification quality
Timing checks done at IP level
Portable across designs

## Slide 13: Limitations
HISIG
Timing checks b/w soft IP’s last and hard IP’s first bit flops are not fully proven
Hard block IO toggle info is from RTL sims
Not driven by actual netlist
GLS snapshot to be regenerated for each Test
Data integrity checks done using assertions
Not done with VIP’s and SB

## Slide 14: Conclusion
HISIG is Simple, effective and reusable across designs
Optimizes IP GLS DV cycle by ~90%
HISIG applied on a live design already taped-out
  Achieved desired timing and functional coverage
  No IP timing issues found in SoC GLS
Completes timing checks early in the design cycle
Improved overall IP quality

## Slide 15: References
[1] Gagandeep Singh “Addressing Renewed Gate Level Simulation Needs for 10nm-28nm and Below”, DVCON Europe, 2016
[2] Ateet Mishra, Deepak Mahajan and Shiva Belwal “Absolute GLS Verification- An Early Simulation of Design Timing Constraints”, DVCON India, 2015
[3] Ashok Chandran, Roy Vincent “Gate level Simulations: Continuing Value in Functional Simulation”, DVCON India, 2014
[4] Vishal Dalal, “Relevance of Gate Level Simulations in Today's SoC Verification” short tutorial at 13th VLSI Design and Test Symposium, VDAT India, 2009
[5] Synopsys PowerReplay flow, https://www.synopsys.com/verification/simulation/powerreplay.html

## Slide 16
Thank you!
Questions?