## Slide 1: Formal Verification + CIA Triad: Winning Formula for Hardware Security
Vedprakash Mishra, Anshul Jain
Intel Corporation

## Slide 2: Contents
Big Fuzz ?
Or
Genuine Concern ?
H/W Security
Role of FV
Confidentiality
Integrity
Availability
CIA Triad
FV Approach
Design Details
Security Bugs
Insights
Case Study
Results
FV for Security
Conclusions

## Slide 3: Hardware Security
In SOCs, several agents compute cores, accelerators and IO devices interact to process workloads
All agents may not be equally trustworthy
What does Security mean for Hardware?
Goal of Hardware Security?
Protect sensitive assets from hackers
Prevent security attacks from causing performance and functional breakdown
Hardware security attacks exploit vulnerabilities and steal assets
Assets such as control and status registers (CSRs), encryption/decryption keys, regions in memory, etc.
Critical aspect of overall cybersecurity
Even the most robust software protections can be compromised if the underlying hardware is vulnerable

## Slide 4: Role of FV in Hardware Security
Valid Invalid
Input Input
All possible system states
Valid Invalid
Input Input
All possible system states
A rigorous mathematical technique for proving design correctness through exhaustive exploration of all input combinations and system states
Powerful technique for exposing security flaws/vulnerabilities of designs “well in-time (pre-silicon)”
Verifies that a design works as per specification and satisfies a set of security properties, such as confidentiality, integrity, and availability
If your IP handles secure information of the SOC chassis, then this talk will
Help in Security Verification Planning through Formal Verification
Create awareness about potential attack scenarios and their implications
Prepare to take risk mitigation steps and achieve shift-left

## Slide 5: Role of FV in Hardware Security (Contd.)
RELAX CONSTRAINT
ENHANCE MODELLING
Crucial for exploring a wide range of input scenarios (compliant and non-compliant) to detect potential security weaknesses
Upgrade abstractions, reference models, incorporate threat modeling, define security properties and assertions for effective security verification
Benefits: Enhances design resilience against unknown vulnerability attacks, aids in early vulnerability detection, and provides a more robust security verification process

## Slide 6: CIA Triad
Confidentiality ensures the data is only accessible to authorized parties
Availability ensures the system is operational and accessible when needed
Integrity ensures that data is not tampered with or modified during transportation
Confidentiality
Availability
Integrity
Verifying the design satisfies CIA, we ensure the hardware is secure

## Slide 7: Confidentiality: Secure Access of Assets
Memory Fabric
IO Fabric
Processor
Cache
Accelerator
Memory
Device
Memory
Device
Memory
DRAM
SRAM
secret
What happens if the initiator attributes are modified in the transit?
A fake or spoofed attribute may end up granting an untrusted initiator access to an asset while it should have been denied
Critical headers
/bits corrupted
Un-synced
micro-architectures
Critical input exposed
Insecure source or destination IDs
Unsecure Access
Identification and role attributes for initiators and responders play a vital role in hardware systems.
They uniquely identify entities, define their roles, and enable secure access, authentication, authorization, and accountability
By incorporating these attributes, hardware systems ensure authorized interactions, prevent unauthorized access, and maintain confidentiality

## Slide 8: Confidentiality: FV Approach
Similarly, properties like “if a particular transaction is filtered (based on the attributes) then it cannot be seen on the output interface” should also be written
FPV
Enables the verification of properties related to attribute constraints, which play a crucial role in preserving confidentiality
Ensures that transactions having incorrect attributes (E.g., Src/Dest IDs) i.e., not belonging to allowed hardware allowed Port IDs should not be propagated.

## Slide 9: Integrity: Accurate and Consistent Service
Integrity is a critical aspect of security, ensuring data and systems' accuracy, consistency, and trustworthiness
Breaching integrity involves unauthorized changes to the completion response of a legal transaction, leading to severe consequences for system reliability and data integrity
Manipulating the completion response can compromise the service provided, falsely indicating success or failure, leading to incorrect actions, compromised data processing, and potential security breaches
The consequences of such manipulation can range from financial losses, operational disruptions, compromised data integrity, to potential security breaches, depending on the context and system involved

## Slide 10: Integrity: FV Approach
To ensure the integrity of a system, it is essential to deploy both functional correctness properties and data correctness measure
Functionality correctness checker:
If the transaction is legal as per decoded attributes and read/write of config register is allowed/read, then only a successful completion should be sent, otherwise unsuccessful completion
Data correctness checker:
If config register was read, then completion data sent should match the read data

## Slide 11: Availability: Hang free system (No DoS)
Pipeline hang or stuck stages can impact security availability, potentially leading to a denial of service (DoS) attack
IP was able to detect that the transaction is corrupt. Should IP discard that transaction or raise an error?
(E.g., Number of flits sent by intruder is incorrect, FSM is stuck waiting for correct number of flits)
Corrupted transaction was a non-posted transaction; shouldn’t an unsuccessful completion is required ?
(Non-posted transaction requires completion response, otherwise entire architecture will hang)
Let’s say IP sent an unsuccessful completion, but instead of sending one completion response sent two.
(One request-one response)
01
02
03

## Slide 12: Availability: FV Approach
Safety and Correctness : If an illegal transaction is received then unsuccessful completion corresponding to this transaction should be sent out within finite number of cycles
Spuriousness: Number of completion responses sent should never be more than number of non-posted request received
FV can also be used to detect potential pipeline hangs and ensure the correctness of the
pipeline design

## Slide 13: Case Study : Design Details
IP is responsible for integrating different subsystem IPs in a System-on-Chip (SOC) and providing a unified modular interface
It manages interactions with subsystem IPs for power and reset management purposes, directing transactions to the corresponding power manager or reset handler
IP also routes transactions related to config registers and static registers to the appropriate modules for configuration and control of settings within the subsystem IPs

## Slide 14: Case Study: Bug Example
01
02
03
Correct Decoding
Zero
Credits
Incorrect
Response
Non-posted request received first, had successful access of CSR. Corrupted post was correctly decoded, and an error was flagged
Completion response corresponding to the non-posted request was not asserted due to the unavailability of credits
Successful field got de-asserted because of the posted error when credits became available and incorrect completion response got reported
Manipulation-of-service bug caught through FPV

## Slide 15: Case Study: Results
Chart: 
| Security Issues | Functional Issues
Sales | 14 | 7
Unsecure Access to CRs: Transaction Agent (TA) claims transactions without security attributes, allows the attackers to modify/access Control/Status Registers (CSRs) (2 vulnerabilities)
Denial of Service/ Hang: TA fails to check header containing security attributes for malformed transaction, exposes TA to attackers for create hangs (3 vulnerabilities)
Manipulation of Service: TA unable to ignore malformed transactions appropriately, allows attackers to corrupt successful responses by injecting malformed transactions (1 vulnerability)
Issues related to Integrity and availability are hard to catch by formal apps like Security Path Verification (SPV). FPV has selective advantage over here because of its exhaustiveness

## Slide 16: Conclusion
FPV allows checking confidentiality, integrity, and availability simultaneously, unlike traditional security approaches that may focus solely on confidentiality.
Exploiting the same functional properties with loosened constraints can verify security leaks, making formal setup reusability possible with minimal effort.
For security-critical IPs, formal verification should be employed to check both functional, performance, and security aspects.
Formal verification is an effective method for detecting and mitigating security risks in hardware designs, ensuring security, and vulnerability-free hardware while achieving shift-left.

## Slide 17: THANK YOU