## Slide 1: PropGen: An Automated Flow to Generate SVA Properties for Formal and Simulation methods
Amith Shambhu, Vishal Dalal
Infineon Technologies, Bangalore.
Basavaraj Naik
Infineon Technologies, Munich.

## Slide 2: Contents
Introduction
Problem Statements
Proposed Solution – PropGen Flow
PropGen Architecture
PropGen for FSM Design Verification (DV)
Porting assertions from Formal Verification (FV) to Simulations
Results
Conclusion

## Slide 3: Introduction
Today’s Design Under Test (DUT) verification is challenging
Complexity of these DUTs’ is increasing
State space explosion
Design specifications constantly change
Verification of complex DUT poses several challenges
Intricate Test Bench (TB) architecture
Corner case bugs misses
Coverage scenario
DV Quality is utmost critical
DV automation is a MUST
Combination of both simulation and FV techniques needed

## Slide 4: Need for DV Automation
Coverage
Subsequent design changes
Design complexity
Labour intensive to generate the Tests manually
Repetitive efforts to regenerate tests, assertions etc
Undetected bugs
Corner cases covered?

## Slide 5: Problem Statements
Assertions are derived from the specifications
Specifications and Design undergo multiple changes during the execution
Assertion generation need to be automated to save repetitive efforts
Is Simulation coverage alone enough to do quality DV sign-off?
Can Formal Verification (FV) help to automate and verify exhaustively?

## Slide 6: Proposed Solution – Property Generator (PropGen)
PropGen can fill the automation gap
Relies on design specification (e.g. VISIO/XML/XLS) to generate SVA assertions
Checks various Use Cases
Register access checks
Safety critical sub-blocks
FSM Verification
User inputs limited for RTL Input/output ports
Needed for SV bind
Fully automated flow

## Slide 7: PropGen Flow
Compatibility
Portable from FV to simulations
Minimal constraints in FV
Automated flow
Generated directly from Specifications
Minimal user inputs
Specifications formats supported
Widely used

## Slide 8: PropGen Architecture
SVA Property File
SVA Templates
Design I/O signals (RTL)
PropGen
SVA Templates
Spec to XML converter

## Slide 9: PropGen Stages
fromState | toState | condition
0:IDLE | 0:IDLE | start_i == 1’b0
0:IDLE | 1:START | start_i ==1’b1
1:START | 2:REQUEST | 
2:REQUEST | 2:REQUEST | req_i == 1’b0
2:REQUEST | 3:GRANT | req_i == 1’b1
3:GRANT | 3:GRANT | gnt_i == 1’b0
3:GRANT | 0:IDLE | gnt_i == 1’b1
property state_cond_trans(STATE1, cond, STATE2);
@(posedge Clk) disable iff(!AsyncRst)
(state == STATE1) && cond |=> (state == STATE2);
endproperty
check_IDLE_to_START_condition : assert property(state_cond_trans(IDLE,(start_i== 1’b1),START));
Visio to XML
XML to SVA

## Slide 10: PropGen Use Cases
PropGen is applied to generate SVA for
  Register verification for various access policies
  Safety critical building blocks integration verification
  FSM verification
PropGen generated properties are
  Achieve 100% code coverage at block level FV
  Portable from block level FV to IP level simulations
Block level DV signed off using FV
End-to-end data integrity checks signed-off using simulations

## Slide 11: PropGen for FSM DV
DV Scenarios
5
4
1
2
3
State Transition Checks
Async Reset Checks
Livelock Checks
Deadlock Checks
State Output Value Checks

## Slide 12: Assertions Pass at Block Level FV
FV use unconstrained clock
@(posedge Clk)
(!async_rst) |-> (!output_1) && (!output_2);

## Slide 13: Porting Assertions from FV to IP Level Simulations
Block level FV assertions are portable to simulations
Some of FV assertion don’t enter Active state in simulations ---> Not sampled
  Clock gating is done at IP level during Async reset ---> Shuts-off the clock to sub-block
  Assertions in simulations remain at “inactive” state (Async Reset)

## Slide 14: Resolving Porting Challenges
Use the built-in SV feature $assertoff()
  Selectively disable assertions (e.g. clock gating)
  Only selective assertions from block level FV are disabled
  Usage : $assertoff (0, dut_top.<assertion binding_hierarchy path> )
Rest of the assertions Re-used at IP level simulations
  Effort saving
  Huge focus on verification Re-use
  No need to convert FV “assume” to IP level “assert”

## Slide 15: Black boxing of Multipliers
Impact
Fix
Issue
This is shown as a warning message in FV
  Need to be carefully reviewed before final waive-off
  Avoid auto black-boxing of multipliers
One assertion got impacted due to auto black-boxing
  Failed in FV as random values were driven
  Passed in simulations as multipliers were NOT blackboxed
Multipliers are often black boxed by FV tools.
  They are complex and resource intensive
  Significantly increase the runtime of FV

## Slide 16: Results
 | FSM Designs |  |  |  | 
 | PropGen DV |  |  |  | Manual DV
 | FSM1 | FSM2 | FSM3 | FSM4 | 
# SVA Properties | 103 | 48 | 29 | 97 | Same #
First FV report | 0.5 D | 0.5 D | 0.5 D | 0.5 D | 10 D( 90%)
Formal Code coverage | 100% | 100% | 100% | 100% | 100%
FV to Simulations portability | YES | YES | YES | YES | YES
SVA re-generation for design changes | 0.25 D | 0.25 D | 0.25 D | 0.25 D | 4 D ( 90%)
(*D = Days)
Notes: Include up arrow in Manual DV column for 90% to show efforts got increased here

## Slide 17: Conclusion
Specification based flow
SVA generated directly from specification provided in Visio/XLS/XML
Minimal manual user intervention
Simple and easy to use
DV cycle optimization
~90% DV schedule improvement
100% code coverage achieved using FV
Portable from sub-block to IP level
Assertions portable from block level FV to IP level simulations

## Slide 18: References
[1] Smith, A., et al. "Accelerating Design Verification through Automated Techniques." IEEE Transactions on VLSI Systems, vol. 42, no. 2, pp. 245-256.
[2] Johnson, B., and Lee, C. "Efficiency Improvement in Design Verification through Automation." IEEE Design & Test of Computers, vol. 39, no. 4, pp. 78-84.
[3] A. Shambu, V. Dalal, B. Naik and S. M, "Automation of FSM Verification Using Formal Tools," 2023 International Conference on Communication, Circuits, and Systems (IC3S), BHUBANESWAR, India, 2023, pp. 1-5. DOI: 10.1109/IC3S57698.2023.10169571.
[4] 1800-2017 - IEEE Standard for SystemVerilog--Unified Hardware Design, Specification, and Verification Language. IEEE, 2017.
[5] Chen, Q., Wang, L., & Li, Z.,"Formal Verification of ASICs: Challenges and Opportunities". IEEE Transactions on Computer-Aided Design of Integrated Circuits and Systems, 42(5), 987-1001, 2023.
[6] S. Johnson, B. Anderson, "Efficient Verification Strategies for Complex ASIC Designs." IEEE Transactions on VLSI Systems, vol. 30, no. 5, pp. 987-1001 2022.
Notes: Please add references here

## Slide 19: Thank you!
Q & A