## Slide 1: A 360 Degree View of UVM Events
Vikas Billa, Nagesh Kokonda
Microsemi India Pvt. Ltd, Hyderabad, India.
vikas.billa@microsemi.com, nagesh.kokonda@microsemi.com

## Slide 2: Agenda
Introduction
System Verilog event
uvm_event and uvm_event_pool
A Case Study
  Interrupt Mechanism
  Callbacks
  RAL
  Reset Aware Testbench
Conclusion
References

## Slide 3: Introduction
In a verification environment, the test-bench components often communicate in a synchronized manner, to effectively implement the time accurate checks
System Verilog events are dedicated and are widely used data types to achieve the desired synchronized communication between the components
UVM library has a built-in dedicated class around System Verilog events which has broaden the application and usage of event based communication
This paper is a collective case study of projects, highlighting the usage and benefits of uvm_event
Notes: System Verilog events are dedicated and are widely used data types to achieve the desired synchronized communication between the components.

## Slide 4: System Verilog Events
  A System Verilog event is a data type which has no storage. It can be triggered using the “->” operator, and an event triggering occurrence can be captured by using “@” operator or inbuilt .triggered method
Declaration:
event sv_event;
Triggering an event
->sv_event
Waiting for an event:
@sv_event
prone to race conditions
Persistent Trigger:
wait(sv_event.triggered)
eliminate common race conditions
Notes: 1) A System Verilog event is a data type which has no storage. It can be triggered using the “->” operator, and an event triggering occurrence can be captured by using “@” operator or inbuilt .triggered method.
2) uvm_event is a parameterized wrapper class created using System Verilog event construct. It provides some additional services such as setting call-backs, data delivery, and maintaining number of waiters, on-off state and timing information.

## Slide 5: UVM EVENT & UVM EVENT POOL
METHODS

## Slide 6: uvm_event
  uvm_event is a parametrized wrapper class created using the Systemverilog event construct
  Hierarchy
  Signature
  class uvm_event #(type T=uvm_object) extends uvm_object;
uvm_void
uvm_object
uvm_event_base
uvm_event#(T)

## Slide 7: uvm_event Methods
Frequently used Methods | Description
trigger(T data = null) | Trigger an event
wait_trigger() | Waiting for an event. A system Verilog equivalent of @ operator
wait_ptrigger() | Waiting for a persistent trigger. A system Verilog equivalent of .triggered. Avoids any race condition
get_trigger_data() | Gets data if any provided by the last call to trigger
wait_trigger_data(output T data) | Call and returns get_trigger_data method value followed by wait_trigger
wait_ptrigger_data(output T data) | Call and returns get_trigger_data method value followed by wait_ptrigger

## Slide 8: uvm_event_pool
uvm_event_pool is a singleton class built around an associative array of uvm_events indexed by string
This allows items to be shared amongst components throughout the verification environment
Hierarchy
uvm_void
uvm_object
uvm_pool
uvm_object_string_pool#(uvm_object)
uvm_event_pool

## Slide 9: uvm_event_pool Methods
Frequently used Methods | Description
get_global_pool() | Returns the singleton global pool for the item type, T.
get_global(key) | Returns the specified item instance from the global item pool.
get(key) | Returns the item with the given key.
add(key,item) | Adds the given (key, item) pair to the pool. If an item already exists at the given key it is overwritten with the new item.
Notes: This allows items to be shared amongst components throughout the verification environment.
If no item exists by that key, a new item is created with that key and returned.
Adds the given (key, item) pair to the pool. If an item already exists at the given key it is overwritten with the new item.
Other methods :
num - Returns the number of uniquely keyed items stored in the pool.
delete - Removes the item with the given key from the pool.
exists - Returns 1 if a item with the given key exists in the pool, 0 otherwise.
first - Returns the key of the first item stored in the pool., If the pool is not empty, then key is key of the first item and 1 is returned.
last - Returns the key of the last item stored in the pool., If the pool is empty, then 0 is returned and key is unchanged, If the pool is not empty, then key is set to the last key in the pool and 1 is returned.
next - Returns the key of the next item in the pool., If the input key is the last key in the pool, then key is left unchanged and 0 is returned., If a next key is found, then key is updated with that key and 1 is returned.
prev - Returns the key of the previous item in the pool., If the input key is the first key in the pool, then key is left unchanged and 0 is returned., If a previous key is found, then key is updated with that key and 1 is returned.

## Slide 10: uvm event and pool usage
class triggering extends uvm_component;
uvm_event_pool event_pool; //Declaration of pool
uvm_event an_event; //Declaration of event
function buid_phase(uvm_phase phase);
event_pool = uvm_event_pool::get_global_pool(); //Global pool handle will be passed to event_pool
an_event = event_pool.get(“event_key”) //new item is created with event_key and returned
endfunction
task run_phase(uvm_phase phase);
//code not shown here
an_event.trigger(); //Trigger event
//code not shown here
endtask
endclass
class waiting extends uvm_test;
uvm_event_pool event_pool;
uvm_event an_event;
task run_phase(uvm_phase phase);
//code not shown here
an_event.wait_ptrigger(); //Waiting for event
//code not shown here
endtask
endclass

## Slide 11: A CASE STUDY
POLARFIRE

## Slide 12: A Case Study
PolarFire Overview
  Microsemi's lowest power, cost-optimized mid-range PolarFire FPGA
  Applications within wireline access networks and cellular infrastructure, defense and commercial aviation markets, as well as industrial automation and IoT markets
  An FPGA with an ARM Cortex M3 Processor and programmable analog, offering full customization, IP protection and ease-of-use

## Slide 13
INTERRUPT MECHANISM

## Slide 14: Interrupt Mechanism
Interrupt is an event that is triggered by a Design or an IP block once certain conditions are fulfilled; the CPU has to service these events
Actions that are to be taken care by CPU while servicing the interrupts are collectively called as -Interrupt Service Routines (ISR)

## Slide 15: Interrupt Mechanism
INT FIFO`
INT_OBJX
INT_OBJX+1
INT_OBJX+2
Interrupt Monitor
Interrupt IF
INT_EV_POOL
UVM POOL
Sequence
ISR
GET
Wait for event
PUT
INT FIFO
INT_OBJ1
INT FIFO
INT_OBJ2
INT_OBJ3
INT_OBJ4
INT FIFO
INT FIFO
INT FIFO
INT_OBJ5
TIME LINE:
SEQ1
ISR
SEQ1
ISR
SEQ2
ISR
SEQ2
SEQ1
ISR
ISR
INT_EV INT_OBJ1
INT_EV
INT_OBJ2 & 3
INT_EV
INT_OBJ4
INT_EV
INT_OBJ5
Triggering of interrupts
FIFO Status
(Two intr triggered at same instance)

## Slide 16: Interrupt Mechanism - Monitor
class isr_monitor extends uvm_monitor;
trans_c trans;
uvm_event #(trans_c) isr_event;
function buid_phase(uvm_phase phase);
isr_event=cfg.event_pool.get(“interrupt_event”)
endfunction
task run_phase(uvm_phase phase);
forever begin
//Capturing and triggering the event
@(posedge isr_if.int_n);
isr_event.trigger(trans);
end
endtask
endclass: isr_monitor
event triggered
monitor
class env_cfg extends uvm_object;
//event pool declaration
uvm_event_pool event_pool;
endclass: env_cfg
event declaration

## Slide 17: Interrupt Mechanism - Sequence
class isr_seq extends uvm_sequence;
trans_c trans;
uvm_event #(trans_c) isr_event;
task body();
// code not shown here
isr_event.wait_ptrigger_data(trans);
// Store the event in the queue.
m_sequencer.grab(this);
// isr scenario
m_sequencer.ungrab(this);
endtask
endclass: isr_seq
class env_base_test extends uvm_test;
uvm_event_pool evt_pool;
function buid_phase(uvm_phase phase);
evt_pool=uvm_event_pool::get_global_pool();
cfg.event_pool=evt_pool;
endfunction
endclass: env_base_test
sequence
Test
waiting for the event
grab the sequencer

## Slide 18
CALLBACKS

## Slide 19: Callbacks
The uvm_event_callback class is an abstract class that is used to create a callback object which is attached to uvm_event#(T) as shown in below code
The uvm_event_callback class has two empty virtual methods
The user has to create a callback class which extends from uvm_event_callback and has to override the virtual methods to implement the required functionality
The callbacks support is one of the main feature of any VIP
virtual class uvm_event_callback#(type T=uvm_object) extends uvm_object;

## Slide 20: Callbacks - Driver
class pkt_dvr extends uvm_driver;
uvm_event #(trans) ev1;
uvm_event #(trans) ev2;
// new constructor
virtual function void build_phase(uvm_phase phase);
ev1 = cfg.event_pool.get(“ev1”);
ev2 = cfg.event_pool.get(“ev2”);
endfunction
task run_phase ( uvm_phase phase);
seq_pkt pkt;
start(pkt)
->ev1.trigger(pkt);
process(pkt);
->ev2.trigger(pkt);
endtask
endclass:pkt_dvr
driver class
ev1 triggered after the start(pkt) method
class env_cfg extends uvm_object;
//event pool declaration
uvm_event_pool event_pool;
endclass: env_cfg

## Slide 21: Callbacks – User Callback class
class user_event_cb extends uvm_event_call_back #(trans);
// new constructor
virtual function bit pre_trigger(uvm_event ev, trans pkt);
//change trans/data before triggering the event
endfunction
virtual function bit post_trigger(uvm_event ev, trans pkt);
//change data/trans after triggering the event
endfunction
endclass
user callback
post_trigger
pre_trigger

## Slide 22: Callbacks – Test
class my_test extends uvm_test;
uvm_event ev1;
uvm_event_pool evt_pool;
user_event_callback my_event_cb;
function buid_phase(uvm_phase phase);
evt_pool=uvm_event_pool::get_global_pool();
cfg.event_pool=evt_pool;
ev1 = cfg.event_pool.get(“ev1”);
endfunction
virtual function void build_phase(uvm_phase phase);
super.build_phase(phase);
my_event_cb = user_event_cb:: type_id :: create ("my_event_cb");
ev1.add_callback(my_event_cb);
// code not shown
ev2.delete_callback(my_event_cb);
endfunction
endclass
test
add callback
delete callback
class env_cfg extends uvm_object;
//event pool declaration
uvm_event_pool event_pool;
endclass: env_cfg

## Slide 23
REGISTER ABSTRACTION LAYER (RAL)

## Slide 24: RAL
uvm_reg_cb provides some standard callback methods like
  pre_write
  pre_read
  post_write
  post_read
  post_predict
uvm_event can be used for communication from register callback class to other components like scoreboard, reference model, sequences etc.
Adopting the uvm_event for RAL to TB communication requires minimal testbench code changes and also the data delivery through uvm_event helps a great deal especially in score-boarding and reference modeling

## Slide 25: RAL
class trans_capture_cb extends uvm_reg_cbs;
uvm_event#(uvm_reg_item) wr_event;
uvm_event#(uvm_reg_item) rd_event;
//new constructor
virtual function void post_write(uvm_reg_item rw);
wr_event = cfg.event_pool.get(“reg_write_event”);
wr_event.trigger(rw);
endfunction
virtual function void post_read(uvm_reg_item rw);
rd_event = cfg.event_pool.get(“reg_read_event”);
rd_event.trigger(rw);
endfunction
endclass : trans_capture_cb
register callback class
triggering write event with packet as parameter
triggering read event with packet as parameter

## Slide 26: RAL
class ref_model extends uvm_component;
uvm_event#(uvm_reg_item) wr_event;
uvm_reg_item reg_wr;
uvm_object reg_obj;
//new constructor
virtual function void build_phase(uvm_phase);
wr_event = cfg.event_pool.get(“reg_write_event”);
endfunction : build_phase
task run_phase()
forever begin
wr_event.wait_ptrigger_data(reg_obj);
if(!$cast(reg_wr, reg_obj)) begin `uvm_fatal(…) end
process_wr_pkt(reg_wr);
end
end
endtask
endclass
capturing event from RAL
trans_capture_cb trans_cap_cb;
trans_cap_cb = new(…);
uvm_reg_cb::add(env.reg_model.reg*, trans_cap_cb);
Reference model

## Slide 27
RESET AWARE TESTBENCH

## Slide 28: Reset Aware Testbench
Handling on-the-fly reset is one of the challenges in the testbench design
The UVM methodology does not define how an on-the-fly reset must be handled
The reset is a major disruptive event which can occur at any point of time, it’s very important to ensure that the chip exists out of reset and resumes normal operation without any issue

## Slide 29: Reset Aware Testbench
Here is how the 4 major components Driver, Monitor, Scoreboard and Sequences must behave on capturing the reset event:
Driver:
  Should not drive data under reset and wait until reset is removed.
Monitor:
  Should be monitoring the bus and trigger report error for conditions on bus which are not expected under reset.
  Should treat the bus data as invalid if a reset is applied in between a transaction.
Scoreboard:
  On application of the reset, all FIFO’s must be flushed.
Sequences:
  Immediately after reset, the configuration sequence should be driven before driving any other sequence.

## Slide 30: Reset Aware Testbench
Virtual Sequencer
t1
t2
t3
t4
Agent1 Seq
Agent2 Seq
AGent2 Config seq
AGent1 Config seq
Reset Driver
Agent1 Driver
Can be Global reset seq or Agent 1 reset seq or Agent 2 reset seq
Configuration sequences driven immediately after reset
Agent must end its current seq on reset assertion
Reset Seqs
t5
t6
Agent2 Driver
Reset IF
Agent 1
Agent 2
Reset Monitor
Agent 1 Monitor
Agent 2 Monitor
DUT
How to propagate the monitored reset to other components of testbench?
Notes: Handling on-the-fly reset is one of the challenges in testbench design. The UVM methodology does not define how an on-the-fly reset must be handled. The reset is a major disruptive event which can occur at any point of time, it’s very important to ensure that the chip exists out of reset and resumes normal operation without any issue.

## Slide 31: Reset Aware Testbench
virtual function void build_phase(uvm_phase);
global_reset_ev = cfg.event_pool.get(“global_reset”);
agentX_reset_ev = cfg.event_pool.get(“agentX_reset”);
endfunction : build_phase
task run_phase()
...
forever begin
fork
agentX_reset_ev.wait_ptrigger();
global_reset_ev.wait_ptrigger();
join_any
reset_procedure();
end
...
endtask
In reset aware components
Waiting for Reset

## Slide 32: Conclusion
The uvm_event and event pool provides synchronization between multiple threads or concurrent processes in the verification environment
It is observed that by using uvm_event we can achieve better synchronization without making major changes to the exiting test-bench
The uvm_event wrapper class around the traditional system Verilog event with added methods makes uvm_event to be applicable to a broader and complex application than just synchronization

## Slide 33: References
[1] Verilab - Advanced UVM Register Modeling – “There’s More Than One Way to Skin A Reg” – Mark Litterick and Marcus Harnisch
[2] DVCON INDIA 2014 - Global Broadcast with UVM Custom Phasing Jeremy Ridgeway, Dolly Mehta - Avago Tech
[3] Accellera, “UVM User Guide, v1.1d”, www.uvmworld.org
[4] Accellera, “UVM Reference Guide, v1.1d”, www.uvmworld.org
[5] Dialog Semiconductor – “The UVM Register Layer Introduction and Experiences” - Steve Holloway

## Slide 34: Acknowledgement
We profoundly thank colleagues and management team at Microsemi India Pvt. Ltd, Hyderabad for their valuable support
Thanks to DVCON INDIA for giving us this opportunity

## Slide 35: Questions