## Slide 1
Niharika Sachdeva, Arjun Suresh Kumar, Raviteja Gopagiri, Anil Deshpande, Somasunder Kattepura Sreenath, Damandeep Saini
Samsung Semiconductor India Research (SSIR)
A Generic Configurable Error Injection Agent
for All On-Chip Memories

## Slide 2: Agenda
01
02
03
04
05
06
07
08
09
10
Motivation
On chip Memories
ECC encoding and decoding
Existing methodologies
Proposed Agent
Configurable parameters and patterns
Agent in action
Results
Conclusion
Future scope

## Slide 3: Motivation
Memory Errors
Soft Errors
Hard Errors
Memories exist everywhere
High Probability of Bit Flips
Need for Error Correction and Detection
Agnostic verification of ECC Algorithm
Federal Voting: 18th May 2003, Belgium

## Slide 4: On-Chip Memories
On-Chip Memory
Random Access
SRAM
MRAM
EPROM
DRAM
PROM
FLASH
Read-Only
NAND
NOR
EEPROM

## Slide 5: Error Detection and Correction
ECC Encoder
ECC Decoder
Data_in[m:0]
Data_out[m:0]
parity_out[n:0]
Flip or error
Write data
Read data
Data_rd[m:0]
Parity_in[n:0]
Corrected Data[m:0]
Detection or uncorrectable flags
Parity Code
Checksum
Cyclic Redundancy Check
Hamming code
BCH code
Techniques

## Slide 6: Existing Methodologies
Formal Based
Formal Reasoning
Formal Modelling
Simulation Based
  Error injection (Reactive)
  Memory transaction patterns required

## Slide 7: Proposed Agent
Existing VE
Error Injection Agent
0
1
1
0
1
DUT IP
Virtual Interface
1
2

## Slide 8: Proposed Agent
Sequences
Configuration Class
Coverage
Sequencer
Driver
Virtual Sequencer (Target VE)
DUT
Memory
CONFIG_ERRINJ_AGENT
Monitor
Scoreboard
TB_TOP (Existing Memory Controller/SoC/StandAlone Memory)
Virtual Interface

## Slide 9: Configurable Parameters and Patterns
Type of Error
SEI,DEI,TEI,MEI
Error Injection Mode
Random,Fixed,Incremental address mode
Ratio mode
MEI in ratios
Non stop mode
Continuously Error injection
Fixed Error Position
Address and Position range
Used to create Stuck at faults
Error Count
Error to be injected on a selected range of Address
Number of ECC’s
In incremental mode, user can configure number of errors injected.
Use Reference Memory
Parallel testing for those blocks whose data width is covered by different ECC modules
To enable or disable checks for Memory DATA IN and DATA OUT
March C
{↨ w0, ↑ (r0, w1), ↑ (r1, w0), ↓ (r0, w1), ↓ (r1, w0), ↨ r0}
Scan
{↑ w0, ↑ r0, ↑ w1, ↑ r1}
Checkerboard
{↑ w0/1, ↑ r0/1; ↑ w1/0, ↑ r1/0}
Random
{↑ w, ↑ r, ↓ w, ↓ r, ↨ w, ↨ r}

## Slide 10: Agent in action
EccErrInject: Tells if Error was injected
ErrinjPos: Tells which bit position was flipped
SRAM Memory Signals: Indicates Read Operation on XA address

## Slide 11: Results
Memory Type | Data width | No of ECC Blocks | Number of coverage bins (RTL design code) | Simulation time saved to achieve 100% coverage | Test bench development time saved
MRAM | 64 data bits + parity bits | 1 | 7100 | 25% | 40%
MRAM | 2*(128 data bits + parity bits) | 2 | 18400*2 | 35% | 45%
SRAM | 32 bits + parity bits | 1 | 400 | 20% | 50%
FLASH | 32 bits + parity bits | 1 | 1589 | 25% | 35%

## Slide 12: Results

## Slide 13: Conclusion & Future Ahead
Early detection of bugs in embedded ECC logic
Comprehensive and early coverage closure for ECC circuit logic
No overhead in simulation time
Easy to integrate with any UVM environment
Optimizing on memory test patterns to close verification faster
Extension on actual memory netlists (non-behavioral model) and then compare the performance metrics.

## Slide 14
Questions & Comments