## Slide 1: A UVM Based Methodology for Processor Verification
Abhineet Bhojak, Tejbal Prasad
Freescale Semiconductor

## Slide 2: Processor Verification Challenges
Presence of multicycle instruction along with single cycle instruction
  Various hazards (e.g. WAR,WAW)
Dedicated Hardware Accelerator
Excessive number of GPR (~200)
Debug hooks for easier debugging
Stimuli Generator
Hazard scenario
Accelerator
Test generation
Meaningful program
Debug
Hooks for localization of failure
Need of multiple test
Jump & Loop cmd

## Slide 3: Existing Technologies
Random test pattern generation (RTPG) and Test plan automation
  Combine architecture specific knowledge and testing knowledge and uses a CSP solver to generate efficient test programs
  there is a significant learning curve involved to leverage these RTPG’s in an industrial environment
Formal verification
  Useful and efficient in some cases
  it requires significant mathematics skill and computational resources to relate to the scenarios and analyze them
Pure directed testing
  Gives confidence on different functionalities
  Achieving desired coverage may take large amount of time

## Slide 4: PROPOSED METHODOLOGY
Layered architecture
Scenario
Program Generator
Atomic Transaction

## Slide 5: Proposed Stimulus Generation Flow
A fine blend of Top Down control and Bottom layer intelligence
Scenario
Skeleton of the program is generated
Program Generator
It does the decision making based on Scenario level information
Atomic Transaction
Data for the program is controlled
Size of the program is controlled
It Randomizes atomic transaction based on fixed/random type or to a fixed /random instruction
It randomizes all the fields and pack them into one instruction.
Provides the Top Down Control
Bottom layer intelligence
Extension for instruction grouping for better reuse
Takes care of infinite loop
Does instruction operand interlinking

## Slide 6: Bottom Layer Intelligence
load address1, R3
load address2, R4
add R3, R4, R5
store R5, address3
Potential Hazard Candidate
Interesting scenario
How to put in this intelligence w/o complicating constraint solver ?
Conventional Way
Randomize the whole program
Use foreach constraint to make relation between instruction operand
Innovative Way
Randomize one instruction at a time.
Keep copy of last few instruction.
While randomizing current instruction 1st decide to what depth (rel_depth) you want to link it
Use last instruction copy & rel_depth to decide the current instruction operand

## Slide 7: Bottom Layer Intelligence
Operand Interlinking

## Slide 8: Bottom layer Intelligence
JMP LEN1
JMP LEN2
BZ End
SUB R1,1
Loop:
MOV R1,VAL
BNZ Loop
SUB R1,1
HALT
End:
BRANCH
BEQ
BLT
BGT
BN
BC
ALU
ADD
SUB
XOR
OR
CMP
INSTRUCTION GROUPS
Jump Length constraints
LEN1
LEN2
W-MARK
LENGTH
FILL
Infinite Loop Avoidance

## Slide 9: Debugging Hooks
Debug cannot be an afterthought.
Localization of Failure
Scenario Replication
Zero time Reference model Vs pipelined processor
Checking only at interfaces is not enough for complex scenarios
At some point in time we need to run programs developed by other team
Switch based flow for directed stimulus
Out-of-order execution of pipeline Vs In-order execution of model
Need checker based on register content change – Data trace checker
File & queue based Checker
Debug of Debug

## Slide 10: Debugging Hooks

## Slide 11: Evaluation of the Proposed Flow
Design Complexity
Scalar, Vector & Matrix operation, 9 ALUs, 4 Multiplier, ~256 GPRs & Hardware Accelerator like SORT, HISTOGRAM etc
Verification
30 man weeks of effort, Verification Environment created from Scratch, ~200 test /15 K runs, ~10 k functional cover points, 200 odd defects were found
First Pass Success
No additional bugs found after IP signoff.
Silicon has been evaluated - considered to be a first pass success.

## Slide 12: Thank You Q & A