## Slide 1: An Introduction to the Accellera Portable Stimulus Standard

## Slide 2: Today's Speakers
Introduction: Srivatsa Vasudevan, Synopsys
Portable Stimulus Concepts & Constructs: Pradeep Salla, Mentor
Building System-Level Scenarios: Sharon Rosenberg, Cadence
Generating Tests from Portable Stimulus: Adnan Hamid, Breker
Hardware/Software Interface Library: Karthick Gururaj, Vayavya Labs
Coverage in Portable Stimulus: Srivatsa Vasudevan, Synopsys
Conclusion: Bishnupriya Bhattacharya, Cadence

## Slide 3: Portable Stimulus The Next leap in Verification & validation Productivity
Srivatsa Vasudevan, Synopsys

## Slide 4: A Brief History of Verification
ad hoc Verification teams
Directed
Testing
System Verilog
CRV & MDV
Standard
Methodology
UVM
VMM
OVM
Portable Stimulus
Verification?
Verification Productivity

## Slide 5: SoC-level Verification
Design complexity continues to increase
Outstripping Verification Productivity (again)
State space at system-level is too big for effective UVM Constrained-Random
Multiple platforms
Need to reuse Test Intent
  Higher abstraction
  Reuse from block to system
  Map to different platforms
EMULATION
SIMULATION
FPGA PROTO
STIMULUS
FULL SYSTEM
IP BLOCK
SUBSYSTEM
Notes: In order to understand why Portable Stimulus is needed, we have to look, yet again, at the problem of increasing complexity. Regardless of whether you measure design complexity by number of gates, amount of IP, number of embedded processors, software content, or any other metric, the relentless increase in complexity continues. This means that once again, we're at the point where Verification needs a productivity boost to be able to keep pace. One issue is that the verification process itself has become a larger problem where, to support large SoC design verification, many different execution platforms are used, from simulation to emulation and FPGA prototyping. Historically, each of these platforms required a different way of specifying tests, usually written by different stakeholders. We're at the point where productivity demands that we be able to reuse test intent across all these platforms. Just like synthesis enabled the design productivity jump from gate-level to RTL, and UVM enabled the verification productivity jump from directed testing to constrained random transaction-level testing, the problem of SoC-level verification requires a higher level of abstraction and, just like synthesis and constrained-random, the use of automation.

## Slide 6: Reuse of Test Intent Across Platforms/Users
Different tests used throughout a project
  Wastes Time
  Error Prone
UVM constrained-random is too limited for directing SoC-level testing
C tests usually directed for specific use-cases
  Hard to create
  Miss corner cases
EMULATION
SIMULATION
FPGA PROTO
FULL SYSTEM
IP BLOCK
SUBSYSTEM
UVM
C
Notes: Taking a closer look, a typical project tends to migrate from doing IP block testing in simulation using SystemVerilog and UVM, to running subsystem or full system tests in emulation or prototyping where the test might be C code running on an embedded processor. The cost of migrating tests from one format to another is very high. Even if you successfully convert your tests along the way, it still takes time to do, and errors are always introduced along the way. We've come a long way in using UVM to create constrained-random tests at the block level, but for performance and other reasons, as we'll see, UVM is not the best solution for creating complex system-level tests. System-level tests are typically written in C and, while they might be able to rely on a bit of UVM to drive external traffic, they are mostly directed tests, which limits their effectiveness as we all know. They are hard to create in the first place and, because SoC-level interactions are so complex, they often miss corner cases which is a huge problem.

## Slide 7: Reuse of Test Intent Across Platforms/Users
Single specification of test intent is critical
Constrain and randomize at the Scenario Level by capturing:
  interactions
  dependencies
  resource contention
Abstraction lets tool automate generation
  of Correct-by-construction legal tests
  for Multiple targets
  with Target-specific customization
UVM
C
Portable Stimulus
IP BLOCK
SUBSYSTEM
FULL SYSTEM
EMULATION
SIMULATION
FPGA PROTO
Notes: Instead, what we need is a single specification of the test intent that can be reused across all of these platforms and by all the different users in a typical project. The ideal way to ensure the portability, as we'll see, is to define the test at the scenario level, where we capture the interactions between the different parts of the system as well as their dependencies and resource contention issues, since these are usually the source of problems at the system level. By specifying the test intent at this higher level of abstraction, we can let a tool automate the generation of target-specific implementations of the tests, regardless of what platform we're targeting, and also to customize the generated test based on specific requirements of the desired platform. As we'll see, this also allows us to reuse these Portable Stimulus tests from project to project, where important factors like the number of embedded processors, or the number of available DMA channels or other design-specific parameters might change.

## Slide 8: PSS Tool Operating in a UVM Environment
AXI
VIP
UART
DDR MEM
DMAC
UART
VIP
AXI
VIP
PSS Model
PSS Tool
UVM
Sequences
UVM Testbench
PSS tool composes UVM sequences for existing UVM environment from abstract use case specification
Tool handles verification checks and coverage collation against original spec
Streamlines testbench authoring using an “executable specification”

## Slide 9: PSS Tool Operating in a SoC Environment
TB
AXI
VIP
UART
DDR MEM
DMAC
UART
VIP
CPU
UVM
Sequences
C-test
Sync
SoC Testbench
PSS tool generates synchronized
IO data and SW tests
Use cases may be reused from other process stages including simulation
A single scenario can drive complete test sets for emulation, reusing VIP
PSS Model
PSS Tool

## Slide 10: What Portable Stimulus Is Not
A UVM replacement
A reference implementation
One forced level of abstraction
  Expressing intent from different perspectives is a primary goal
Monolithic
  Representations would typically be composed of portable parts
Two standards
  DSL and C++ input formats describe 1:1 semantics
  Tools shall consume both formats
Just stimulus
  Models Verification Intent
  Stimulus, checks, coverage, scenario-level constraints

## Slide 11: concepts & constructs
Pradeep Salla, Mentor

## Slide 12: The Steps to Creating a Portable Stimulus Model
Step 1: Identify Behaviors
Step 2: Identify Data Flow
Step 3: Where do Actions Execute?
Step 4: What System Resources are required?
Data
UART
MEM
Command
DMAC
component uart_c {
resource uart_r {…};
pool [1] uart_r uart_p;
bind uart_p {*};
action read_in_a {
output data_str data;
lock uart_r u_busy;
};
action write_out_a {
input data_str data;
lock uart_r u_busy;
};
}
data_str

## Slide 13: The Steps to Creating a Portable Stimulus Model
Step 1: Identify Behaviors
Step 2: Identify Data Flow
Step 3: Where do Actions Execute?
Step 4: What System Resources are required?
Data
UART
MEM
Command
DMAC
component dma_c {
resource chan_r {…};
pool [1] chan_r chan_p;
bind chan_p {*};
action u2m_a {
input data_str src_data;
output mem_b dst_data;
lock chan_r chan;
};
action m2u_a {
input mem_b src_data;
output data_str dst_data;
lock chan_r chan;
};
action m2m_a {… };
}
data_str
mem_b

## Slide 14: Defining the Data Structures
Portable Stimulus only cares about the structure of data
Data type defines scheduling constraints
  buffer = sequential
  stream = parallel
Data
UART
MEM
Command
DMAC
struct data_seg_s { rand int[4..1024] size; rand bit[63:0] addr; };
buffer mem_b : data_seg_s {
};
enum data_dir_e {in, out};
stream data_str : data_seg_s { rand data_dir_e dir; rand int[1..2] stop_bits; };
data_str
mem_b
Notes: A flow object represents incoming or outgoing data/control flow for actions

## Slide 15: Data Flow Objects
Specialized struct objects
  Each may inherit from a struct; May not inherit from each other
buffer
stream
state
name
[rand] struct_fields;
}
read_in_a
u2m_xfer
m2m_xfer
observed behavior
m2m
buff
u2m
rd_i
strm
Stream = Parallel
Buffer = Sequential
1:many
1:1
many:many
:struct_type
OOP Inheritance
{
Notes: Buffer objects represent data items in some persistent storage that can be written and read. Stream objects represent transient data or control exchanged between actions during concurrent activity State objects represent the state of some entity in the execution environment at a given time

## Slide 16: Adding Data Constraints
Data constraints limit the solution space
Actions that share a data object must have compatible constraints
Data
UART
MEM
Command
DMAC
action read_in_a {
output data_str data;
lock uart_r u_busy;
constraint data.dir == in;
};
action u2m_a {
input data_str src_data;
output mem_b dst_data;
lock chan_r chan;
constraint src_data.dir == in;
constraint src_data.size == dst_data.size;
};
action m2m_a {
input mem_b src_data;
output mem_b dst_data;
lock chan_r chan;
constraint src_data.size == dst_data.size;
constraint src_data.addr != dst_data.addr;
};
data_str
mem_b

## Slide 17: Constraints Narrow the Solution Space
g
m.x>8
a
m.x>2
b
m.x<12
buffer mbuf { bit[3:0] x;
constraint {x < 10;}
};
action do_b { input mbuf m;
constraint {m.x < 12;}
};
action do_a { output mbuf m;
constraint {m.x > 2;}
};
action do_g { output mbuf m;
constraint {m.x > 8;}
};
action do_p { input mbuf m;
constraint {m.x < 8;}
};
p
m.x<8
mbuf
x=9..11
mbuf
x=3..11
mbuf
x=3..7
mbuf
x = Ф
mbuf
x =3..9
mbuf
x = 9

## Slide 18: Assembling the Top-Level Model
pss_top
dma0
u2m
m2m
m2u
chan_p
buff_p
uart0
rd_i
wr_o
uart_p
strm_p
component pss_top {
uart_c uart0;
dma_c dma0;
pool data_str stream_p;
bind stream_p {*};
pool mem_b mem_p;
bind mem_p {*};
}

## Slide 19: Assembling the Top-Level Model
component pss_top {
uart_c uart0;
dma_c dma0;
pool data_str stream_p;
bind stream_p {*};
pool mem_b mem_p;
bind mem_p {*};
action loopback_test {
uart_c::read_in_a rd_i; dma_c::u2m_a u2m;
uart_c::write_out_a wr_o; dma_c::m2u_a m2u;
bind rd_i.data u2m.src_data;
bind wr_o.data m2u.dst_data;
bind u2m.dst_data m2u.src_data;
activity {
parallel { rd_i; u2m; }
parallel { wr_o; m2u; }
}
}
}
m2u
wr_o
d_str
memb
d_str
u2m
rd_i

## Slide 20: Activity
activity {
that;
do an_a;
parallel {a1, a2};
sequence {a3, a4};
select {a5, a6};
schedule {a7, a8};
if (i == 0) {a9;} else {a10;}
repeat (2) {a11, a12};
foreach (arr[j]) { a13 with {a13.val == arr[j];};
}
that
an_a
a1
a2
a3
a4
a7
a8
a7
a8
a8
a7
a11
a12
a11
a12
i==0
a9
a10
T
F
a13
a13
a13
Action instance traversal
Anonymous action traversal
Subject to flow/resource constraints
a5
a6

## Slide 21: Assembling the Top-Level Model
component pss_top {
uart_c uart0;
dma_c dma0;
pool data_str stream_p;
bind stream_p {*};
pool mem_b mem_p;
bind mem_p {*};
action loopback_test {
uart_c::read_in_a rd_i; dma_c::u2m_a u2m;
uart_c::write_out_a wr_o; dma_c::m2u_a m2u;
bind rd_i.data u2m.src_data;
bind wr_o.data m2u.dst_data;
bind u2m.dst_data m2u.src_data;
activity {
parallel { rd_i; u2m; }
parallel { wr_o; m2u; }
}
}
}
u2m
rd_i
m2u
wr_o
d_str
memb
d_str

## Slide 22: Assembling the Top-Level Model
component pss_top {
uart_c uart0;
dma_c dma0;
pool data_str stream_p;
bind stream_p {*};
pool mem_b mem_p;
bind mem_p {*};
action loopback_test {
uart_c::read_in_a rd_i;
uart_c::write_out_a wr_o;
activity {
rd_i;
wr_o;
}
}
}
u2m
rd_i
m2u
wr_o
d_str
memb
d_str

## Slide 23: Assembling the Top-Level Model
component pss_top {
uart_c uart0;
dma_c dma0;
pool data_str stream_p;
bind stream_p {*};
pool mem_b mem_p;
bind mem_p {*};
action loopback_test {
uart_c::read_in_a rd_i;
uart_c::write_out_a wr_o;
activity {
rd_i;
wr_o;
}
}
}
u2m
rd_i
d_str
m2u
wr_o
d_str
memb
m2m
data
memb

## Slide 24: Mapping to Implementation
exec blocks define target language implementation for actions
  Target-language templates (C or SV)
  Import external procedures from legacy code
Exec blocks can only be defined for leaf-level actions
  activity and exec body block are mutually exclusive
action read_in_a {
output data_str data;
lock uart_r u_busy;
constraint data.dir == in;
exec body C = """ init_uart_rx( {{data.stop_bits}} ); gen_uart_traffic( {{data.stop_bits}}, {{data.size}} ); """ }
}
action read_in_a {
output data_str data;
lock uart_r u_busy;
constraint data.dir == in;
exec body SV = """
init_uart_rx( {{data.stop_bits}} );
gen_uart_traffic( {{data.stop_bits}}, {{data.size}} );
"""
}
}
import void init_uart_rx(bit[1:0] stop_bits);
import void gen_uart_traffic(bit[1:0] stop_bits, int sz);
action read_in_a {
output data_str data;
lock uart_r u_busy;
constraint data.dir == in;
exec body {
init_uart_rx( data.stop_bits );
gen_uart_traffic( data.stop_bits , data.size );
}
}
}
"Moustache" notation to refer to PSS fields
int main(int argc, char **argv) {
// …
init_uart_rx(1);
gen_uart_traffic(1, 128);
// …
init_uart_rx(2);
gen_uart_traffic(2, 27);
return 0;
}
class uvm_test1 extends uvm_test_base;
virtual task body();
// …
init_uart_rx(1);
gen_uart_traffic(1, 128);
// …
init_uart_rx(2);
gen_uart_traffic(2, 27);
endtask
endclass

## Slide 25: Summary
component uart_c {
resource uart_r {…};
pool [1] uart_r uart_p;
bind uart_p {*};
action read_in_a {
output data_str data;
lock uart_r u_busy;
constraint data.dir == in;
exec body {…}
};
action write_out_a {…};
}
component dma_c {
resource chan_r {…};
pool [1] chan_r chan_p;
bind chan_p {*};
action u2m_a {
input data_str src_data;
output mem_b dst_data;
lock chan_r chan;
constraint src_data.dir == in;
constraint src_data.size ==
dst_data.size;
exec body {…}
};
action m2u_a {…};
action m2m_a {…};
}
component pss_top {
uart_c uart0;
dma_c dma0;
pool data_str stream_p;
bind stream_p {*};
pool mem_b mem_p;
bind mem_p {*};
action loopback_test {
uart_c::read_in_a rd_i;
activity {
rd_i;
wr_o;
}
}
}
Data
UART
MEM
Command
DMAC
data_str
mem_b
int main(int argc, char **argv) {
// …
init_uart_rx(1);
gen_uart_traffic(1, 128);
// …
init_uart_rx(2);
gen_uart_traffic(2, 27);
return 0;
}
pss_top
dma0
u2m
m2m
m2u
chan_p
buff_p
uart0
rd_i
wr_o
uart_p
strm_p
rd_i
wr_o
u2m
m2u
d_str
memb
d_str

## Slide 26: building system-level scenarios
Sharon Rosenberg, Cadence Design Systems

## Slide 27: A Sub-system Example
UART
VIP
BUS
VIP
virtual
Sequences
Data
Command
UART
DDR MEM
DMAC

## Slide 28: A Simple SoC Example
UART
VIP
BUS
VIP
virtual
Sequences
CPU
Graphics
Crypto
UART
DDR MEM
DMAC
Quad-core CPU: Write, Read or Copy memory buffers
Transmit or Receive Data
Multi-channel System DMA
Encrypt or Decrypt Data
Decode Images or Videos
Virtual sequence
Cannot be reused
In fast platforms need UART transactor or HW
So How do we achieve Vertical reuse?

## Slide 29: A Simple SoC Example
TB
UART
DDR MEM
DMAC
CPU
Graphics
UART
VIP
Step 2: Compose actions into activities to specify scenarios
Step 1: Define component types and their operations as actions
write
copy
read
transfer
read_in
write_out
The description of the stimuli space (e.g. using a firmware routine or a UVM sequence) is secondary
Crypto
encrypt
decrypt

## Slide 30: What are System-Level Scenarios?
The whole is greater than the sum of its parts!
  And so are its bugs...
Application use-cases involve multiple IPs interoperating
  Example – read video off a mass-storage device, decode, split audio data from video frames, process by dedicated multi-media engines
Stress and performance use-cases involve saturated utilization of shared resources
  Example – all processors and DMA-enabled controllers access a certain memory controller in parallel
System low-power use-cases need to be crossed with functional scenarios
System coherency of caches/TLBs requires coordinated pattern of accesses from CPUs and non-processor masters

## Slide 31: Reuse IP Models Step #1: Modeling
Actions are abstract, declarative, concise, well encapsulated units of behavior
One action should not assume the existing of another action
component dma_c {
resource struct channel_s {};
pool [32] channel_s chan;
bind chan *;
action mem2mem_xfer { input data_buff_s src_data; output data_buff_s dst_data;
lock channel_s channel; constraint src_data.seg.size ==
dst_data.seg.size; };
...
};
DMA
transfer
buff
buff
component crypto_c {
action encrypt { input data_buff_s src_data; output data_buff_s dst_data;
constraint {
// operates on 128-byte blocks
(src_buff.seg.size % 128) == 0;
(dst_buff.seg.size % 128) == 0;
// output is encrypted, input not
!src_buff.encrypted;
dst_buff.encrypted;
}
};
};
Crypto
encrypt
buff
buff
component uart_c {
action write_out { input data_stream_s src_data; };
action read_in { output data_stream_s dst_data; };
};
UART
write_out
stream
read_in
stream

## Slide 32: SW Operations Modeling Step #1: Modeling
component cpu_c {
abstract action sw_operation {
lock core_s core;
};
action check_data : sw_operation { input data_buff_s src_data; };
action write_data : sw_operation {
output data_buff_s dst_data;
};
action copy_data : sw_operation {
input data_buff_s src_data; output data_buff_s dst_data;
constraint c1 {src_data.size == dst_data.size;}
};
};
CPU
component pss_top {
...
pool [4] core_s chan;
bind core_s *;
};
Processor cores are resources that can be locked or shared by other components' actions (e.g. for their control)
resource struct core_s {
rand core_tag_e core_tag;
rand cluster_tag_e cluster_tag;
constraint {
cluster_tag == CLUSTER_A -> core_tag inside [CORE_A0, CORE_A1];
cluster_tag == CLUSTER_B -> core_tag inside [CORE_B0, CORE_B1];
};
Attributes and constraints can be associated with resources
check_data
buffer
copy_data
buff
buff
write_data
buffer

## Slide 33: Specifying Multi-IP Data Flows Step #2: Scenario Creation
action chain1 {
cpu_c::create_data_a write;
crypto_c::encrypt enc;
cpu_c::copy_data_a copy;
crypto_c::decrypt dec;
cpu_c::check_data_a check;
activity {
write;
enc;
copy;
dec;
check;
bind write.out_buff enc.src_buff;
bind enc.dst_buff copy.src_buff;
bind copy.dst_buff dec.src_buff;
bind dec.dst_buff check.in_buff;
};
};
action multi_chain {
activity {
schedule {
do chain1;
do chain2;
};
};
};
start
engine
create_data_a
crypto_a
channel
core
databuf
size addr
tag
copy_data_a
core
crypto_a
engine
core
check_data_a
databuf
databuf
databuf
create_data_a
crypto_a
channel
core
databuf
copy_data_a
core
crypto_a
engine
core
check_data_a
databuf
databuf
databuf
Resource conflict is automatically taken care of by serializing the contending actions

## Slide 34: Specifying Coordinated Flows Step #2: Scenario Creation
A simple coherency scenario
  CPU core writes data to cacheable region
  A different core and a DMA read that same memory region
action simple_io_coherency {
cpu_c::write_data write;
cpu_c::copy_data_a copy;
dma_c::mem2mem_xfer_a xfer;
activity {
write with { out_buff.seg.cacheable == true; };
repeat (20) {
parallel {
copy with { core.instance_id != write.core.instance_id; };
xfer;
}
}
bind write.out_buff {copy.src_buff, dma_xfer.src_buff};
}
};
write_data_a
core
databuf
size addr
tag
cacheable
copy_data_a
core
m2m_xfer_a
DMA
Actions can be realized with true RTL CPUs / device, or with testbench bus transactors

## Slide 35: Layering System Power Concern
Two power domains A, and B
  Each power can be in mode S0 (active), S1 S2 (sleep modes)
Subsystem operations depend on respective domain active state
TB
Domain A
Domain B
UART
DDR MEM
DMAC
CPU
Graphics
UART
VIP
Crypto
Should reuse base model of behaviors and scenarios as is!

## Slide 36: Defining Power Logic Step #1: Modeling
enum power_state_e {S0, S1, S2};
state power_state_s {
rand power_state_e dmn_A, dmn_B;
constraint initial -> { dmn_A == S0 ; dmn_B == S0 ; }
};
component power_ctrl_c {
pool power_state_s sys_pwr_statevar;
action change_power_state {
input power_state_s prev;
output power_state_s next;
};
};
State object representing aggregate system power state
enum attribute for each domain
Both domains start out active
extend pss_top {
power_ctrl_c power_ctrl;
bind power_ctrl.sys_pwr_statevar *;
};
Power transition action reads the previous power state and establishes a new state
State variable is bound to actions' inputs/outputs by state type

## Slide 37: Introducing Power Dependencies
extend graphics_c::decode {
input power_state_s curr_power_state;
constraint curr_power_state.dmn_B == S0;
};
extend crypto_c::encrypt{
input power_state_s curr_power_state;
constraint curr_power_state.dmn_A == S0;
};
Input state with a precondition
Dependencies layered on top of existing action definitions in a non-intrusive way
change_pwr
pwr_state
dmn_A=S0
dmn_B=S0
pwr_state
dmn_A=S0
dmn_B=S2
encrypt
pwr_state
dmn_A=S0
dmn_B=S0
change_pwr
action encrypt_after_low_A {
activity {
do change_power_state with {
next.dmn_A != S0;
};
do encrypt;
};
};
Tool must infer additional action due to action precondition
PSS also supports overrides of types and instances

## Slide 38: Exercising Power Scenarios Step #2: Scenario Creation
change_pwr
change_pwr
pwr_state
dmn_A=S0
dmn_B=S0
pwr_state
dmn_A=S2
dmn_B=S0
pwr_state
dmn_A=S0
dmn_B=S1
copy
decode
encrypt
decode
copy
encrypt
action rand_traffic {
activity {
select {
do cpu_c::copy;
do crypto_c::encrypt;
do graphics_c::decode;
}
}
};
action phased_pwr_traffic {
activity {
repeat (2) {
do change_power_state;
do rand_traffic;
};
};
};
A PSS compliance tool analyzes the entire scenario and trims the scenario space

## Slide 39: Building system-level scenarios summary
PSS DNA is built for portability and reuse
  Applicable both for bottom-up and top-down reuse
  Can reuse both the model and scenarios intent
PSS Solving capabilities allows automation of system concerns
  Take randomization and constraint-solving to the next level
We gathered a set of usage examples to demonstrate these capabilities
  The examples will be part of the PSS release

## Slide 40: Portable Stimulus IN C++11 (and semantic Equivalence to DSL)
Adnan Hamid, Breker Verification Systems

## Slide 41: The UART Component in DSL
Step 1: Identify Behaviors
Step 2: Identify Data Flow
Step 3: Where do Actions Execute?
Step 4: What System Resources are required?
Data
UART
MEM
Command
DMAC
component uart_c {
resource uart_r {…};
pool [1] uart_r uart_p;
bind uart_p {*};
action read_in_a {
output data_str data;
lock uart_r u_busy;
};
action write_out_a {
input data_str data;
lock uart_r u_busy;
};
}
data_str

## Slide 42: UART Component in C++
Step 1: Identify Behaviors
Step 2: Identify Data Flow
Step 3: Where do Actions Execute?
Step 4: What System Resources are required?
Data
UART
MEM
Command
DMAC
class uart_c :public component{
PSS_CTOR(uart_c, component);
class uart_r :public resource{…};
pool<uart_r> uart_p {"uart_p",1};
bind b {uart_p};
class read_in_a :public action {
PSS_CTOR(read_in_a, action);
output<data_str> data {"data"};
lock<uart_r> u_busy{"u_busy"};
};
type_decl<read_in_a> ri_t;
class write_out_a :public action{
PSS_CTOR(write_out_a, action);
input<data_str> data {"data"};
lock<uart_r> u_busy{"u_busy"};
};
type_decl<write_out_a> wo_t;
};
data_str

## Slide 43: DMAC Component in DSL
Step 1: Identify Behaviors
Step 2: Identify Data Flow
Step 3: Where do Actions Execute?
Step 4: What System Resources are required?
Data
UART
MEM
Command
DMAC
component dma_c {
resource chan_r {…};
pool [1] chan_r chan_p;
bind chan_p {*};
action u2m_a {
input data_str src_data;
output mem_b dst_data;
lock chan_r chan;
};
action m2u_a {
input mem_b src_data;
output data_str dst_data;
lock chan_r chan;
};
action m2m_a {… };
}
data_str
mem_b

## Slide 44: The Steps to Creating a Portable Stimulus Model
Step 1: Identify Behaviors
Step 2: Identify Data Flow
Step 3: Where do Actions Execute?
Step 4: What System Resources are required?
Data
UART
MEM
Command
DMAC
class dma_c : public component {
class chan_r :public resource{…};
pool<chan_r> chan_p{"chan_p",1};
bind b {chan_p};
class u2m_a : public action {
input<data_str> src_data{"src_data"};
output<mem_b> dst_data{"dst_data"};
lock<chan_r> chan{"chan"};
};
class m2u_a : public action {
input<mem_b> src_data{"src_data"};
output<data_str> dst_data{"dst_data"};
lock<chan_r> chan{"chan"};
};
class m2m_a : public action {… };
};
data_str
mem_b

## Slide 45: Data Structures in DSL
Portable Stimulus only cares about the structure of data
Data type defines scheduling constraints
  buffer = sequential
  stream = parallel
Data
UART
MEM
Command
DMAC
struct data_seg_s { rand int[4..1024] size; rand bit[63:0] addr; };
buffer mem_b : data_seg_s {
};
enum data_dir_e {in, out};
stream data_str : data_seg_s { rand data_dir_e dir; rand int[1..2] stop_bits; };
data_str
mem_b

## Slide 46: Data Structures in C++
Portable Stimulus only cares about the structure of data
Data type defines scheduling constraints
  buffer = sequential
  stream = parallel
Data
UART
MEM
Command
DMAC
data_str
mem_b
class data_seg_s : public structure {
rand_attr<int> size {"size",
range<int>(4,1024) };
rand_attr<bit> addr {"addr",
width(63,0) };
};
class mem_b : public data_seg_s,
public buffer {};
class data_dir_e : public enumeration {
PSS_ENUM(data_dir_e, enumeration, in, out);
};
class data_str : public data_seg_s,
public stream {
rand_attr<data_dir_e> dir {"dir"};
rand_attr<int> stop_bits {"stop_bits",
range<int>(1,2) };
};

## Slide 47: Top-Level Model in DSL
component pss_top {
uart_c uart0;
dma_c dma0;
pool data_str stream_p;
bind stream_p {*};
pool mem_b mem_p;
bind mem_p {*};
action loopback_test {
uart_c::read_in_a rd_i;
uart_c::write_out_a wr_o;
activity {
rd_i;
wr_o;
}
}
}
u2m
rd_i
d_str
m2u
wr_o
d_str
memb
m2m
data
memb

## Slide 48: Top-Level Model in C++
class pss_top : public component {
uart_c uart0 {"uart0"};
dma_c dma0 {"dma0"};
pool<data_str> stream_p {"stream_p"};
bind b1 {stream_p};
pool<mem_b> mem_p{"mem_p"};
bind b2 {mem_p};
class loopback_test : public action {
action_handle<uart_c::read_in_a> rd_i {"rd_i"};
action_handle<uart_c::write_out_a> wr_o {"wr_o"};
activity a {
rd_i,
wr_o
};
};
};
u2m
rd_i
d_str
m2u
wr_o
d_str
memb
m2m
data
memb

## Slide 49: Generating Tests from Portable Stimulus
Adnan Hamid, Breker Verification Systems

## Slide 50: Consider Two Deployment Models
AXI
VIP
UART
DDR MEM
DMAC
UART
VIP
AXI
VIP
PSS Model
PSS Tool
UVM
Sequences
TB
AXI
VIP
UART
DDR MEM
DMAC
UART
VIP
CPU
PSS Model
PSS Tool
UVM
Sequences
C-test
Sync
UVM Testbench
SoC Testbench

## Slide 51: Exec Block Types
…
Specify mapping of PSS entities to their implementation
pre_solve
constraint solving
post_solve
body
pre_solve
constraint solving
post_solve
body
header
declaration
run_start
run_end
#include <stdint.h>
void declared_func() {
…
}
void test_main() {
do_run_start();
fork_threads();
do_run_end();
}
void thread0() {
…
// step N
do_body();
…
};
void thread1() {
…
}
file
gcc –c test.c –DBARE_METAL
test.c
test.sh
Could be multiple threads on one core,
or threads running on different cores
Could be SV
or other language

## Slide 52: Three Strategies for Implementing Exec Blocks
Target Template: text templates for code generation
Import Function: import and call external procedures/functions, assign to non random attributes
Hardware/Software Interface: abstracted operations for registers, memory and interrupts

## Slide 53: Target Template
AXI
VIP
UART
DDR MEM
DMAC
UART
VIP
AXI
VIP
TB
AXI
VIP
UART
DDR MEM
DMAC
UART
VIP
CPU
class uvm_test1 extends uvm_test_base;
virtual task body();
// …
init_uart_rx(1);
gen_uart_traffic(1, 128);
// …
init_uart_rx(2);
gen_uart_traffic(2, 27);
endtask
endclass
action read_in_a {
output data_str data;
lock uart_r u_busy;
constraint data.dir == in;
}
action read_in_a {
output data_str data;
lock uart_r u_busy;
constraint data.dir == in;
exec body SV = """
init_uart_rx( {{data.stop_bits}} );
gen_uart_traffic( {{data.stop_bits}}, {{data.size}} );
"""
}
}
int main(int argc, char **argv) {
// …
init_uart_rx(1);
gen_uart_traffic(1, 128);
// …
init_uart_rx(2);
gen_uart_traffic(2, 27);
return 0;
}
action read_in_a {
output data_str data;
lock uart_r u_busy;
constraint data.dir == in;
exec body C = """ init_uart_rx( {{data.stop_bits}} ); gen_uart_traffic( {{data.stop_bits}}, {{data.size}} ); """ }
}
"Moustache" notation to refer to PSS fields

## Slide 54: Import Function
AXI
VIP
UART
DDR MEM
DMAC
UART
VIP
AXI
VIP
TB
AXI
VIP
UART
DDR MEM
DMAC
UART
VIP
CPU
action read_in_a {
output data_str data;
lock uart_r u_busy;
constraint data.dir == in;
}
import void init_uart_rx(bit[1:0] stop_bits);
import void gen_uart_traffic(bit[1:0] stop_bits, int sz);
action read_in_a {
output data_str data;
lock uart_r u_busy;
constraint data.dir == in;
}
import void init_uart_rx(bit[1:0] stop_bits);
import void gen_uart_traffic(bit[1:0] stop_bits, int sz);
action read_in_a {
output data_str data;
lock uart_r u_busy;
constraint data.dir == in;
exec body {
init_uart_rx( data.stop_bits );
gen_uart_traffic( data.stop_bits , data.size );
}
}
class uvm_test1 extends uvm_test_base;
virtual task body();
// …
init_uart_rx(1);
gen_uart_traffic(1, 128);
// …
init_uart_rx(2);
gen_uart_traffic(2, 27);
endtask
endclass
int main(int argc, char **argv) {
// …
init_uart_rx(1);
gen_uart_traffic(1, 128);
// …
init_uart_rx(2);
gen_uart_traffic(2, 27);
return 0;
}

## Slide 55: Hardware/Software Interface Layer
TB
AXI
VIP
UART
DDR MEM
DMAC
UART
VIP
AXI
VIP
TB
AXI
VIP
UART
DDR MEM
DMAC
UART
VIP
CPU
class uvm_test1 extends uvm_test_base;
virtual task body();
// …
uart_regs.lcr.stop_bits = 1;
gen_uart_traffic(1, 128);
// …
uart_regs.lcr.stop_bits = 2;
gen_uart_traffic(2, 27);
endtask
endclass
int main(int argc, char **argv) {
// …
write_reg(UART_LCR, 1 << 2);
gen_uart_traffic(1, 128);
// …
write_reg(UART_LCR, 2 << 2);
gen_uart_traffic(2, 27);
return 0;
}
import void gen_uart_traffic(bit[1:0] stop_bits, int sz);
action read_in_a {
output data_str data;
lock uart_r u_busy;
constraint data.dir == in;
}
import void gen_uart_traffic(bit[1:0] stop_bits, int sz);
action read_in_a {
output data_str data;
lock uart_r u_busy;
constraint data.dir == in;
Uart_regs uart_regs;
}
import void gen_uart_traffic(bit[1:0] stop_bits, int sz);
action read_in_a {
output data_str data;
lock uart_r u_busy;
constraint data.dir == in;
Uart_regs uart_regs;
exec body {
uart_regs.lcr.stop_bits = data.stop_bits;
gen_uart_traffic( data.stop_bits , data.size );
}
}

## Slide 56: The Hardware/Software Interface Library
Karthick Gururaj, Vayavya Labs

## Slide 57: What is HSI?
Hardware/Software Interface layer is
  …an abstraction responsible for device management
    Device initialization, operations such as configure, transmit/receive
    Registration of device capabilities
  …set of constructs for capturing the Hardware aspects required to implement the abstraction
    Programming registers, setting up descriptor chains, interrupt properties and handling, …
    Capture all programming sequences
  …to summarize: construct the programmer’s view of a device agnostic to the underlying verification environment

## Slide 58: What HSI Enables
DMAC (DUT)
Test bench
(in SV)
RTL Simulation
DMAC (DUT)
Test cases
(in C, on host)
FPGA, w/ external PCIe master
DMAC (DUT)
Test cases
(in C, on target)
FPGA, w/ embedded core
DMAC (DUT)
Test cases
(in C, on host)
Accelerated simulation with Emulator
Driver
(in SV)
Driver
(in C, on host)
Driver
(in C, on host)
Driver
(in C, on target)
HSI Spec
(Test realization)
Stimulus Spec
(Test intent)
Test Intent is portable… but test realization environment specific?
HSI ensures Portability of test realization across Environments

## Slide 59: What HSI Enables
UART A
MEM
DMAC A
Test cases
Test cases
Test scenarios
UART B
MEM
DMAC B
Driver for DMAC-A
HSI Spec for DMAC-A
Driver for UART-A
HSI Spec for UART-A
Driver for DMAC-B
HSI Spec for DMAC-B
Driver for UART-B
HSI Spec for UART-B
Enables Portability of Scenarios across Devices/SoCs

## Slide 60: HW/SW Interface Spec Elements
Registers
FIFOs
Virtual registers
Descriptor management
Interrupt management
Sequences
Device capabilities

## Slide 61: Test Realization Using HSI
class dma_src : public pss::reg
{
public:
dma_src(/* ... */) : pss::reg (
description("Source address")
, offset(0x0)
, width(32)
, access(pss::PSS_ACCESS_RW)
, reset(0x0))
{ }
};
class dma_dst : public pss::reg
{
/* ... */
};
class chan_regs : public pss::reg_group
{
public:
dma_src src{"src"};
dma_dst dst{"dst"};
/* Other registers */
};
class dmac_regs : public pss::reg_group
{
public:
pss::vector<chan_regs> channel{"channel", 8};
/* Other registers */
};
class dmac_interrupts : public pss::intr_line
{
public:
pss::intr_event xfer_done{"xfer_done"};
/* ... */
};
class dmac : public pss::hsi
{
public:
dmac(/* ... */) { }
dmac_regs regs;
dmac_interrupts intr;
void mem2mem_xfer(dma_xfer_request &req)
{
regs.channel[req.rc].src = req.src_data.address();
regs.channel[req.rc].dst = req.dst_data.address();
regs.channel[req.rc].size = req.src_data.size();
regs.channel[req.rc].ctrl.src_incr = FIXED;
regs.channel[req.rc].ctrl.dst_incr = INCR;
regs.intr_enable.xfer_done = 1;
regs.channel[req.rc].enable = 1;
wait(intr.xfer_done);
}
};
Registers
Register Groups
Interrupts
Sequences
All elements of HSI specification, including sequences, captured in C++
HSI specification will integrate with test intent (in PSS-C++ or DSL)
From HSI specification, driver APIs for desired environment/platform and language (C, SystemVerilog, etc) can be generated
HSI specification currently under discussion in the WG, expect updates in upcoming revisions

## Slide 62: Coverage in Portable Stimulus
Srivatsa Vasudevan, Synopsys

## Slide 63: Portable Stimulus Coverage Opportunity & Challenge
Examples of system level coverage:
  Connectivity and addressability testing
  Power state sequencing
  Resource utilization - Did all internal memories get used by DMA tests?
==
Introduction of random => Need coverage to confirm usefulness
Portability challenge – collecting coverage in non-simulation environments
  Lack of visibility in HW-based platforms makes traditional coverage collection difficult
Formalization of system level scenarios and models
Ability to formally describe coverage of the legal scenarios and attributes

## Slide 64: Types of Coverage in Portable Stimulus
Action Coverage
  Were all (or a specified subset of) defined actions executed?
Scenario (Action Sequence) Coverage
  What legal sequences of actions were exercised? Aka “control path coverage”
Datapath Coverage
  Were all legal sources and sinks for an action sequence datapath (input/output) covered?
Value Coverage
  Think covergroups for attributes (config values, state values, … )
Resource Coverage
  Any resources added to a resource pool that went unused?
Crosses of any of the above types

## Slide 65: Defining Scenario (Action Sequence) Coverage
Scenarios are all legal behavior defined between entry and exit points
  Choices are made by the tool between these points
      e.g. alternative actions, resource usage, data source
If we can enumerate the choices, we can measure coverage of them
  In theory a tool could also target this coverage
      i.e. make choices based on what has/hasn’t been covered
Warning: with great power comes great responsibility
  Be careful of the number of choices between your entry and exit points
  Don’t try to target a coverage with more choices than atoms in the universe
Notes: Note: Spiderman is very apropos, not just because of the quote, but because, well “action sequence”…

## Slide 66: Monitoring Coverage
Stimulus monitoring
  Generation time tool can output what it generated/scheduled
    As long as test “passes”, the coverage data is valid
Runtime State monitoring
  Requires generation of monitoring code
    May be C/C++ code running on target cpu
        –e.g. data sent out “trickbox” mechanism
    May be “off-chip” monitoring via test ports
      or other communication ports
B-





Notes: Remember the Portability Challenge of monitoring coverage on non-simulation platforms??

## Slide 67: Simple Example: UART
Data
UART
MEM
Command
DMAC
stream data_stream_s {
rand int size;
rand dir_enum direction;
rand bit[1:0] inside [1..3] stop_bits;
}
buffer data_buff_b {
rand int size;
}
action u2m_xfer {
input data_stream_s src;
output data_buff_b dst;
}
DMA pkt stream into mem buffer
action read_in_a {
output data_stream_s data;
};
Generate pkt stream
action write_out_a {
input data_stream_s data;
coverspec {
size_cp : coverpoint data.size {
bins size_bins [1..20]:1;
}
};
Notes: action data_in sends a pkt_stream into the data port.
action setup sets the uart in tx(1)/rx(0) mode, configures dmac with src address, dest address, and two flags indicating whether src/dest address increases or not. If uart is src/dest, address does not increment. If mem is src/dest, address does increment. If uart is transmitting, command sets the number of stop bits.
dma_d2m action takes a stream input, so it runs in parallel with data_in, uart in receive mode, data concurrently dma'd into mem via pkt_buf output. Will add dma_channel resource later
dma_m2d action takes a memory input, so it runs in parallel with data_out, uart in transmit mode, data concurrently dma'd into uart via pkt_buf input. Will add dma_channel resource later

## Slide 68: conclusion
Bishnupriya Bhattacharya, Cadence

## Slide 69: We Hope You Learned…
Portable stimulus is a high-value solution for many real problems we have today – even within a single platform
Portable stimulus can stretch productivity and quality across platforms, users, integrations, and configurations
Portable Stimulus Standard is a serious and timely industry effort under Accellera (over 15 companies involved)
How this standard offers unique concepts and constructs (components, actions, flow objects and resources) to build powerful scenarios that map with flexibility to target platforms.

## Slide 70: We Hope You Will…
Participate in shaping this promising standard with your suggestions, use cases and requirements through:
  your company’s Accellera representation
  EDA vendor voicing your thoughts
  reading the Early Adopter spec: http://www.accellera.org/downloads/drafts-review
  providing feedback on Accellera Portable Stimulus Forum: http://forums.accellera.org/forum/40-portable-stimulus-discussion/
  contacting any of the speakers or PSWG officers
Be an agent of change
  Rethink verification and validation efficiency for your team and consumers
  Cross the aisle and communicate with peers in other platforms to accomplish more reuse with portable stimulus

## Slide 71: We Thank…
Accellera and DvCon India 2017 for offering PSWG the opportunity and real estate to deliver this tutorial to the community
All speakers who spent several hours and weeks preparing and improving this tutorial
All PSWG members for their feedback to improve this tutorial’s message and content