## Slide 1: Choice is yours : Either struggle to tame ‘X’ in the wilderness of multimillion gates and nets, OR Take it for a walk in the RTL park
Nitin Jaiswal , Harsh Garg , Mayank Bindal

## Slide 2: Blood-Shed by the Beast

## Slide 3: Agenda
X-optimism – The Beast
X-prop – Lets tame it
Freescale case studies – Taming the creature
X-bloodbath leads to
Conclusion

## Slide 4: How does he manage to escape RTL and grow into a “BEAST” ?

## Slide 5: X-optimism at RTL due to Verilog Semantics – Unclean edge
The direction of the change towards the value 1 is posedge and towards the value 0 is negedge, i.e.
  — A posedge shall be detected on the transition from 0 to x, z, or 1, and from x or z to 1
  — A negedge shall be detected on the transition from 1 to x, z, or 0, and from x or z to 0
always @ (posedge clk)
q<=d;
clk
d
q
1’b1
Is this behaviour realistic ?

## Slide 6: X-optimism at RTL due to Verilog Semantics – IF statement
If control expression of “IF” statement evaluates to true, then first statement shall be executed. But if it evaluates to false (value is 0 or x or z), then the else statement shall be executed.
if( cond )
Y = a;
else
Y = b;
a
b
cond
y
cond | a | b | RTL | GLS | On Silicon
X | 0 | 0 | 0 | 0 | 0
X | 0 | 1 | 1 | X | X
X | 1 | 0 | 0 | X | X
X | 1 | 1 | 1 | X | 1
Achieved by Xprop at RTL stage itself

## Slide 7: Introduction to X-prop
VCS has introduced improved semantics for handling “X” value in RTL simulations under X-propagation technology where it,
Considers effect of both 0 and 1 for all possible assignments controlled by an X and creates new pseudo-variables
At the end, merges the pseudo-variables using “merge mode” and assigns to the original (destination) variable(s)
  tmerge : Yields X when all values are different (like ternary op)
  xmerge : Yields X always (unconditional)
if( cond )
a = 0;
else
a = 1;
a1 = 0;
a2 = 1;
Rename
a = merge(a1, a2);
Merge & Assign

## Slide 8: Taming the creature in Freescale Designs

## Slide 9: Corrupting the clock you want to be sampled - If statement
POR Sampling Logic
cfg_eng_use_p
diff_sysclk_b
sysclk
sel0
if (sel0)
begin
out = sysclk;
end
else
begin
out = diff_sysclk_b;
end
// single_clk_selection
1
Normal Simulations
Xprop Simulation

## Slide 10: Normal VCS Behavior
Select line X
Valid output clock despite X at slect line

## Slide 11: Xprop behavior
Select line X
Xprop on output clock due to X on select line
Xprop on downstream logic and fdbk path due to X on clock
Xprop on downstream logic and fdbk path due to X on clock

## Slide 12: Small delays can corrupt big designs – Unclean edge
int_ind_pad
jtag_upd_data
ipp_ibe_b
ibe_pwrseq
pad_int_in
1 -> 0
0 -> 1
count

## Slide 13: Xprop – The big picture
X propagating due to delay of the buffers.

## Slide 14: Security lapse – If statement
Core
Hreset_b
IP Converter
Datapath
System Fabric
Security block
Security block
Individual Reset from battery
DANGER !!! Security breached

## Slide 15: Problematic Code
For normal simulations , ips_rwb never latches X.

## Slide 16: Miss in normal simulations
Ips_rwb is not getting corrupted inspite of ipm_rwb being corrupt

## Slide 17: Xprop catches it
Ips_rwb getting corrupted

## Slide 19: X-bloodbath at GLS leads to
Loss of precious after logic freeze time
  Painful debug in a mesh of multi million gates .
  Localization of ‘X’ becomes difficult
  If confirmed bug , schedule slip on charts
Confidence on design
  Only 1-5% of testsuite run on GLS
Stabilizing testbench is a daunting task.
  Most of the time , issue is found in testbench than design
Analyzing and implementing ECO becomes risky

## Slide 20: Conclusion
Although initial bring-up can be challenging, X-Prop presents an effective solution to the problem of X-optimism in RTL simulations
Capable of reducing testbench bring-up time and number of iterations of gate level simulations.
  Reduced bring up time in IDC Digital Networking Freescale projects by more than 50 % .
Normal RTL/GL Simulations may fail to catch various functional issues.
We were able to catch various design/testbench issues in simulation by selectively enabling XPROP on various Freescale designs.
No critical logical ECOs after deployment of Xprop in Freescale IDC Digital Networking designs.
Enabling Xprop increases simulation time by 15-20% (effective ROI .. !)

## Slide 21: Questions