## Slide 1: Compliance driven Integrated circuit development based on ISO26262
Haridas Vilakathara
Manikantan panchapakesan
NXP Semiconductors, Bangalore

## Slide 2: Outline
Functional safety basic concepts (ISO26262 view)
  IC failure and their causes
Management of random faults
  Safety architecture
  Safety analysis
Management of systematic faults
  Product creation process
  Compliance driven development process
  Safety management after release to production

## Slide 3: Functional safety basic concepts
IEC 61508/ISO 26262 safety concept
  It is impossible to develop a zero error (bug free) system
    Specification, implementation or realization errors
    Random hardware failure may occur due to
      Reasonably foreseeable operational errors,
      Reasonably foreseeable misuse.
  It is is possible to build a system with acceptable failure rate
    Acceptable failure rates vary per application
    Classified by automotive safety integrity levels (ASIL) &
    frequency and severity of functional failures
  If a failure occurs, the system needs to be transferred into a safe state
    Failure event should not lead to unacceptable risk
      System must detect all faults that could lead to a hazardous event
      The fault reaction time to achieve safe state must be short enough to avoid any hazardous event
    Safe state can be defined as
      Fail safe or fail operational
        Depends on application

## Slide 4: IC failure and their causes
Random failures
  Due to
    Random defects inherent to Semiconductor process
    Environmental conditions
    Usage & handling
Systematic failures
  Bugs introduced during, specification, design, development
  n detected bugs during verification cycle
  Due to not following best practices and methodologies for product development
Safety architecture for detection and management of random failure (manage fault)
Compliance driven process development and continues improvement (avoid fault)

## Slide 5: Outline
Functional safety basic concepts (ISO26262 view)
  IC failure and their causes
Management of random faults
  Safety architecture
  Safety analysis
Management of systematic faults
  Product creation process
  Compliance driven development process
  Safety management after release to production

## Slide 6: Functional safety architecture
Based on fault reaction time & safety strategy
  How much a system can tolerate the IC functional failure
  Fail safe, fail operational etc.
    Based on application profile
    Type of IC (ASIC, MCU, SoC etc)
Safety architecture to detect fault, diagnose fault and to act on fault within reasonable time

## Slide 7: Application consideration
IC Developed specifically for a customer (in context)
  Clear specification from customer including safety requirements
    Handle ISO26262 requirements through a development interface agreement (DIA)
IC Developed for more than one applications (safety element out of context)
  Assumptions are made on application profile
    system level design, safety concept, and requirements based on the product application scenarios
  Validate the assumptions through “proven in use” kind of arguments

## Slide 8: Safety architecture (key requirements)
To detect fault
  Shall incorporate sufficient failure detection & diagnostic features
    To detect environmental conditions
      Temp sensor, voltage sensor etc.
    To detect operational anomalies
      Memory errors, watchdog features etc.
    Safe island
      Protected heavily to guarantee reliable operations under extreme conditions
        Provide diagnostic information back to system within FTTI
Process fault
  Logic to isolate fault and to assess the severity of fault
Act on fault
  Depends on application requirements
    Fully operational (redundancy) Fail safe ( safe mode of operation), fail operational (reduced functionality)
Validate fault
  Its hall be possible to fully verify & validate safety requirements
    Fault injection testing

## Slide 9: Outline
Functional safety basic concepts (ISO26262 view)
  IC failure and their causes
Management of random faults
  Safety architecture
  Safety analysis
Management of systematic faults
  Product creation process
  Compliance driven development process
  Safety management after release to production

## Slide 10: Qualitative safety analysis (FMEA)
FMEA results
  Potential IC failure modes and causes.
  Critical characteristics of the IC
    Help in design priority setting
    Recommended actions for reducing severity,
    Eliminate or reduce the causes of IC failure modes
    Improve failure detection
  Feedback of design changes to the design community

## Slide 11: Quantitative safety analysis (FMEDA)
Based on Diagnostics coverage
  Ratio of detectable failures probability against all failure probability
  Diagnostic or self checking elements modelled
    Complete Failure Mode Coverage .
    All failure modes of all components must be in the model
Failure Mode Classifications in FMEDA
  Safe or Dangerous: Failure modes are classified as Safe or Dangerous
  Detectable : Failure modes are given the attribute DETECTABLE or UNDETECTABLE
  Four attributes to Failure Modes: Safe Detected(SD), Safe Undetected(SU), Dangerous Detected(DD), Dangerous Undetected(DU)
Goal : Statistical Safety: based on Safety Integrity Level (ASIL)

## Slide 12: Combined Safety analysis
D-FMEA inputs (function criticality) are used as scaling factor in FMEDA
Technology
FITs
DFMEA
Functions
Hardware
Blocks failure rate
1
2
Map to IC
mission profile
Life test +
Field data
SPFM / LFM
FMEDA
Diagnostics Coverage
(safety self-monitoring
to detect deviations)
FMEA inputs used
as a scaling factor
Operating Conditions
Failure modes and fault-sensitivity from Design-FMEA.

## Slide 13: Outline
Functional safety basic concepts (ISO26262 view)
  IC failure and their causes
Management of random faults
  Safety architecture
  Safety analysis
Management of systematic faults
  Product creation process
  Compliance driven development process
  Safety management after release to production

## Slide 14: Safe IC development process
Product creation process
  Based on a gated product Creation and Management process
Compliance driven development process
  V model with safety extensions
Safety analysis
  Combined qualitative (FMEA) and quantitative (FMEDA)
  fault injection testing for validation of diagnostic coverage
Safety management after release to production
  Managed through a separate department (test and product engineering)

## Slide 15: Outline
Functional safety basic concepts (ISO26262 view)
  IC failure and their causes
Management of random faults
  Safety architecture
  Safety analysis
Management of systematic faults
  Product creation process
  Compliance driven development process
  Safety management after release to production

## Slide 16: Product creation and management
Divide the project into manageable phases and sub phases
  Thorough gate review process
    Product and process compliance at every gate review/audit

## Slide 17: Outline
Functional safety basic concepts (ISO26262 view)
  IC failure and their causes
Management of random faults
  Safety architecture
  Safety analysis
Management of systematic faults
  Product creation process
  Compliance driven development process
  Safety management after release to production

## Slide 18: Safety lifecycle on top of “V” model
s

## Slide 19: Safety life cycle extension
Project plan | Safety extension to project plan | Proof of safety
Project planning Project organization Development process | Safety life cycle activities ( Safety org, Safety manager, safety plan, tracking & assessment) Safety team organization & management | Safety case and Safety arguments
Requirement management |  | 
Requirement capture & requirement engineering, FMEA(qualitative) | Derive Safety goals, safety requirements, safety concept, and safety requirements and methods. FMEA, FMEDA & FTA ( quantitative) | Safety goals, Safety concept Safety requirements with proof of traceability FMECA/FMEDA/FTA reports Safety manual
Verification & validation |  | 
Product assessments V&V Reviews/audit | Safety V&V, Safety assessment, Tool qualification | Safety V&V reports Safety assessment reports Validation reports (proven in use argument)
Configuration management |  | 
Work products Baseline management Change management | Safety case as CI Impact analysis on safety functions(for CR) | Baseline for safety case & safety case reports Traceability and impact analysis report liked to requirement management
QM & process assurance |  | 
Quality manual Template/guidelines, Checklist/examples | Safety culture, Project level tailoring, Continuous improvements Reviewing and tracking compliance with plans. Identifying and documenting deviations from plans. | Tool confidence report, Evidence on safety culture deployment, Project tailoring report. Qualification reports, Risk assessment reports, Periodic confirmation review reports

## Slide 20: Safety organization
Safety plan integrated into overall project plan
Safety extension to key process

## Slide 21: (Safe)Requirement management
DOORS based formal requirement management with bi directional traceability
  Formal process to track
    Customer requirements
    Allocated requirements from system
  All requirements can be tracked to a design, verification and validation item
  No design element in repository without an assigned requirement
  Any PR raised can be tracked to a corresponding requirement ID
  Impact on existing requirements can be identified for CR

## Slide 22: Requirement management tree

## Slide 23: Requirement Verification
Requirements Verification (product right)
  Checks consistency of the requirements specification artefacts and other development products (design, implementation, ...)
    Req->design->RTL/schematics-> netlist-> Back End ->GDS2
    Safety not compromised during design translation process
  Each requirements are associated with a verification item
Verification is performed throughout the entire safety lifecycle, by each specific party involved, for each of the major work products.
Compliance driven verification is the key

## Slide 24: Requirement validation
Requirements Validation (right product)
  Check IC requirements specification against customers goals and requirements
  Provides assurance that the hardware item derived requirements are correct and complete with respect to system requirements allocated to the hardware item
  Ensure that the highest level safety requirement, the safety goal, has been met and that they are correct
    The product is safe to use within the mission profile
Validation has a specific meaning against “safety element out of context”. Make sure that safety goals are met trough creation of “proven in use arguments”

## Slide 25: V&V work flow (safety extension)
Clear ownership on who does what within V&V organization

## Slide 26: Compliance driven Verification scope
Compliance driven verification
  Coverage: Link coverage item to requirements with evidence( 100% requirements coverage) In addition to other standard coverage metrics
  Test plan, test item, test results linked to DOORS to establish traceability
  Verification at every stage of data translation ( req-design-RTL-netlist-post layout)
Constraints driven
  Interface constraints(limit, boundary value etc.), rules, design constraints such as Boundary value analysis, negative testing, control flow (protocols), data flow (protocol), overflow, underflow
Design intent verification
  Intended operational environment and rules
  Temporal behavior to stimuli (protocol sequence, error recovery
Risk oriented
  Inputs from FMEA/FMECA
Fault injection testing
  Coverage for safety architecture components & diagnostic capabilities
Structural
  formal review, audit, code walkthrough

## Slide 27: Validation (safety extensions)
Check whether safety goal is met
  Customer driven or safety element out of context
  Confirmation check on safety goals, safety architecture against functional safety of the items at intended use case level
Use case validation
  Question/review safety goals from a use case perspective
  Compliance with governing standards and other regulatory requirements
    Interface standards, EMI/EMC etc.
Fault injection testing
  Validate safety architecture and diagnostic features
Evidences against all the above

## Slide 28: Verification & validation flow

## Slide 29: Requirement traceability
Both requirements and test items are in DOORS data base
Impact on verification items due to requirement changes are immediately notified
Easy to trace back a problem report back to the originating requirement
Automated reporting on V&V progress
Chart: Test Effort
| wk1122 | wk1123 | wk1124 | wk1125 | wk1126 | wk1127 | wk1128 | wk1129 | wk1130 | wk1131 | wk1132 | wk1133 | wk1134 | wk1135 | wk1136 | wk1137 | wk1138 | wk1139 | wk1140 | wk1141 | wk1142 | wk1143 | wk1144 | wk1145 | wk1146 | wk1147 | wk1148 | wk1149 | wk1150 | wk1151 | wk1152 | wk1201 | wk1202 | wk1203 | wk1204 | wk1205 | wk1206 | wk1207 | wk1208 | wk1209 | wk1210 | wk1211 | wk1212 | wk1213 | wk1214 | wk1215 | wk1216 | wk1217 | wk1218 | wk1219 | wk1220 | wk1221 | wk1222 | wk1223 | wk1224 | wk1225
items pass for Bronze | 0 | 0 | 0 | 0 | 0 | 2 | 9 | 9 | 9 | 110 | 110 | 110 | 110 | 110 | 114 | 114 | 58 | 58 | 58 | 58 | 58 | 58 | 58 | 60 | 62 | 100 | 107 | 107 | 117 | 117 | 117 | 117 | 95 | 96 | 98 | 101 | 90 | 90 | 112 | 112 | 112 | 114 | 116 | 116 | 118 | 118 | 118 | 118 | 118 | 118 | 118
items fail for Bronze | 0 | 0 | 0 | 0 | 0 | 10 | 29 | 29 | 29 | 25 | 25 | 25 | 25 | 25 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 16 | 16 | 22 | 23 | 16 | 16 | 6 | 6 | 6 | 6 | 10 | 19 | 15 | 14 | 19 | 19 | 4 | 2 | 2 | 2 | 2 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0
items pass for Silver | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 13 | 13 | 68 | 68 | 68 | 68 | 68 | 68 | 42 | 78 | 77 | 150 | 222 | 390 | 440 | 472 | 472 | 472 | 373 | 424 | 431 | 509 | 443 | 463 | 530 | 530 | 530 | 526 | 532 | 532 | 535 | 535 | 535 | 535 | 535 | 542 | 544
items fail for Silver | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 42 | 42 | 42 | 42 | 42 | 42 | 7 | 23 | 53 | 53 | 70 | 73 | 25 | 25 | 25 | 25 | 18 | 131 | 132 | 27 | 94 | 74 | 13 | 13 | 13 | 13 | 7 | 7 | 3 | 3 | 3 | 3 | 3 | 0 | 0
items pass for Gold | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 6 | 6 | 20 | 53 | 92 | 92 | 92 | 92 | 43 | 52 | 60 | 152 | 160 | 206 | 283 | 283 | 283 | 309 | 293 | 308 | 316 | 316 | 316 | 316 | 316 | 372 | 335
items fail for Gold | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 6 | 6 | 3 | 3 | 6 | 6 | 6 | 6 | 3 | 12 | 65 | 41 | 120 | 114 | 32 | 32 | 32 | 36 | 49 | 39 | 27 | 27 | 27 | 27 | 27 | 17 | 2
items pass for MRA | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3 | 3 | 6 | 6 | 6 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 42 | 57
items fail for MRA | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 6 | 6 | 0 | 0 | 0 | 3 | 3 | 3 | 0 | 0 | 0 | 0 | 0 | 12 | 0
target items MRA | 801 | 801 | 801 | 801 | 801 | 801 | 801 | 801 | 801 | 801 | 801 | 801 | 801 | 801 | 801 | 801 | 794 | 794 | 794 | 831 | 831 | 830 | 830 | 838 | 838 | 848 | 848 | 848 | 1125 | 1125 | 1125 | 1125 | 1071 | 1108 | 1110 | 1110 | 1109 | 1109 | 1130 | 1130 | 1130 | 1130 | 1130 | 1130 | 1114 | 1103 | 1103 | 1103 | 1103 | 1103 | 1115
target items Gold | 801 | 801 | 801 | 801 | 801 | 801 | 801 | 801 | 801 | 801 | 801 | 801 | 801 | 801 | 801 | 801 | 794 | 794 | 794 | 831 | 831 | 830 | 830 | 838 | 838 | 848 | 848 | 848 | 1119 | 1119 | 1119 | 1119 | 1065 | 1102 | 1069 | 1069 | 1065 | 1065 | 1086 | 1086 | 1086 | 1086 | 1086 | 1086 | 1070 | 1049 | 1049 | 1049 | 1049 | 1049 | 1049
target items Silver | 533 | 533 | 533 | 533 | 533 | 533 | 533 | 533 | 533 | 533 | 533 | 533 | 533 | 533 | 533 | 533 | 531 | 531 | 531 | 533 | 533 | 567 | 567 | 575 | 575 | 585 | 585 | 585 | 743 | 743 | 743 | 743 | 666 | 678 | 680 | 680 | 657 | 657 | 662 | 662 | 662 | 662 | 662 | 662 | 656 | 660 | 660 | 660 | 660 | 660 | 660
target items Bronze | 131 | 131 | 131 | 131 | 131 | 131 | 131 | 131 | 131 | 131 | 131 | 131 | 131 | 131 | 131 | 131 | 131 | 131 | 131 | 131 | 131 | 131 | 131 | 131 | 131 | 131 | 131 | 131 | 125 | 125 | 125 | 125 | 109 | 115 | 115 | 115 | 111 | 111 | 116 | 116 | 116 | 116 | 116 | 116 | 118 | 118 | 118 | 118 | 118 | 118 | 118

## Slide 30: Tool qualification
Why tool qualification
  IC design involves many translation process, and tool in general has the capacity to introduce error during various translation process
    e.g. RTL-> Synth netlist -> post layout
  Verification tools may fail to detect errors in the hardware items
Tool qualification makes sure that tool correctly functions (improve confidence in tool function)
The library components and different views used during the design translation process also need to be of mature quality and qualified one

## Slide 31: Tool qualification flow

## Slide 32: Configuration & Change management process
Configuration management plan aligned with ISO TS 16949, ISO9001
  Maintenance of safety case as a living argument to provide a mechanism to establish the interdependency between the elements of safely case
Change management
  Establish link between change management & problem reporting process and requirement management (through DOORS)
Safety representative in CCB
  Ascertain the impact on functional safety w.r.t change requests

## Slide 33: Quality management and process assurance
Process Gap analysis (safety)
Safety culture within organisation & project team
Process tailoring with respect to the project
Process assurance
  Design data base management
  Design assurance

## Slide 34: Process gap analysis

## Slide 35: Gap analysis
Requirement engineering | Demonstrate process for - Requirement capture - To establish requirement traceability
Process assurance | Reviewing and tracking compliance with plans. Identifying and documenting deviations from plans. Determining if transition criteria have been met between lifecycle stages.
Configuration management | Demonstrate supporting processes - Change Management - Management of Requirements - Configuration Management
Quality management | Quality manual update for safety life cycle process & methodologies Supporting process (check list, templates guide lines ) e.g. FMEA/FMEDA template & process
Safety culture | Evidence of management of Safety Life Cycle activities Organisation chart showing safety role Competence management (training & qualification program) Safety assessment

## Slide 36: Safety culture
Normal development process | Safety culture
Safety measures are not planned. No Specific budget for safety | Necessary measures are planned according to safety plan (planning, tracking, coordination). Safety plan is integrated into project plan (receivables, deliverables, and resources)
Risk analysis & tracking is done, but may not structured (updated on regular basis) | Structured risk analysis is a must at beginning of project, and is continuously updated with evidence
Typically an FMEA cycle is followed (qualitative analysis) | Both qualitative (FMEA) and quantitative (FMECA/FMEDA,FTA) analysis is a followed at beginning of a project and is continuously updated with evidence
Change request are accepted at any stage (primarily look only into schedule impact) | Change requests are analyzed and evaluated against functional safety and accepted only through a strict formal change management process ( four eye principle) and impact analysis
Safety assessment not a must | Safety assessment is a must and evidence preserved until end of life

## Slide 37: ISO 26262 tailoring for IC (HW only) project (example)
ISO26262 tailoring for Dolphin | Applicability | Remark
2 –Management of functional safety | Applicable | Based on functional safety plan
3 –Concept phase | Driven by customer inputs | 
4 –Product development at the system level | Mostly applicable | Primarily towards system validation
5–Product development at the hardware level | Applicable | Most of the diagnostic requirements are here
6–Product development at the software level | Limited (for IC do not contain a MCU) | Validate API (MCU) interface
7 –Production and operation | Applicable (IC test & production & engineering) | Big influence on FIT by Sem Con manufacturing process
8 –Supporting processes | Mostly applicable | 
9 –ASIL oriented and safety analysis | Based on customer inputs & application profile | Different use cases

## Slide 38: Design environment management
Focus on effort spend up front to prevent design problems due to design environment
Infrastructure review Scope
  Data base structure
  Development standards & flows
  CM, CR/PR system and tracking methodology
  Effective simulation analysis and regression systems
    E.g. Automation in simulation/synthesis log analysis.
  Communication between architects, design engineers, & verification engineers
    Documentation availability & traceability
Planned audit
  Collect the documentation maintained w.r.t database
    Check all the team members in the team get right information at right time
    Establish inks & traceability
  Audit on CR /PR tracking
    Defect density
    CR/PR flow
  CM audit

## Slide 39: Design assurance
Formal reviews & audits
  By external experts
    IP Vendor & IP quality checklist (IP reuse & IP intake strategy )
    Technology Library
    Process Reliability measures
  Project level
    Data base (CM, CR/PR, Documentation)
    Compliance check against FRS/Impl/Verification
    Verification strategy/methodology review
    Verification coverage review
    Explicit SoC constraints review
    Non functional requirement review (coverage)
    Layout review by a separate team
    Pin/PAD list

## Slide 40: Questions
Finalize slide set with questions slide