## Slide 1: Coverage Closure – Is it a “Game of Dice” or “Top 10 Tests” or “Automated Closure”?
Aditya Sharma, T. Nagasundaram,
M. Nitin Kumar, Nikhita Raj J

## Slide 2: Agenda
Conventional Coverage Closure : CRV
Smart Selection of Coverage Rich Tests : Test Ranking
Automated Coverage Closure : GBV
Summary & Conclusion

## Slide 3: Conventional Coverage Closure
“Calling-it-a-day” in a typical SoC verification project?
  approach is to use the coverage metrics available
Though not silver bullets (functional & assertion coverage), but are the most formidable
Now with the acknowledged coverage metrics, the process involves three phases:
─ Coverage definition
─ Coverage collection (running simulations)
─ Coverage analysis & closure (iterative)

## Slide 4: CRV ─ more of a “Game of Dice”
Hit & Try
Typical constraint random
generator has well known
redundancy built in
Coupon Collector’s Problem
Expected number of trails grows as Θ(nlog(n))

## Slide 5: Game of Dice - Samples
APB-SPI IP
  Number of Coverage Points or (State Space) : 192 (N)
  NUM_XACTNS needed for 100% Coverage ≥ N*ln(N)
  N*ln(N) : 1009
UVM SoC Reference Kit
  Number of Coverage Points or (State Space) : 2749 (N)
  NUM_XACTNS needed for 100% Coverage ≥ N*ln(N)
  N*ln(N) : 21769

## Slide 6: A typical UVM environment for a SoC looks as below:

## Slide 7: Smart selection of Coverage Rich Tests : Test Ranking
SoC verification comprises of several tests for single & multiple peripherals
Typical regression of these individual tests are run with different seeds to cover a good state-space
Now the question is how to arrive at a minimal sub-set to cover reasonable state-space automatically?

## Slide 8: Test Ranking
This is where a Test Ranking feature can be very useful!
The challenge is : Out of existing huge
set of tests (and seeds) identify the top
contributors!

## Slide 9: Test ranking in UVM
Most EDA tools support this feature today
We have used Aldec’s Riviera-PRO
Below are few screenshots from other vendor tools (for completion sake)
VCS
IUS

## Slide 10: Test Ranking Results : UVM SoC Reference Kit
UVM SoC Kit – Initial donation by Cadence
CVC ported to other tools, scripts, updated code
Freely available at www.accellera.org
TCL commands

## Slide 11: Test Ranking Results with Aldec

## Slide 12: Automated Coverage Closure : GBV
GBV enables capturing entire state space one-shot in a single graph
N vs. N*ln(N) advantage
Stimulus coverage goals
often correlate to existing
functional coverage goals
Hence facilitating faster
coverage closure

## Slide 13: APB-SPI Use Case : Cover Group
Closer look to covergroup depicts total 192 cross coverage bins

## Slide 14: GBV with TrekUVM
In this work we used Breker Verification System’s TrekUVM as a test generator & APB-SPI UVM verification environment as a case study
Automated Coverage Closure can be a reality with a model of state space driving a test generator to provide the needed UVM sequences
192 paths corresponding to 192 cross coverage bins for APB-SPI can be depicted in a single graph
Turn On Coverage Closure Mode
Automatically fill the holes & get 100% Coverage 

## Slide 15: Auto Coverage Mode OFF/ON

## Slide 16: NUM_XACTNS vs. FCOV : APB-SPI IP
Chart: 
| 1 | 100 | 192 | 1009
FCOV | 29 | 75 | 81 | 100

## Slide 17: Summary
CRV : Redundancy is inherent. Good at times, many a times too much redundancy. Leads to lot of manual coverage closure
Test Ranking : Helps identifying high value tests. No rescue from manual coverage closure
GBV : Eliminates redundancy totally while still preserving constraint randomness. Small effort to capture state-space as graph, fills coverage holes automatically.
  We used it in this case study for input stimulus only

## Slide 18: Conclusion
CRV is closely correlated to Coupon Collector Problem in probability theory
First 80% vs. Rest 20% - 80-20 rule
Coverage Closure above 80% solely via randomness is not feasible 
Lesser time to tapeout-s
Coverage closure via smart automation techniques can become the key differentiator technology

## Slide 19: Reference
Coupon collector’s problem: http://en.wikipedia.org/wiki/Coupon_collector’s_problem
Model Based Testing: https://en.wikipedia.org/wiki/Model-based_testing
Breker Verification Systems (http://www.brekersystems.com)
http://tinyurl.com/uvmsoc

## Slide 20: Questions…?

## Slide 21: The Coupon Collector’s Problem
N – total number of different coupons.
Xi – time to get the i-th coupon.
=
Only one coupon in a pack.
Target is to collect all coupons.
How many packs to be bought?