## Slide 1
DUT converts packets from one protocol to that of another using complex state tracking, ID management and transaction dependencies
DUT handles response, data re-ordering and management of data buffer
Master uses proprietary protocol for coherent accesses to the memory
DUT consists of ASIL-B, protection unit and performance monitor unit
Introduction
FPV Testbench Implementation
Proposed Methodology
RTL Bug1: Packet is getting dropped when design re-enters IDLE
Floating pulse method is used for data integrity checks:
A random packet is coloured at the input
On the output, checked the coloured packet
A mapping function was created which maps input to output
For ordering check we again used colouring:
Two different coloured packets were sent
Output order of the packets was noted and checked for re-ordering
Pulicharla Ravindrareddy, Lead Engineer, Senior
Chayan Pathak, Engineer, Senior
Venkatesh Chepuri, Engineer
Nitin Neralkar, Engineer, Principal/Manager
Formal Verification Accelerating Coherent Bridge IP Development and Fast Forward DV
RTL Bug 2: Wrong packet deallocated due to simultaneous deallocation
Conclusion
Removed Dozen plus block level sim DV effort
SEC - Clock gating verification, Auto formal checks, CSR and debug connectivity speeds up the verification
ASIL-B - ECC & parity feature verification closure using FV
FV complements simulation and catches critical corner case bugs early in DV cycle
Found 35 % RTL bugs and 10% SPEC bugs by FV of Total IP's bugs
Formal Verification left shifted verification closure by 4 Months
Formal Verification Accelerating Coherent Bridge IP Development and
Fast Forward DV
Packet transactions between Controller interface and FABRIC starts when the FSM is in RUN state
Packets are sent from Controller, stored in FIFO and the FIFO becomes full
Ready from the Fabric is not available yet and the packets from the FIFO are not fetched
Now the FSM goes to the IDLE state, and the FIFO write pointer gets reset which leads to loss of data
There are two deallocation interfaces – one for tracker A and one for B.
Only one tracker should deallocate in a cycle, hence both use the same ID.
In the scenario, FV triggered a simultaneous deallocation of:
    Transaction a - due to special opcode dropping data (Tracker A)
    Transaction b - due to data moving out (Tracker B)
Due to use of same ID for deallocation-transactions b and c are dropped (both ID 7)
Result:
    Incomplete transaction c is dropped
    Deallocation does not happen for transaction a
RUN State
RUN State
IDLE State
Full
Start
FSM
IDLE -> RUN
Data enters FIFO
FIFO Full
Ready from Fabric is not available
Ready
Valid
oupValid
FIFO location count is reset
Previous FIFO contents gets overwritten
Data enters FIFO
FSM
IDLE -> RUN
FSM
RUN -> IDLE
Input_valid
Input_data
output_valid
output_data
always_ff @(posedge Clk) begin
if (Reset) begin
pulse_reg <= 0;
end
else if (pulse) begin
pulse_reg <= 1; // When pulse is seen this signal
end // goes high & prevents further pulse
end
pulse_occurs_once : assume property (
@(posedge Clk) disable iff (Reset)
pulse_reg |-> !pulse);
DUT
Tracker A
a (ID 5)
c (ID 7)
Tracker B
b (ID 7)
Dealloc
DUT
Tracker A
5
Tracker B
Dealloc
DUT
1
2
3
2
1
3
PMU
DEBUG
ASIL Compliant
CSR
Link Layer
Translation Layer
(ID Table + Conversion)
Protection Unit
Controller IP
Fabric
Request dir a
data
response
Req dir b
data
response
data
response
Req dir b
Request dir a
response
data
Sourabh Bhattacharjee, Engineer, Staff
Piyush Upadhyay, Engineer, Staff
Madhusudhan Koothapaakkam, Engineer, Principal
Dozen plus subblock level formal verification
Following types of checks were done:
    Data integrity
    Data and response re-ordering
    Data progress
    Coherent protocol conversion
Formal Coverage
FVIP protocol compliance
IP level FPV
CSR verification
Connectivity Verification
Auto Formal Checks
Module level FPV
SEC - CG Verification
FV Methodology