## Slide 1: MDLL & Slave Delay Line performance analysis using novel delay modeling
Abhijith Kashyap, Avinash Shambu, Kalpesh Shah

## Slide 2
Introduction
Problem Definition
Existing approach and proposed solution
Case study using integrated MDLL + SDL setup
  Analysis
  Design refinement
Summary and Conclusions
Outline
Notes: Abstract or Outline for the presentation

## Slide 3: Introduction
Master Delay locked loop (MDLL)
  Continuously tracks changes in VT and provides a PTV compensated code
  Takes a reference clock and measures its period in terms of delay taps
Slave Delay Line (SDL)
  Instantiates 1 delay line
  SDL delays its input clock by the amount specified by the code from MDLL
CODE
UPDT
MDLL_CLK
SDL_CLK
SDL_CLK_DLY
MDLL
DL1
DL2
Slave Delay Line
DL

## Slide 4: Problem Definition
DLLs are PTV dependent and transient changes affect the behavior of the loop.
Need to model OCV and Supply Noise impact on delay elements in functional verification (RTL) of MDLL and Slave Delay Line (SDL)
Need to find corner cases not covered by traditional verification
  MDLL may update a wrong code to SDL
  MDLL entering a infinite loop condition, without further tracking and update

## Slide 5: Typical Model for verification
Traditional Delay Line modeling and Verification
  Each Delay Element with a fixed delay ‘tf’
    Every element in this model behaves identical (gives the same delay)
    ‘tf’ modeled as Verilog parameter and hence a constant
  MDLL will always give a fixed output code for a given input condition
    Using this model of delay line will not verify MDLL under OCV and Supply noise condition
CLK GEN
tf
tf
tf
tf
Phase
Detector
CLK_REF
CLK1
CLK2
CONTROL
UP
DOWN
Delay Tap
Select (Code)
LOCK
CODE
MDLL
UPDT
Delay Line

## Slide 6: Proposed Solution - Overview
Initial RTL and PD Database
With first cut architecture
Spice Characterization
DL being the critical block is characterized at different PTVs
Noise model based on Spice Data
Arrive at a Noise model which can be implemented in Verilog.
RTL Simulations and DB refinement
Silicon Ready DB
Based on Simulations, modify the Delay line / RTL to meet specification.
Silicon Data
Update Noise models
Final RTL
Final Database
Usage of noise components at multiple frequencies to analyze impact
Repeat from step 2 till required
Database with extensive verification is ready for Silicon
Analyze and correlate Silicon data with Spice characterization
Correlate with assumed noise models
To match the Silicon data as closely as possible
Simulate with new noise models
Minor changes to architecture depending on results
Production quality database

## Slide 7: New models for verification
Dynamic Delay Line Model
  Each Delay element modeled with a fixed delay component ‘tfn’ and a variable delay component ‘tv’
    With ‘tf1’ to ‘tfn’, delay variation (due to OCV) between individual elements is modeled
    With ‘tv’, delay variation due to noise is modeled
    ‘tfn’ & ‘tv’ modeled as Verilog real data type
CLK GEN
Phase
Detector
CLK_REF
CLK1
CLK2
CONTROL
UP
DOWN
Delay Tap
Select (Code)
LOCK
CODE
MDLL
UPDT
Delay Line
tv+tf1
tv+tfn-1
tv+tfn

## Slide 8: Modeling the Delay elements
Data from Spice Simulation of delay element used to set ‘tfn’
  Setup for a particular corner condition
  Run mismatch (Monte-Carlo) simulations
  For ever delay code (tap), delay difference between input and output of the delay line is tabulated
  Average, Min and Max values obtained from this simulation is used to set ‘tf1’ to ‘tfn’
    Example illustrated below
tf1= avg+2
tf2= avg-1
tf3= avg-5

## Slide 9: Modeling the Delay elements
Data from Spice Simulation of delay element used to set ‘tv’
  Setup for a particular corner condition
  Model the supply variation in spice
  Use single sinusoid on supply, with different noise amplitude
  Measure delay variation with respect to applied noise
  Derive a linear relationship for amplitude(A) of delay change with respect to noise amplitude
  Using the above, delay variation
    where F is noise frequency, T is simulation time
  This represents the transient behavior of delay elements

## Slide 10: Modeling the Delay elements
DE
Supply variation
Delay Variation (Ai)

## Slide 11: Case Study
MDLL
Slave Delay Module
CODE
UPDT
MDLL_CLK
SDL_CLK
SDL_CLK_DLY
tv+tf1
tv+tf2
tv+tfn-1
tv+tfn
DL1
DL2
DL
Delay Line - Internals
MDLL and SDL were hardened IPs in 28nm technology
Expected to provide delays over a large range : 1.7ns to 4.5ns
Jitter performance critical as this was clocking a high speed media interface
The code on SDL always produces a quarter cycle shift w.r.t its input clock period
The relation between MDLL_CLK and SDL_CLK is always 2:1

## Slide 12: Spice data for delay element
PTV | Code | Delay | Delay/Element | Variation/Element | Percent variation of delay
S_-40_1.029 | 2 | 84.22 | 21.055 |  | 
S_-40_1.071 | 2 | 77.64 | 19.41 |  | 
 |  |  |  | 1.645 | 8%
No effect on frequency on delay variation :
  Frequency in the interested range
  Effect of frequency seen only after 2.5GHz +
Linear variation w.r.t supply noise :
  4% supply variation  8% delay variation
  1x variation on supply leads to 2x delay variation

## Slide 13: Verification Setup
The verification environment initializes each elements delay
  ‘tf1’ to ‘tfn’ => models OCV
  ‘tv’ => models supply noise
The supply noise is modeled as a sinusoid with below components
  1 MHz, 64 MHz and 200 MHz : Chosen based on clock frequencies on the supply line
  1 MHz Noise Amplitude > 64 MHz Noise > 200 MHz Noise : Decoupling capacitors would filter the noise to an extent
Experiments done by enabling/disabling each noise component independently
Using this, cycle - cycle delay is measured between pos-edges of SDL_CLK and SDL_CLK_DLY and plotted

## Slide 14: Supply noise models
Final Noise Waveform
Mapped to ‘tv’ of delay elements
1 MHz Component
64 MHz Component
200 MHz Component
Final Noise Waveform
Mapped to ‘tv’ of delay elements
1 MHz Component
64 MHz Component
200 MHz Component

## Slide 15: Results
Chart: All Noise Sources ON
Chart: 200MHz Source Switched OFF
Output w/o jitter (Noise Src OFF)
Output w/ jitter (Noise Src ON)
Notes: Tables or Graphs on results
Waveform dumps
Comments on these results

## Slide 16: Results
Chart: 64MHz Source Switched OFF
Chart: 1MHz Source Switched OFF
Notes: Tables or Graphs on results
Waveform dumps
Comments on these results

## Slide 17: Results
Chart: Only 200MHz Source ON
Chart: Only 64MHz Source ON
Notes: Tables or Graphs on results
Waveform dumps
Comments on these results

## Slide 18: Results
Chart: Only 1MHz Source ON
Notes: Tables or Graphs on results
Waveform dumps
Comments on these results

## Slide 19: Analysis
The table captures the amount of jitter (peak-peak) seen on the Slave Delay Line with various noise components
The jitter observed on Slave Delay Line has contribution from two sources – Noise source & MDLL code variation
Notes: Tables or Graphs on results
Waveform dumps
Comments on these results

## Slide 20: Inferences and design changes
Main inference is that MDLL code changes do not respond appropriately in noisy conditions.
  The loop response has to be dampened to reduce jitter
Design changes introduced :
  Introduced an average logic in MDLL
  The average logic averages MDLL code over multiple samples before updating Slave Delay Line
Verification is re-run on the new database
Notes: Tables or Graphs on results
Waveform dumps
Comments on these results

## Slide 21: Results after design change
  The average logic on MDLL’s code results in less delay variation on the Slave Delay Line
Notes: Tables or Graphs on results
Waveform dumps
Comments on these results

## Slide 22: Summary of the proposed solution
Traditionally delay lines used are modeled using a fixed delay step
In reality, delay elements show variation due to Static and Dynamic conditions
Using the proposed model helps in verifying of MDLL + SDL with OCV and Supply noise on delay elements
Impact of various noise models can be analyzed
This ultimately leads to a more robust verification of the MDLL + SDL
Gives an early feel of Jitter performance & helps to identify solution for improved performance
In this particular case, adding average logic helped in improving the jitter performance
Notes: Tables or Graphs on results
Waveform dumps
Comments on these results

## Slide 23: Novelty of the Proposed Solution
Using Verilog's ability to change path delay dynamically to model a more realistic Delay Line. Will work with existing test environments
A faster way to integrate Spice data and verify MDLL and SDL
  Spice simulation is only done on delay elements, not on the complete MDLL and SDL
Helps in verifying MDLL’s behavior under OCV and Supply noise
All this at RTL stage – makes analysis, debug & fix very easy

## Slide 24: Scope for further work
A frame work for verifying AVS and DVFS can be developed
Similar methodology for digital circuits having sensitivity to transient changes in PTV.
A method to have variable delay (over that annotated using SDF) implemented at GLS can be explored. Currently there is no way to vary delay dynamically after SDF annotation

## Slide 25: Questions

## Slide 26: Other Noise Patterns Used
Voltage Ramp Up w/ abrupt changes during transition
Voltage Ramp Down w/ abrupt changes during transition
Voltage Step Up-Down
Voltage Step Down-Up
Triangular waveform with abrupt random changes during ramp
Notes: Tables or Graphs on results
Waveform dumps
Comments on these results