## Slide 1: Dynamic Parameter Configuration of SystemC Models
Shruti Baindur
Simranjit Singh
Anand Patil

## Slide 2: Index
Motivation
Traditional Approach and its Drawbacks
Solution Approach
Dynamic Configurator Overview
Configuration at Run-Time
Conclusion

## Slide 3: Motivation
Configuring a VP for different use cases
Early Software Development
  Debug message
  Exit on Error condition
  Runtime configurations
Architectural Exploration
  Memory size
  Memory address offset
  Delay/Wait cycles
  Register offset
Performance Analysis
  Timing information
  Cycle timing
Configurability

## Slide 4: Traditional Approach
Parameters of a design set at construction time
  Drawbacks
    Recompile for every parameter value change
    Maintaining different configurations is difficult
    VP user does not have flexibility to change values
VP tools provide mechanism for configuration
  Drawbacks
    Approach is tool dependent
    Reuse of setup with another tool not possible

## Slide 5: Solution Approach
Config Data Base
Configuration Data Base
- Can be an input file like XML or INI
Complete System in the form of an executable
A mechanism that sets parameter values dynamically
System.exe
CPU
I2C
Memory
Configuration Reader
Configuration Reader
- Reads & stores configuration data base
- Provides configuration information

## Slide 6: Dynamic Configuration at Infineon
Parameter file
Configuration file
- Is a XML file
- Uses SystemC like hierarchy to differentiate between parameters
System.exe
CPU
I2C
Memory
Configuration Reader
Module implementation
- Parameters special class inherited from ‘sc_attribute’
- During construction, queries configurator for values
Configurator is a SystemC module
- Reads in configuration file in XML format
- If parameter string found in database sets value

## Slide 7: Dynamic Configuration
@ Construction time
System.exe
Configurator
Module1
Parameter1
Parameter XML
Module2
Parameter1
Reader
Parameter Database
Parameter Info Handler
Query value
Returns control
If parameter string match set value
Value : 10
20
Stores reference to the parameter

## Slide 8: Parameter Configuration File
Configure complete system
  Parameter for each module instance can be configured
  Also supports YAML file format
System.exe
CPU
I2C
Memory
Configurator
Parameter.XML hierarchy
System
|---CPU
| |---Core1
| |--- Dvalue
| |--- Value
|---Memory
| |---StartAddr
| |--- Dvalue
| |--- Value
|---I2C
| |---Param
| |--- Dvalue
| |--- Value

## Slide 9: Parameter GUI
Tedious to modify XML file however big or small
  Mechanism to simplify file handling
System.exe
CPU
I2C
Memory
Configurator
Parameter XML
Parameter GUI
System Meta Information
PyQt Based GUI
- Reads parameter XML file
- User modifies value
- Tool dumps a new file with new values
System Meta Generation Mechanism
Has system meta information of the design
Generates initial XML file
Modify existing XML file by taking the already available XML file
It is possible to have many configuration files

## Slide 10: For New Designs
Possibility to re-use old parameter information
System.exe
CPU
I2C
Memory
Configurator
Parameter XML
Parameter GUI
System Meta Information
System Meta Generation Mechanism
New parameters added to metadata
Updated configuration file with new parameter entries
- Takes old configuration file

## Slide 11: Configuration at Run-Time
Need to update configuration during simulation
  E.g. Activation of debug messages
  APIs to set parameter values at run time provided
Configuration runtime scenario for a VP
  From within
    An extra module within VP that sets new parameter values
  From the outside
    Using an interface that communicates with VP to set new values

## Slide 12: Configuration within VP
System.exe
Configurator
Module1
Parameter1
Module2
Parameter1
Reader
Parameter Database
Parameter Info Handler
Action Control
@100 ns: Module1.Parameter1
@101 ns: Module2.Parameter1
Sets value from Action Control unit
@ Run time
Request Set value
Updates referenced value

## Slide 13: Configuration outside VP
System.exe
Configurator
Module1
Parameter1
Module2
Parameter1
Reader
Parameter Database
Parameter Info Handler
Interface(e.g. Python)
@100 ns: Module1.Parameter1
@101 ns: Module2.Parameter1
Requests set value using functions exposed to interface
Updates referenced value
Sets value from command line
@ Run time

## Slide 14: Related Work
Configuration Control and Inspection (CCI WG)
  Provides solution similar to Configurator
    CCI : ‘Broker’  Infineon: ‘Configurator’
    CCI : ‘Parameter’  Infineon: Special class called ‘Attribute’
  Many other features provided
  Is not yet available as a standard
In future it will be possible to easily migrate to CCI
  Structure is similar
  Present setup updated to use CCI underneath

## Slide 15: Conclusion
Generic solution to configure modules
Mechanism is tool agnostic and can run standalone
Saves time as re-compilation time for parameter changes is reduced
Enables configurable design

## Slide 16: Questions?