## Slide 1: Expedite any Simulation with DMTCP and Save Decades of Computation
Balaji R, Sathish Kumar Sugumaran, Rohan Garg, Jiajun Cao, Gene Cooperman

## Slide 2: Agenda
Introduction
DMTCP Overview
DMTCP Advantages
DMTCP Limitations
Use Cases
Results
Conclusion
Q & A

## Slide 3: Introduction
SoC validation putting more focus on shift left using simulation, emulation & FPGA validation techniques
Simulation is the workhorse of PreSi validation
SoC simulation is becoming complex day by day
Takes more time to execute
Need to execute simulation efficiently
One way is to avoid executing common initialization sequences using save restore
And avoid rerunning test from beginning to debug test failure
DMTCP is one such tool that provides this capability

## Slide 4: DMTCP Overview
DMTCP is a checkpoint and restore tool developed by Northeastern University
It stands for Distributed Multi-Threaded Check-Pointing
It works under Linux with no modifications to the kernel / application binaries.
This allows non privileged user to use the solution
DMTCP follows a server client architecture hence multiple programs can be grouped and check-pointed

## Slide 5: DMTCP Advantages
Supports check-point & restore of Distributed applications connected through network sockets.
Works completely in User space & does not require modifications to kernel hence allowing non privileged users to use it
It is open source and follows a plugin architecture allowing it to be easily extensible
It is tried & tested -> relatively more stable

## Slide 6: DMTCP Limitations
DMTCP relies on standard symbol lookup & resolution mechanism provided by linker. Hence issues were observed with non standard mechanism followed by signal dumper libs during restore
It also won’t be able to utilize the simulator internal mechanisms that comes with native save restore. For example native save restore allows one to change the command line arguments during restore
Checkpointing statically linked apps are not supported
Checkpointing GDB & GUI apps is not supported

## Slide 7: Use Case I
Skipping Reset / any common initialization sequence
  Useful when multiple tests have common initialization sequence and use the same model
  DMTCP provides info about whether the program is being restored
  One can add extra code to execute a different test post-restore
  Hence eliminating re-execution of the common sequences.

## Slide 8: Skipping Reset
Init sequence
Test1 Seq
Init sequence
Without ckpt
With ckpt
Init sequence
Test2 Seq
Test2 Seq
Test1 Seq

## Slide 9: Use Case II
Periodic saves for faster debug
  Helps to reach point of failure faster
  Checkpoint adds overhead so should not be abused
  Code can be added to track restore and do something useful
  For example enabling signal dumps, force/deposit/release signals, change random seed etc.,

## Slide 10: Periodic Checkpoint
4.x h
1 h
1 h
1 h
1 h
Without ckpt
With periodic ckpt

## Slide 11: Use Case III
Multi process distributed test benches
  Multi socket simulation can be achieved by simulating each socket as a separate simulation process and connected through network socket
  Other similar use model is Hybrid test bench where portion of test-bench/DUT is written in C++ And remaining in RTL which are connected through network socket.

## Slide 12: Multi Process Test Bench
Simv / Prog Socket0
DMTCP Client
DPI calls
DMTCP Coordinator
DMTCP Restore
Simv / Prog Socket1
DMTCP Client
DPI calls

## Slide 13: Use Case IV
Test content outside the model like SCAN
  The original test is read from a file and the initialization sequences are same across tests
  The scan sequences are read from a file and the scan content is validated using simulation
  During restore one can swap the file and run a different test.

## Slide 14: Results
The first run that creates the checkpoint may take a little longer to complete because of the checkpoint creation overhead.
Subsequent runs take much lesser time because of skipping the common portion
The main gains are achieved when test content can be changed without the need to rebuild the model and without the need to run with different pre conditions and configurations

## Slide 15: Conclusion
One can conclude that by using this method of save restore, great benefits can be achieved in terms of saving computation.
On average 50 to 60% of simulation time can be saved and one can achieve up to 95% time saving in cases where the model and preconditions doesn’t change between tests and actual test itself doesn’t consume much time

## Slide 16: Questions
Finalize slide set with questions slide