## Slide 1: Introducing UVM-SystemC For a Resilient And Structured ESL Validation
Akhila M

## Slide 2: Outline
Intro to UVM-SystemC
Pre-UVM-SystemC Verification Environment
Migrating to UVM-SystemC

## Slide 3: Introduction to UVM-SystemC
UVM-SystemC = UVM implemented in SystemC/C++
No structured nor unified verification methodology available for ESL designs
Porting UVM to SystemC/C++ enables
  Re-use tests and test benches across verification (simulation) and validation (HW-prototyping) platforms.
  Verification components can be re-used across block and system level.
Target to make UVM truly universal, not tied to a particular language

## Slide 4: UVM(UVM-SC) Layered Architecture
#Interfaces
#Drivers = #Interfaces

## Slide 5: Pre-UVM-SystemC Verification Environment
Custom test functions & test engine
  test functions (test ports) created to mimic bus transaction drivers; one per transaction type
  Individual functions for each test scenarios
Distinct methods for writes and reads
  Number of methods depends on types of valid write/read as per the protocol being implemented viz. single, burst, posted or non-posted
Self-checking and parametrized tests
Additional task created for running multiple tests in parallel from different interfaces
  Vector classes used to keep track of test functions being launched from each interface

## Slide 6: Test Port and Sample Write Method
  class ahb_test_port: public test_port
  {
  public:
  // Each test port has individual parameters
  typedef sc_uint<AhbAddrWidth> AhbAddr_t;
  typedef typename sc_suint<AhbDataWidth>::T AhbData_t;
  static const unsigned AHB_RESP_WIDTH = (AHB_FULL_PORT) ?
  amba_sysc::AHB_FULL_RESP_WIDTH :
  amba_sysc::AHB_LITE_RESP_WIDTH;
  public:
  // AHB bus signals
  sc_signal<bool> hsel;
  sc_signal<AhbAddr_t> haddr;
  sc_signal<sc_uint<amba_sysc::AHB_TRANS_WIDTH> > htrans;
  sc_signal<bool> hwrite;
  sc_signal<sc_uint<amba_sysc::AHB_SIZE_WIDTH> > hsize;
  sc_signal<sc_uint<amba_sysc::AHB_BURST_WIDTH> > hburst;
  sc_signal<sc_uint<amba_sysc::AHB_PROT_WIDTH> > hprot;
  sc_signal<AhbData_t> hwdata;
  sc_signal<bool> hready;
  sc_signal<AhbData_t> hrdata;
  sc_signal<bool> hready_resp;
  sc_signal<sc_uint<AHB_RESP_WIDTH> > hresp;
  explicit ahb_test_port (const sc_module_name &name, FlexibleClk* f_clk,
  const std::string& port_name,
  int port_id) :
  test_port(name, port_name, port_id, 0, 0, f_clk)
  {}
  virtual void reset()
  {
  haddr.write(0);
  hsel.write(0);
  hwrite.write(0);
  htrans.write(0);
  hsize.write(0);
  hburst.write(0);
  hready.write(0);
  hwdata.write(0);
  }
  virtual void b_write(ApiAddr_t addr,
  ApiData_t data,
  unsigned wid = 0,
  unsigned wstrb = 0xFFFF,
  unsigned burst_size = amba_axi::ASIZE_32,
  unsigned checkResp = 0)
  {
  // ADDRESS PHASE
  while (!hready_resp) wait();
  hsel.write(1);
  hready.write(1);
  haddr.write(addr);
  hwrite.write(1);
  htrans.write(amba_sysc::HTRANS_NONSEQ);
  hsize.write(burst_size);
  hburst.write(0);
  hwdata.write(0);
  wait();
  // DATA PHASE
  htrans.write(amba_sysc::HTRANS_IDLE);
  hwdata.write(data);
  wait();
  while (!hready_resp) wait();
  }

## Slide 7: Multiport Tests in Parallel
/**
* Push each supplied test to a corresponding port
* This method blocks until all test will finish.
*/
void run() {
// Wait for all involved ports to be idle, i.e. not having pending or
// launched tests
for (int i = 0; i < tasks.size(); i++) {
while (tasks[i]->port->isWorking()) wait();
}
// Run tests
for (int i = 0; i < tasks.size(); i++) {
test_port::port_task tmp;
tasks[i]->was_run = true;
tmp.first = tasks[i]->test;
tmp.second = tasks[i]->ctx;
tasks[i]->port->task_fifo.write(tmp);
}
wait();
// Wait until all tests will finish
for (int i = 0; i < tasks.size(); i++) {
while (tasks[i]->port->isWorking()) wait();
}
class MultiPortTask {
std::vector<Task*> tasks;
public:
/**
* Filled task object (however not yet launched) are added using this method
* Each added task should have a port specified
*/
MultiPortTask& add(Task& task) {
assert(!task.was_run);
// Check that there's no tasks with the same port in the queue
for (int i = 0; i < tasks.size(); i++) {
assert (task.port->getPortId() != tasks[i]->port->getPortId());
}
tasks.push_back(&task);
return *this;
}
}
};}

## Slide 8: Limitations and Potential Reasons for UVM-SystemC Adoption
Limitations of Non-UVM-SC testbench
  Higher learning curve for new user as TB has no standardized architecture
  Minimal reuse of tests/components across projects
  Configurability of testbench is limited
  Inadequate constrained randomization
  Narrow scope of IP to SoC reuse (SoC usually has UVM-SV based framework)
Reasons for UVM-SC adoption:
  Re-usability
  Configurability
  Constrained randomization
  Standardization across languages
  Easier adoption for UVM-SV users

## Slide 9: Migrating to UVM-SystemC framework
UVM-SystemC adheres to the UVM-SystemVerilog standard layered architecture
  Migration of previous components to their respective layers required

## Slide 10: Signal Layer
Create interface and transaction classes as needed by the protocol
Connect DUT to the interface
Pass this interface to other components throughout the testbench hierarchy
  int sc_main(int, char*[]) {
  ahb_clk_reset_gen* clk_rst_gen
  = new ahb_clk_reset_gen("clk_rst_gen");
  ahb_if* dut_if_in = new ahb_if("dut_if_in");
  dut_if_in->hclk(clk_rst_gen->ahb_clk);
  dut_if_in->hresetn(clk_rst_gen->reset_val);
  dut ahb_dut("ahb_dut");
  ahb_dut.hclk(clk_rst_gen->ahb_clk);
  ahb_dut.hresetn(clk_rst_gen->reset_val);
  ahb_dut.haddr(dut_if_in->haddr);
  ...
  uvm::uvm_config_db<ahb_if*>::set
  (0, "*", "vif", dut_if_in);
  uvm::uvm_config_db<sc_event*>::set
  (0, "*", "reset_done", clk_rst_gen->reset_done);
  run_test("ahb_wr_rd_test");
  return 0;
  }

## Slide 11: Component Layer
All components in this layer, are mapped to a transaction type
  The transaction class constitutes on the packet type which is being transmitted across components
Driver-Sequencer to follow a standard handshaking interface as per UVM standard
Driver is the key component where all protocol intelligence has to be implemented
Monitor can implement protocol checks, data integrity checks etc.
  Taps the DUT signal directly

## Slide 12: AHB Driver Component(1/3)
class ahb_driver : public uvm::uvm_driver<ahb_transaction> {
public:
UVM_COMPONENT_PARAM_UTILS(ahb_driver);
ahb_if* ahb_vif;
sc_event* reset_event_driver;
sc_semaphore ahb_pipeline_lock;
ahb_driver( uvm::uvm_component_name name = "ahb_driver"):
uvm::uvm_driver<ahb_transaction>( name ),ahb_pipeline_lock(1)
{ ... }
void build_phase(uvm::uvm_phase& phase) {
UVM_INFO(this->get_name(), "build_phase Entered", UVM_LOW);
uvm_driver<ahb_transaction>::build_phase(phase);
reset_event_driver = new sc_event("reset_event_driver");
if(!uvm_config_db<ahb_if*>::get(this, "*", "vif", ahb_vif)) { UVM_FATAL(this->get_name(),"AHB Virtual Interface missing“);
}
if(!uvm_config_db<sc_event*>::get
(this, "*", "reset_done", reset_event_driver))
{
UVM_FATAL(this->get_name(), “Reset event missing");
}
}

## Slide 13: AHB Driver Component(2/3)
void run_phase(uvm::uvm_phase& phase) {
UVM_INFO(this->get_name(), "run_phase Entered", UVM_LOW);
if(ahb_vif->hresetn == 0) wait( *reset_event_driver );
while(true) {
SC_FORK
sc_spawn(sc_bind(&ahb_driver::send_transaction, this),"drive1"),
sc_spawn(sc_bind(&ahb_driver::send_transaction, this),"drive2")
SC_JOIN
}
UVM_INFO(this->get_name(), "run_phase finished", UVM_LOW);
}

## Slide 14: AHB Driver Component (3/3)
void send_transaction() {
ahb_transaction req, rsp;
ahb_pipeline_lock.wait();
UVM_INFO(this->get_name(),"send_transaction: next item",UVM_LOW);
this->seq_item_port->get_next_item(req);
ahb_vif->htrans = req.htrans;
ahb_vif->haddr = req.haddr;
ahb_vif->hsize = req.hsize;
...
wait(AHB_CLK);
while (ahb_vif->hready != 1) wait(AHB_CLK);
rsp.set_id_info(req);
this->seq_item_port->item_done();
this->seq_item_port->put_response(rsp);
ahb_pipeline_lock.post();
}

## Slide 15: AHB Monitor Component
class ahb_monitor : public uvm::uvm_monitor {
public:
uvm::uvm_analysis_port<ahb_transaction> item_collected_port;
ahb_if* vif;
ahb_monitor(uvm::uvm_component_name name = "ahb_monitor"):
uvm_monitor(name),item_collected_port("item_collected_port"),vif(0)
{ ... }
UVM_COMPONENT_UTILS(ahb_monitor);
void build_phase(uvm::uvm_phase& phase) {
uvm::uvm_monitor::build_phase(phase);
if (!uvm::uvm_config_db<ahb_if*>::get(this, "*", "vif", vif)) {
UVM_FATAL(name(), "Virtual interface not defined!");
}
}
void run_phase( uvm::uvm_phase& phase ) {
ahb_transaction pkt;
while (true) { // monitor forever
std::ostringstream str;
wait( vif->hresetn.posedge_event());
if(vif->hclk == 0) sc_core::wait( vif->hclk.posedge_event());
pkt.htrans = vif->htrans;
...
item_collected_port.write(pkt);
}

## Slide 16: Transaction Layer(UVM Tests)
#include "ahb_wr_rd_sequence.h"
class ahb_wr_rd_test : public uvm::uvm_test
{
public:
ahb_wr_rd_sequence* ahb_wr_rd_seq;
ahb_basic_env* top_env;
UVM_COMPONENT_UTILS(ahb_wr_rd_test);
ahb_wr_rd_test( uvm::uvm_component_name name = "ahb_wr_rd_test") : uvm::uvm_test( name ),
top_env(0) {}
virtual void build_phase(uvm::uvm_phase& phase)
{
std::cout << sc_core::sc_time_stamp() << ": build_phase " << name() << std::endl;
uvm_test::build_phase(phase);
top_env = ahb_basic_env::type_id::create("top_env",this);
}
virtual void run_phase(uvm::uvm_phase& phase)
{
std::cout << sc_core::sc_time_stamp() << ": UVM test with ahb_wr_rd_seq started " << name() << std::endl;
phase.raise_objection(this);
ahb_wr_rd_seq = new ahb_wr_rd_sequence("ahb_wr_rd_seq");
ahb_wr_rd_seq->start(top_env->agent->ahb_sequencer_inst);
phase.drop_objection(this);
std::cout << sc_core::sc_time_stamp() << ": UVM test with ahb_wr_rd_seq finished " << name() << std::endl;
}
};

## Slide 17: Random Sequences Using SCV
Create scv_extensions for the sequence item class i.e. for the transaction type
SCV_EXTENSIONS(ahb_transaction) {
public:
scv_extensions<sc_uint<ahbConfig::AhbAddrWidth>> haddr;
scv_extensions<sc_uint<ahbConfig::AhbDataWidth>[BURSTLENGTH]>
hwdata;
scv_extensions< sc_uint<ahbConfig::AhbBurstSize>> hburst;
scv_extensions< sc_uint<ahbConfig::AhbSize>> hsize;
SCV_EXTENSIONS_CTOR(ahb_transaction) {
SCV_FIELD(haddr);
SCV_FIELD(hburst);
SCV_FIELD(hsize);
SCV_FIELD(hwdata);
}
bool has_valid_extensions() { return true; }
};
Create constraints class using smart_ptr of sequence item class type
class ahb_trans_constraints : virtual public scv_constraint_base {
public:
scv_smart_ptr<ahb_transaction> req;
SCV_CONSTRAINT_CTOR(ahb_trans_constraints) {
SCV_CONSTRAINT((req->haddr() * 0x3) == 0x0);
SCV_CONSTRAINT(
(req->hburst() >= ahbConfig::HBURST_SINGLE) &&
(req->hburst() <= ahbConfig::HBURST_INCR16)
);
SCV_CONSTRAINT(
(req->hsize() >= ahbConfig::HSIZE_BYTE) &&
(req->hsize() <= ahbConfig::HSIZE_WORD)
);
// For wrapping bursts, start address from an address
// other that 0x00 offset
SCV_CONSTRAINT(
if_then(req->hburst() == ahbConfig::HBURST_WRAP4,
((req->haddr() * 0x7) != 0x0) );
);
}

## Slide 18: Hierarchical Sequences using Random Sequence Items (SCV)
class ahb_wr_rd_sequence : public uvm::uvm_sequence<ahb_transaction>
{
public:
UVM_OBJECT_UTILS(ahb_wr_rd_sequence);
UVM_DECLARE_P_SEQUENCER(ahb_sequencer<ahb_transaction>);
ahb_if* ahb_vif_seq;
ahb_wr_rd_sequence( const std::string& name = "ahb_wr_rd_sequence") :
uvm::uvm_sequence<ahb_transaction> ( name ){}
uint8_t xactType;
unsigned addrValue;
unsigned dataValue;
void body()
{
UVM_INFO(this->get_name(), "Starting sequence", uvm::UVM_INFO);
ahb_trans_constraints constr_req("constr_req");
scv_smart_ptr<ahb_transaction> rand_smart_ptr_ahb_pkt;
ahb_basic_sequence* ahb_seq;
ahb_seq = new ahb_basic_sequence("ahb_seq");
constr_req.next();
rand_smart_ptr_ahb_pkt.write(constr_req.req.read());
ahb_seq->xactType = rand_smart_ptr_ahb_pkt ->hwrite;
ahb_seq->hburstValue = rand_smart_ptr_ahb_pkt ->hburst;
ahb_seq->addrValue = rand_smart_ptr_ahb_pkt ->haddr;
ahb_seq->dataValue = 0xabababab;
ahb_seq->start(m_sequencer);
constr_req.next();
rand_smart_ptr_ahb_pkt.write(constr_req.req.read());
ahb_seq->xactType = rand_smart_ptr_ahb_pkt ->hwrite;
ahb_seq->hburstValue = rand_smart_ptr_ahb_pkt ->hburst;
ahb_seq->addrValue = rand_smart_ptr_ahb_pkt ->haddr;
ahb_seq->start(m_sequencer);
UVM_INFO(this->get_name(), "Finishing sequence", uvm::UVM_INFO);
}
class ahb_basic_sequence : public uvm::uvm_sequence<ahb_transaction>
{
public:
UVM_OBJECT_UTILS(ahb_basic_sequence);
uint8_t xactType;
unsigned addrValue,dataValue,,hburstValue, hsizeValue;
ahb_basic_sequence( const std::string& name = "ahb_basic_sequence") : uvm::uvm_sequence<ahb_transaction> ( name ) {}
void body()
{
UVM_INFO(this->get_name(), "Starting sequence ahb_basic_sequence", uvm::UVM_INFO)
ahb_transaction* req_pkt;
ahb_transaction* rsp;
req_pkt = new ahb_transaction();
rsp = new ahb_transaction();
single_wr_rd(addrValue,xactType,dataValue, req_pkt, rsp);
}
void single_wr_rd(unsigned addrValue, unsigned xactType, unsigned dataValue,
ahb_transaction* req_pkt, ahb_transaction* rsp)
{
UVM_INFO(this->get_name(), "Initiating non-burst accesses", uvm::UVM_INFO);
req_pkt->haddr = addrValue;
req_pkt->hsel = 1;
req_pkt->hready = 1;
req_pkt->htrans = ahbConfig::HTRANS_NONSEQ;
req_pkt->hsize = hsizeValue;
req_pkt->hwrite = xactType;
req_pkt->hwdata[0] = (sc_uint<32>)dataValue;
this->start_item(req_pkt);
this->finish_item(req_pkt);
this->get_response(rsp);
}

## Slide 19: Sequence Item Using CRAVE
class ahb_transaction : public uvm_randomized_sequence_item {
public:
UVM_OBJECT_UTILS(ahb_transaction);
// define some rand variables
crv_variable< sc_uint< ahbConfig::AhbAddrWidth > > haddr;
crv_variable< sc_uint< ahbConfig::AhbSize > > hsize;
crv_variable< sc_uint< ahbConfig::AhbDataWidth> > hwdata[BURSTLENGTH];
crv_variable< unsigned > hburst;
// Add some constraints
crv_constraint valid_hburst_range {HBURST_SINGLE <= hburst() <= HBURST_INCR16};
crv_constraint valid_hsize_range {HSIZE_BYTE <= hburst() <= HSIZE_WORD};
crv_constraint valid_addr_range {haddr() * 0x3 == 0x0};
crv_constraint addr_for_wrap_burst {if_then(hburst() == HBURST_WRAP4, (haddr() * 0x7) != 0x0)};
// Constructor
ahb_transaction(crv_object_name name = "ahb_transaction") : uvm_randomized_sequence_item(name) {
...
};
};

## Slide 20: Hierarchical Sequences using Random Sequence Item(CRAVE)
#include "ahb_basic_sequence.h"
class ahb_wr_rd_sequence : public uvm_randomized_sequence<ahb_transaction>
{
public:
UVM_OBJECT_UTILS(ahb_wr_rd_sequence);
ahb_wr_rd_sequence( crave::crv_object_name name = "ahb_wr_rd_sequence") : uvm_randomized_sequence<ahb_transaction> ( name )
{
cout << "Entered constructor of ahb_wr_rd_sequence " << endl;
}
void body()
{
UVM_INFO(this->get_name(), "Starting sequence", uvm::UVM_INFO);
ahb_basic_sequence* ahb_seq;
ahb_seq = new ahb_basic_sequence("ahb_seq");
ahb_seq->hburstValue = ahbConfig::HBURST_SINGLE;
ahb_seq->start(m_sequencer);
UVM_INFO(this->get_name(), "Finishing sequence", uvm::UVM_INFO);
}
};

## Slide 21: Base Sequence With CRV_VARIABLE
class ahb_basic_sequence : public uvm_randomized_sequence<ahb_transaction>
{
public:
UVM_OBJECT_UTILS(ahb_basic_sequence);
crv_variable<uint8_t > xactType;
crv_variable<unsigned > addrValue;
crv_variable<unsigned > dataValue;
unsigned hburstValue, hsizeValue;
unsigned readData;
unsigned returnResp;
ahb_basic_sequence( crave::crv_object_name name = "ahb_basic_sequence") : uvm_randomized_sequence<ahb_transaction> ( name )
{}
virtual ~ahb_basic_sequence() {
};
void body()
{
UVM_INFO(this->get_name(), "Starting sequence ahb_basic_sequence", uvm::UVM_INFO);
ahb_transaction* req_pkt;
ahb_transaction* rsp;
req_pkt = new ahb_transaction();
rsp = new ahb_transaction();
single_wr_rd(addrValue,xactType,dataValue, req_pkt, rsp);
}
}
/* Method for initiating single writes/reads to particular address with specific data
*/
void single_wr_rd(unsigned addrValue, unsigned xactType, unsigned dataValue, ahb_transaction* req_pkt, ahb_transaction* rsp)
{
UVM_INFO(this->get_name(), "Initiating non-burst accesses", uvm::UVM_INFO);
this->randomize();
req_pkt->haddr = addrValue;
req_pkt->hsel = 1;
req_pkt->hready = 1;
req_pkt->htrans = ahbConfig::HTRANS_NONSEQ;
req_pkt->hsize = hsizeValue;
req_pkt->hwrite = xactType;
UVM_DO_WITH(req_pkt, req_pkt->haddr() == addrValue);
UVM_INFO(this->get_name(), "Exiting non-burst accesses", uvm::UVM_INFO);
}

## Slide 22: Potential benefits of UVM-SystemC methodology
Less design time for testbench components
  Base library provides analysis ports and callbacks
Low learning curve for new users to the IP
  Testbench framework well known in verification circles
Less time in test coding for IP validation at SoC level using UVM-SV
  Langauge specific updates between SC and SV via simple script
Reduced coding time for testbench components for IP at SoC level
  Re-use of custom bus functional model written at IP level
Reduced man power required
  Same owner can work on IP and SoC validation

## Slide 23: Sample Conversion Capabilities of the UVM-SC to UVM-SV script
Changing class extension syntax
  class ahb_transaction : public uvm_randomized_sequence_item to
  class ahb_transaction extends public uvm_randomized_sequence_item
Updating the component phase arguments
  void run_phase(uvm::uvm_phase& phase) to function void run_phase(uvm::uvm_phase phase)
Modifying the constructor calls
  ahb_driver( uvm::uvm_component_name name = "ahb_driver"):
uvm::uvm_driver<ahb_transaction>( name ),ahb_pipeline_lock(1)
{ ... } to
function new (string name = "ahb_driver"):
super.new(name);
endfunction
Replacing loop constructor brackets with begin-end
  if(!uvm_config_db<ahb_if*>::get(this, "*", "vif", ahb_vif)) { … } to
  if(!uvm_config_db<ahb_if*>::get(this, "*", "vif", ahb_vif)) begin … end

## Slide 24: Conclusion
UVM-SystemC based validation framework enables development of configurable, re-usable and structured components
Standard implementation technique enables resilient testbench across multiple users
UVM-SC methodology should be adopted across companies and EDA vendors to make validation truly language agnostic and enhance the UVM-SystemC VIP portfolio

## Slide 25: Thanks You!
Questions ?

## Slide 26: Motivation
UVM-SystemC = UVM implemented in SystemC/C++
No structured nor unified verification methodology available for ESL designs
Porting UVM to SystemC/C++ enables
  Re-use tests and test benches across verification (simulation) and validation (HW-prototyping) platforms.
  Verification components can be re-used across block and system level.
Target to make UVM truly universal, not tied to a particular language

## Slide 27: Part 1: Previously used verification environment

## Slide 28: Conventional SystemC Testbench
Custom test functions & test engine
  test functions (test ports) created to mimic bus transaction drivers; one per transaction type
  Individual functions for each test scenarios
Distinct methods for writes and reads
  Number of methods depends on types of valid write/read as per the protocol being implemented viz. single, burst, posted or non-posted
Self-checking and parametrized tests
Additional task created for running multiple tests in parallel from different interfaces
  Vector classes used to keep track of test functions being launched from each interface

## Slide 29: Limitations and Potential reasons for UVM-SystemC
Limitations of Non-UVM-SC testbench
  Higher learning curve for new user as TB has no standardized architecture
  Minimal reuse of tests/components across projects
  Configurability of testbench is limited
  Inadequate constrained randomization
  Narrow scope of IP to SoC reuse (SoC usually has UVM-SV based framework)
Reasons for UVM-SC adoption:
  Re-usability
  Configurability
  Constrained randomization
  Standardization across languages
  Easier adoption for UVM-SV users

## Slide 30: Migrating to UVM-SystemC framework
UVM-SystemC adheres to the UVM-SystemVerilog standard layered architecture
  Migration of previous components to their respective layers required

## Slide 31: Transaction Layer
Create interface and transaction classes as needed by the protocol
Connect DUT to the interface
Pass this interface to other components throughout the testbench hierarchy
  int sc_main(int, char*[]) {
  ahb_clk_reset_gen* clk_rst_gen
  = new ahb_clk_reset_gen("clk_rst_gen");
  ahb_if* dut_if_in = new ahb_if("dut_if_in");
  dut_if_in->hclk(clk_rst_gen->ahb_clk);
  dut_if_in->hresetn(clk_rst_gen->reset_val);
  dut ahb_dut("ahb_dut");
  ahb_dut.hclk(clk_rst_gen->ahb_clk);
  ahb_dut.hresetn(clk_rst_gen->reset_val);
  ahb_dut.haddr(dut_if_in->haddr);
  ...
  uvm::uvm_config_db<ahb_if*>::set
  (0, "*", "vif", dut_if_in);
  uvm::uvm_config_db<sc_event*>::set
  (0, "*", "reset_done", clk_rst_gen->reset_done);
  run_test("ahb_wr_rd_test");
  return 0;
  }

## Slide 32: Component Layer
All components in this layer, are mapped to a transaction type
  The transaction class constitutes on the packet type which is being transmitted across components
Driver-Sequencer to follow a standard handshaking interface as per UVM standard
Driver is the key component where all protocol intelligence has to be implemented
Monitor can implement protocol checks, data integrity checks etc.
  Snoops the DUT signals directly

## Slide 33: AHB Driver Component
class ahb_driver : public uvm::uvm_driver<ahb_transaction> {
public:
UVM_COMPONENT_PARAM_UTILS(ahb_driver);
ahb_if* ahb_vif;
sc_event* reset_event_driver;
sc_semaphore ahb_pipeline_lock;
ahb_driver( uvm::uvm_component_name name = "ahb_driver"):
uvm::uvm_driver<ahb_transaction>( name ),ahb_pipeline_lock(1)
{ ... }
void build_phase(uvm::uvm_phase& phase) {
UVM_INFO(this->get_name(), "build_phase Entered", UVM_LOW);
uvm_driver<ahb_transaction>::build_phase(phase);
reset_event_driver = new sc_event("reset_event_driver");
if(!uvm_config_db<ahb_if*>::get(this, "*", "vif", ahb_vif)) { UVM_FATAL(this->get_name(),"AHB Virtual Interface missing“);
}
if(!uvm_config_db<sc_event*>::get
(this, "*", "reset_done", reset_event_driver))
{
UVM_FATAL(this->get_name(), “Reset event missing");
}
}

## Slide 34: AHB Driver Component contd..
void run_phase(uvm::uvm_phase& phase) {
UVM_INFO(this->get_name(), "run_phase Entered", UVM_LOW);
if(ahb_vif->hresetn == 0) wait( *reset_event_driver );
while(true) {
SC_FORK
sc_spawn(sc_bind(&ahb_driver::send_transaction, this),"drive1"),
sc_spawn(sc_bind(&ahb_driver::send_transaction, this),"drive2")
SC_JOIN
}
UVM_INFO(this->get_name(), "run_phase finished", UVM_LOW);
}

## Slide 35: AHB Driver Component contd..
void send_transaction() {
ahb_transaction req, rsp;
ahb_pipeline_lock.wait();
UVM_INFO(this->get_name(),"send_transaction: next item",UVM_LOW);
this->seq_item_port->get_next_item(req);
ahb_vif->htrans = req.htrans;
ahb_vif->haddr = req.haddr;
ahb_vif->hsize = req.hsize;
...
wait(AHB_CLK);
while (ahb_vif->hready != 1) wait(AHB_CLK);
rsp.set_id_info(req);
this->seq_item_port->item_done();
this->seq_item_port->put_response(rsp);
ahb_pipeline_lock.post();
}

## Slide 36: AHB Monitor Component
class ahb_monitor : public uvm::uvm_monitor {
public:
uvm::uvm_analysis_port<ahb_transaction> item_collected_port;
ahb_if* vif;
ahb_monitor(uvm::uvm_component_name name = "ahb_monitor"):
uvm_monitor(name),item_collected_port("item_collected_port"),vif(0)
{ ... }
UVM_COMPONENT_UTILS(ahb_monitor);
void build_phase(uvm::uvm_phase& phase) {
uvm::uvm_monitor::build_phase(phase);
if (!uvm::uvm_config_db<ahb_if*>::get(this, "*", "vif", vif)) {
UVM_FATAL(name(), "Virtual interface not defined!");
}
}
void run_phase( uvm::uvm_phase& phase ) {
ahb_transaction pkt;
while (true) { // monitor forever
std::ostringstream str;
wait( vif->hresetn.posedge_event());
if(vif->hclk == 0) sc_core::wait( vif->hclk.posedge_event());
pkt.htrans = vif->htrans;
...
item_collected_port.write(pkt);
}

## Slide 37: Transaction Layer(UVM Tests)
#include "ahb_wr_rd_sequence.h"
class ahb_wr_rd_test : public uvm::uvm_test
{
public:
ahb_wr_rd_sequence* ahb_wr_rd_seq;
ahb_basic_env* top_env;
UVM_COMPONENT_UTILS(ahb_wr_rd_test);
ahb_wr_rd_test( uvm::uvm_component_name name = "ahb_wr_rd_test") : uvm::uvm_test( name ),
top_env(0) {}
virtual void build_phase(uvm::uvm_phase& phase)
{
std::cout << sc_core::sc_time_stamp() << ": build_phase " << name() << std::endl;
uvm_test::build_phase(phase);
top_env = ahb_basic_env::type_id::create("top_env",this);
}
virtual void run_phase(uvm::uvm_phase& phase)
{
std::cout << sc_core::sc_time_stamp() << ": UVM test with ahb_wr_rd_seq started " << name() << std::endl;
phase.raise_objection(this);
ahb_wr_rd_seq = new ahb_wr_rd_sequence("ahb_wr_rd_seq");
ahb_wr_rd_seq->start(top_env->agent->ahb_sequencer_inst);
phase.drop_objection(this);
std::cout << sc_core::sc_time_stamp() << ": UVM test with ahb_wr_rd_seq finished " << name() << std::endl;
}
};

## Slide 38: Part 2: Randomization using SCV & CRAVE

## Slide 39: Random Sequences Using SCV
Create scv_extensions for the sequence item class i.e. for the transaction type
SCV_EXTENSIONS(ahb_transaction) {
public:
scv_extensions<sc_uint<ahbConfig::AhbAddrWidth>> haddr;
scv_extensions<sc_uint<ahbConfig::AhbDataWidth>[BURSTLENGTH]>
hwdata;
scv_extensions< sc_uint<ahbConfig::AhbBurstSize>> hburst;
scv_extensions< sc_uint<ahbConfig::AhbSize>> hsize;
SCV_EXTENSIONS_CTOR(ahb_transaction) {
SCV_FIELD(haddr);
SCV_FIELD(hburst);
SCV_FIELD(hsize);
SCV_FIELD(hwdata);
}
bool has_valid_extensions() { return true; }
};
Create constraints class using smart_ptr of sequence item class type
class ahb_trans_constraints : virtual public scv_constraint_base {
public:
scv_smart_ptr<ahb_transaction> req;
SCV_CONSTRAINT_CTOR(ahb_trans_constraints) {
SCV_CONSTRAINT((req->haddr() * 0x3) == 0x0);
SCV_CONSTRAINT(
(req->hburst() >= ahbConfig::HBURST_SINGLE) &&
(req->hburst() <= ahbConfig::HBURST_INCR16)
);
SCV_CONSTRAINT(
(req->hsize() >= ahbConfig::HSIZE_BYTE) &&
(req->hsize() <= ahbConfig::HSIZE_WORD)
);
// For wrapping bursts, start address from an address
// other that 0x00 offset
SCV_CONSTRAINT(
if_then(req->hburst() == ahbConfig::HBURST_WRAP4,
((req->haddr() * 0x7) != 0x0) );
);
}

## Slide 40: Hierarchical Sequences using Random Sequence Items (SCV)
class ahb_wr_rd_sequence : public uvm::uvm_sequence<ahb_transaction>
{
public:
UVM_OBJECT_UTILS(ahb_wr_rd_sequence);
UVM_DECLARE_P_SEQUENCER(ahb_sequencer<ahb_transaction>);
ahb_if* ahb_vif_seq;
ahb_wr_rd_sequence( const std::string& name = "ahb_wr_rd_sequence") :
uvm::uvm_sequence<ahb_transaction> ( name ){}
uint8_t xactType;
unsigned addrValue;
unsigned dataValue;
void body()
{
UVM_INFO(this->get_name(), "Starting sequence", uvm::UVM_INFO);
ahb_trans_constraints constr_req("constr_req");
scv_smart_ptr<ahb_transaction> rand_smart_ptr_ahb_pkt;
ahb_basic_sequence* ahb_seq;
ahb_seq = new ahb_basic_sequence("ahb_seq");
constr_req.next();
rand_smart_ptr_ahb_pkt.write(constr_req.req.read());
ahb_seq->xactType = rand_smart_ptr_ahb_pkt ->hwrite;
ahb_seq->hburstValue = rand_smart_ptr_ahb_pkt ->hburst;
ahb_seq->addrValue = rand_smart_ptr_ahb_pkt ->haddr;
ahb_seq->dataValue = 0xabababab;
ahb_seq->start(m_sequencer);
constr_req.next();
rand_smart_ptr_ahb_pkt.write(constr_req.req.read());
ahb_seq->xactType = rand_smart_ptr_ahb_pkt ->hwrite;
ahb_seq->hburstValue = rand_smart_ptr_ahb_pkt ->hburst;
ahb_seq->addrValue = rand_smart_ptr_ahb_pkt ->haddr;
ahb_seq->start(m_sequencer);
UVM_INFO(this->get_name(), "Finishing sequence", uvm::UVM_INFO);
}
class ahb_basic_sequence : public uvm::uvm_sequence<ahb_transaction>
{
public:
UVM_OBJECT_UTILS(ahb_basic_sequence);
uint8_t xactType;
unsigned addrValue,dataValue,,hburstValue, hsizeValue;
ahb_basic_sequence( const std::string& name = "ahb_basic_sequence") : uvm::uvm_sequence<ahb_transaction> ( name ) {}
void body()
{
UVM_INFO(this->get_name(), "Starting sequence ahb_basic_sequence", uvm::UVM_INFO)
ahb_transaction* req_pkt;
ahb_transaction* rsp;
req_pkt = new ahb_transaction();
rsp = new ahb_transaction();
single_wr_rd(addrValue,xactType,dataValue, req_pkt, rsp);
}
void single_wr_rd(unsigned addrValue, unsigned xactType, unsigned dataValue,
ahb_transaction* req_pkt, ahb_transaction* rsp)
{
UVM_INFO(this->get_name(), "Initiating non-burst accesses", uvm::UVM_INFO);
req_pkt->haddr = addrValue;
req_pkt->hsel = 1;
req_pkt->hready = 1;
req_pkt->htrans = ahbConfig::HTRANS_NONSEQ;
req_pkt->hsize = hsizeValue;
req_pkt->hwrite = xactType;
req_pkt->hwdata[0] = (sc_uint<32>)dataValue;
this->start_item(req_pkt);
this->finish_item(req_pkt);
this->get_response(rsp);
}

## Slide 41: Sequence Item Using CRAVE
class ahb_transaction : public uvm_randomized_sequence_item {
public:
UVM_OBJECT_UTILS(ahb_transaction);
// define some rand variables
crv_variable< sc_uint< ahbConfig::AhbAddrWidth > > haddr;
crv_variable< sc_uint< ahbConfig::AhbSize > > hsize;
crv_variable< sc_uint< ahbConfig::AhbDataWidth> > hwdata[BURSTLENGTH];
crv_variable< unsigned > hburst;
// Add some constraints
crv_constraint valid_hburst_range {HBURST_SINGLE <= hburst() <= HBURST_INCR16};
crv_constraint valid_hsize_range {HSIZE_BYTE <= hburst() <= HSIZE_WORD};
crv_constraint valid_addr_range {haddr() * 0x3 == 0x0};
crv_constraint addr_for_wrap_burst {if_then(hburst() == HBURST_WRAP4, (haddr() * 0x7) != 0x0)};
// Constructor
ahb_transaction(crv_object_name name = "ahb_transaction") : uvm_randomized_sequence_item(name) {
...
};
};

## Slide 42: Hierarchical Sequences using Random Sequence Item(CRAVE)
#include "ahb_basic_sequence.h"
class ahb_wr_rd_sequence : public uvm_randomized_sequence<ahb_transaction>
{
public:
UVM_OBJECT_UTILS(ahb_wr_rd_sequence);
ahb_wr_rd_sequence( crave::crv_object_name name = "ahb_wr_rd_sequence") : uvm_randomized_sequence<ahb_transaction> ( name )
{
cout << "Entered constructor of ahb_wr_rd_sequence " << endl;
}
void body()
{
UVM_INFO(this->get_name(), "Starting sequence", uvm::UVM_INFO);
ahb_basic_sequence* ahb_seq;
ahb_seq = new ahb_basic_sequence("ahb_seq");
ahb_seq->hburstValue = ahbConfig::HBURST_SINGLE;
ahb_seq->start(m_sequencer);
UVM_INFO(this->get_name(), "Finishing sequence", uvm::UVM_INFO);
}
};

## Slide 43: Base sequence with crv_variable
class ahb_basic_sequence : public uvm_randomized_sequence<ahb_transaction>
{
public:
UVM_OBJECT_UTILS(ahb_basic_sequence);
crv_variable<uint8_t > xactType;
crv_variable<unsigned > addrValue;
crv_variable<unsigned > dataValue;
unsigned hburstValue, hsizeValue;
unsigned readData;
unsigned returnResp;
ahb_basic_sequence( crave::crv_object_name name = "ahb_basic_sequence") : uvm_randomized_sequence<ahb_transaction> ( name )
{}
virtual ~ahb_basic_sequence() {
};
void body()
{
UVM_INFO(this->get_name(), "Starting sequence ahb_basic_sequence", uvm::UVM_INFO);
ahb_transaction* req_pkt;
ahb_transaction* rsp;
req_pkt = new ahb_transaction();
rsp = new ahb_transaction();
single_wr_rd(addrValue,xactType,dataValue, req_pkt, rsp);
}
}
/* Method for initiating single writes/reads to particular address with specific data
*/
void single_wr_rd(unsigned addrValue, unsigned xactType, unsigned dataValue, ahb_transaction* req_pkt, ahb_transaction* rsp)
{
UVM_INFO(this->get_name(), "Initiating non-burst accesses", uvm::UVM_INFO);
this->randomize();
req_pkt->haddr = addrValue;
req_pkt->hsel = 1;
req_pkt->hready = 1;
req_pkt->htrans = ahbConfig::HTRANS_NONSEQ;
req_pkt->hsize = hsizeValue;
req_pkt->hwrite = xactType;
UVM_DO_WITH(req_pkt, req_pkt->haddr() == addrValue);
UVM_INFO(this->get_name(), "Exiting non-burst accesses", uvm::UVM_INFO);
}

## Slide 44: Part 3: Migration Results & Conclusion

## Slide 45: Potential benefits of UVM-SystemC methodology
Less design time for testbench components
  Base library provides analysis ports and callbacks
Low learning curve for new users to the IP
  Testbench framework well known in verification circles
Less time in test coding for IP validation at SoC level using UVM-SV
  Langauge specific updates between SC and SV via simple script
Reduced coding time for testbench components for IP at SoC level
  Re-use of custom bus functional model written at IP level
Reduction in man power required
  Same owner can work on IP and SoC validation

## Slide 46: Sample Conversion Capabilities of the UVM-SC to UVM-SV script
Changing class extension syntax
  class ahb_transaction : public uvm_randomized_sequence_item to
  class ahb_transaction extends public uvm_randomized_sequence_item
Updating the component phase arguments
  void run_phase(uvm::uvm_phase& phase) to function void run_phase(uvm::uvm_phase phase)
Modifying the constructor calls
  ahb_driver( uvm::uvm_component_name name = "ahb_driver"):
uvm::uvm_driver<ahb_transaction>( name ),ahb_pipeline_lock(1)
{ ... } to
function new (string name = "ahb_driver"):
super.new(name);
endfunction
Replacing loop constructor brackets with begin-end
  if(!uvm_config_db<ahb_if*>::get(this, "*", "vif", ahb_vif)) { … } to
  if(!uvm_config_db<ahb_if*>::get(this, "*", "vif", ahb_vif)) begin … end

## Slide 47: Conclusion
UVM-SystemC based validation framework enables development of configurable, re-usable and structured components
Standard implementation technique enables resilient testbench across multiple users
UVM-SC methodology should be adopted across companies and EDA vendors to make validation truly language agnostic and enhance the UVM-SystemC VIP portfolio

## Slide 48: Thanks You!
Questions ?