## Slide 1: MIPI M-PHY Analog Modeling in verilog-AMS (Wreal) and verification using SV/UVM-MS methodology
Mallikarjuna Reddy Y, Project Lead, T&VS
Venkatramana Rao K, Sr Engineer, T&VS
Somanatha Shetty A, Delivery Head, T&VS

## Slide 2: AGENDA
INTRODUCTION
MIXED-SIGNAL VERIFICATION
ANALOG BLOCKS MODELING
M-PHY PURPOSE AND FEATURES
PLL CASE STUDY
M-PHY END-TO-END VERIFICATION
ISSUES AND CHALLENGES
RESULTS
REFERENCES

## Slide 3: INTRODUCTION
Need for mixed-signal designs for consumer products growing rapidly
  Smart phones,
  LEDs (TVs, bulbs etc.,)
  Digital cameras and watches
  Storage devices
  And other High end technology devices
  Mixed signal designs verification and time to market are becoming more and more challenging

## Slide 4: Mixed-Signal Verification
Mixed-signal verification involves many different levels of abstraction
Transistor-level simulation with Spice remains the gold standard for analog IP verification
  Provides high accuracy
  Very slow until extremely selectively
  To achieve reasonable simulation speeds, mixed-signal teams employ analog behavioral modeling
  five to 100 times faster than Spice
  The actual speedup varies widely depending on the application and the level of detail in the model

## Slide 5: Mixed-Signal Verification Contd..
As design complexity increases,
  The cost of simulations increases in a non-linear fashion
  For full-chip verification, the cost becomes too high (prohibitive)
    It is no longer possible to meet all verification goals.
    Results in chip re-spins and delays.
The block verification process
  Does not cover possibilities, when the block is integrated in the SoCs.
In the absence of top-down verification plan, these errors typically caught at the later stages of verification which further impacts time to market delay.

## Slide 6: Mixed-Signal Verification Contd..
A mixed-signal simulation involves the following three functions:
  solving the analog part of the design using a system of nonlinear differential equations which are continuously varying over time.
  Solving the digital part of the design by processing a time sorted collection of events over discrete time intervals
  Perform-signal synchronization based on the events and variables owned by either simulations kernel that are in the sensitivity list of the other kernel.

## Slide 7: Analog Behavioral Modeling
Verilog-AMS(electrical): A mixed-signal modeling language can be defined for both analog and digital behavior, offering both continuous-time and event-driven modeling semantics.
Verilog-AMS(Wreal): The continuous-time subset of Verilog-AMS, aimed at analog design.
VHDL-AMS: similar in concept to Verilog-AMS, this language provides analog and mixed-signal extensions.
Verilog : Behavioral modeling is also done for analog blocks with limitations.
System Verilog: Extension of verilog with added real data types and other advanced features.
Behavioral Modeling
SV/SysC
VerilogAMS
Verilog
VHDL
VHDLAMS
VerilogAMS Wreal
VerilogAMS electrical

## Slide 8: Analog Behavioral modeling Contd ..
The wide range of accuracy and performance that is possible for Verilog-AMS and VHDL-AMS behavioral models.
Pure digital simulation can only represent an analog signal as a single logic value, but it might be sufficient for connectivity checks in mixed-signal SoCs.
Real number modeling (RNM) with the “real” and “wreal” data types, which make it possible to represent analog signal values in digital simulations.
Wreal/RNMs are the most effective way to abstract AMS functionality for full chip simulation.

## Slide 9: Analog Behavioral modeling Contd..
Important factor is the effort required to set up a simulation .
  Spice simulations run slowly, they’re relatively easy to set up.
  The time required to create a high-quality analog behavioral model, however, can range from hours to days, or even weeks.
  RNM is restricted to a signal-flow approach, it doesn’t require analog convergence, and there’s no new language to learn.
  Consequently, the real/wreal modeling effort is less than that for Verilog-AMS (electrical) or VHDL-AMS.

## Slide 10: Analog Behavioral modeling Contd..
Blocks can be modeled at different levels of abstraction.
Verilog-AMS (wreal)/RNM: at a high level
Verilog-AMS (electrical): more intermediate level
Spice netlist from schematics: very low level
Blocks can be combined, using appropriate abstractions, to allow for various level of focus on specific areas of the system or for block-based, macro-based or full-chip verification.
Verification is performed to verify both functional intent and to ensure desired specification and performance levels are being met.

## Slide 11: PURPOSE OF MIPI M-PHY
A serial interface technology with high bandwidth capabilities particularly developed for mobile applications
This requires wide bandwidth, low-pin count (serial) and highly power-efficient (network) interfaces
M-PHY is the successor of D-PHY, requiring less pins and providing more bandwidth per pin (pair) with improved power efficiency.

## Slide 12: MIPI MPHY FEATURES
Burst mode of operation for improved power efficiency
Multiple transmission modes with
  different bit-signaling
  clocking schemes for different bandwidth, better power efficiency over a large range of data rates
Multiple power saving modes
  STALL, SLEEP, HIBERN8, DISABLED, UNPOWERED
  allow optimization of power consumption,
  offering different recovery times
Symbol coding (8b10b) for spectral conditioning, clock recovery, and in-band control options for both PHY and Protocol level.

## Slide 13: MIPI M-PHY FEATURES Contd..
Multiple transmission speed ranges/rates per BURST mode to
  scale bandwidth to application needs
  For mitigation of interference problems.
Clocking flexibility: able to operate with independent local reference clocks at each side, but suitable to exploit the benefits of a shared reference clock
Optical friendly: enables
  low-complexity electro-optical signal conversion
  optical data transport inside the interconnect between MODULEs
Distance: optimized for short interconnect (<10 cm)
  Can be extendable to a meter with good quality interconnect
  Even further with optical converters and optical waveguides.

## Slide 14: M-PHY Block diagram
TX
RX
PLL
Digital(RTL)
CAL
BIAS

## Slide 15: LINK, LANE configuration

## Slide 16: Analog PHY
Pure Analog blocks :- PLL, BIAS, Calibration etc., are modeled in Verilog-AMS
TX
CAL
PLL
RX
BIAS

## Slide 17: PLL Block (Stand-alone verification)
Mphy_od
REF_CLK
Input divider
(PLL_M)
CP&FILTER
Feed Back divider
(NPC+NSC)
VCO
PFD
Pre divider
(PRE_FDIV)
CLK0
mux
Mphy_clk2

## Slide 18: PLL CASE STUDY
All internal blocks are modeled in Verilog AMS (Wreal)
Critical Blocks were PFD, CP&FILTER, VCO
Mapping the equivalent voltage value for the UP and DN signal from the PFD block.
Verified different modes of PLL .
Power down Condition:
  When PLL_PDB is low, outputs are reset.
Normal Operation:
  In normal operation, PLL_PDB is high

## Slide 19: PLL CASE STUDY contd..
All the inputs of the PLL dividers which are in digital were driven/controlled by UVM TB.
Fixed stimulus e.g., Analog stimulus for analog pins were assigned in the uvm tb_top.
Fixed input frequencies were given from UVM Test Bench and verified.
Similarly input frequencies randomly selected in the range 19.2MHz to 104Mhz to get different output range of frequencies.
Different input dividers were selected randomly from UVM TB to get desired frequencies.
For Frequency output: The equation logic was incorporated in the monitor which is further passed to score board to compare the actual and expected, for “pass”/”fail” criteria.

## Slide 20: PLL Results
we have achieved 100% functional coverage for stand-alone verification.
We have achieved code coverage close to 100%

## Slide 21: End to End Verification
Digital controls were controlled through attribute/ register .
To verify the TX path, transmitted the data after setting the MODE and GEAR through registers from RMMI TX driver and captured the DPDN TX data at the DPDN Agent.
To verify the RX path, setting the MODE and GEAR through registers from RMMI RX driver and the data is transmitted from DPDN driver & RMMI RX agent will capture the data
The data integrity is checked in the scoreboard
Real values are converted to bits ($realtobits)
Real values are propagated as analog signals using uvm_real
HS_BURST and PWM_BURST Transfers were verified

## Slide 22: RX, TX transactions
Analog RX
8b/10bi8bit/10bit Decoder
RX_Rmmi
10bit symbol data
Analog TX
8b/10bit Encoder
TX_Rmmi
8bit symbol data

## Slide 23: Portion of run script
irun -uvm -TIMESCALE 1ns/1ns -v93 -messages -sv -linedebug -svseed $user_seed -licqueue \
irun -64bit -uvm -timescale 1ns/1ps \
+mixedlan -dpiheader svdpi.h -nowarn TRNEGDEL \
+wreal_res_info \
-wreal_resolution sum \
-access rwc \
-linedebug \
#-f ./flist.f \
-f ../compile/mphy_analog_model_compile_list_WREAL.fl \
-f ../compile/mphy_rtl_compile_list.fl \
-f ../compile/mphy_wreal_tb_compile_list.fl \
+UVM_TESTNAME=$testcase_name \

## Slide 24: ISSUES AND CHALLENGES
HS_BURST & PWM_BURST both were enabled simultaneously (which is not recommended), and we could see HiZ on Analog TX where it should be ‘1’ or ‘0’.
Data conversion (8bit/10bit) was not happening properly, issue with 8bit /10 bit encoder, later it was resolved by designer.
Connectivity bug in analog were found by modeling when compared both schematic results and model results.

## Slide 25: TB BLOCK DIAGRAM

## Slide 26: SCORE BOARD DIAGRAM

## Slide 27: SEQUENCE FLOW

## Slide 28: ASSERTIONS/CHECKERS
Example
always@(posedge clk)
assert((1.68 < = top.VDDH_SUPPLY)&& (top.VDDH_SUPPLY<= 1.8))
else $error (“supply > 1.8”)
always@(posedge clk)
assert((0.68 < = top.VDDH_SUPPLY)&& (top.VDDH_SUPPLY<= 0.8))
else $error (“supply > 0.8”)
Support for wreal in PSL: wreal net type represents a real-valued physical connection between structural entities in some vendor implementation of the verilog AMS language.
Expressions involving such wreal type objects that are explicitly declared can appera within PSL assertions in boolean expressions, clocking expressions ans as actual arguments in property and sequence instances.
wreal mywreal1, mywreal2;
reg clk;
// psl assert always ((mywreal1 > 1.68; mywreal2 < 1.8))@(posedge clk);
Analog events in assertion clocking:
verilog-AMS (electrical) analog event functions cross and above are supported as clocking events in PSL assertion.
Electrical sig1, sig2, sig3;
reg a, b;
//psl assert always ((V(sig1)>0.0;a) |=> (V(sig2)<0.3;b)) @ cross (V(sig3)-0.0));

## Slide 29: ASSERTIONS/CHECKERS Contd..
Threshold_checker: Checks that analog signal remains within a given high and low threshold. Can perform this check synchronously or asynchronously.
Frequency_checker : Checks that analog signal frequency is within a given tolerance.
Stability_checker: Checks that analog signal remains below or above a given threshold. Can perform this check synchronously or asynchronously.

## Slide 30: Results
End to end Results:
MPHY_TOP:
code coverage: 79.84%
functional coverage: 100%

## Slide 31: Results Contd..
MPHY_ANA_TOP Results:
Code coverage: 73.63%
Functional Coverage: 100%

## Slide 32: Coverage group and Cover points

## Slide 33: Acknowledgements
We would like to thank Ranganath Polimera, Thyagarajula Naidu Gurajala, Anoop MS and Ramprasad Banakar for their vital contribution, help and support during the project execution.

## Slide 34: References
www.mipi.org
www.accellera.org
www.cadence.com

## Slide 35: Questions?
Thank you for your Interest and Time