## Slide 1: Making Formal Property Verification Mainstream: An Intel® Graphics Experience
M Achutha KiranKumar V
Bindumadhava S S
Abhijith A Bharadwaj

## Slide 2: AGENDA
Why?
Need for FV Deployment Drive
How?
VPG FV Deployment Planning and Execution
What was Achieved?
Results of FV Deployment

## Slide 3: Need of FV Deployment Drive
Formal needs no introduction:
  Established 100% state space coverage
  NO/Minimal Bug Escapes
  High Verification Confidence
  Testbench Free Verification
  Various dedicated Apps for Specific problems:
    RTL Equivalence Sequential Check, Connectivity, X verification, Security, Low power, etc
Still…
Why are the FV adoption rates are still low?
Why was the dedicated FV deployment drive in VPG needed?

## Slide 4: Need of FV Deployment Drive
Common FV Roadblocks:
  FEAR:
    MYTH: FV is only meant for PhDs
    MYTH: Will drain my time/resources
                No Progress Metrics
                No intermediate check-points
  ROI:
    TRUTH: What eventually matters?: ROI
    How to compare with DV results?

## Slide 5: AGENDA
Why?
Need for FV Deployment Drive
How?
VPG FV Deployment Planning and Execution
What was Achieved?
Results of FV Deployment

## Slide 6: VPG FV Deployment Drive

## Slide 7: VPG FV Deployment Drive

## Slide 8: VPG FV Deployment Drive:
Survey
  Immediate needs for most of the users:
    Automated setup/property_coding
    Assertion Libraries for common design components
    Dedicated Trainings
    Local Contact Points

## Slide 9: VPG FV Deployment Drive: Preparation Phase
GUI creation
  Provided a quick setup
  interface to new users
  One stop shop for all formal
  flows
  Easy way of generating all
  collaterals for formal

## Slide 10: VPG FV Deployment Drive: Preparation Phase
Cookie-cutter Property
Templates
  Automated properties

## Slide 11: VPG FV Deployment Drive: Preparation Phase
Cookie-cutter Property
Templates
  Automated properties
  Standard Interfaces

## Slide 12: VPG FV Deployment Drive: Preparation Phase
Cookie-cutter Property
Templates
  Automated properties
  Standard Interfaces
  Arbiter Properties

## Slide 13: VPG FV Deployment Drive

## Slide 14: VPG FV Deployment Drive: Training Phase
Identifying Local Experts
  FV champion from each cluster
  Immediate support
Setting-up Self Help Materials
  Dojos
  FAQs
Training Dungeons
  2-week rigorous training

## Slide 15: VPG FV Deployment Drive

## Slide 16: VPG FV Deployment Drive: Test Planning Phase
Clear Goal Definitions
  Assigning FV problem to correct category
FV Problem
Full Proof
Only Bug Hunting
Equivalence Check

## Slide 17: VPG FV Deployment Drive: Test Planning Phase
Progress Continuum
  Defining measurable sub-goals
  Allows progress to be graded w.r.t. time
  Decided % completions to be achieved for each Val Milestone

## Slide 18: VPG FV Deployment Drive: Test Planning Phase
Activity Ownership
  Designer needs to monitor FV completion for his unit

## Slide 19: VPG FV Deployment Drive

## Slide 20: VPG FV Deployment Drive: Execution & Closure
Execution and Tracking
  Round-the-clock support extended to FV owners after dungeons
  Weekly FV progress tracked and published
Deep Bug Exploration
  Abstractions, different engine settings
  Lots of Covers added
Coverage and Closure
  Line and branch coverage obtained
  Properties added for holes

## Slide 21: VPG FV Deployment Drive

## Slide 22: VPG FV Deployment Drive: Communicate Results
ROI calculation standard was established
ROI numbers calculated for activity and compared against DV
Parameter | Depiction
Number of engineers worked on the problem | NE_F
Average bandwidth/engineer | BW_F
Number of weeks spent on effort | Ww_F
Total time spent in hours | Ts_F = Bw_F a Ww_Faa 40b
Project schedule in weeks | Pw_F
Scaled engineering costs | CE_F = Ts_F/(Pw_F a 40)
Machines used for computations | Mc_F
Runs/week | Rw_F
Number of days of run | Dw_F
Total machine-days/week | Tm_F = Mc_F a Rw_F a Dw_F
Project machine-days/week | Pm_F
Scaled machine costs | Cm_F = Tm_F/Pm_F
Coverage (% cover points hit) | Covtot_F
Bugs found by the method | NB_F
aAssuming eight hours/day for a five-day work week = 40 hours/week. bMachine runs are not limited to a working day but for the whole week | 
ROI Parameter | Formal | Dynamic | Relative
Bugs% found by FV | NB_F/(NB_F+NB_D) | NB_D/(NB_F+NB_D) | NB_F/NB_D
Total coverage achieved | Covtot_F | Covtot_D | 
Bug - engineering cost ROI | BEC_F = NB_F/CE_F | BEC_D = NB_D/CE_D | BEC_F/BEC_D
Bug - machine cost ROI | BMC_F = NB_F/Cm_F | BMC_D = NB_D/Cm_D | BMC_F/BMC_D
Coverage - engineering cost ROI | CEC_F = Covtot_F/CE_F | CEC_D = Covtot_D/CE_D | CEC_F/CEC_D
Coverage - machine cost ROI | CmC_F = Covtot_F/Cm_F | CmC_D = Covtot_D/Cm_D | CmC_F/CmC_D

## Slide 23: VPG FV Deployment Drive

## Slide 24: VPG FV Deployment Drive: Check-In & Regress
FV cannot be done once & forgotten
  RTL in constant churn
  Regressions to be enabled to find bugs due to changes

## Slide 25: AGENDA
Why?
  Need for FV Deployment Drive
How?
  VPG FV Deployment Planning and Execution
What was Achieved?
  Results of FV Deployment

## Slide 26: Results of VPG FV Deployment
Quality of reception:
  80+ engineers became FV experts
  15 bugs caught within 2 weeks of activity
FV is awesome; I write code, run FV before even committing it to my local repo, and get it clean.
If it wasn't for this tool, I'd be building micro-testbenches before the ULT is ready.
Found couple of dozen bugs even before DV was up and helped clean the RTL
On a FV Quality bug hit:
Hitting this bug in functional random env would have taken a long time and the bug is fatal enough to cripple the feature.
FV is the prime mode of validation for one of my unit. While DV gave me a bill of 6-8 weeks, we verified all the DCN changes in less than 2 weeks using FV
It uncovered many scenarios in the beginning for which the Fulsim tests came very late. it has given very high confidence that new RTL has achieved the original health.
Achutha KiranKumar V M, Intel Corp.
26

## Slide 27: Results of VPG FV Deployment
Quality of Bugs:
  85+ bugs caught in 12 weeks (activity was started after half way through DV drive)
  Most of the bugs caught fell in corner-case category
32-bit Internal Counter (CI)
A
B
If CI = 32’h8001_000; ABBB seq at I/P received
|-> CO = (CI – 2)
CO
Expected Value = 32’h8000_FFFE
Actual Value = 32’h8001_FFFE

## Slide 28: Results of VPG FV Deployment
ROI:
  Weighted ROI of 220x compared to DV
  Some activities gave as much as 138x w.r.t. engg costs; 3692x w.r.t. machine costs
Chart: FV ROI on Globals
| Bugs/Engg costs | Bugs/Machine costs
FV | 138.5 | 3692
DV | 1 | 1

## Slide 29: CONCLUSION
FORMAL VERIFICATION IS NOW FORMALLY IN THE PROJECT!!

## Slide 30: Questions