## Slide 1: Novel approach for SoC pipeline latency and connectivity verification using Formal
Deepak Mohan, Senior Engineer,
Senthilnath Subbarayan, Senior Staff Engineer, Sandeep Kumar, Principal Engineer
Qualcomm

## Slide 2: Agenda
Motivation
Introduction
Problem Statement
Proposed Methodology
Implementation
Implementation Advantages
Implementation Results
Conclusion
Q & A

## Slide 3: Motivation
Increase in design size and complexity.
Short Time to Market.
Overall verification window should be reduced.
Verification flow should be scalable.
Critical bugs should be caught at the earliest.
2019
2020
2021
2022
Gate count
SOC complexity
Gate Count vs Time

## Slide 4: Introduction
What are pipelines?
  Design elements introduced between SoC blocks to meet the timing requirements based on physical design feedback.
  Key pipeline specifications are,
    Pipeline latency (Delay)
    Finite State Machine ( based on AHB, AXI etc ..)
SoC
BLOCK A
BLOCK B
PIPELINE
Interface

## Slide 5: Problem Statement
  Latency verification for SoC pipelines is done during late stages of functional verification and thus right shifts critical bugs.
  Sideband signal coverage of SoC pipeline is also done during late stages of functional verification.
  For large number of SoC pipelines, latency verification and sideband signal coverage at early stages of DV can be laborious and time consuming.
  Manual work is not scalable and prone to errors.

## Slide 6: Proposed Methodology
Proposed approach consist of
  Automated Pipeline Utility which consumes connectivity, pipeline specification and generates CSV files , clocks, resets, and the constraints required for each pipeline.
  Formal connectivity checker application.
Pipeline specification (.xls)
Connectivity specification(.xls)
Automated Pipeline Utility
Connectivity CSVs in required format
Clock, resets and any other constraints required for pipeline
Commands file with required tool options
Formal Connectivity checker application

## Slide 7: Implementation
Pipeline Specification
Connectivity Specification
Automated Pipeline Utility
Connectivity SPEC
  Extracts the pipeline specification data.
Pipeline SPEC
  Extracts the connectivity information.
Generates constraints
  Generates CSV files using the information extracted above and interface specification.
Generates CSV
  Generates any constraints based on design hierarchy, if required, in specific format.
Generates clocks and resets
  Generates clock and reset information for the formal connectivity checker, in specific format.
Output CSV

## Slide 8: Implementation Advantages
Early pipeline latency verification.
Early sideband signal coverage.
Detects open ports in pipeline connectivity.
Detects signals which are not passing through the pipelines.
Connectivity verification through pipeline.
Open connections
Connections not going through pipeline

## Slide 9: Implementation Result
  Developed utility enables reduced verification environment setup time.
  Enables early detection of pipeline latency and connectivity bugs in multiple projects.
  Further, the utility is scalable on both dimensions :
    horizontally : w.r.t number of pipelines,
    vertically : Different levels of design implementation.
Chart: daYS
| Manual Effort | Automated Effort
Setup time | 21 | 1
Verification time | 10 | 10
* Assuming 100-200 SoC pipelines

## Slide 10: Implementation Result : An Example
Pipeline based on AXI4 Protocol
Processor
NOC
Awqos
Awqos (OPEN)
Awqos
Awqos
(TIED OFF)
If not caught early, this issue will be only found during performance verification stage (late stage of functional verification).

## Slide 11: Conclusion
SoC pipeline latency and connectivity verification flow using Formal technique enables left shifting of,
  Pipeline latency verification,
  Pipeline sideband signal coverage.
The proposed flow is scalable across design hierarchies.
Automated Utility reduces the environment setup time with a single click deployment.
Removes scope of manual errors in generating connectivity checkers.
Overall, the proposed flow reduces time/effort with increased verification quality.

## Slide 12: Thank you. Questions ?