## Slide 1: Obscure face of UVM RAL: To tackle verification of error scenarios
Subhash Pai, Analog Devices
Lavanya Polineni, Analog Devices

## Slide 2: Register Verification
Access all DUV registers
Might need to provide additional data e.g. device address
Error scenarios like
  Write into read only registers
  Access non-existent registers
  Protocol violations e.g. framing error
  Device in error state

## Slide 3: UVM RAL
UVM RAL advantages
  Allows protocol independent test cases
  Easy handling of register changes
  Standardized way to access registers
Use of UVM RAL for typical non-error scenarios is well understood and is widely used.

## Slide 4: Register Verification
Use of UVM RAL for error scenarios is not well understood
  How do we model DUV response for error scenario?
  How do we pass error information via UVM RAL API to driver?
Error stimulus has two traditional approaches
  Transaction/Sequence item based
  Configuration Object based
DUV response for error is normally handled with custom register models

## Slide 5: Transaction Method for Error Stimulus
Use transaction based sequence for register error scenarios
Sequence item captures reg addr, data and error but has a major limitation: No UVM RAL
  Code maintenance issues
  Difficult to re-use/Portability issues

## Slide 6: Config Method for Error Stimulus
Use configuration object for passing error.
  User can use UVM RAL API for error cases.
Use of Config object for passing error has drawbacks
  Mixing of Concerns
    Config object meant to capture static or quasi-static data .Error is dynamic in nature.
  Transaction data now present in two streams viz. sequence item and configuration object
    Mapping these two streams gets complicated for complex protocols e.g. pipelined and buffered transactions

## Slide 7: Extension Approach
Use extension argument of UVM RAL (read/write/update)
Extension argument used to transfer protocol specific data for RAL
  Use the same mechanism to pass error information
Advantages
  Use of RAL API allows easy code maintenance, re-use
  Error and transaction data is captured in a single stream

## Slide 8: Extension Argument
Error passed as extension
Extension arg received by adapter
Error info passed to the seq item

## Slide 9: Comparison of Error Stimulus
Feature | Seq Item | Config Obj | Extension Arg
UVM RAL API | No | Yes | Yes
Single Stream for Data and Error | Yes | No | Yes
Separation of Concerns | Yes | No | Yes
Stimulus

## Slide 10: Capturing Error Info
Use of enum for error capture would limit user to single type of error
Use multiple variables each representing one type of error
              Or
Create a single variable, each bit representing one type of error
Each bit represents one type of error
Different types of errors

## Slide 11: DUV Response for Error
DUV Error Response
DUV ignores transaction and no response is sent
DUV ignores transaction and error response is sent
DUV accepts transaction and error response is sent
Maintain old reg value
Use transaction value

## Slide 12: Modeling DUV Error Response
When DUV response is UVM_NOT_OK, UVM RAL resets the mirrored value of reg fields to zero.
  No longer can rely on RAL model to perform data comparison.
  Changing UVM library code to handle this limitation is highly undesirable
  Creation of custom register models is cumbersome, error prone and needs careful review
This issue can be resolved with proposed UVM register callback approach!

## Slide 13: Callback Approach for Error Modeling
Derive callback from uvm_reg_cbs
Override post_predict function
Register callback with fields
Update callback properties based on Txn Error
No need to change UVM library
Needs minimal change to verification environment
Callbacks are often used to model quirky registers

## Slide 14: Callback Fields
Callback will have two fields
  error_condition
  update_reg

## Slide 15: Callback Definition
Error condition
field retains
previous value
field value updated
to bus value

## Slide 16: Callback Registration
Callback instantiation
Callback registration

## Slide 17: Updating Callback
Error transaction
No response from DUV, maintain old value
Violation of access policy, maintain
Old value
DUV sends err response ,
updates to DUT value

## Slide 18: Summary
We recommend use of UVM RAL for Error Scenarios
  Use extension argument for Error Stimulus
  Use callback for modeling DUV response
Greatly reduces effort for verification of reg error scenarios
  No need to modify UVM library code or write custom models
  Easy to integrate into existing environment
  Callback code is generic and easily Re-usable for any protocol

## Slide 19: Questions