## Slide 1
PROBLEM STATEMENT
AUTOMATION ARCHITECTURE
Following are the objects of the Automation,
Transaction Tagging – Key Enabler for Automation
Infosys Limited, Bangalore, India
Email: Kamalesh_v@Infosys.com, Senthilkumar_n03@infosys.com, Kaustubh_Godbole@infosys.com, Deepak_Sadasivam@Infosys.com
Kamalesh V, Senthilkumar N, Kaustubh G, Deepak S
Pre-Silicon Debug Automation using Transaction Tagging and Data-Mining
Reference
Efficient Failure Triage with Automated Debug: a Case Study Author: Sean Safarpour, Evean Qin, and Mustafa Abbas
Advanced Techniques for RTL Debugging Author: Yu-Chin Hsu , Bassam Tabbara , Yirng-An Chen , Furshing Tsai
From RTL to Silicon: The Case for Automated Debug Author: Andreas Veneris, Brian Keng, Sean Safarpour
Debug Limited No More: The Case for Debug Automation Author: Andreas Veneris
Search, Match, Update
Over-all savings from method
Pre-Silicon Debug at Chip Level takes considerable effort and consumes about 30% of chip design cycle time. Often bugs are sighted late in the design-cycle resulting in re-work, re-spin and tremendous cost to company.
A Key enabler for automation is the ability to tag transaction in design and validation environment.
Such tagged transactions reveal a trace which can be interpreted by the architecture model.
The diagram shows two such fault traces in the SoC indicating potential fault in module I which can be used to classify the failure and auto-triage.
Known failures meta data (aka signature) is stored with in database.
Rules are coded to indicate match with known signatures.
Exact match triggers auto-triage.
When Exact match is not present, match with high correlation is looked for.
A high correlation leads to a new bucket entry formed.
A low correlation index triggers manual entry creation in signature database.
Regression/Log Reports | Checker Error Based Classification | Signature Based Classification
Number of Buckets in Typical Weekly Regression | 300 to 500 | 30 to 70
Number of known buckets auto triaged | 10 to 15 (approx. 3 %) | 10 to 20 (approx. 30%)
Number of buckets debugged every week | 150 to 200 (50% to 70%) | Usually 100 %
Life of bug in Full chip | Typically between 3 to 5 weeks to record a new signature | Typically 1 week to record new signatures.
Cross GEO co-ordination | Every day stand-up meeting in morning , followed by late night sync-up in 1:1 with counterparts on debug progress | Thrice a week call, less frequent 1:1 sync-up on debug progress
Objective | Method
Repository for failure Knowledge | If the failures are well documented in the tool, helps in easy coordination and communication.
Automatic Triaging | Reduce manual effort on well known signatures.
Meaningful Bucketing | Improve bucketing by incorporating architecture & transaction knowledge.
Assist in prioritization | Prioritize failures based on transaction types, signature frequency, DUT configuration etc.
Team Co-ordination | Need for efficient co-ordination and effective in cross-site communication.
A
B
C
D
E
F
G
H
I
J
K
L
M
N
Illustrative System-on-Chip Example
Individual block represents IP/Sub-system module
Rule Based Architecture Model