## Slide 1: Recipes for better Simulation Acceleration Performance
Vijayakrishnan Rousseau, Anoop Hc, Gaurang Nagrecha

## Slide 2: Agenda
Transaction Based Acceleration Overview
Identifying the bottlenecks in TB
Guidelines for improving performance
Multithreaded testbench : Radically uplift your gain
Results and Conclusion

## Slide 3: Transaction Based Acceleration Overview
Generator, Agent, Scoreboard are transaction based and part of the untimed domain executed by the simulator .
Driver, Monitor and DUT are timed and executed by the Emulator.
SIMULATOR
AGENT
SCOREBOARD
GENERATOR
CHECKER
EMULATOR
DUT
DRIVER
MONITOR
SCE-MI

## Slide 4: Identifying Bottlenecks in TB
TB bottlenecks are noticeable in Emulation.
Profile the Simulation for a set of tests.
TTot = TDut + TTB + TMisc
where
  TTot = total time taken for the simulation
  TDut = time spent by the simulator in DUT
  TTB = time spent by the simulator in testbench
  Tmisc = time spent in assertion etc.
Average time spent in TB is <25%, good case for Simulation Acceleration.

## Slide 5
SIMULATOR
DUT
BFM 1
Pseudo BFM 2
BFM 3
Identifying Bottlenecks in TB
Pseudo BFM –light weight behavioral code that mimics original BFM on a per test basis.
In simulation replace a BFM with pseudo BFM and re-profile.
If time spent in TB is reduced considerably then explore to optimize the BFM.

## Slide 6
SIMULATOR
DUT
BFM 1
Pseudo BFM 2
BFM 3
Identifying Bottlenecks in TB
Leaving the original BFM along with pseudo BFM will help identify in-efficient data structures in BFM.
BFM 2

## Slide 7: Guidelines for improving performance
Avoid array locators which will result in searching the entire arrays like find(), find_index.
logic [31:0] _Hash[*];
int indexQ[$];
indexQ = _Hash.find_index with ( item == 32’h111 );
In this example, call to find_index may result in an exhaustive search of the associative array which can slow down.

## Slide 8: Guidelines for improving performance
Associative arrays with large size of key can result in slowing down the TB.
Using a nested associative arrays (associative array of associative array) can help improve the TB performance.
class Key_Store;
bit [255:0] key_has[bit[127:0]];
endclass
class Field4_Class;
bit [255:0] Field4_HT[bit[31:0]];
endclass : Field4_Class
class Field3_Class;
Field4_Class Field3_HT[bit[31:0]];
endclass : Field3_Class
class Field2_Class;
Field3_Class Field2_HT[bit[31:0]];
endclass : Field2_Class
class Field1_Class;
Field2_Class Field1_HT[bit[31:0]];
endclass : Field1_Class

## Slide 9: Multithreaded TestBench
Each Agent is typically independent in most of the cases.
Separate TestBench for each of the Agents and executed as independent processes – Single Agent Simulations.
A multi-threaded C TestBench in which each thread on one end communicates with a Single Agent Simulation and on the other end communicateS with the Emulator.
Two inter process communication channels exist between each of the Single Agent Simulations one for transferring transactions from Simulator to Emulator and vice-versa.

## Slide 10: Multithreaded TestBench
SIMULATOR
AGENT
SCOREBOARD
GENERATOR
CHECKER
AGENT
SCOREBOARD
GENERATOR
CHECKER
AGENT
SCOREBOARD
GENERATOR
CHECKER
EMULATOR
DUT
DRIVER
MONITOR
DRIVER
MONITOR
DRIVER
MONITOR
SCE-MI
C TESTBENCH
THREAD 2
SCE-MI
SCE-MI
IPC
IPC
IPC
THREAD 1
THREAD 3

## Slide 11: Results
Certain tests originally took >1 day to run on emulator. BFM was recoded to get rid of array locator methods and use basic methods. With this change, the tests completed in <20min.
Slowness for certain real world workloads was root-caused to a BFM by using the pseudo BFM approach. Huge associative arrays were replaced with nested, smaller arrays. This resulted in drastic improvement of runtime from >5hours to <10min.
Multi-threaded TB gives > 3x over the default single-threaded transactor-based acceleration
Notes: The techniques discussed in the current paper were applied and implemented for the simulation acceleration of a DUT with 10M gate count. These resulted in substantial performance improvement.

## Slide 12: Conclusion
Bottlenecks in TB are prominently seen in emulation and will limit the performance gain. Identifying the bottlenecks in TB and fixing them is key to maximize the gain in emulation.
Multi-threaded TB setup can be implemented for TB in which the agents do not communicate with each other.

## Slide 13: Questions