## Slide 1: Reusable UVM_REG Backdoor Automation
Balasubramanian G, Design Services, PMC-Sierra India Pvt Ltd.

## Slide 2: Agenda
Verification challenges
What is IP-XACT?
Limitations of IP-XACT and vendor tool automation.
Custom Automation Solution
Testing and Statistics
Summary

## Slide 3: Verification challenges
Notes: SoC designs have become modular and complex and configurable registers have increased in an SOC.
Block level designs have programmable registers in them. These block level designs are reused in SOC or top-level environment.
Programming a register through a BUS protocol (like APB, AXI, etc.) consumes considerable simulation time. Configuring or bringing up a Device level DUT through front door access takes high wall clock times or CPU time.
Backdoor access becomes increasingly valuable.
Backdoor access at block level needs to be reused at SoC level
Need for custom backdoor automation explained in this paper.

## Slide 4: IP-XACT and Register definitions
Programmable registers are captured in IP-XACT XML format.
iregGen vendor toolset parses the IP-XACT XML and generates UVM_REG register definitions.
Backdoor access forces or probes a RTL net directly.
Notes: The types of a register, register fields, register access types (like RO, RW, W, RW1C), default value, etc are captured in IP-XACT XML format.
Made use of cadence iregGen toolset to convert the IP-XACT XML to UVM_REG register definitions.
We try to add backdoor paths to the UVM_REG registers defined above.
Backdoor RTL net path needs to be set for every register defined in verification.

## Slide 5: IP-XACT and vendor tool limitations
RTL implementation of a register field could not be captured properly.
Notes: Typical register field implementation can blast every bit defined inside a register field into separate HDLPATHs in design.

## Slide 6: IP-XACT and vendor tool limitations
RTL implementation of a register or an array of registers could not be captured.
Notes: First part tries to capture a single dimensional array of registers. Every bit of a register instance can point to different HDLPATHs in RTL.
Second part tries to capture a multi-dimensional array of registers. Every bit of a register instance can point to different HDLPATHs in RTL.

## Slide 7: IP-XACT and vendor tool limitations
Capturing combination of sub-fields and arrays in IP-XACT is challenging.
Handling or splitting HDLPATH instantiation hierarchy.
setting HDLPATHs to composite registers.
Notes: ireggen toolset uses vendorExtensions:hdlpath tags to capture the design path to the actual register.
Hdlpath tags cannot be customized based on pattern matching other than indices of the array.
Not possible to Capture arrays using hdlpath tags.
Some design paths do not have sufficient hierarchy.
Some register fields are implemented as vectors and some others are implemented as single bits.

## Slide 8: Custom Backdoor Automation solution
Register declarations captured in IP-XACT XML format.
register hdl_paths captured in separate backdoor XML file.
Notes: Backdoor XML contains one-to-one mapping of a register bit to its design PATH.
The backdoor XML contains heterogeneous information with respect to actual design path to allow user customization.

## Slide 9: Custom Backdoor Automation solution
script parses the backdoor file and...
Creates a derived class that inherits the top-level class of the front door register file generated by iregGen toolset
Extends build method to setup hdlpaths to a single bit and instance of an array as follows:
  REG_BLK.SAMPLE_REG1.add_hdl_path_slice("xcbi_nregs_m0.singlebitr1_0x0.dout", 29, 1, “RTL”);
  REG_BLK.rsvd.SAMPLE_REG2[1].add_hdl_path_slice(“xcbi_nregs_m0.multibitrw_0x104”, 0, 32, “RTL”);
Use add_hdl_path() configuration to add additional hdlpaths to the hierarchy.
  REG_BLK.add_hdl_path(“top_testbench.dut.block_inst1", “RTL”);
Notes: add_hdl_path_slice() method gives us the freedom to map individual bits, arrays etc., to some hdlpath.
The scripts creates add_hdl_path_slice() commands based on the RTL implementation.

## Slide 10: Results and statistics
Number of register access | CPU time (sec) taken for frontdoor access | CPU time taken (in seconds) for backdoor access | Acceleration
100 | 5 | 1 | 5x
1000 | 50 | 3 | 17x
10000 | 418 | 19 | 22x
100000 | 4567 | 208 | 22x
Notes: We used a simple test bench that verifies a AXI slave DUT that has registers in it.
We instantiated the register model after backdoor automation.
CPU time taken to perform a write followed by read in front door and backdoor modes were compared.

## Slide 11: Results and statistics
Chart: 
| 100 | 1000 | 10000 | 100000
backdoor | 0 | 2 | 19 | 208
frontdoor | 5 | 50 | 418 | 4567

## Slide 12: Results interpretation
Front door access typically happens through AXI protocol (in our test environment).
Results indicate that backdoor is 20+ times faster than the front door access.
  In practice, the acceleration will always be better than reported here: The DUT used for testing was very simplistic .
Backdoor access reduces simulation configuration time of an SOC.
Notes: Front door access has to go through the VALID/READY handshaking of AXI BUS protocol.

## Slide 13: Summary
HDLPATHs can be incrementally setup based on hierarchy to enable reuse backdoor information
Backdoor automation can drastically reduce simulation time.

## Slide 14: Thank you… Questions???