## Slide 1: Thinking In Transactions Visualizing and Validating
Rich Edelman, Mentor
Mustufa Kanchwala, Mentor

## Slide 2: Waveform Debug
Waveform Debug is what happens most often to find problems
Why is this signal ‘1’?
Which signal changed most recently?
How many edges have happened since time 10?

## Slide 3: Transaction Debug
Sometimes Transaction Debug is used to find problems
Why did this transfer take so long?
Is any transfer causing delay of other transfers?
How many bytes per second are being transferred?
What’s the state of the cache? How many flushes have happened?

## Slide 4: What is a Transaction?
A transaction is an event. It occurs at some time.
It might have a begin time and an end time. It might other have a begin time.
It might have attributes: ADDR, DATA, ID, etc.
A transaction might represent
  A bus transfer
  A cache read or write
  A cache flush
  An ALU operation

## Slide 5: Transaction Viewing
You can “see” things with transactions
Two simple RW channels on the initiator

## Slide 6: Stripe Viewing
Search / Filter
  Find WRITE transactions with address between c00 and fff
  There are 40 of them

## Slide 7: Creating Monitors
UVM Monitor
  Implement a write routine and connect analysis ports.
    ap.write(t)
PLI based transaction recording
Simple CSV generator

## Slide 8: UVM Monitor
class monitorA extends uvm_monitor;
`uvm_component_utils(monitorA)
virtual abc_if vif;
uvm_analysis_port #(sequence_item_A) ap;
sequence_item_A t;
task run_phase(uvm_phase phase);
forever begin
@(posedge vif.CLK);
if ((vif.READY!==1) || (vif.VALID!==1)) begin
t = sequence_item_A::type_id::create("t");
t.rw = vif.RW;
t.addr = vif.ADDR;
if (t.rw == 1) begin /* READ */ end
else begin /* WRITE */ end
ap.write(t);
end
endtask
endclass
class recorder extends uvm_subscriber#(sequence_item_A);
`uvm_component_utils(recorder)
function void write(sequence_item_A t);
$display(“...”);
endfunction
endclass

## Slide 9: PLI based transaction recording
Instrument code with PLI calls.
  Begin
  End, Free
  Add Attribute
For example, recording transactions
Every vendor has a set of these routines
task READ(transaction t);
tr = $begin_transaction(stream, "READ");
$add_attribute(tr, t.tag, "tag");
$add_attribute(tr, t.addr, "addr");
$add_attribute(tr, t.qos, "qos");
...
$add_attribute(tr, t.data, "data");
$end_transaction(tr);
$free_transaction(tr);
endtask
http://www.boyd.com/1364_btf/report/full_pr/attach/435_IEEE_TR_Proposal_04.pdf

## Slide 10: Example design
FABRIC
FABRIC
TARGET
(memory)
INITIATOR
(master)
monitor
monitor
monitor
monitor
monitor
monitor

## Slide 11: The Bus - Channel
Simple Bus – ready/valid signaling
  READ
    RA – Read Address
    RD – Read Data, with byte count
  WRITE
    WA – Write Address
    WD – Write Data, with byte count
    B – Write Response
typedef bit [ 31:0] tag_t;
typedef bit [ 31:0] addr_t;
typedef bit [127:0] data_t;
interface channel(input wire clk);
logic RA_ready; // RA Channel
logic RA_valid;
tag_t RA_tag;
addr_t RA_addr;
int RA_beat_count;
logic RD_ready; // RD Channel
logic RD_valid;
tag_t RD_tag;
int RD_beat_count;
data_t RD_data;
...
endinterface

## Slide 12: The Monitor
Simple monitor
  @posedge clk
  Ready && Valid
  “Transaction”
interface monitor_interface(channel bus);
always @(posedge bus.clk)
if ((bus.WA_ready == 1 ) && (bus.WA_valid == 1)) begin
end
always @(posedge bus.clk)
if ((bus.WD_ready == 1 ) && (bus.WD_valid == 1)) begin
end
always @(posedge bus.clk)
if ((bus.RA_ready == 1 ) && (bus.RA_valid == 1)) begin
end
always @(posedge bus.clk)
if ((bus.RD_ready == 1 ) && (bus.RD_valid == 1)) begin
end
always @(posedge bus.clk)
if ((bus.B_ready == 1 ) && (bus.B_valid == 1)) begin
end
endinterface

## Slide 13: Simple Instrumented Code
Info about “outstanding transactions”
  Struct of useful information
  Associative array (index by TAG)
Display a CSV “Header Row”
typedef struct {
time begin_time;
time end_time;
int number_of_bytes;
bit first_RD_beat;
bit first_WD_beat;
} outstanding_t;
outstanding_t outstanding[int];
initial begin
if (onetime == 0)
$display("CSV: HEADER: name,rw,tag,begin,end,nbytes,mbps");
onetime = 1;
end

## Slide 14: Simple Instrumented Code – Read Channel
BEGIN a transaction -> RA
  Save the time and set a flag.
always @(posedge bus.clk) begin
if ((bus.RA_ready == 1 ) && (bus.RA_valid == 1)) begin
stats["RA"]++;
outstanding[bus.RA_tag].begin_time = $time;
outstanding[bus.RA_tag].first_RD_beat = 1;
-> stat_change;
end
end

## Slide 15: Simple Instrumented Code – Read Channel
RD Phase. Data byte. If it is the first, remember the byte count.
always @(posedge bus.clk) begin
if ((bus.RD_ready == 1 ) && (bus.RD_valid == 1)) begin
outstanding[bus.RD_tag].end_time = $time;
if (outstanding[bus.RD_tag].first_RD_beat == 1) begin
outstanding[bus.RD_tag].first_RD_beat = 0;
outstanding[bus.RD_tag].number_of_bytes = bus.RD_beat_count*16;
end

## Slide 16: Simple Instrumented Code – Read Channel
RD Phase. Last Data Byte
else if (bus.RD_beat_count == 0) begin
Mbytes_per_second =
real'(1000 * outstanding[bus.RD_tag].number_of_bytes) /
real'(outstanding[bus.RD_tag].end_time –
outstanding[bus.RD_tag].begin_time);
$display("CSV: STAT: %m,READ,%0d,%0t,%0t,%0d,%0f",
bus.RD_tag,
outstanding[bus.RD_tag].begin_time ,
outstanding[bus.RD_tag].end_time ,
outstanding[bus.RD_tag].number_of_bytes,
Mbytes_per_second
);
outstanding.delete(bus.RD_tag);
end
end
end

## Slide 17: CSV Database
grep CSV transcript | sed –e ‘s/^CSV.*: //’ > transactions.csv
name,rw,tag,begin,end,nbytes,mbps
top.mono0,WRITE,4098,2640,22960,32,1.574803
top.monm0,WRITE,4098,1960,26040,32,1.328904
top.mono1,WRITE,344065,1480,27280,208,8.062016
top.monm1,WRITE,16385,1060,28960,208,7.455197
top.moni1,WRITE,2,1480,29120,32,1.157742
top.mono0,WRITE,4100,11960,29600,192,10.884354
top.mono0,WRITE,4102,12440,30080,16,0.907029
top.moni0,WRITE,1,440,30640,208,6.887417
top.monm0,WRITE,4100,8840,31480,192,8.480565
top.monm0,WRITE,4102,9320,31960,16,0.706714
...
top.monm1,WRITE,16389,9040,44320,0,0.000000
top.moni0,WRITE,5,5600,47540,0,0.000000
top.mono1,READ,348169,38880,49380,32,3.047619
top.mono0,READ,10,34160,51260,224,13.099415
top.monm1,READ,20489,35560,52880,32,1.847575
top.mono1,WRITE,344071,12400,53360,176,4.296875
top.monm1,WRITE,16391,9140,53400,176,3.976502
top.moni0,WRITE,7,6100,53440,176,3.717786
...
$display("CSV: STAT: %m,READ,%0d,%0t,%0t,%0d,%0f",
bus.RD_tag,
outstanding[bus.RD_tag].begin_time ,
outstanding[bus.RD_tag].end_time ,
outstanding[bus.RD_tag].number_of_bytes,
Mbytes_per_second);

## Slide 18: Infrastructure
Python
Flask
D3.js
Simulation
CSV
SQL DB
Web Server
Python
Flask
D3.js
Visualization

## Slide 19: Schema
What’s a transaction?
  Data transfer
  Cache state change
  Memory Read/Write
  For our purposes a simple definition
CREATE TABLE ttransaction (
name text,
rw text,
tag integer,
begin integer,
end integer,
nbytes integer,
mbps real)

## Slide 20: Populating the SQL database
import csv
import sqlite3
conn = sqlite3.connect('transaction.db')
cur = conn.cursor()
cur.execute("""DROP TABLE IF EXISTS ttransaction""")
cur.execute("""CREATE TABLE ttransaction
(name text, rw text, tag integer, begin integer, end integer,
nbytes integer, mbps real)""")
with open('transaction.csv', 'r') as f:
reader = csv.reader(f.readlines()[1:]) # exclude header line
cur.executemany("""INSERT INTO ttransaction VALUES (?,?,?,?,?,?,?)""",
(row for row in reader))
conn.commit()
conn.close()

## Slide 21: Running SQL Queries
Just SQL…
Simple queries
Full power of SQL available.
SELECT * FROM ttransaction;
SELECT * FROM ttransaction where name = 'moni0';
SELECT SUM(nbytes) FROM ttransaction where name = 'moni0';
SELECT SUM(nbytes) FROM ttransaction where begin between 5000000 AND 6000000;
SELECT name,nbytes FROM ttransaction;
SELECT name,SUM(nbytes) FROM ttransacction GROUP BY name;

## Slide 22: Flask…
View the whole database  http://192.168.122.1/viewdb
View a specific “RW”  http://192.168.122.1/rw/WRITE
View a specific “monitor”  http://192.168.122.1/name/monm0
@app.route("/name/<name>")
def fname(name):
rows = execute_query("""SELECT * FROM ttransaction WHERE name = ?""", [name])
return '<br>'.join(str(row) for row in rows)
@app.route("/rw/<rw>")
def sortby(rw):
rows = execute_query("""SELECT * FROM ttransaction WHERE rw = ?""", ([rw]))
return '<br>'.join(str(row) for row in rows)
@app.route("/viewdb")
def viewdb():
rows = execute_query("""SELECT * FROM ttransaction""")
return '<br>'.join(str(row) for row in rows)

## Slide 23: Bandwidth Visualization
Draw the graph  http://192.168.122.1/bw
Bw.html contains the smarts
  About 80 lines of javascript
  Uses d3.js
  Magic!

## Slide 24: Flow Visualization

## Slide 25: Other Visualizations

## Slide 26: What we’ve done
Instrument the simulation
Simulate
Collect Info into an SQL database
Use web infrastructure including
  Flask
  D3.js
Now the hard part – use your imagination to create visualizations that are important to you.

## Slide 27: Questions
Contact authors for source code