## Slide 1: Transactional Memory Subsystem Verification for an ARMv8 server class CPU
Ramdas M
Parveez Ahamed
Brijesh Reddy
Jayanto Minocha

## Slide 2: Agenda
Memory Sub System Verification Challenges
Transactional Integration Test bench Overview
Stimulus generation
Test bench configurations
Tests/Controls
Results

## Slide 3: Introduction
X-Gene® family ARMv8 CPU
  First enterprise class 64-bit ARMv8 server CPU
  Unique grounds-up high performance, custom core ARM®v8 64-bit server
  Highly scalable multi-core memory subsystem with a custom coherency protocol implementation

## Slide 4: Multi Core Memory Sub System

## Slide 5: Multi Core Memory Sub System
Challenges
  Huge Verification space
    Large number of cores, IO agent, Multiple levels of caches
    Transaction types, responses, cache states
    Coherent , Non-coherent and IO traffic
    Multiple configuration options in each subsystem component
    Micro architectural details across units (FIFOs, arbiters etc)
    Cross product of all of above is huge

## Slide 6: Multi Core Memory Sub System
Challenges
  Stimulus Generation
    Instruction level stimulus doesn’t give good controllability
    Over constrained random stimulus not efficient for Subsystem
    Unit level verification not sufficient for memory coherency
    Standard Multi processor algorithms need to be simulated
    Long harmonic patterns to stress cache state transitions, address collisions, resource starvation etc
Memory coherency and ordering best verified at sub-system level to stress micro architecture

## Slide 7: Transactional Testbench Overview
Highly configurable integration testbench
  One or more units can be configured to be RTL/Model
Maps Instruction Set to Transactions for memory access
  Self checking Sequences for multiprocessor stimuli
  Improves simulation efficiency
Complex Scenarios to stress micro architecture
  Focus on deadlock/live lock, resource starvation etc
Enables early performance benchmarking
  Focus on memory bandwidth/latency at sub-system level

## Slide 8: Stimulus Generation
Multi processor specific Stimuli
  Producer/consumer scenarios
  Spin lock, Message passing algorithms
  Barriers, locks, semaphores
Implemented as C/Assembly programs traditionally
  Needs full CPU core in simulation
  Control between C tests and BFMs in SV world hard
Implement as self checking sequences at Subsystem
  Runs faster and can be mixed with other random stimuli

## Slide 9: Instruction Set in Transactional Domain
Every instruction set or a software program has following basic constructs
  Sequential execution
  Loops (for, repeat , while)
  Two-way Decision (if .. else .. )
Each construct can be mapped to a sequence if we implement response channel on the sequence-driver API

## Slide 10: Mapping Program Constructs to Sequences
Program construct | Translated sequences
if (flag==0) { do_something(); } else { do_something_else(); } | read_get_response_seq.start(); if (response ==0) begin do_something(); end else begin do_something_else(); end
while (flag =0) { do_something(); } | read_get_response_seq.start(); while (response_data ==0) begin do_something(); read_get_response_seq.start(); end
wait (flag ==1) | do begin read_sequence.start(); rand_delay(); end while (response data != 1)

## Slide 11: Sample MP constructs
Basic building blocks for MP programs |  | Equivalent Sequence Style | 
atomic increment: loop: ldex r1, addr r1 += 1 stex r1, addr retry loop if stex_fail |  | do begin r1 = rd_get_resp_seq (addr) r1 = r1+1;(); excl_pass = write_excl_seq (addr, r1); end while ( !excl_pass) | 
flag=0; data=0; producer: while(flag!=0) {}; data =1; flag =1; | Consumer: while (flag !=1){}; print data; flag =0; | Producer: rd_wait_seq(flag,0) write_seq (data,1) write_seq (flag,1) | Consumer: rd_wait_seq(flag,1) rd_seq (data); write_seq (flag,0);
DMB (Memory barriers) |  | barrier_seq(): -drive flush stores -wait till no pending stores | 

## Slide 12: Stimulus Generation
Complex System Level Scenarios
  Higher level system scenarios translated to multiple lower layer sequences
  Focus on Concurrent Stimulus
  Address Generation Controls
  Controlled delays and repeated sequence execution to create long harmonic patterns

## Slide 13: Stimulus Generation
Multi-stage generation for stressing micro architecture
  Each stage of stimulus generation changes various settings/modes, targeting individual buffers/FIFOs/arbiters in the cache/switch.
  Dynamically adjust weights for each stage controlled with monitors that probe stress points in the RTL.

## Slide 14: Test bench Hierarchy

## Slide 15: Configurability of Testbench
Test bench configuration
  One or more units can be configured as RTL/Model
  Enables early integration testing as soon as 2 units are stable
  Enables picking efficient configuration for different category of tests
Design configuration
  Large number of configuration options across multiple unit
  Uniform configuration mechanism at unit level helped

## Slide 16: Tests/Controls
Test starts one or more virtual sequences
  Higher level scenarios with self check
    Atomic increment, Writes with barrier, False sharing pattern, Read-Modify-Write etc
  Random irritator sequences
  Random configuration using knobs

## Slide 17: Reuse from unit level Verification
Reuse from Unit level enabled by OVM
  All Sequencer/Drivers/Checkers/Monitors
  All configuration classes and knobs
  Base sequences from unit level
Feedback to enhance unit level verification for better integration testing
  Uniform configuration at each unit level verification
  Coding unit level sequences with Request-Response style

## Slide 18: Results
Rapid progress on integration testing
  Integration testing started as early with two units ready
  Uncovered integration level bugs early in design
Reduced Time, effort and resources
  Better Simulation efficiency compared to programmatic stimulus
  Reused unit level components and base sequences to create efficient SubSystem level stimulus
  No over constraining of random stimulus

## Slide 19: Results
Feedback to strengthen unit level verification
  Feedback in terms of coverage and coding styles
  Feedback in terms of real system delays to unit level stimulus
Enabled early performance benchmarking
  Memory latency/bandwidth analysis started much before full chip simulations

## Slide 20: Questions