## Slide 1: UVM-RAL: Registers on demand Elimination of the unnecessary
Sailaja Akkem
Microsemi Corporation, Hyderabad

## Slide 2: Agenda
UVM RAL high level overview.
Conventional Register Modelling.
Dynamic Register Modelling.
Functional implementation of dynamic modelling.
  Issues.
  Solutions.
A Verification environment using dynamic register modelling.
Performance Metrics.

## Slide 3: UVM RAL high level overview

## Slide 4: Register Model Fabric

## Slide 5: Base classes
Significant UVM RAL base classes: uvm_reg, uvm_reg_field, uvm_reg_block.
  Provide utilities to establish register model framework in both static and dynamic register modelling.
  Provide quintessential APIs for performing backdoor and front door writes (through any element in the hierarchy).
  Versatile enough so as to customize the register model to replicate any type of design.
Hence these base classes could not be eschewed in our Environment.

## Slide 6: Conventional Register Modelling
FACTORS AFFECTING PERFORMANCE
OVERHEAD DUE TO SIZE OF COMPILED DATA
SIMULATION OVERHEAD DUE TO SUPERFLUOUS HANDLES

## Slide 7: Conventional Register Modelling – Overhead due to compiled data
Creates a class prototype for standard building elements: register block, register and field.
  Usually auto generated and compiled into a package and loaded into simulation.
  Model is built top-down.

## Slide 8: Conventional Register Modelling – Overhead due to compiled data (cont.)
Register Model class prototypes serve chiefly two purposes:
  Maintain hierarchy of registers.
  Contain all the necessary information for creating bus transaction.
Register Model is created by parsing Register specification document.
  Typically in the form of Mark Up Language file.

## Slide 9: Conventional Register Modelling –Overhead due to superfluous handles
During simulation, handles are created for every Register Model element.
In a standard test, number of registers that need to be accessed is in hundreds.
Simulator is laden with handles and compiled class prototypes, which are superfluous to the requirement being verified.

## Slide 10: Dynamic Register Modelling - Conventions
Register Elements:
  primary constituents of the Register Model (i.e., Register group, Register, Field).
Custom Register Element:
  Classes which extend UVM RAL base register element classes (i.e., “uvm_reg_block”, “uvm_reg”, “uvm_reg_field”).
  Contain couple of maintenance API’s to smoothen the process of dynamic register modelling.
  Can be further overridden to support any project specific requirements.
Structures that we see in the dynamic register modelling are:
  Place holders for attributes of register elements.
  Not substitutes for actual register elements in the dynamic register model but instead aid the building up of model dynamically.
  Attributes of registers mean: “address”, “hdl_paths”, “parent” etc., Attributes of fields mean: “width”, “position in the address map”, “access_type” etc.,

## Slide 11: Dynamic Register Model Fabric
All the interactions to the register model occur only through custom core service.
Returns handles on request.
  Since handles are dynamically created, there is no simulation overhead of expendable handles.
Class prototypes are not needed.
  Reduces compilation overhead.
VERIFICATION ENVIRONMENT
CUSTOM CORE SERVICE
Maintenance of Register data base is done here by custom core service
UVM REG Base Classes
Custom Register Block
Custom Register
Custom Register Field
BACK DOOR / FRONTDOOR WRITES OR READS
ALL REGISTER ACCESS
FROM ENVIRONMENT
SV Structures with attributes of register elements

## Slide 12: Dynamic Register Modelling - Compilation Overhead circumvented
Two stages of parsing performed:
  Capture the information from register spec into a “TEXT FILE”.
    Independent of compilation process (i.e., compilation of verification environment does not depend on this parsing), done using a perl script.
    This first level of parsing creates a text file, containing relevant information necessary to construct a register model.
    The text file contains information for entire chip (or block for sub-chip level verification).
  Parse this text file further during simulation.
    This second level of parsing extracts information from the text file and stores it into intermediate “System Verilog structures” (Next slide).
    Custom core service uses these structures to create dynamic register model.
    This parsing should be done prior to any register requests (say during build_phase).
No Expensive class Prototypes
Less Compilation Overhead

## Slide 13: Dynamic Model Approach

## Slide 14: Simulation Overhead Check List
Chart: SIMULATION OVERHEAD
| COMPILED DATABASE
CONVENTIONAL REGISTER MODEL | 5
DYNAMIC REGISTER MODEL | 1

## Slide 15: Dynamic Register Model generation
Once information is available in structures, if any request for register/field access is made:
  Custom Core Service creates (instantiates) requested register element (register group or register or field elements extended from UVM RAL Base classes and overridden) and configures this instance using the attributes from the parsed SV structures,
  Creates the element hierarchy (If not yet created till then),
  And fits the element in the hierarchy.
Instantiation of register elements thus occurs only when requested.
  Thereby reducing the number of objects of classes in a simulation.

## Slide 16: Simulation Overhead Check List
Chart: SIMULATION OVERHEAd
| COMPILED DATABASE | SUPERFLUOUS HANDLES
CONVENTIONAL REGISTER MODEL | 5 | 2.5
DYNAMIC REGISTER MODEL | 1 | 1

## Slide 17: Functional Implementation of Dynamic Register Model - Issues
….But UVM RAL base classes are rigid.
  Do not allow register elements to be added into an existing hierarchy after block is locked.
  And without locking, any register write or read process cannot be performed.
No dynamic addition
If Reg block is locked
No Reg Element Process
If Reg block is “NOT“ locked
Write/
Read
Dynamic
Addition
MUTUALLY EXCLUSIVE

## Slide 18: Functional Implementation of Dynamic Register Model - Issues (2/2)
Nevertheless, UVM RAL base classes are versatile.
Following API hooks enable to re-configure the hierarchy at any point:
  “configure” function in registers and fields do not check for lock.
    Hence, “configure” function can be called anytime irrespective of whether the block is locked or not.
  These “configure” functions are the ones which create the hierarchy of register elements: They decide parent of a register element, address of registers, position of fields etc., which are the attributes of the register element.
  Similarly, number of hooks like “set_parent”, “set_hdlpath”, “add_map” etc., do not check whether the model is locked.
Use these hooks to resolve this quandary.

## Slide 19: Functional Implementation- Issues solved
Custom core service utilizes API hooks (previous slide) to:
  create a new register block handle with same attributes.
  (re-) configure the hierarchy to this newly created handle.
For attributes of any new register element (i.e., block/reg/field) which was not created yet (but requested to be created),
  custom core service uses information that was stored into structures (during build_phase).
Effectively uses semaphores and state variables to maintain synchronization.
Request to Core Service
Does the handle for block of registers exists?
- Create handle to custom register block class*
- Conditionally lock the register block.
- Perform any requested operation.
* Note: Custom register element classes (i.e., register block, register and field classes) extend UVM RAL Base register element classes.
Custom classes contain couple of maintenance API’s. These custom classes can be extended further (if needed) and request to override can be made to custom core service.
Does the handle for the requested register exist in the block of registers?
Is the block locked?
- Create handle to custom register class* and configure it.
- Return the register handle to perform the requested operation (i.e., write or read etc.,) on the handle.
- Create a new handle to the register block class and configure it with same attributes as the previous register block class (These attributes are present in structures).
- Reconfigure all the existing registers in that block to have this newly created handle (in above step) as their parent.
- Conditionally lock the model.
- Perform any requested operation.
UCT
YES
NO
YES
NO
NO
YES
- Return the register handle or perform the requested operation (such as read or write) on the handle.

## Slide 20: Access using the Custom Core Service
Custom core service is a singleton class, and can be accessed from any class in the test bench.
Access to all the handles of register elements is through Custom Core Service.
  To efficiently synchronize amongst all simultaneous requests.

## Slide 21: A Verification Environment using Custom Core Service (1/3)
Environment devised to meet the re-usability prerequisites.
Common configuration object in a VIP containing standard (IEEE for example) prescribed variables.
DUT configuration layer separate from VIP.
  Maps variables from common configuration objects into DUT’s registers.
  Performs register writes of the mapped variables.
  This map layer “may” change across the projects, but the common configuration object and the other elements of VIP “should” not change.
Similar approach is followed for statistics Agents.

## Slide 22: A Verification Environment using Custom Core Service (2/3)

## Slide 23: A Verification Environment using Custom Core Service (3/3)
CPU Writes using Custom core service is done through its singleton handle.

## Slide 24: Comparison chart
Conventional Register Model
Register elements’ prototypes defined at compile time.
Creates all handles in build function.
Cannot delete handles while keeping information intact.
Overhead when using functions like: update/mirror/get_*_from_name()
Dynamic Register Model
Register elements’ prototypes at run-time, further facilitated by overriding.
Creates handles only when needed.
Allows for handles to be deleted “and” re-constructed later.
Can use these utilities efficiently without exclusion checks

## Slide 25: Performance
Performance improvement comes because of:
  Static compilation & loading improvement.
  Elimination of superfluous handles’ creation in the test.
Improvement is seen in terms of:
  Speed of compilation and simulation.
  Process Memory consumption of simulation.
  Disk space usage of the compiled and simulated data base.

## Slide 26: Performance metrics
ATTRIBUTE | CONVENTIONAL REG MODEL DEPLOYMENT | DYNAMIC REGISTER DATABASE DEPLOYMENT
SIMULATION TIME | 3845.0685 Seconds | 3444.6392 Seconds
PROCESS MEMORY USAGE | 721105428 Bytes | 595249622 Bytes
SIM WORK DIR DISK USAGE | 403 MB | 282 MB
COMPILED DATA BASE DISK USAGE | 17 M | 4.2 M
ATTRIBUTE | CONVENTIONAL REG MODEL DEPLOYMENT | DYNAMIC REGISTER DATABASE DEPLOYMENT
SIMULATION TIME | 1362.83 Seconds | 1263.15 Seconds
PROCESS MEMORY USAGE | 707724820 Bytes | 568761830 Bytes
SIM WORK DIR DISK USAGE | 397 MB | 276 MB
COMPILED DATA BASE DISK USAGE | 17 M | 4.2 M
Performance metrics for ~525 register writes
Performance metrics for ~140 register writes

## Slide 27: Summary
Dynamic register implementation improves Simulation Performance.
Avoid expensive register class prototyping when not needed.
Create handles for register elements only when access is performed.

## Slide 28: Questions?