## Slide 1: UVM, VMM and Native SV: Enabling Full Random Verification at System Level
Ashok Chandran, Analog Devices

## Slide 2: Introduction
Latest Product in Blackfin Processor Family – BF70x
  Enhanced Core
  Low Power System
  Memory
  Peripherals
  Security

## Slide 3: Overall DV Methodology
Bottom Up Approach
  MDV for blocks
  Spec->Executable Vplan-> CRV >Coverage->QA
  Significant set of VIP in VMM/UVM/SV
Focus on System Level Verification
  Constrained random verification at system level
  Complemented by Formal for connectivity, glue logics

## Slide 4: System Level Approach
Core Independent Testbench
  Why ? – We work with Blackfin, ARM, Sharc Cores
  Uses BFM Driver for MMR and Memory access initiated by Core
  Enables peripheral and system oriented verification
Core System DV
  Dynamic Backdoor Memory load with random code generation
  Actual core executes random code (cache, data, execute)
Arbitration Mechanism between BFM and actual core

## Slide 5: System Level Approach
What we had - VMM based SoC Level Testbench
  Has worked well for past projects
VMM Features Used
  Register/memory Model
  Memory Allocation
  MS Scenarios
MS
MS Gen
X(A)
X(B)
X(C)
R
S(D)
S(C)
S(B)
S(A)
X(D)
Xactor Start-Stop
A,B,C and D represent different IO
S is a scenario of the IO
MS represents a multi-stream scenario
MS gen is a MS scenario generator
X is the xactor which handles the scenario
R is the xaction router and xactor manager
MS
MS
All transactions pass through common xaction router
Callback To Modify/drop Transactions

## Slide 6: Adopting UVM - Challenges
Industry trend - UVM is now preferred for block DV
Challenges for us in moving to UVM:
  Top level was VMM based
  Wide variety of VIPs
    Huge set of VMM based VIPs – Scenario Driven
    SV and pure Verilog Testbenches (file based)
    New UVM Testbenches – Sequence Driven
  Goals
    Randomize and execute across all VIPs independent of the Methodology
    Manage shared system resources effectively between all components
    Layered approach to ensure reusability
Unify the methodologies by a new layer on top for multi-peripheral verification

## Slide 7: Key Requirements
System Resource Management
  Shared resources should be managed
  Configuring system resources should be simplified
    Standard DMA, Interrupts, Pinmux, Interconnect priorities
Enabling VMM blocks inside UVM sequences
Block to system reuse of UVM agents
Multi-Peripheral Wrapper
  Allow to run VMM and UVM block together

## Slide 8: System Level UVM Platform
Migrated Top Level to UVM
  Takes time, but was an investment for future
Testbench Integration Approach Improved
  Components for UVM testbench – register model, mem, configuration are generated from spec directly
  Verilog side is instantiated for multiple instances and stitched by script based on pinmux spec – UVM config db helps pass interfaces

## Slide 9: System Level UVM Platform
Layered Approach
  Made migration to UVM easier
  Xactors were switched in place with UVM components
  New system transaction for UVM components

## Slide 10: System Level UVM Platform
Register Model Migration
  Had been using reg model from VMM
  Created the toplevel register and memory model in UVM
  The access methods were identical
  Scripts to change functions which differed

## Slide 11: Resource Allocation
Environment maintains a resource database
Resource Management is at input side itself (Lossy generator)
VMM transaction router queries the DB and drops if resource conflict is present

## Slide 12: Resource Allocation (contd .. )
In UVM side, system sequence checks resource DB

## Slide 13: Resource Allocation (contd .. )
Ensuring Randomness in allocation
  For Shared resources, need to ensure that randomly different sources should get the resource
  Ensured by starting all scenarios and sequences at the same time.
  Resource checking should be the first action in the system level virtual sequence for a uvm block.

## Slide 14: Resource Management
System resources (which are now allocated to each peripheral) are managed by individual system components
  DMA, Pinmux, Each interrupt Interface , Interconnect, Fault Management etc
  Manages all resource requirements for the peripheral
Block environments communicate to system resources via transactions and utility functions

## Slide 15: Resource Management (contd …)
DMA1
DMA0
n
UVM Block Testbench
VMM Block Testbench
Dm
Dm
Int
Int
Core 0 Int
m
R
R
VSr
X
Dr
Transaction router
TLM Port
TLM Port

## Slide 16: Running VMM block
Sequence
Running a VMM Scenario/MS Scenario
  Macros wrap VMM Scenarios under UVM sequences
  VMM scenario generators are instantiated inside the syslvl_vir_sequencer
MS Scenario
Scenario
Sequencer
MS Generator

## Slide 17: Running SV block
Pure Verilog/SV blocks present for some IO blocks
  File based – reading from file into Verilog arrays
  Arrays mapped to memories via UVM register model
  Read/write via backdoor of register model
Need to create components to randomize
Verilog Array
Agent Register
HDL Path

## Slide 18: Running UVM blocks
UVM Sequences can be run directly
Need to create system virtual sequence
  Performs system configuration
  Performs resource allocation
  Extends from common class to allow multi-peripheral seq
Sys Virtual Sequence
Sys Virtual Sequencer
SQR(A)
S(A)
SQR(A)
Block Sequencers

## Slide 19: Multi-Peripheral Sequence
Enables VMM and UVM blocks to run together
Macros create virtual sequences for uvm and vmm from common base class
Sequences are registered inside multi_periph_test
Randomly picks “N” sequences out of “M” registered items.

## Slide 20: Results
Integrated UVM and VMM into single environment
  Capable of randomly picking UVM/VMM/SV blocks
  Ensures random resource allocation
Ease of integration of new peripheral environments
Reused into other ADI projects
Many bugs caught through random verification
  First silicon sampling to customers

## Slide 21: Questions