## Slide 1: Verification Techniques for CPU Simulation Model
Sandeep Jain, Freescale
Gaurav Sharma, Circuit Sutra
TM

## Slide 2: Agenda
Simulation Models & Verification
The Design under Test
Related work
Our Methodology
Test Generation
Trace Generation
Trace Analysis
Conclusion & Future Directions

## Slide 3: Simulation Models & Verification
Simulation Models are used for a variety of purposes
  Design of systems
  Development of system operating policies
  Research to develop system understandings
Model and its results must be correct for its ‘use’
[1] R G Sargent, “Verification and validation of simulation models”, Journal of Simulation (2013)

## Slide 4: Simulation Models & Verification
A model should be developed for a specific purpose (or application)
  Its validity determined with respect to that purpose
Often too costly and time consuming to determine ‘absolute’ validity
Tests and evaluations are conducted until sufficient confidence is obtained

## Slide 5: The Design-Under-Test (DUT)
Instruction-level fast simulation model (Just in time dynamic binary translation) of a modern 64b Processor
Optimized for simulation speed: block chaining, DMI, host register allocation, hierarchical TLB and Translation caching
Functional only
  No timing
Caches, pipeline stages and debug logic not modeled
Instruction Accurate
  Unmodified binaries can be ported from simulator to silicon

## Slide 6: Synchronized State Comparison
Very little work has been done on verifying correctness of processor simulators [2]
Previous work in this area has been focused on
  Hardware Verification
  Simulation Functionality
  Simulation Speed
[2] Bob Glamm and David J Lilja, “Automatic Verification of Instruction Set Simulation using Synchronized State Comparison”, IEEE Simulation Symposium (2001)

## Slide 7: Fuzzing based Automatic Test Generation
EmuFuzzer : Fully automated testing methodology for CPU emulators, based on fuzzing [3]
  Random Test case generation
  CPU assisted test case generation
Several functional defects reported in state-of-the-art CPU emulators – QEMU, Valgrind, Pin, BOCHS
  Development of CPU emulator is a very challenging task
  Need for specialized testing methodology
[3] Lorenzo Martignoni, et al, “Testing CPU Emulators”, ISSTA, 2009

## Slide 8: Test Framework

## Slide 9: Test Generation
Initialization Phase
  Register initialization
    Various Register Files: GPR, FPR, VR, Condition Code Registers
    System Register considerations (Invalid State Constraints, MMU constraints)
  Memory initialization
    Page Table Setup
    Opcode Fill
Execution Phase
  Instruction randomization
  Exception handling code insertion
Termination Phase
  Breakpoint on computed end address or exception address
  Instruction limit

## Slide 10: GPR and VR Initialization
Constrained-Random initial values for all register files
General purpose registers: Min, Max and 64-b random values
Vector registers: Min, Max and 128-b random values
SIMD operations enable/trap

## Slide 11: FPR Initialization
Floating point registers
  IEEE 754 Single, Double and Half precision formatting
  Special Values: Signed zeros, Subnormal numbers, Infinities, NANs
  FPCR: Rounding Modes, Default NAN, Trap Enables

## Slide 12: Processor State Initialization
Processor State
  Multiple test variants to cover all possible processor state settings
  Constraints to not enable processor states not modeled (debug, etc)
  Directed constrained tests to cover illegal/interrupt scenarios
Field | Description | Randomization
NZCV | ALU Flags | Fully randomized
DAIF | Exception Mask Bits | Fully randomized
SPSel | SP Select | Fully randomized
Current EL | Current Exception Level | Fully randomized
IL | Illegal Flag | Constrained
SS | Single Step | Don’t generate
E | Data Endian-ness | Fully randomized

## Slide 13: System State Initialization
System registers
  Multiple test variants to cover all interesting combinations
  Execution at all exception levels, computation modes, exception endianness, alignment control, vector base addresses, interrupt routing modes
  Avoid invalid state settings

## Slide 14: Test Generation: Instruction Randomization
Instruction decoding information from simulator fed to test generator
  Valid instructions with operands fully randomized
ADD (Shifted Register)
Instruction Operation
ADD Rd, Rn, Rm {<shift>, <amt>}
SF: 32b/64b values
S: Set Condition Codes
Shift: Shift Type to be applied
Imm6: Immediate Operand
Rd, Rn, Rm: Register Operands
Instruction Decode Data
Encoding: 0x0B000000
Mask: 0x7F200000
~Mask: 0x80DFFFFF
Generated Instruction Test
Encoding | (< 32b random value > & ~Mask)

## Slide 15: Test Generation: Invalid Operands
For some instructions, certain combination of operands result in illegal encoding
  Processor takes undefined interrupt when such instructions are executed
  Not possible to generate such instructions since assembler/compiler will never generate such opcodes
    Can be generated if using raw decode data from simulator itself for test generation
ADD (Vector)
Instruction Operation
ADD Vd, Vn, Vm
If size:Q == ‘110’ then undefined;
Instruction Decode Data
Encoding: 0x0E208400
Mask: 0xBF20FC00
~Mask: 0x40DF03FF
Generated Instruction Test
Encoding | (< 32b random value > & ~Mask)

## Slide 16: Test Generation: Using Assembler
Exception/Interrupt handling typically supported late in simulator development phase
Mechanism to generate tests without illegal operand combinations
  Retain capability to randomize operands
  Generate instructions as per the assembler syntax
ADD (Vector): add $V5, $V5, $V5
Generated Test
add V8, V20, V1
add V7, V3, V29
add V0, V12, V14
AND (Shifted Regsiter): and $X5, $X5, $X5, $SHIFT_R_4 #$UNSIG6
Generated Test
and X8, X20, X1 , ASR #32
add X7, X3, X29 , LSR #52
add X0, X12, X14 , LSL #38

## Slide 17: Test Generation: Alignment Requirements
Load/Store instructions have alignment requirements
  Stack Pointer needs to be aligned
  Any load/store address must be aligned under certain conditions
    Accessing Device Memory
    MMU disabled
    Alignment Check forced via system register settings
Add fix-ups in test generator to avoid alignment interrupts
  Add extra instructions to mask the index register value
  When using SP as index register
    Insert a instruction to align SP
    Insure immediate offsets are 16-byte aligned
ldrh Test: GPR as index
and X10,X10, 0xfffff00
ldrh W5, [X10], #112
and X14,X14, 0xfffff00
ldrh W16, [X14], #-25
ldrsh Test: SP as index
and SP, SP, 0xfffff00
ldrsh W10, [SP, #-240]!
ldrsh W22, [SP, #10]!

## Slide 18: Test Generation: Handling Branches
Fully randomized branch instruction operands can take the control to unknown memory addresses
Will result in uninitialized memory being read as instruction opcode
  Resulting in illegal/undefined interrupts
Add extra instruction to save the return address in X0
Fill uninitialized memory with “return X0” opcode
Constrain branch operands to be outside the test instruction memory range
branch test
adr x0, 8
B 67066032
adr x0, 8
B -30761752
branch test command line
./sim -s sim.uninit_mem_fill_word=+str(get_mem_fill_word(arch_prefix)) <rest of the arguments>
Example: ./sim -s sim.uninit_mem_fill_word=0x00005fd6 <other arguments>

## Slide 19: Test Generation: MMU Initialization
MMU Enabled or Disabled
System Register Controls
  Write Execute Never (WXN)
  Top bit – address size
  Page & Granule Size
  Translation Table Base Addresses
  Stage 1, Stage 2 enables
  Don’t care: Shareability and Cacheability controls
Address Translation System
  Translation regimes & stages
  Translation table format
  Memory Attributes
  Translation Faults

## Slide 20: Trace Generation
Both DUT and reference model generate execution trace when running a test
  Instruction address & opcode
  Register updates
    Any register update due to execution of the instruction will be captured – destination registers extracted from decode data
      GPR, FPR, VR, SPR, CR
    Any register update due to instruction taking exception/interrupt will be captured – custom tracing
      ELR, ESR, FAR, SPSR, CPSR, etc
  Memory updates
    Load/Store instructions accessing/updating memory
      Custom tracing via memory access interface
< Inst No > < Addr > < Opcode > : < Disassembly >
< Inst No > R < Reg Name > < Value >
< Inst No > MR< width > < VA > : < PA > < Value >
< Inst No > MW< width > < VA > : < PA > < Value >

## Slide 21: An Example Trace
2 1004 8b87a61d : ADD x29,x16,x7, ASR #41
2 R X29 CB613045F7B498D7
...
4 1008 f84c84c7 : LDR x7,[x6],#0xc8
4 MR8 0000fa00:00000000fa00 d65f0000_d65f0000
4 R X7 D65F0000D65F0000
4 R X6 000000000000FAC8
...
7 1018 f808148a : STR x10,[x4],#0x81
7 R X4 000000000007FE81
7 MW8 0007fe00:00000007fe00 76ace219_000ff900
…
9 1020 f800802a : STUR x10,[x1,#8]
9 R ESR_EL2 93ca8044
9 R FAR_EL2 00000002f2ebbd20
9 R ELR_EL2 00000000000001020
9 R SPSR_EL2 000003c5
9 R CPSR 000003c9
Arithmetic Inst
Memory Read Inst
Memory Store Inst
Memory Store Inst Causing Exception

## Slide 22: Trace Analysis
Post processing of execution traces from DUT and reference model
Determines equivalence between the two traces for each instruction execution
  Instruction address
  Instruction opcode
  Register updates
  Memory updates
Detect special scenarios
  Undefined behavior
    Exception during execution of a micro-op
  Known limitations
    Self Modifying code
    Low Power Instruction execution

## Slide 23: Generated Test Suites
Test Suite | Description | Number of Tests
Single Starter (ss) | Exercise Basic Functionality of every instruction – Integer, Floating Point, SIMD, Crypto: Arithmetic, Logical, Load, Store, Branch, System, etc Registers randomized – Fix-ups to avoid alignment requirement violations Operands constrained to avoid generating exceptions All computation modes | 20K
Jump Starter (js) | Same behavior as ss, but in a repeated fashion 100s of same instruction with different/random operands executing back to back | 20K
Instruction Mix (imix) | Random mix of various instructions with valid operands 1000s of instructions per test | 5K
Random ss/js/imix | ss/js/imix suites with System Registers randomized Execute instructions under different contexts set by system register settings | 45K
Random operands | Generated using raw decode data from simulator to cover invalid operand combinations – stresses on negative test case scenarios and exception handling | 45K
MMU Validation | Individual Control of MMU at different exception levels Support for virtual address, validation of different translation levels , TLB caching Random mix of Load, Store and Branch Instructions for different exception levels and computation modes | 5K

## Slide 24: Conclusion & Future Directions
Tests developed along with ISS development
  No extra/dedicated effort for model verification
  Leverage in-depth understanding as well as simulator code for ISS for model verification
  Instrument ISS for trace generation as required
Minimize test framework effort
  Instrumentation of golden model for trace generation
  Development of trace analysis tool
Thorough testing of required simulator features along with simulator development
  Several hard to find defects caught and fixed early in the development phase
Much less tests required to be generated to achieve desired coverage
  A few hundred thousand, instead of millions in pure fuzzing based approach
Future directions
  Code coverage measurement to detect simulator aspects weekly tested and increase focus on covering such aspects
    Challenges with JIT DBT as static instrumentation approach will not work with dynamically emitted/executed code

## Slide 25: Questions