## Slide 1: VirtIO based GPU model
Pratik Parvati
Lead Engineer
Vayavya Labs Pvt Ltd.

## Slide 2: CONTENT
The Problem
Host GPU accelerated Model
The Solution – Virtio
  Devices, Drivers.
  VirtIO transport layer.
VirtIO-GPU
  Devices, Drivers
Host GPU accelerated Model
  Controlq, cursorq
  Virglrenderer.
Demo

## Slide 3: What is the problem we are trying to address?
GPUs are essential components of modern computer systems.
CPU and GPU data transfer via slow off-chip interconnections (i.e., PCIe), which become the performance bottleneck.
RTL Design of GPU is time consuming – validating a system or subsystem is burdensome.
Challenges involved in modeling a full blown GPU.

## Slide 4: A sample block diagram with GPU
USB
GPU
DSP
MCU
Crypto
A/V interface
Interconnect
NVM
SRAM
Analog RF
DMA
ETH
SATA
HDMI
LPDDRx
PCIe
I-Cache
D-Cache
ARM
PHY Interface
RTL Design
Simulation Environment

## Slide 5: How do we model GPU
Cons with Full-blown SystemC model
  GPUs requires data structures that are more rigid than on conventional processors (CPU).
    Designed exclusively for high performance computing applications.
  GPUs have hundreds to thousands of processing elements.
    AMDs Radeon HD 6000 series of GPUs contain more than 1000 processing elements on a single GPU die.
  GPUs have hundreds to thousands of processing elements.
  Demands parallel simulators as sequential simulators are slow.
  Synchronization overhead by simulating the parallel components of the GPU architecture independently using multiple simulation threads.

## Slide 6: Host-GPU accelerated model
© Accellera Systems Initiative
6
USB
RTL Design
Simulation Environment
GPU is modelled on top of vitio interface.
Virtio-gpu driver compatible device.
Virtio-gpu driver is treated as embedded software on CPU.
Exploits Host CPU and GPU resources.
GPU
DSP
MCU
Crypto
A/V interface
Interconnect
NVM
SRAM
Analog RF
DMA
ETH
SATA
HDMI
LPDDRx
PCIe
I-Cache
D-Cache
ARM
PHY Interface
virtio

## Slide 7: Some graphics terms
Pixels - Rectangular grid, arranged in rows and columns on the screen.
Vertices - Co-ordinates of an objects like lines, curves and polygon.
Primitives - Building blocks containing lines, curves and polygon, which can be combined to create more complex graphical images.
Shader – Program that rests on GPU, that transforms set of inputs to output as per an algorithm.
Texture Mapping - Texture mapping applies an image to the faces of our geometry and adds realism to the scene.
OpenGL - Software interface to the graphic hardware
MESA drivers – Graphics library, is an open source implementation of OpenGL, Vulkan, and other graphics API specifications

## Slide 8: Introduction to VirtIO
VirtIO stands for virtual input & output and was developed by Rusty Russell.
VirtIO is an abstraction layer over a host’s devices in para-virtualized hypervisor.
Offloading the majority of the work to the host.
  Speeds up VM operation over more traditional "emulated" devices.
VirtIO is a standardized interface
Host NIC
Host
Request
Response
virtio_net
VM
NIC

## Slide 9: Why VirtIO?
Straightforward: VirtIO devices use normal bus mechanisms of interrupts and DMA.
Efficient: VirtIO devices consist of rings of descriptors for both input and output.
Standard: VirtIO makes no assumptions about the environment in which it operates.
Extensible: VirtIO devices contain feature bits which are acknowledged by the guest operating system during device setup.
Improved host and guest performance.
Exports a common set of emulated devices and make them available through common API.

## Slide 10: VirtIO Devices
Support different kinds of devices (network, block, video, GPU...)
Exposed to the emulated environment using PCI, Memory Mapping I/O, Channel I/O.
Device Model
VirtIO Frontend
VirtIO Backend
Host OS
Guest OS
VirtIO Transport Layer
VRing
The frontend component is the
guest side of the virtio interface.
The backend component is the
host side of the virtio interface.
VirtIO Transport Layer is a
channel between front -end
and back -end

## Slide 11: VirtIO Devices Cont..
Device IDs are used to identify different types of virtio devices.
All VirtIO devices have a Vendor ID of 0x1AF4, and have a DeviceID between 0x1000 and 0x103F.
All devices have a common “header” block of registers.
Offset (Hex) | Name
00 | Device Features
04 | Guest Features
08 | Queue Address
0C | Queue Size
0E | Queue Select
10 | Queue Notify
12 | Device Status
13 | ISR Status
The Guest Features register is used by the guest VM to communicate the features that the guest VM driver supports.
The Device Status field is used by the guest VM to communicate the current state of the guest VM driver.

## Slide 12: VirtIO Drivers
The front-end driver is the device
driver installed in the guest OS.
Accepts I/O requests from the user
process and transfer I/O requests to
back-end driver.
The back-end driver resides in the
hypervisor and is responsible for
accessing the physical device.
Accepts I/O requests from front - end
driver and perform I/O operation via
physical device.
virtqueues
Virtio front-end drivers
Device Emulation
Guest VM
Hypervisor(Qemu, KVM etc..)
Virtio back-end drivers

## Slide 13: VirtIO Transport Layer: VirtQueue
Virtqueue is a queue of guest’s buffer that host consumes, either by reading them or writing to them.
Virtqueues are shared in guest physical memory - driver and device access the same page in RAM.
The descriptors/buffer can be chained.
Driver to device notifications via doorbell method.
Device to driver notification via interrupt.
Virtqueue interface -
  add_buf: expose buffer to other end.
  kick: update after add_buf.
  get_buf: get the next used buffer.

## Slide 14: VirtIO Transport Layer: VRing
Vring is a memory mapped region between Host process (Device model) and guest OS.
Vring is the memory layout of the VQs abstraction.
Holds the actual data being transferred.
A virtio device contains one or more VQs.
VQs has three types of VRings (or areas):
  Descriptor ring (descriptor area)
  Available ring (driver area)
  Used ring (device area)

## Slide 15: VirtIO Transport Layer: Desc Area
Virtio Buffers: Guest drivers (front-end) communicate with hypervisor (back-end) drivers through buffer.
Guest provides one or more buffers representing the request.
These buffers are added to virtual queues in memory.
struct Buffers[QueueSize]
{
uint64_t Address; // 64-bit address of the buffer on the guest machine.
uint32_t Length; // 32-bit length of the buffer.
uint16_t Flags; // 1:linked buffer index; 2: Buffer is write-only.
// 4: Buffer contains additional buffer addresses.
uint16_t Next; // If flag is set, contains index of next buffer in chain.
}

## Slide 16: Virtio Transport Layer: Avail and Used Area
Avail Area: References to available descriptors in the descriptor ring.
Used Area: References to used descriptor entries on the descriptor ring.
struct Available
{
uint16_t Flags; // 1: Do not trigger interrupts.
uint16_t Index; // Index of the next ring index to be used.
uint16_t Ring[QueueSize]; // List of available buffer indexes from the Buffers array
}
struct Used
{
uint16_t Flags; // 1: Do not notify device when buffers are added to available ring.
uint16_t Index; // Index of the next ring index to be used. (Last used ring buffer index+1)
struct Ring[QueueSize]
{
uint32_t Index; // Index of the used buffer in the Buffers array above.
uint32_t Length; // Total bytes written to buffer.
}
uint16_t AvailEvent; // Only used if VIRTIO_F_EVENT_IDX was negotiated
}

## Slide 17: VirtIO Transport Layer: Data Exchange
addr | len | flags | next
0x100 | 0x100 | W¦N | 1
0x200 | 0x100 | W | 1
0x300 | 0x100 | W | 0
0
2
0
Desc area (collection of buffers)
Avail area
Used area
last avail idx
idx
last used idx
idx
Virtio driver
Virtio device model
Guest user space
Guest kernel space
Host user space
Process
Notification
Host kernel space
Hypervisor (KVM etc)
Interrupt
1
struct buffer{
….
};
1
Allocate/create buffer.
2
2
Populate descriptor entry.
3
3
Update avail index.
4
4
Send notification to device

## Slide 18: VirtIO Transport Layer: Data Exchange
addr | len | flags | next
0x100 | 0x100 | W¦N | 1
0x200 | 0x100 | W | 1
0x300 | 0x100 | W | 0
0
2
0
Desc area (collection of buffers)
Avail area
Used area
last avail idx
idx
last used idx
idx
Virtio driver
Virtio device model
Guest user space
Guest kernel space
Host user space
Process
Notification
Host kernel space
Hypervisor (KVM etc)
Interrupt
1
struct buffer{
….
};
2
3
4
5
5
Process the descriptors.
6
6
Send interrupt to driver.

## Slide 19: Virtio-GPU
Operate in 2D mode and in 3D (virgl) mode.
3D mode will offload rendering ops to the host gpu.
Supports two VQs
  Controlq: queue for sending control commands.
  Cursorq: queue for sending cursor updates.
Feature bits
  VIRTIO_GPU_F_VIRGL (0): virgl 3D mode is supported.
  VIRTIO_GPU_F_EDID (1): EDID is supported.
Configuration layout
  events_read signals pending events to the driver.
  events_clear clears pending events in the device.
  num_scanouts specifies the maximum number of scanouts supported by the device.

## Slide 20: Virtio-GPU - Device Operation
Create a framebuffer and configure scanout
  Create a host resource using VIRTIO_GPU_CMD_RESOURCE_CREATE_2D.
  Allocate a framebuffer from guest ram, and attach it as backing storage to the resource just created, using VIRTIO_GPU_CMD_RESOURCE_ATTACH_BACKING.
  Use VIRTIO_GPU_CMD_SET_SCANOUT to link the framebuffer to a display scanout.
Update a framebuffer scanout
  Use VIRTIO_GPU_CMD_TRANSFER_TO_HOST_2D to update the host resource from guest memory.
  Use VIRTIO_GPU_CMD_RESOURCE_FLUSH to flush the updated resource to the display.
Using pageflip
  It is possible to create multiple framebuffers.
  Update the invisible framebuffer using VIRTIO_GPU_CMD_TRANSFER_TO_HOST_2D.

## Slide 21: Device Operation: controlq
VIRTIO_GPU_CMD_GET_DISPLAY_INFO: Retrieve the current output configuration.
VIRTIO_GPU_CMD_GET_EDID: Retrieve the EDID data for a given scanout.
VIRTIO_GPU_CMD_RESOURCE_CREATE_2D: Create a 2D resource on the host.
VIRTIO_GPU_CMD_RESOURCE_UNREF: Destroy a resource.
VIRTIO_GPU_CMD_SET_SCANOUT: Set the scanout parameters for a single output.
VIRTIO_GPU_CMD_RESOURCE_FLUSH: Flush a scanout resource Request data.
VIRTIO_GPU_CMD_TRANSFER_TO_HOST_2D: Transfer from guest memory to host resource.
VIRTIO_GPU_CMD_RESOURCE_ATTACH_BACKING: Assign backing pages to a resource.
VIRTIO_GPU_CMD_RESOURCE_DETACH_BACKING: Detach backing pages from a resource.

## Slide 22: Device Operation: cursorq
VIRTIO_GPU_CMD_UPDATE_CURSOR : Update cursor.
VIRTIO_GPU_CMD_MOVE_CURSOR: Move cursor.

## Slide 23: Virglrenderer
Virglrenderer is a virtual 3D GPU library that
  enables a virtualized operating system to use the host GPU to accelerate 3D rendering.
Mesa handing commands are channeled through virtio-gpu on the guest to the host.
The host gets the raw state (Gallium state) and translates it into an OpenGL form using virglrenderer.
It is then run as regular OpenGL on the host system.

## Slide 24: Virglrenderer Contd..
Guest
Host
Application
virgl
virtio_gpu driver
Mesa
Kernel
Host Process
virtio_gpu device
virglrenderer
GPU Driver
GPU Hardware

## Slide 25: Qemu demo